## Slide 1: Automatic Guitar Tuner
Trenton Ahrens, alex capo, Ernesto wong
Group 1

## Slide 2: Motivation
Tuning can be time consuming
Difficult without extra equipment especially for beginners
The interest in music

## Slide 3: Specifications
Tune within 30 seconds
Within a noticeable difference of +/- 5 cents (100 cents/semitone)
5 tuning preferences on Android application
At least 24 hours of battery life

## Slide 4: 4-String Bass

## Slide 5: Overall System Block Diagram

## Slide 6: Division of Labor
Ernesto
  Android app development
  Code for tuning algorithm
  Bluetooth communication
  Trenton
  Signal Processing
  Mounting
  PCB design
  Alex
  Power supply
  Mounting
  Code for tuning algorithm

## Slide 7: Mobile Application
User Interface
Android Platform Version 4.4.X+
Android Studio
Java
Bluetooth communication with microcontroller
  Defined MAC address for module

## Slide 8: Android Studio IDE
Java language
  Object-Oriented
Class (.java file)
    Define variables and methods
Layout (.xml file)
  Widget (ie. buttons, text field) placement
Android Manifest
  Bluetooth Permissions

## Slide 9: Bluetooth Communication
Built in Bluetooth capabilities on phone
HC-05 Bluetooth module
5V VCC with 3.3V logic level Rx

## Slide 10: Microcontroller
ATMega328p chip
6 analog inputs 10-Bit ADC
12 Digital inputs/outputs
16 MHz operating freq.
24 pin dip package
C++ (Arduino bootloader)

## Slide 11: Pickups
Magnetic field seen by the pickups will induce an analog voltage that will be read by the ADC inputs
Magnetic single coil pickups

## Slide 12: Frequency Calculating
Midpoint crossings (2.5V)
Timer to determine period
T = 1/F
ISR

## Slide 13: Motor Control
Follows algorithm based on string, tuning preference
+/- 0.2 Hz threshold

## Slide 14: DC Offset & Amplification
Guitar signal from pickups is about 20mV-40mV
ADC 0-5V
DC offset to 2.5V

## Slide 15: Rail Splitter
TLE2426 “Rail Splitter”
Creates virtual ground
More stable than two individual batteries

## Slide 16: Motor Mounting Bracket
22 gauge sheet metal

## Slide 17: Tuning Mechanism
ROB 12472 standard gear motor
3-12 V operational input
38 lb-in torque
Bi-directional rotation
H-Bridge driver (L293DNE)
1A output
2 H-Bridge per chip

## Slide 18: Power
Battery Power – NiMH (Nickel Metal Hydride) rechargeable batteries
8xAA battery holster (Adafruit) = 9.36 V 2500 mAh
2x9V batteries in series = 18V

## Slide 19: Components to be Powered
Atmega328p (Amazon) 1.8-5V Operating voltage 0.2mA current draw while active
4x ROB-12472 Standard Gear Motor (Sparkfun) 3-12V operating voltage 95mA current draw @ 12 V
HC-05 Bluetooth 5 V
TL082CP OP Amp +/- 9 V
4xMotor(95mA) + Atmega328p(0.2mA) = 380.2mA
2500mAh/380.2mA = 6.57 hours battery life
2500mAh/95.2mA = 26.26 hours battery life (realistically)

## Slide 20: PCB Design
Eagle 7.2.0 light edition
OSH Park

## Slide 21: Component Decisions
6-String Electric Guitar vs. 4-String Bass Guitar
Polyphonic vs. Single Coil
ATmega328p
Threshold crossings vs. FFT
Gearmotor vs. Stepper vs. Servo
NiMH vs. Li ion
IC H-Bridge vs. DIY H-Bridge
Android > Apple

## Slide 22: Operational Procedure
Power on device tuning box
Select tune (T) on switch to select tuning
Activate Bluetooth on mobile application
Open Android application on mobile device
Connect mobile device to Bluetooth module
Select tuning preference
Tune strings

## Slide 23: Difficulties
Mounting of motors
  Cutting sheet metal
  Aligning motors
Bluetooth communication
  3.3V signal level
  Error message on app use
3 out of 4 motors working
  Pinout configuration on the board and in the code

## Slide 24: Budget
Part | Cost
4-String Bass Guitar | $0
4x Gear motors ROB-12472 | $ 119.96
Arduino Uno | $25.75
HC-05 Bluetooth module | $8.40
Shaft couplers & motor mounts | $46.00
2x H-Bridge (L293DNE) | $14.49
Sheet metal bracket | $20.00
Misc. wire & passive components | $20.00
Total: $254.60
Funding provided by Boeing : $200

## Slide 25: Questions?