## Slide 1: G.A.R.V.I.S. Gesture-controlled Automated Residency Via Intelligent System
Joshua Illes (EE)
Andres Mujica (EE)
Grant Schleich (EE)
Sarah Strauss (CpE)

## Slide 2: Roles and Responsibilities
Joshua Illes- EE
  Board Design (PLC and Capacitive Touch)
  Mechanical Packaging
Andres Mujica- EE
  Embedded Systems
  Glove Interface
Jackson Schleich- EE
  Board Design (Microcontroller and Power)
  Algorithms
Sarah Strauss- CpE
  UI Design
  Software

## Slide 3: Goals and Objectives
Make devices that are Plug and Play (Easy to install)
  Powerline Communication
Interface with the user in several ways
  LCD Screen, Android App, Smart Glove
Create “wearable tech” to control the system via gesture control
  Smart Glove
Gather useful data from every room of the house
  Smart Switch
Improve house environmental control
  Vent Control
Make an intelligent, autonomous, energy saving system
  Adaptive Algorithms
Notes: Combine motivations and Goals and Objectives into 1 slide

## Slide 4: Project Overview
Central Manager
Glove
Smart Switch
Home Hardware
Load
Controller
Home Hardware
Vent
Controller
Home HVAC
User Interfaces
Automation Hardware
Notes: Fix pictures, add more, talk about master/slave, mention

## Slide 5: Central Manager
Central Manager
Glove
Smart Switch
Home Hardware
Load
Controller
Home Hardware
Vent
Controller
Home HVAC
User Interfaces
Automation Hardware
Notes: Finish

## Slide 6: Central Manager: Hardware
Beaglebone
LCD Screen
Cape Requirements:
  Interface with PLC card
  Hold extra MSP430 for reading PLC signals
  Take power inputs for Beaglebone, LCD screen and PLC card
  Mounting headers for Xbee Module
  Control HVAC
Notes: Finish

## Slide 7: Processor Selection
 | BeagleBone Black Rev C | Raspberry Pi B+
Price | $54.49 | $39.95
Processor | AM335x 1GHz ARM Cortex-A8 | Broadcom SoC 700MHz
RAM | 512 MB | 512 MB
GPIO | 65 pins | 40 pins
Peripherals | 4 UARTs, 2 I2C ports, 2 SPI ports, 7 analog inputs, 8 PWMs, 4 timers | 1 UART, 2 I2C ports, 1 SPI port
*Other things to consider:
Library availability, capes/shields, personal preference

## Slide 8: LCD Screen Selection
 | 4D 7” LCD Cape | SainSmart 7” LCD Display
Price | $89.00 | $67.99
Resolution | 800 x 480 | 800 x 480
Driver | Included in Linux distro, plug and play | eGalaxTouch Driver for Linux
Power Source | via BeagleBone, 5V 2A | 5V 2A
Requirements:
Touchscreen
Minimum 7” size
BeagleBone Compatability

## Slide 9: Central Manager: Software Design
Front end
  Qt GUI
  Android Application
Back end
  I/O Control
    Touchscreen I/O
    UART I/O
    HVAC I/O
  Algorithms
    Gesture Recognition
    Adaptive Command and Control
  Server

## Slide 10: Operating System: Embedded Linux Debian Distribution
Open source, helpful for our budget
More readily available drivers, allows touch screen to be plug and play
Plenty of documentation and online support
The team has previous knowledge of Linux

## Slide 11: UI Framework: Qt
Qt is an application and UI framework for developing in C++
Cross platform – allows for use in desktop, mobile, and embedded applications
  Same application can run on both embedded Linux and Android
Qt kits allow for the correct configuration of build and run settings for cross platform compatibility
  Front end can remain the exact same while back end deals with variations in the OS being ran on
Small learning curve, very similar to C++
Easy to import libraries, BlackLib in particular

## Slide 12: Central Manager GUI

## Slide 13: Central Manager GUI
Setup and Configuration
Add a new room
Select a room
  Start Detect Device Sequence
Enable/disable Smart Decision Mode

## Slide 14: Central Manager GUI
Room Manager
Select a room
All devices in room can be configured and all sensor data is displayed

## Slide 15: Adaptation
Smart Decision Mode enables autonomous adaptation
Adaptation Parameters: Fringe condition/error control with short term data
Adaptive Algorithms: Pattern recognition with long term server data
Parameter | Restraint
HVAC Ventilation Command | If commanded on, must remain on for a minimum of 10 minutes. If commanded off, must remain off for a minimum of 10 minutes.
Home Lighting Device Command | If commanded on, must remain on for a minimum of 5 seconds. If commanded off, must remain off for a minimum of 5 seconds.
Humidity Status | If humidity reaches dangerously high conditions for extended amounts of time, turn on ventilation system.
Temperature Status | If temperature reaches user defined maximum and minimum thresholds, automatically turn on/off AC/heater

## Slide 16: Smart Switch
Central Manager
Glove
Smart Switch
Home Hardware
Load
Controller
Home Hardware
Vent
Controller
Home HVAC
User Interfaces
Automation Hardware

## Slide 17: Smart Switch Overview
Front End Board
Capacitive Touch Human Interface
Ambient Light
Microphone
Haptic Feedback
LEDs
Microcontroller Board
Communicate with other chips
Communicate to PLC board
Temperature & Humidity Sensors
Power Line Communication
Use TI AFE031 to interface w/ mains
Handle signal filtering and conditioning
Transform digital data to mains transmissions
Power Supply
Input120VAC
Outputs 15, 5& 3.3 VDC
Notes: Fix text – Josh, We need to mention how this is the main focus of the project

## Slide 18: Smart Switch
Notes: Add - Josh

## Slide 19: Smart Switch Requirements
Specification | Value | Unit
Capacitive Reaction Time | 2 | Seconds
Temperature Accuracy | +/- 1 | Degree
Humidity Accuracy | +/- 5 | Percent
Passive Infrared Range | 12 | Meters
Ambient Light Sensitivity | 10 | Lumens
Physical Size | Must fit within single gang box | 
Notes: Make this a table

## Slide 20: Front End Design Choices
TI TLC5947 - LED Driver
  Controls 24 separate PWM channels
  Uses serial interface to reduce total I/O
  Internal oscillator
Atmel QT1085 – Capacitive Touch Driver
  8 capacitive touch channels
  Embedded haptic engine
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 21
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 22: Front end PCB
Layout
Physical Front
Physical Back
Front End Board
Microcontroller Board
Power Line Communication
Power Supply
Notes: Get rid of white on layout - Josh

## Slide 23: Microcontroller Board Overview/Design Choices
Must mate with surrounding boards
Electrical – Two microcontrollers
  MSP430G2553 – Reads PLC signals, translates Analog data to Digital signals
  MSP430F5529 – Interprets commands, monitors sensors, user interface
Features
  JTAG ports
  Debug I2C, LEDs & pins
Timing – 32.768 kHz crystal for real-time-clock
Front End Board
Microcontroller Board
Power Line Communication
Power Supply
Notes: Finish

## Slide 24
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 25
Front End Board
Microcontroller Board
Power Line Communication
Power Supply
Notes: Grant, label the measurement units

## Slide 26: PLC Overview
Transmit Data with 60Hz 120V Carrier Wave via Frequency Shift Keying
Carrier Wave
Carrier wave with data
MSP430
Digital Data
Amplified FSK Sine Waves
High Pass Filter (block 60 Hz)
AC Mains
Front End Board
Microcontroller Board
Power Line Communication
Power Supply
Notes: Finish - Josh

## Slide 27
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 28
1.5”
2.75”
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 29: Power Supply Board Overview
Maximum Power Requirements
  15V – 9W – PLC communication, low duty cycle
  5V – 3W – Various sensors,
  3.3V - 2W – Powered off of 5V rail, Microcontrollers and ICs
Constraints
  Transformer and Bulk Capacitor Size
120VAC
F48-250-C2-B Transformer
24VAC
Z4DGP408L-HF Full Bridge Rectifier
1800uF Bulk Capacitor
33VDC
5V Regulator
LM43602
15V Regulator
TPS54336
3.3V Regulator
TPS61240
15VDC
5VDC
3.3VDC
Front End Board
Microcontroller Board
Power Line Communication
Power Supply
Notes: Fix picture, add bulk capacitor equations

## Slide 30: Smart Switch Power Supply
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 31: Smart Switch Power Supply
Front End Board
Microcontroller Board
Power Line Communication
Power Supply
Voltage (V) | Inominal (mA) | Ipeak (mA) | Pnominal (W) | Ppeak (W)
15 | 200* | 600* | <1* | 9*
5 | 100 | 200 | .5 | 1
3.3 | 110 | 550 | ~.36×(2-e) | ~1.82×(2-e)
Max Power from Transformer
~12W
Bridge Rectifier e≈.97
*At max power
Voltage Regulator e≈.9
Available Power
~10.46W
e = efficiency of 5V regulator

## Slide 32
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 33
Front End Board
Microcontroller Board
Power Line Communication
Power Supply

## Slide 34: Smart Switch Interface
Notes: Add animation for title/picture

## Slide 35: Smart Switch Software Path
Notes: Make state diagram, add CTS/RTS interrupt system

## Slide 36: Load Control
Central Manager
Glove
Smart Switch
Home Hardware
Load
Controller
Home Hardware
Vent
Controller
Home HVAC
User Interfaces
Automation Hardware

## Slide 37: Load Control
Utilize Triacs for AC power control
Use power MOSFETS for DC control
Load Power Consumption Monitoring
Spec | Limit | Units
DC Voltage | 24 | Volts
DC Current | 5 | Amps
AC Voltage | 240 | Volts
AC Current | 20 | Amps
Notes: Diagram showing how triac control works

## Slide 38: Vent Control
Central Manager
Glove
Smart Switch
Home Hardware
Load
Controller
Home Hardware
Vent
Controller
Home HVAC
User Interfaces
Automation Hardware

## Slide 39: Vent Control
Electrically Actuated Vent to allow or restrict airflow into a room.
Communicate to Central manager over PLC
Measure temperature of airflow
Courtesy of SunCourt and Smarthome.com
Notes: Update, add pictures

## Slide 40: Vent Control
TI DRV8818
Stepper Motor Driver
Use Smart Switch boards for power, logic & PLC
Temperature sensor mounted inside vent
Notes: Add pictures

## Slide 41: Smart Glove
Central Manager
Glove
Smart Switch
Home Hardware
Load
Controller
Home Hardware
Vent
Controller
Home HVAC
User Interfaces
Automation Hardware

## Slide 42: Glove Requirements
Capable of measuring degree of bend for each finger
Measure linear and radial acceleration fast and accurate enough to allow for hand gesture detection
Have an intuitive user friendly interface with feedback
Notes: Combine this slide with next slide

## Slide 43: Glove Hardware
Part Number | Manufacturer | Description | Range | Resolution | Interface
LSM303DLHC | STMicroelectronics | 3-axis Accelerometer | ±16g | 16 bits | I2C
L3GD20 | STMicroelectronics | 3-axis Gyroscope | 2000 °/s | 16 bits | I2C
FSL0022253ST | SpectraSymbol | Flex Sensor | 25 kΩ - 100 kΩ | 36 °/V | Analog
ATMEGA328 | Atmel | Microcontroller | N/A | N/A | N/A
CEM-C9745 | Challenge Electronics | Microphone | 100Hz-10kHz | N/A | Analog
PS1240 | TDK | Piezo Buzzer | 1.5kHz – 8kHz | N/A | Digital
063048 | Unionfortune | LiPo Battery | 2.75V – 4.2V | N/A | N/A

## Slide 44: Glove Overview

## Slide 45: Glove Schematic

## Slide 46: Glove PCB

## Slide 47: Glove State Diagram

## Slide 48: Glove Software
Input Control
  Receives and un-packages raw sensor data from glove
Data Manager
  Stores all sensor data and provides it to the output control and gesture recognition algorithms
Command Creation Algorithms
  Converts raw analog data into usable sensor data
  Calculates what gesture was recognized and creates a command for the gesture
Output Control
  Sends commands to external applications

## Slide 49: Prototypes
3D Printed Cover
3D Printed Cover (Higher Res)
Touch Board Mechanical Outline
Acrylic Touch Panels
Notes: Add more pictures/slides

## Slide 50: Finances
Item | Total Price | Supplier | Category
Beaglebone Black | $ 54.95 | Amazon | Hardware
4D systems LCD | $ 99.95 | Sparkfun | Prototyping
SainSmart LCD | $ 65.00 | Amazon | Prototyping
SunCourt Vent | $ 60.00 | Amazon | Parts
Power Supply v1 | $ 9.97 | Osh Park | PCB
Power Supply v2 | $ 32.30 | Osh Park | PCB
Glove | $ 22.00 | Osh Park | PCB
PLC Communication | $ 29.30 | Osh Park | PCB
Power Supply v1 | $ 98.20 | Digikey | Electronic Components
Power Supply v2 | $ 156.20 | Digikey | Electronic Components
Smart Glove | $ 91.33 | Digikey | Electronic Components
PLC Communication | $ 147.18 | Digikey | Electronic Components
Smart Switch | $ 42.09 | Digikey | Electronic Components
Breakout Boards | $ 73.10 | Sparkfun | Prototyping
Stepper motor | $ 6.95 | Sparkfun | Parts
Xbees | $ 46.90 | Sparkfun | Prototyping
Li-Ion Battery | $ 17.90 | Sparkfun | Parts
Miscellaneous | $ 39.70 | Multiple | Electronic Components
Prototyping | $ 15.99 | Multiple | Miscellaneous
Total | $ 1,109.01 |  | 
Company | Amount
Duke Energy | $1725.50
Leidos | $ 700.00
SoarTech | $ 500.00
Total | $ 2925.50
Notes: Add total funding, fix table

## Slide 51: Progress
Chart: 
| Glove | Smart Switch | Central Manager | Load Control | Vent Control
Implementation | 0.5 | 0.2 | 0.4 | 0.05 | 0.3
Design | 0.8 | 0.65 | 0.5 | 0.1 | 0.8
Research | 0.9 | 0.9 | 0.9 | 0.7 | 0.9
Notes: Make legend bigger

## Slide 52: Successes Summary
Central Manager
LCD Touchscreen Works
GUI prototype works
Smart Switch
Successfully controlling LED Driver chip
Successfully communicating with Capacitive Touch Chip
3D printed Smart Switch Cover
All Smart Switch PCBs fit in standard switch enclosure
Smart Glove
Smart glove prototype is functional and moving mouse on screen with accelerometer/gyroscope data
Glove PCB eliminates need for development board and fits on top of user’s hand
Overall
Majority of PCBs have been sent out

## Slide 53: Moving Forward…
PLC communication code
Manufacturing of remaining PCBs
Testing all PCBs
Adaptive Algorithms
Server
Porting to Android App
Notes: Organize

## Slide 54: Questions?