## Slide 1
Sponsored by:
Duke Energy Leidos Texas Instruments Anaren
Group #26
Shawn Mahon Dennis Moy Junhao Liang

## Slide 2: Project Description
The “Cool Roommate” system will be a third party, A.I. system, capable of controlling temperature environments using household infrastructure
Consists of four units
  Master Controller (Thermostat)
  3 Slave Controllers (Fan, Vents, and Blinds)
Units will be automated, and will read in data to adjust environments.

## Slide 3: Goals
To maximize energy efficiency
Provide target climate control
Have automated response from system, to watch your house while you are away
Ideal for a variety of users

## Slide 4: Objectives
Master Controller (Powered by Tiva C)
Evaluate current temperature conditions.
  Actively monitor temperature conditions and response will be from requested user input
  Specify “target” zones so a user can be able to focus on specific rooms to combine efficiency with specificity.
  Transmit data to slave controllers to operate
Slave Controllers (Powered by MSP430)
Operate on command from Tiva C
Have automotive response to perform action
Wirelessly receive instructions from Master Controller.

## Slide 5: Physical Layout

## Slide 6: Cool Roommate
Each function is independent and controlled by the Tiva C.
The Tiva C also takes feedback from the MSP430’s temperature sensors and send different signals to each control according to the reading.
  Ex: Room is too hot, so it focuses the air circulation to cool off the room.
Slave controllers are not capable of communicating between each other. All messages are passed through the master.

## Slide 7: Hardware for Deliverables
Cortex M4 TM4C1294NCPDT
RF Module
LCD Display
Temperature sensor
Wi-Fi module (Optional).

## Slide 8: Cool Roommate Subsystem
RF Module MSP430 Servo Motor (Task Pending)

## Slide 9: Choosing temperature sensor
 | LM35 | INA330 | TMP006
Supply Voltage Range | +4V to +20V | +2.7V to +5.5V | 2.2 V to 5.5 V
Operating Temperature Range | -55°C to 150°C | –40°C to +85°C | –40°C to +125°C
Typical Accuracy | ±1⁄4˚C | 0.009°C | ±0.5°C
Pin Count | 3 | 10 | 8
Price | $5.00 | $4.95 | $4.33
Notes: LM 35 was free.

## Slide 10: Thermometer Sensor
To receive the output for controllers to read and react.
High precision temperature sensors factory calibrated with a typical accuracy of ±1⁄4˚C.
Notes: Advantages
Wide input range typically 4V to 20V
Typical accuracy of ±1⁄4˚C
Low cost
Rated operating range of −55˚ to +150˚C
Available in a variety of packages
Free courtesy of Texas Instruments

## Slide 11: LM35 Implementation Test
The output voltage changes based on temperature

## Slide 12: Vent Automation
Vent-Miser
Opted to purchase an automated vent from Vent-Miser.
As a result, resources and the budget had limited impact.
  Mechanical issues avoided

## Slide 13: Design Approach
Keep the system simple
  Maximize efficiency and focus of product
  Plug-N-Play design
Achieve precision and accuracy with sensors
  LM35 is within 2% accuracy
  Servos selected to maintain precise movements, know position at all times
Low Power to not overwhelm resources
  Power Supply averages 78% efficiency
Notes: Need formulas

## Slide 14: Core System Block Diagram
Notes: Micro Controller CK

## Slide 15: MicroController
 | Device | Flash | Pin Count | Max Frequency | RAM | CPU | Max I/O pins | SPI | Temp. Sensor | Min VCC | Max VCC | Active Power (μA/MHz) | Standby Power (μA) | Operating Temperature Range (oC) | Package |  |  |  | Price
32-bit AVR UC3 | AT32UC3L032 | 32 Kbytes | 48 | 50 MHz | 16 Kbytes | 32-bit AVR | 17 | 5 | Yes | 1.62 V | 3.6 V | 165 | 0.6 | -40 to 85 | 48-pin TQFP/QFN/TTLGA |  |  |  | $9.07
megaAVR | ATmega328P | 32 Kbytes | 32 | 20 MHz | 2 Kbytes | 8-bit AVR | 23 | 2 | Yes | 1.8 V | 5.5 V | 200 | 0.75 | -40 to 85 | 28-pin PDIP | 32-lead TQFP | 28-pad QFN/MLF | 32-pad QFN/MLF | $4.21
MSP430 | MSP430G2553IN20 | 16 Kbytes | 20 | 16 MHz | 512 Bytes | 16-bit MSP430 | 16 | 1 | Yes | 1.8 V | 3.6 V | 330 | 0.7 | -40 to 85 | 32VQFN | 20TSSOP | 28TSSOP | 20PDIP | $3.64
Notes: CK

## Slide 16: Slave Controller
Notes: Capacitor is a low pass filter, suppress noise and block out high freq. The reset pin requires a resistor. Active Low reset. The switch is tethered to ground, so when the switch connects it becomes low. CK

## Slide 17
Notes: CK

## Slide 18
Notes: CK

## Slide 19: Liquid Crystal Display
Separate unit from the MCU
  Attached to Tiva C
Plug-N-Play capabilities
  Simplifying the need for parts and reducing load on integration
Less maintenance
Notes: Dennis

## Slide 20: Design Implementation
Notes: Dennis

## Slide 21: Design Implementation
3D printed a turn key for the vent.
Will be connected to servo that will receive commands
  Tested and Working
Still need to integrate!
Notes: Dennis

## Slide 22: Blinds Integration

## Slide 23
Notes: Dennis

## Slide 24: Relay for fan
Rating
  Single-Pole Single-Throw
  10A contact
  5V coil
  100mΩ max contact resistance
Notes: Need a higher current relay because devices may be directly connected to the wall. Within the scope of the project to design efficiently and can allow for 300V. Have a light to show on and off. Diode is in reverse bias to protect the rest of the circuit. Typical applications include home appliances and vending machines.
Dennis

## Slide 25: RF Wireless
A low-power wireless transceiver compatible with the MSP430 microcontroller
Advantages
  Low power consumption
  Low Cost
  ISM Bands at 868/915MHz
Notes: ISM Bands beneficial because it is in an uncongested frequency, better to pass through walls than the standard 2.4GHz
Dennis

## Slide 26
Notes: Dennis

## Slide 27: Development Environments
Language: C/C++
Testing: Energia
Implementation: Energia
  Wireless: Unlicensed ISM Band 868/915MHz
Schematics: KiCad EDA
Notes: CK

## Slide 28
MCU Master Flowchart
Notes: CK

## Slide 29: MCU Slave Flowchart
Notes: CK

## Slide 30
Tiva C Schematic
Notes: CK

## Slide 31: Relay Board
Notes: Fan, Heat, and Cool each relay

## Slide 32: Power Management
Wide input range
  4-40V DC input or 6-24V AC
5V 1A Output
  Supply to LCD and Relays
3.3V 1.5A Output
  MCU,RF transceiver, and other sensor units
  Linear regulator improves efficiency
Notes: The 3.3V is tethered to the 5V power rail, therefore limiting the output capabilities of the 3.3 rail to 5Watts. Data sheet for 3.3v suggests a 3Amp capability
CK

## Slide 33: Low Voltage Power Supply
Notes: CK

## Slide 34: Voltage Ripple
Voltage ripple across the output power rails is currently
  5V power rail has approximately 28mV ripple effect
  3.3V power rail has approximately 24mV ripple effect
Notes: If swing is too high, such as a one volt ripple can create a lot of noise as well as create an unwanted voltage swing.
CK

## Slide 35: Current Market
Advantages
Disadvantages
Scalable
Efficient
Cost Effective
Future Growth Capabilities
Hard to integrate
Sacrifice quality for price
Notes: shawn

## Slide 36: Remaining Tasks
Finish Tiva C PCB Design
Order Board
Debug Debug Debug
Integration and Test
Notes: shawn

## Slide 37: Progress
Chart: 
| Research | Design | Parts Acquistion | Software | Testing | Overall
Completed | 0.95 | 0.7 | 0.75 | 0.8 | 0.3 | 0.7
To Go | 0.05 | 0.3 | 0.25 | 0.2 | 0.7 | 0.3
Notes: shawn

## Slide 38: Budget
Subsystem | 
PCB | $25.55
Vent-Miser (2) | $15.11
Circuit Equipment | $57.97
Blinds | $25.88
Pizza and Steak | $1015.49??
Total | $124.51
Current budget
Predicted spending
Part | Quantity | Total
MCU | 4 | $100.00
Wireless Module | 4 | $100.00
PCB | 4 | $80.00
Sensors | 4 | $80.00
Servo Motor | 4 | $80.00
LCD Display | 4 | $400.00
Miscellaneous |  | $300.00
Alloted Budget |  | $1140.00
Notes: shawn

## Slide 39: Questions?