## Slide 1: Maze Twinbots
Group 28
Uyen Nguyen – EE
Ly Nguyen – EE
Luke Ireland - EE

## Slide 2: Project Goals and Objectives
Create a team of maze solving robots that find the optimal solution to a maze using two algorithms
Robots must consume low power
Robots must be low cost
Robots must communicate via wireless technology

## Slide 3
Specifications

## Slide 4: Motor Selection
 | Stepper Motor | Servo Motor | DC Motor
Pros | Ideal for positional control | Precise and quiet | Ideal for speed control
 | Requires no tuning | Available in several standard sizes | 
Cons | Slow and noisy | Requires tuning | Requires an H bridge
 | Requires an external control circuit Limited sizes | Rotate up to 180° but can be modified for continuous rotations | 

## Slide 5: Microcontroller Selection: MSP430F5529
Coincides with low power goals of the project
More than enough I/O pins (Analog and Digital)
All team members are familiar with it
Plenty of documentation and support
Energia IDE for programming

## Slide 6: Different Communication Methods
Wi-Fi- connection can be made anywhere that has internet access, however, this frequency and is highly susceptible from interference
Bluetooth- Low power, efficient, lots of support, however, has shorter range due to low power output in transmit
Sub-GHz- Low Power, farther range than 2.4 GHz, less noise in utilized frequency band

## Slide 7: Communication Decision
Sub-GHz RF
  Same advantages as Bluetooth (low power consumption)
  Has longer range than a 2.4 GHz counterpart (2.4 GHz requires about 8.5 dB additional input power for same range as 900 MHz)

## Slide 8: Communication Hardware
Integrate transceiver and antenna
Small package (9 x 16 x 2.5mm)
900-928 MHz operating frequency
Low power consumption (200 nA sleep mode current consumption , 15 mA in receive)
“Burst transmission” of up to 60 bytes
AIR Module Boosterpack from TI to use for prototyping
Interfaces with SPI on MCU for easy configuration
Anaren AIR Module

## Slide 9: Challenges with Communication Hardware
Understanding how to integrate AIR module to MCU
  Had to compare four different sets of documentation to understand what each pin needs
Deciding which pins to use to avoid eliminating UART communication capabilities

## Slide 10: Sensors
 | Advantages | Disadvantages
Magnetic | Operate at high frequency | Affected by external magnetic fields
Capacitive | Cheap, low power | Affected by temperature and humidity
Inductive | Accurate, high switching rate | Cannot detect non-metallic objects
Ultrasonic | Not affected by colors, rain or dust | Affected by air movements
Infrared | Cheap, low power | Can’t detect objects that are too close Cross interference

## Slide 11: Ultrasonic sensor

## Slide 12
Linearize IR sensor

## Slide 13: Dead End Filler
Good
Fast
Requires little memory
Bad
Cannot be used to solve the maze

## Slide 14: Trémaux’s algorithm
Good
Prevent robot going in circle and visiting the same place more than twice
Bad
Need some sort of marking mechanism

## Slide 15: Pledge Algorithm
Good
Require little memory
Bad
Not compatible with the maze structure

## Slide 16: Wall following method
If possible, turn left
Else, go straight
Else, turn right
Else, turn around
Good
Fast
Require little memory
Always find the exit if there’s one
Bad
Go in a circle if the start or the end points are inside the maze

## Slide 17: System Block Diagram
Switching Regulator
Battery
3.6 V
Left Sensor
Right Sensor
Middle Sensor
Left Servo
Right Servo
5 V
LDO Regulator
Microcontroller
3.6 V
3.3 V
PWM Signal
PWM Signal
Radio Module
Sensor data
3.3 V
SPI bus data

## Slide 18: Schematic

## Slide 19: Schematic
POWER REGULATION

## Slide 20: Schematic

## Slide 21: Schematic
SERVOS AND SENSORS HEADERS

## Slide 22: Robot Model

## Slide 23: Maze Construction
One optimal solution
Walls will be approximately 8 inches tall
Pathways will be wide enough for robot to fully turn around
Maze will be made of wood and be reconfigurable

## Slide 34: Budget

## Slide 35: Division of Labor
Uyen | Ly | Luke
Sensor Integration | PCB Design/Layout | Communication Hardware
Maze Solving Algorithm | Hardware Integration | Maze Construction/Design
Software Integration | Motor Integration | PCB Assembly

## Slide 36: Progress
Chart: 
| Total | Prototyping and Testing | Design | Research
Series 1 | 0.5 | 0.25 | 0.8 | 0.95