## Slide 1: Maze Twinbots
Group 28
Uyen Nguyen – EE
Ly Nguyen – EE
Luke Ireland - EE

## Slide 2: Project Goals and Objectives
Create a team of maze solving robots that find the optimal solution to a maze using two algorithms
Robots must consume low power & be low cost
Robots must communicate via wireless technology
Serve the students as a learning experience on system design and integration

## Slide 3
Brief Overview of Maze Solving Algorithms

## Slide 4: 3D Perfect Maze
No loop
No inaccessible areas
Has exactly 1 solution
Rectangular cells intersect at 90°
Start and exit at the outermost wall

## Slide 5: Wall Follower
Left-hand robot
If possible, turn left
Else, go straight
Else, turn right
Else, turn around
Pros
Fast
Require little memory
Always find the exit if there’s one
Cons
Go in a circle if the start or the end points are inside the maze

## Slide 6: Hardware Overview

## Slide 7: Requirements
Component | Parameter | Value
Battery | Max Voltage | 4.8V
Microcontroller | Min. # of Analog Pins Min. # of Digital Pins Memory Clock Speed | 4 6 >24 kB >= 16 MHz
Motor | Speed Weight Torque | ~50 RPM <50 g >2 kg-cm
Sensor | Measuring Distance | 4-100 cm
Wireless | Range | > 3 m

## Slide 8: Motor Selection
Parallax servo
Requires no external control circuit like DC and stepper motors
Doesn’t require modification for continuous rotation
Acquired for free

## Slide 9: Servo Specifications
Voltage input: 4-6 V
Maximum current drawn: 140 +/- 50 mA at 6 V in no load condition
Weight: 42.5 g
Speed: 0 to 50 RPM

## Slide 10: Pulse Width Modulation (PWM)
20 ms delay between pulses
Robots PWM:
  CCW: 1600
  CW: 1400

## Slide 11: Servo Challenges
Requires multiple calibrations during tests
Servo centering
Lost positional control
  After scanning, front servo doesn’t return to center point
  Requires adjustment every 2-3 turns

## Slide 12: Sensors
 | Advantages | Disadvantages | Specification
Ultrasonic | Not affected by colors, rain or dust | Can cross-talk with other ultrasonic sensors if not positioned properly | Voltage: 5 V Current: 15 mA Range: 2cm – few meters
Infrared | Cheap, low power | Can’t detect objects that are too close Cross interference | Voltage: 5V Current: 12 mA Range: 4cm – 30cm

## Slide 13: Ultrasonic sensor HC-SR04

## Slide 14
Linearize Sharp IR sensor

## Slide 15: Microcontroller Selection: MSP430F5529
Coincides with low power goals of the project
More than enough I/O pins (Analog and Digital)
All team members are familiar with it, LaunchPads available for prototyping
Plenty of documentation and support, E2E community
Energia IDE for programming
High enough clock speed for quick data processing (25MHz)
128 kB of memory to store program

## Slide 16: Communication Decision
Sub-GHz RF
  Same advantages as Bluetooth (low power consumption)
  Has longer range than a 2.4 GHz counterpart (2.4 GHz requires about 8.5 dB additional input power for same range as 900 MHz)
  Could have used Bluetooth for our application since range is not large, team wanted to become familiar with a popular wireless communication technology being used in industry

## Slide 17: Communication Hardware
Integrate transceiver and antenna
Small package (9 x 16 x 2.5mm)
900-928 MHz operating frequency
Low power consumption (200 nA sleep mode current consumption , 15 mA in receive)
“Burst transmission” of up to 60 bytes
AIR Module Boosterpack from TI
Interfaces with SPI on MCU for easy configuration
Anaren AIR Module
Reprinted with permission from Anaren

## Slide 18: Challenges with Communication Hardware
Understanding how to integrate AIR module to MCU
  Had to compare four different sets of documentation to understand what each pin needs
Deciding which pins to use to avoid eliminating UART communication capabilities

## Slide 19: System & PCB Design

## Slide 20: System Block Diagram
Switching Regulator
Battery
4.8V
Left Sensor
Right Sensor
Middle Sensor
Left Servo
Right Servo
5 V
LDO Regulator
Microcontroller
4.8 V
3.3 V
PWM Signal
PWM Signal
Radio Module
Sensor data
3.3 V
SPI bus data

## Slide 21: System Schematic

## Slide 22: Power Supply

## Slide 23: JTAG Interface

## Slide 24: Anaren AIR Module

## Slide 25: PCB Layout
2.95”
4.5”

## Slide 26: Lessons Learned in Hardware Design
Reference designs should be utilized whenever possible
Components that are not necessarily in design libraries can be replicated with multiple components that meet same spacing and size requirements
More is not always better, simplifying a design can save hours in hardware troubleshooting and ease routing
Prototype as much as possible before creating PCB

## Slide 27: Navigation Overview

## Slide 28: Right-Wall Following
9 – 10 cm
Go straight
< 9 cm
Slight left
> 10 cm
Slight right
Read right sensor
Maintain straight

## Slide 29: Right-Wall Following
Turn right
Move up
Turn right 90 °
Move up
Adjust to maintain straight if right > 15 cm

## Slide 30: Right-Wall Following
Turn left

## Slide 31: Right-Wall Following
Turn around

## Slide 32: Sensors Challenges
Fluctuations when obstacles are far away
  40 cm – 100+ cm
More fluctuations during movement than stop
  Detect false junctions
Doesn’t have a 360° scanning of the environment
  Sometimes hit obstacles
Sensor placement is critical to maintaining straight and turning correctly
Navigation is highly dependent on individual sensors’ performance
Only one front sensor can detect 4-way junction

## Slide 33: Sensor Challenge Resolutions
Filter out fluctuation by select the lowest value out of 10 samples
Sample every time the previous and next readings differ by 10 cm
Count number of reading jumps to eliminate false -| junction

## Slide 34
Maze Solving Algorithm Overview

## Slide 35: Example Maze

## Slide 36: Left Robot Navigation = LLBSBLLLLSBL

## Slide 37: Right robot solution = SLLR

## Slide 38: Communication
Transmit SLLR
Send a Y as acknowledgement
Right Robot
Left Robot

## Slide 39: LLBSBLL  LRBLL LRBLL  LBL LBL  S

## Slide 40: S is compared to solution SLLR Match!

## Slide 41: LLBSB  LRB Compare to solution SLLR Do Not Match!

## Slide 42: Budget
Item | Cost
Jumper Wires | $24.72
13 Ultrasonic Sensors | $22.85
1 Chassis | $12.74
2 Breadboards | $7.98
2 Battery and Charger | $31.94
3 PCBs | $37.85
5 IR sensor cables, 1 sensor bracket | $23.70
Velcro Tape | $4.79
2 Crystals (4 MHz, 32.768 kHz) | $13.04
2 IR Sensor Cables | $13.74
2 Battery Holders | $5.31
6 Radio Modules | $109.93
2 Wheels, Rubber Bands for Wheels, 2 Servos | $43.04
Miscellaneous Components | $192.92
Wood | $27.96
Total | $572.51

## Slide 43: Division of Labor
Uyen | Ly | Luke
Maze Solving Algorithm | Initial System Design | System & PCB Design/Layout & Assembly
Sensor Testing | Navigation Implementation | Communication Hardware Testing
 | Motor Testing | 

## Slide 44: Questions?