## Slide 1: Electri-Surf
Group 22:
  Alex Amoros – Computer Engineering
  D. Anthony Higgins – Electrical Engineering
  Ryan Taylor – Electrical Engineering

## Slide 2: Project Goal
Design and implement an electric surfboard controlled with a wireless throttle and powered by a rechargeable battery

## Slide 3: Motivation
To Produce a fun project that people may find interesting
Combine learning with an outdoor hobby
Gain hands on experience

## Slide 4: Project Concept
Jet Drive
G
Phone

## Slide 5: Project Specifications
The following specifications are theoretical/ideal
  Ride Time: 30 minutes
  Weight: Less than 40 lbs.
  Wireless Connection Range: 6-10 m
  Battery Durability: 2 recharges per 24 hours
  Speed: 5-10 mph

## Slide 6: System Block Diagram

## Slide 7: Power Source
ZIPPY | Flightmax
Type | Lipo
Voltage | 22.2 V
Capacity | 4500 mAh
Configuration | 6 cell
Discharge | 45C - 55C burst
Weight | 789 grams
Length A | 145 mm
Height B | 51 mm
Width C | 52 mm

## Slide 8: Propulsion
Motor - Turnigy | AquaStar
Weight | 508 grams
Max Current | 105 A
Max Voltage | 37 V
Power | 3050 W
Shaft A | 5 mm
Diameter C | 39 mm
Total Length | 103 mm
Jet Drive | Pump Unit
Model | Jet2805
Max RPM | 20,000
Total Length | 171 mm
Diameter | 28 mm
Propulsion | Impeller

## Slide 9: Microcontroller
The microcontroller that we required for our project had a couple of requirements to meet:
Low price
Support PWM(Pulse Width Modulation)
UARTSerial support.
Couple of pins for general LED usage.
Simple IDE usage for programming.

## Slide 10: Microcontroller
Our first choice was TI’s TMS320F28062 microprocessor.
Key points of the TMS320F28062:
  Simple and easy to use IDE, Energia
  Well documented commands and architecture, with supportive community
  Meet the requirements necessary for the project
However:
  Lack of CAD file for the microcontroller

## Slide 11: Microcontroller
ATMega328p
  Second option
  Development with Arduino UNO
Already owned this dev. board

## Slide 12: Microcontroller
ATmega328P
TMS320F28062

## Slide 13: Bluetooth Communication
Used the a smart phone as the handheld control
  Versatile
  Convenient
Bluetooth compatible
Do not have to build, hardware wise, a hand-control device for the board.

## Slide 14: Bluetooth Communication
The Bluetooth module that was chosen for the project was the HC-05. Here’s a comparison of other Bluetooth modules that we compared.
Bluetooth Module | CC2564MODN | BT900 | HC-05
OPERATING VOLTAGE | -.5-4.8 V | 3.6 V | 3.3 - 5V DC
Size | 7.1 mm x 7.1 mm x 2mm | 2.5mm x 12.5mm x 19mm | 27mm x 13mm x 2mm
Signal range(m) | 10 | 100 | 10
Data Speed | 2.1 Mbps | 3 Mbps | 3 Mbps
Price USD | $13.97 | $15.35 | $5.25
Complex interface | Easy | Easy | Easy
Max Baud Rate | 9600 | 9600 | 9600

## Slide 15: Bluetooth Communication
26.7mm
13 mm

## Slide 16: Mobile App
Used Android Studio IDE for development
Have an option for Advanced Settings
Gives total control over the surfboard’s settings for the user, ie. Speed increments, slow and stop speeds for the board.

## Slide 17: Advanced Settings
Settings within the Electri-Surf application
  Accessed through home screen
Used for changing values:
  Slow speed
  Speed bar increment

## Slide 18: Mobile App cont.
Graphical user interface
  Riding screen
Speed Control:
  Phone volume keys
  Touch screen capability
Progress bar indicators

## Slide 19: Mobile App

## Slide 20: Speed Control
Electronic Speed Control (ESC)
Connects directly to motor, PCB, and battery
Regulates current sent to motor
  Programmed through ATmega328p
  Via pulse width modulation (PWM)

## Slide 21: Electronic Speed Control
Using 120A ESC
Contains universal battery eliminating circuit (UBEC)
No need to have a battery power receiver
  Converter inside esc that drops voltage

## Slide 22: Battery Monitoring
DS2438 smart battery
  Maxim Integrated
Designed for max 12V battery
Circuit implemented to widen capable input range

## Slide 23: Battery Monitoring
Late issues with DS2438 functionality
Used existing voltage divider
Analog pin on microcontroller needed
Adjustments made on PCB

## Slide 24: Battery Monitoring
To MCU

## Slide 25: Battery Monitoring
Calculating approximate voltage
Voltage divider
Where,
Creates 5V to analog pin using 24V supply

## Slide 26: PCB Design
EAGLE
No experience
  Not 100% confident in design
  Multiple runs expected
Limited CAD files
  Switched parts

## Slide 27: PCB Schematic

## Slide 28: Safety Concerns
Rider Safety
  Engine shut off mechanism
  Battery level awareness
Water Hazard – hardware preservation
  Water and electricity don’t mix

## Slide 29: Emergency Cut-off
Sea Dog Kill Switch
  Equipped with lanyard
Hard kill switch
  Creates open circuit
  Cut power directly from battery

## Slide 30: Difficulties
Parts out of stock
CAD files
Little experience
Measurements when building

## Slide 31: Division of Labor
Member | PCB Design | Mobile App | Bluetooth/ Coding | Soldering | Testing | Design Assembly | Administration
Anthony | ✔ |  |  | ✔ | ✔ | ✔ | ✔
Alex |  | ✔ | ✔ |  | ✔ |  | 
Ryan | ✔ |  |  |  | ✔ | ✔ | ✔

## Slide 32: Project Construction

## Slide 33: Project Construction

## Slide 34: Budget
Part | Cost
Surfboard | Free
Jet Drive | $69.95
Battery | $68.68
Motor | $69.89
Battery Charger | $23.00
ESC – Electronic Speed Control | $66.99
Battery Monitor | Free
Microcontroller | $13.72
Custom housing unit | $45.71
Bluetooth | $5.25
LED’s | Free
Waterproofing Supplies | $7.56
PCB and components | $35.88
Current Total | $406.63

## Slide 35: Questions?