## Slide 1: Laboratory Control System (LCS)
UCF Engineering I Cleanroom Laboratory
Borgess, A. Kozorezov J. Ossa, M. Aleksich
Sponsor: Dr. Reza Abdolvand, UCF
Notes: Anatoly

## Slide 2: Motivation
Antiquated logging system
Laboratory equipment control and usage tracking
Ability to reserve machines online
Provide monthly usage reports for billing
Notes: Aaron

## Slide 3: Sponsor requirements
User-serviceable parts, long lasting
System expandability
Diagnostic tool (PCB design)
Integrated with UCF network
Online reservation system
User manual
Notes: Aaron

## Slide 4: System overview
Notes: Aaron

## Slide 5: System overview
Jimmy
Miguel
Anatoly
Aaron
Notes: Aaron

## Slide 6: Design specifications
Description | Requirement
User interaction time | Less than 20 seconds
System longevity | 3 years or more
Machine capacity | 22+ machines
Machine voltage relays | 5VDC, 12VDC, 120VAC, 220VAC
Billing increments | Per hour or once per day
Data encryption | SSL
Size of system | Medicine cabinet 14”x16”x8”
Notes: Aaron

## Slide 7: PLC Selection
Brand | Pros | Cons
Automation Direct | Free software Free tech support Free shipping Many features Expandability | Proprietary software
Every other brand (Allen Bradley, Unilogix) | More features More powerful | Purchase software separately Tech support not guaranteed Expensive to expand
Notes: Anatoly

## Slide 8: Card swipe
Magnetic Card Reader | Operating Voltage | Current | Magnetic Head Life Span | Physical Interface | Price
SU90 (RS-232) | DC5V±0.5 | 10mA | 800,000 | DB9, PS/2 | $44.95
ZAUM120-PL MSR112A (RS-232) | DC 3.3V | 5.5 – 6.5 mA | 500,000 | DB9 | $62.00
POSMATE MSR (USB) | N/A | 3mA | 500,000(min) | USB | $40 ($20 + USB-Serial converter)
Notes: Anatoly

## Slide 9: User interface (touch screen)
3” panel
$205
128 x 64 display
5.7” panel
$299
320 x 240 display
Notes: Anatoly

## Slide 10: User interface (touch screen)
3” panel
$205
128 x 64 display
5.7” panel
$299
320 x 240 display
Notes: Anatoly

## Slide 11: Panel prototype
Notes: Anatoly

## Slide 12: Panel prototype
6”
6”
Card swipe
Touch screen
Card swipe
Terminal strip
Power + circuit breakers
Card swipe
PLC + Expansion
Raspberry Pi
Notes: Anatoly

## Slide 13: Panel power flow
Notes: Anatoly

## Slide 14: User interface (panel)

## Slide 15: PCB – The Diagnostic Tool

## Slide 16: Diagnostic Tool Overview
Runs Parallel to the control system
Provides quick administrative access to the PLC
User friendly interface

## Slide 17: Buck Converter (TPS562200)
Highly Efficient ~ 90%
Complex design, can be costly, high-frequency switching can be noisy

## Slide 18: ATMega 328P and Arduino
WHY THIS?
Cheap
Option to already have Arduino Optiboot
Open Source
Easy to Use
CONFIGURATION
LCD using I2C (SCA, SDA)
TX, RX to implement RS485 Communication
8 digital I/O pins configured for PLC
6 push buttons
16 MHz Crystal Oscillator

## Slide 19: RS485 Communication (MAX 485)
Differential Data Transmission
Half Duplex
Maximum Input/output Voltage: -7 to 12 V
9600 Baud Rate
Twisted Pair to create noise immunity

## Slide 20: PCB Schematic
RS485 Communication
I/O PLC
Comms
Power Regulation
I2C LCD
Comms

## Slide 21: PCB Layout

## Slide 22: Machine Relays/ Machine Control

## Slide 23: Power switch Tail II Relay
Enables power from standard outlet 120 VAC
Optional Normally Open or Normally closed
Large Input voltage range (3-12VDC)
SPST Configuration

## Slide 24: How to Control These????
Electronic/ Magnetic Locks
Lee Electric, SECO-LARM

## Slide 25: Communications
Data must be transferred from one component to another
Must be consistent to allow for seamless communication

## Slide 26: Overview

## Slide 27: Choices
PyMod
JaMod
Modbus Master
PhpModBus

## Slide 28: From PLC to Raspberry Pi
TCP FRAME FORMATS FOR MESSAGES SENT |  | 
Name | Length | Function
Transaction ID | 2 Bytes | Identifies each message sent over the protocol
Protocol ID | 2 Bytes | Is set to zero for the TCP implementation
Length | 2 Bytes | Identifies the length of the message after this field. (2 + the size of the Data transmitted)
Unit ID | 1 Byte | Set to 1 for communication over the protocol
Function Code | 1 Byte | Identifies the action to be performed
DATA | Dynamic in size | The accompanying data that could be written to the registers

## Slide 29: FROM PLC TO RASPBERRY PI
Create A Socket
Constant Monitor
Gets Request
Send acknowledgement
Separate message to bytes and shorts
Decide the next action to follow

## Slide 30: From Raspberry Pi to Database
Send ISO and Machine Number
Take a timestamp
Check ISO and Machine Number
Check Schedules

## Slide 31: Database Back to Raspberry Pi
Calculate total time
Lots of math (originally)
Still lots actually but interesting way to get around it
Milliseconds since the Great Epoch

## Slide 32: Raspberry Pi to PLC
Package the final message
Send message
Update the database
Continue to listen

## Slide 33: Web Development
Front-End
Back-End
Database Design
UCF Network

## Slide 34: Front-End Development
2 Websites — dynamic and static
CSS, HTML, and JavaScript
  Bootstrap
    jQuery DataTables
WordPress

## Slide 35: Back-End Development
Supported by Windows and Ubuntu machines
Supported by UCF Network
XAMPP – Cross platform development environment
Free to use
MySQL
PHP
Apache

## Slide 36: Database
MySQL | PostgreSQL
Large Community | Large Community
Moderate Performance | Great Performance
Support Transactions | Support Transactions
Bundled with XAMPP | Separate Install

## Slide 37: Database Design
Contains User Information
User groups
  Admin
  Faculty
  Student
Machine Information
Reservations and Lab Use
Authorizations

## Slide 38: WordPress Site

## Slide 39: Website Application (Navigation)
Admin | Student

## Slide 40: Web Application (Reservation System)
24 hour reservation system
12 hours displayed at a time
Mobile friendly

## Slide 41: Web Application (Admin Controls)

## Slide 42: Web Application (Admin Controls)

## Slide 43: Integrating with UCF Network
Working with Tech Support
UCF Federated Identity Login

## Slide 44: Administrative Content

## Slide 45: Work Distribution
Section | Primary | Secondary
Main panel | Anatoly | Aaron
DT/Machine control | Aaron | Anatoly
Website | Jimmy | Miguel
Connector | Miguel | Jimmy

## Slide 46: Progress
Chart: 
| Total | Testing | Prototyping | Design | Research
Series 1 | 4 | 4.5 | 3.5 | 2.5 | 4.3

## Slide 47: Progress
Chart: 
| Overall Progress | WordPress Site | Reservations | Diagnostic Tool | Database | Raspberry PI | Server Connector | Machine Control | Main Panel
Series 1 | 0.6625 | 0.2 | 0.9 | 0.7 | 0.85 | 0.5 | 0.7 | 0.6 | 0.8

## Slide 48: Issues
RS232-RS485-TCP/IP Modbus comms
  Card swipe to PLC
  PLC to PC
  DT to PLC
Database records
  Calculating begin and end times
  Reservation requirements/rules
User interface
  Touch screen
  Website/reservation system
Security – SSL, UCF door security, UCF IT

## Slide 49: Budget

## Slide 50: Questions?