## Slide 1: Portable Finish Line for Sprinters Group 30
Michael Colucciello – Computer Engineering
Jamal McNab – Electrical Engineering
Tyler Snell – Electrical Engineering
Argeny Batista – Electrical Engineering

## Slide 2: Motivation
Most sprinters rely on a human with a stopwatch in practice
Lack a convenient method of tracking improvement and progress
Few sprinters have convenient access to automatic timing
Fully Automatic Timing systems typically only used in competition
Want to bring the precision of automatic timing to practice
Most personal Fully Automatic Timing systems not affordable or convenient
Photo Credit to Browertiming.com

## Slide 3: Goals
Bring Fully Automatic Timing systems to practice
Have an affordable option for sprinters of all skill levels
Rechargeable, Lightweight, and portable to be carried to and from practice
Provide a mobile application to wirelessly connect to the device
  Streamlined UI for navigation
  Track previous times and improvement over time

## Slide 4: Specifications
Parameter | Design Specification | 
Battery life on full charge | 3 hours | 
Wireless connectivity range | > 100 m | 
Timing accuracy | To the nearest 0.1 second | 
Size | 1’2’’ x 1’2’’ x 1’2’’ | 
Weight | < 10 lb | 
Volume of speaker | 70 dB at 1 meter | 

## Slide 5: Overall High Level Design

## Slide 6: Power System

## Slide 7: Batteries
Battery Information | 
7.4V 1400mAh Polymer Li-ion Battery Pack | 
Nominal Voltage | 7.4V (working) 8.4V (peak) 4.8 V (cut-off)
Nominal Capacity | 1400 mAh min. (10.36 Wh)
Chemistry | high quality cylindrical 18500 rechargeable cells
Terminal | Charging / Discharging terminals: 6.0" (1007) 22AWG wire for charge / discharge
Charging Rate | Standard: 1.2 A
Max Discharging Rate | 2 amps limited by the PCB
Cycle Life | Greater than 500 cycles (If charged and discharged properly)
Dimensions (L x W x H) | 51mm x 38.1mm x 19mm
 | 2.0" x 1.5" x 0.75"
Weight | 2.5 oz. (70.8g)
There will be 3 batteries necessary
Main concerns:
  Space
  Potential overheating

## Slide 8: Voltage Regulators
Both a 5V and a 3.3V Rail necessary
2 of each regulators (one in each pylon)
3.3V Reg: TPS82130
  High efficiency 92.44%
  Low foot pring

## Slide 9: Voltage Regulators
5 V Reg: TPS6307
  High efficiency 92.58%
  Low Footprint

## Slide 10: Inductor Charger
PICAXE 02M2 (IC1)
  FREQUENCY = 12.9 kHz , DUTY CYCLE = 50%
COIL DIAMETER = 2.5” , APERATURE = 1” ,
SEPARATION = 0.25”
Input Voltage = 12V, Output Voltage 8.06V

## Slide 11: Microcontroller and Sensors

## Slide 12: Microcontroller Selection
 | Esp 32 | Arduino Uno (Atmel) | MSP430/cc3200
Cores | 2 | 1 | 2
Architecture | 32bit | 8bit | 
CPU Frequency | 160/240MHZ | 16MHz | 80MHz
WIFI | Integrated | None | Integrated
Bluetooth | Integrated | None | None
RAM | 512KB | 2KB | 256KB
Flash | 16MB | 32KB | 16MB
Operating Temp | -40 to 125C | -40 to 105C | -40 to 80C
Low Power Deep Sleep | 2.5 uA | 72 uA | 250 uA
Cost | $ 2.50-9 | $3.00 | $9.20
Criteria
Wireless capabilities
Cost
CPU Clock Speed
Package size
ESP 32 chip size
Courtesy of gridconnect.com

## Slide 13: Trip sensor
Other light sources may interfere with LDR reading
Line Laser And LDR Sensor
Wave Length: 650nm
Class II less than 1mW
Line width: 1.2mm @ 1 meter
Operating Voltage: 5v
Easy to implement
Easy to Align with LDR sensor from a distance
CONS

## Slide 14: Schematic
3.3 VREG
FTDI (USB)
Latching Pins
JST

## Slide 15: End Result...
Rough estimate of Boards $5-$7 !!!

## Slide 16: Prototype Structure
Rapid prototyping
  3D printing
  ABS Plastic
2x towers to house all electronics
Diagram Breakdown
  Top Cover
  Laser or LDR with Speaker enclosure
  Acrylic structure for LED ring
  Housing for wireless charger, Power sources and main Board components
  Bottom cap

## Slide 17
Exploded View
Assembled View

## Slide 18: Android Application

## Slide 19: Android Application
Developed in Android Studio
Android ver. 4.2 (API Level 17)
  Bluetooth Low Energy
Prioritize ease of use in UI and design
2 main modes of operation
  Sprint History
  Sprinting

## Slide 20: Use Case Diagram

## Slide 21: Wireless Communication
Bluetooth Low-Energy
Wi-Fi
Implement both
  Bluetooth for general purpose
  Wi-Fi for extended range cases

## Slide 22: Microcontroller Programming

## Slide 23: Microcontroller Software Design
Utilize interrupts and low power modes
  Optimal for extending battery life
Perform all timing on microcontroller

## Slide 24: Accounting for Multiple Sprinters
Need to ignore errors of one sprinter recording more than one time in a race
Microcontroller will have a “grace period”
  Once finish line is crossed, don’t take input for very short amount of time
  Grace period length optimized through testing

## Slide 25: Audio and Visual Subsystem

## Slide 26: Audio and Visual Subsystem
Give the sprinter a stimulus to know when to start running
Provide a visual and auditory countdown for the start of the race
When the user starts the app and chooses to time a new “sprint” this will start a countdown
After a period of time, signals will alert the user when the race will start

## Slide 27
3 instances where the LEDs will blink red with a simultaneous beep from the speaker
The fourth instance the LED will blink and hold green with a simultaneous beep
  This will trigger the app to start recording the time

## Slide 28: Speaker Selection
Speaker | Size (diameter) | SPL (dB) | Power Rated
CDM-20008 | 20 mm | 92 | 300 mW
CDMG15008-03A | 15 mm | 92 | 300 mW
PSR-50F08S-SQ | 50 mm | 92 | 250 mW
PSR20N08AK | 20 mm | 92 | 250 mW

## Slide 29: LED Selection

## Slide 30: Why the Neopixel Ring
Pros
Programmable
  Adjust brightness and delay, etc.
RGB
Easier to synchronize
Cons
Price
Increases the length of code

## Slide 31: Choosing an Amplifier
Audio Amp | Operating Voltage | PSRR | Output Power
TPA721 | 2.5-5.5 | 85 dB | 0.7 W
TPA701 | 2.5 | 78 dB | 0.7 W
LM386N-3 | 4-12 | 50 dB | 0.5-0.7 W

## Slide 34: Administrative Content

## Slide 35: Budget & Finance
Self funded project
Estimated necessary budget initially min ~$250
Project Budget | 
Power Distribution components | $15.96
Batteries | $43.00
Charger Components | $21.50
LED Components | $7.74
Audio Components | $4.28
Laser Components | $4.46
PCB orders (so far) | $90.00
Microcontrollers | $5.00
Current SUM | $191.94

## Slide 36: Work Distribution
Work Distribution |  |  |  | 
Subsystem: | Tyler | Jamal | Argeny | Micheal
Power Distribution | P |  |  | 
Inductive Charger | P |  |  | 
Microcontrollers |  | P |  | S
Laser/LDR |  | P |  | 
LEDs |  |  | P | 
Audio |  |  | P | 
Software Architecture & Interface |  |  |  | P
Smartphone App |  |  |  | P

## Slide 37: Questions?