## Slide 1: OUC SOLAR SCULPTURE
Denis Aybar – EE
Juan Forero – EE
Simon McGlynn – CpE
Daniel Truong – CpE
sponsored by Orlando Utilities Commission

## Slide 2: Motivation
  People perceive solar technology as aesthetically unappealing
  A greater uptake in the use of solar will reduce environmental damage
  Solar sculptures aim to combine beauty with clean energy

## Slide 3: Goals/Objectives
Combine talents of mechanical, electrical, and computer engineers with art students
Create a mechanically sound sculpture that can withstand Florida’s weather
Maintain aesthetic appeal to the public while utilizing PV technology
Have a flexible design for any sculpture

## Slide 4: Specifications
Component | Parameter | Design Specification
Solar panel* | Energy production | > 850 kWh/year
Sculpture* | Physical dimensions | 12x12x20 ft (l x w x h)
LEDs | Lighting | 120
IR Sensor* | Proximity detection | 0.25 m – 3.5 m
Sound sensor | Sound Pressure Level | 18-138 dB-SPL
LCD Screen | Information display | 40x4 characters
*For full scale structure. Prototype will be a 1/8 scale model.

## Slide 5
Sun
PV Panels
Microinverters
Sculpture
Transformer
Grid
PCB
Design Overview

## Slide 6: Hardware Block Diagram

## Slide 7: Software Block Diagram

## Slide 8
Function Call Diagram

## Slide 9
Structure Prototype
Should have recognizable soccer elements
Should be highly visible
Should be structurally sound
Meet NFC and Florida building code

## Slide 10: Panels
Option 3:
Amerisolar AS-6P Polycrystalline
Option 2:
LG NeON 2 72 cell Monocrystalline
Option 1:
LG NeON R 60 cell Monocrystalline
Copyright
Copyright
Copyright

## Slide 11: Panel Comparison
Model type | LG NeON R 60 cell monocrystalline | LG NeON 2 72 cell monocrystalline | Amerisolar AS-6P 340W Polycrystalline
Size | 66.93 x 40.0 x 1.57 inch | 79.69 x 40.31 x 1.57 inch | 77 × 39.1 × 2 in
Weight | 40.78 lbs | 47.84 lbs | 50.7 lbs
Efficiency | 20.3% | 18.8% | 17.52%
Power Output | 350W | 390W | 340W
Current | 9.62A | 9.81A | 9.07A
Voltage | 36.4VDC | 39.8VDC | 37.5VDC
Price | ~$475 | ~$520 | ~$212
Annual output | 492 kWh/Year | 548 kWh/Year | 478 kWh/Year
Equation from PVWatts.nrel.gov
System Size (kW) = Panel Nameplate Size (W) × Number of Panels ÷ 1,000 W/kW
OR
System Size (kW) = Panel Surface Area (m²) × 1 kW/m² × Panel Efficiency (%)

## Slide 12: Microinverter vs. String inverter
Microinverter
String inverter
Copyright
Copyright

## Slide 13: Microinverter
Manufacturer | ABB
Model | MICRO-0.3HV-I-OUTD
Efficiency | 96.5%
Input DC power | 360W
Max voltage input | 79V
Max current input | 10.5A
Cost | $99
Size | 10.5x9.7x1.37in
Weight | < 3.5lb
*Includes monitoring application

## Slide 14: Power Consumption
Component | Max power usage kWh/year | Typical power usage kWh/year
LEDs (120) | 420.08 | 140.16
IR sensors (6) | 8.7 | 8.7 (sensors always on)
Sound sensor | 0.016 | 0.011
MCU | 0.613 | 0.204
LCD screen | 3.136 | 2.536
Current sensor | 0.175 | 0.175
Consumption by system | 435.98 kWh/year | 155.406 kWh/year

## Slide 15: Power Produced
LG NeON R 60 cell monocrystalline | Worst case | Typical case
Yearly output/panel | 492kWh/year | 492kWh/year
Quantity of panels | 3 | 3
Microinverter efficiency | 96.5% | 96.5%
Consumption by system | 435.98 kWh/year | 155.406 kWh/year
Net output | 988.36 kWh/year | 1268.406 kWh/year
Money saved* | $95.47/year | $122.57/year
*Calculated from commercial rate of 9.66¢/kWh

## Slide 16: Microcontroller Choice
Microcontroller | Microchip ATMega2560 | Raspberry Pi 3 Model B | Texas Instruments MSP430 FRXX
GPIO Pins | 86 | 40 | 68
RAM | 256 kB | 1 GB | 8 kB
Operating voltage | 5 V (3.3 V capable) | 4.75 – 5.25 V | 1.8 – 3.6 V
Temperature range | -40°C to 85°C | -40°C to 85°C | -40°C to 85°C
CPU Speed | 16 MHz | 1.2 GHz | 24 MHz

## Slide 17: Microchip Atmega 2560
Large number of GPIO lines (including analog PWM pins)
Low power consumption
Open source hardware and software available
Arduino compatibility with all other components used in project
Manufacturer | Microchip
Part no. | ATmega2560 16au-1738
Price | $12.20
GPIO pins | ~70 free
Memory | 256 KB
Copyright

## Slide 18: 40x4 Parallel Character LCD
Transflective screen “…transmits and reflects light…”
Which allows readability under direct sunlight
Good for harsh weather
Relatively low cost for LCD
Manufacturer | Crystalfontz
Part no. | CFAH4004A-TFH-JT
Price | $23.04
Temperature range | -20°C to 70°C
Viewing area | 147mm x 29.5mm
Copyright

## Slide 19: Adafruit NeoPixel RGBW LED Strips
Individually addressable
IP65 waterproof casing
Flexible strips that can be cut at each LED
RGBW allows for any color choice
5 V max draw
Manufacturer | Adafruit
Part no. | 2842
Price | $26.95/m
LEDs/meter | 60
Voltage | 5 V
Current | 80 mA/LED
Copyright

## Slide 20: Ribbon Star 50/50 LEDs
UL listed
IP68 rating
RGB + warm white colors
Flexible mounting capabilities
Manufacturer | Ecolocity
Part no. | RL-SC-RS50-T-RGBWW-5
Price | $185/5 m
LEDs/meter | 60
Voltage | 12 V
Current | ~20 mA/LED
Copyright

## Slide 21: SparkFun Sound Detector
Ranges from normal talking level to noise of a busy street
Detects frequencies from midrange of human hearing up
Detects both presence of sounds, and volume levels
Manufacturer | SparkFun
Part no. | SEN-12642
Price | $10.95
Frequency range | 10 to 100 kHz
Sound pressure range | 50-75 dB-SPL
Copyright

## Slide 22: GRAS Free-field Rugged Microphone
IP67 rating
High temperature tolerance
Frequency range close to human range of detection
Wide range of sound pressure detection
Manufacturer | Gras
Part no. | 146AE
Price | ~$1700
Frequency range | 3.15 to 20,000 Hz
Sound pressure range | 18 - 138 dB
Temperature range | -40 to 125°C
Copyright

## Slide 23: Sharp IR Distance Sensor (Not PIR)
Manufacturer | Sharp
Part no. | GP2Y0A41SK0F
Price | $13.95
Range detection | 4 cm to 30 cm
Operating temperature | -10°C to 60°C
Good range for model*
Proximity detection
Analog interface
Copyright
* Longer range sensor suggested for full scale (3.5 m)

## Slide 24: ACS711EX Current Sensor
Manufacturer | Allegro
Part no. | ACS711EX
Price | $3.95
Range detection | -15.5 to 15.5 A
Operating voltage | 3 to 5 V
Hall effect-based linear sensor
Fault fail safe to deal with overcurrent
Operating voltage compatible with our system
Able to read high current
Copyright

## Slide 25
Overall schematic
Overall Schematic

## Slide 26
Microcontroller

## Slide 27
LEDs

## Slide 28
ICSP

## Slide 29
LCD Screen

## Slide 30
Sensors

## Slide 31
Power

## Slide 32
Power Output Reading

## Slide 33: Administration

## Slide 34: Progress
Chart: 
| Total | Prototyping | Testing | Design | Research
Progress | 0.975 | 1 | 0.95 | 0.95 | 1

## Slide 35: Work Distribution
Name | PCB Design | Coding | LCD | Sensors | LEDs | Power | Power output recording
Daniel |  | x | x |  | x |  | 
Denis |  |  |  |  |  | x | x
Juan | x |  |  |  |  |  | x
Simon |  | x |  | x | x |  | 

## Slide 36: Budget
Part | Manufacturer | Cost/unit | Quantity | Production cost
LEDs | Adafruit neopixel | $26.95 | 2 | $53.09
IR sensors | Vishay | $2.95 | 7 | $20.65
Sound sensor PCB | OshPark | $2.58 | 1 | $2.58
Minor components (MOSFETS, capacitors, etc.) | Various | $3 | 1 | $3
LCD | Cystalfontz | $11.52 | 1 | $11.52
5 V 10 A Switching Power Supply | Adafruit | $25.00 | 1 | $25.00
ATMEGA2560 | Atmel | $12.20 | 1 | $12.20
PCB manufacturing | PCBWay | $0.50 | 1 | $0.50
Current sensor | Pololu | $3.49 | 1 | $3.49
Total |  |  |  | $132.03
*Funding provided by UCF MAE department and OUC

## Slide 37: Issues
Current sensor and voltage divider are not working together
Sub-contracting to three teams
JST ports have poor connection

## Slide 38: Questions?