## Slide 1: Team RED
ROBOCOPTER
GROUP 28
Pamela Echevarria – EE
Jarryd Salas – EE
Branden Griffin – CE
Joey Velez-Ginorio - CE

## Slide 2: Red Team
Robocopter
Interdisciplinary Project Consisting of
  ME: Matthew Newman, Mathew Pistone, Jeremy Meehan,
Greg Potter
  AE: Anton Keys, Christopher Vallee, Matthew MacAllister
  EE: Pamela Echevarria, Jarryd Salas
  CE: Branden Griffin, Joey Velez-Ginorio
  CS: Tarek Medrano, Khandoker Ahmed, Angel Mercado
Tasked to design and build an autonomous drone who’s motivation is to have a defense vehicle that will not require human life to be at risk. This drone can detect other “prey” drones, attack them, avoid obstacles and transmit Live First Person view video to a ground station via wifi.

## Slide 3: Goals & Requirements
Robocopter
Design and build an autonomous quadcopter
Size ≤ 4x4x4 ft.
Max budget of $2000 → $1500 for final as-demonstrated drone.
Quadcopter must have protective shell within required design limits
Transmit highlighted video imagery via wifi
  Display algorithm used to identify/track prey
Be able to search, pursue, reset, and repair if necessary in attempt to cause a controlled collision with prey drones autonomously
Complete with as many points possible two 10 min rounds of competition

## Slide 4: Hardware Parts

## Slide 5: Frame HJ MWC X-Mode Alien
Materials:
  ABS Plastic (Arms)
  Fiberglass (Body)
  Aluminum (Hardware)
  Propeller range: 10” - 12”
Total Weight: 347g
Ample Surface Area
Well balanced center of mass (red dot)

## Slide 6: Motors Brushless T-Motor Navigator Series MN3110-KV700
Technical Data
Rating: 700kV
Motor Dimension: Φ37.7×28.5mm
Weight: 80g
No.of Cells(Lipo): 3-4S
Max Continuous current(A)180S: 21A
Max. efficiency current: (3-10A)>80%
Thrust Range: 620-1540g

## Slide 7: Propellers RAYCorp 1147 11x4.7
Technical Data
Diameter: 11 inches
Pitch: 4.7
Shaft Diameter : 6 mm
Weight: 6 grams
Material : High Quality ABS Plastic

## Slide 8: Electronic Speed Controller (ESC) T-Motor 30A BLHeli_S 2-4S FPV version ESC
Technical Data
Continuous Current: 30A
  Motor Max Continuous Current - 21A
  Add 20% = 25.2A
Lightweight: 4.3 grams
Size: 25.5mm*12.7mm*5mm
Input Voltage: 7.4V-14.8V
Firmware: BLHeli_S
BEC: No

## Slide 9: Protective Cage
Materials: .060 inch graphite rods and 3D printed Nylon fittings
  Lightweight
  Strong and durable
  Ease of manufacturing
Rectangular Design:
  Low surface area for amount of coverage
  Repetition for easier manufacturing
  Symmetrical design allows efficient mounting
  Ease of modification if needed

## Slide 10: Protective Cage

## Slide 11: Batteries
Motors & Flight Controller
Multistar Lipo Pack
Electronics
eeco Ultra Slim Power Bank
Capacity: 10000mAh
  Total Current Draw: for 2600g thrust @ 85+% throttle 56,160mA. Need 9,379mAh for 10 minutes.
Configuration: 4S1P/ 14.8V
Weight: 803g
Size: 6.3 x 1.4 x 2.6 inches
XT90 to XT60 Adapter used
Capacity: 5000mAh
  Total current draw: 3750mA = 80 minutes
Output: 5V/3A
Type C Port - Micro USB adapter is used
Weight: 128g
Size: 125mm* 68mm*11mm
Notes:   ATMega328 chip: 0.3mA (active mode)
  FTDI Chip: Max 100mA
  Camera: 650mA @5V
  Intel Compute Stick: Max 3A
Motors: 14.04A each=56.16A

## Slide 12: Weight Analysis
Part | Weight (g)
Frame | 347
Cage | 454
Motors | 80
Props (4) | 24
ESCs | 5
Battery 1 | 128
Battery 2 | 803
Camera | 159
Intel Stick | 59
Flight Controller | 16
PCB | 25
IR Sensor | 6
Ultrasonic (4) | 76
XT60 Adapter | 18
Micro to C Adapter | 6
Total: | 2467
MAX: | 2600

## Slide 13: Camera RunCam Split 2
Technical Data
Weight: 23g
Size: PCB-38*38mm/Lens Module-22*20mm
Supports 64GB micro SD card
Has wifi chip
Latency: <= 51.3ms
Input voltage: DC 5-17V/ DC 5V(USB)
Video Resolution: 720@60fps in FPV and 1080@60fps in Recording
Working Current: 650mA@5V

## Slide 14: Prototype LHI 220 Quadcopter Kit Full Carbon Frame Kit
2300KV Brushless Motors
Littlebee 20A Mini ESC
F3 Flight Controller Board Cleanflight
700TVL camera
Weight: 589.67g

## Slide 15: Design

## Slide 16: Hardware Layout
Battery 1
Flight Controller
Power Module
ESC
ESC
ESC
ESC
Motor
Motor
Motor
Motor
PCB
PDB
Camera
Intel Stick
Battery 2

## Slide 17: Schematic
Printed Circuit Board (PCB)

## Slide 18
Flight Controller

## Slide 19: PIXHAWK Mini 3 internal sensors (Gyro/Accel/Mag) Open-source Multiple connections such as UART, I2C, and CAN
Flight Controller

## Slide 20: 915 MHz Telemetry Radio Set allows ground station to communicate to quadcopter allows view of in flight data QGroundControl program open source FrSky ACCST Taranis Q X7 Transmitter with X8R receiver open source firmware multiple channels for multiple flight modes
RC Transmitter/Receiver and Telemetry

## Slide 21
Obstacle Avoidance - Sensors
Feature | SRF02/SRF05 | XL-MaxSonar | Sharp GP2Y0A02YK0F | Sharp GP2Y0A21YK0F
Sensor Type | Ultrasonic | Ultrasonic | Infrared | Infrared
Detection Distance | 0-14.76 ft | 20-25.1 ft | 7.87-59.06 in | 3.94-31.50 in
Response Time | N/A | 10 Hz reading rate | 38 ms | 39 ms
Operating Voltage | 0-5 V | 3.3-5.5 V | 4.5-5.5 V | 4.5-5.5V
Current Consumption | 4mA | 3.4mA | 33mA | 40mA
Weight | .32 oz | .32 oz | .17 oz | .17 oz
Dimensions | 1.81 x 1.1 x .75 in | N/A | 1.16 x 0.5 x .85 in | 1.16 x .52 x .53 in
Price | $7 | $40 | $9 | N/A

## Slide 22: Design 1 (Testing) Ultrasonic sensor (0 - 14 ft range) Positioned closer to base due to longer detection range Infrared sensor ( 8in - 5ft range) Positioned on the ends of the arms due to shorter detection range
Obstacle Avoidance - Sensors

## Slide 23: Design 2 (Probable) Ultrasonic sensors 5 total 1 on each side of base (front/back/left/right) 1 on bottom of base
Obstacle Avoidance - Sensors

## Slide 24: Microcontroller
1.8 to 5.5 V operating voltage
23 GPIO Lines
.2 mA active power draw
32 kb flash memory, 2kb ram
~20 Mhz processing speed
Requirements:
Sufficient I/O Lines
Lightweight
Easy to integrate
Low power requirement
ATmega328p met these requirements
Arduino Uno utilizes this chip

## Slide 25: Software Implementation
Intel Compute Stick processes video feed, returns tracking directions
ATmega328 processes tracking directions and relays them to Pixhawk Mini through MAVlink
ATmega328 also processes sensor information, makes course correction through MAVlink if necessary
Autopilot on Pixhawk Mini takes directional instructions and makes meaningful changes to ESC’s to change course

## Slide 26: Software Functional Flow

## Slide 27: MAVLink
Protocol for communicating with autopilot on flight controller
Will allow us to send messages from ATmega328 to Pixhawk Mini
The serial pins on the telemetry port of the Pixhawk will connect to digital (PWM) pins of ATmega328
Some example commands:
MAV_CMD_NAV_TKEOFF : Takeoff from ground or hand
MAV_CMD_DO_SET_REVERSE : Set direction of aircraft to forward ( = 1) or reverse ( = 0

## Slide 28: Choosing a computer
 | Intel Compute Stick | Raspberry Pi 3b | BeagleBone Blue | Nvidia Jetson TK1
Cost | $130 | $35 | $80 | $192
CPU | <1.44 Ghz | <1.2 GHZ | < 1.5 MHz | < 2.3 GHz
RAM | 2 GBs | 1 GB | 512 MBs | 2 GBs
Weight | 59 g | 42 g | 36 g | 120 g

## Slide 29: Intel Compute Stick
Requirements:
Run an operating system
Easy to integrate
Powerful enough to do video processing

## Slide 30: Operating Cycle - Video Processing
Detection - Convolutional Neural Network (CNN) via TensorFlow
Tracking - Median Flow Tracker via OpenCV

## Slide 31: Detection
Using popular open source machine
library created by Google - Tensorflow
Includes a set of pre-trained models for tasks like object recognition and detection, e.g. CNNs
Also features tools for training your own models for object recognition and detection
There are lots of similar frameworks, but TensorFlow is nice for it’s relative ease of use, well-kept documentation, and Python support

## Slide 32: Tracking
Using another popular open source machine
library - OpenCV
Includes a set of implementations for easier training of tracking algorithms, like Median Flow Tracking
Again, lots of similar frameworks, but OpenCV is nice for it’s large community of users, lots of documentation, and support for Python

## Slide 33: MCU / CPU Communication
Atmega328 will be connected via micro usb to the Intel Compute Stick
Programs on the Compute Stick can open a serial port and send data to the Atmega328
  e.g. direct low-level motor commands with results of video-processing

## Slide 34: Progress

## Slide 35: Drone Progress - Build

## Slide 36: Work Distribution
Pamela Echevarria
Electrical Engineering (BSEE)
Power Supply - Weight Analysis, ESCs/Motors
PCB Design
Build
Jarryd Salas
Electrical Engineering (BSEE)
Flight Management - Sensors, Flight Controller
RC Communication
Build
Branden Griffin
Computer Engineering (BSCE)
MCU - Programming
Communication of the PCB with all components
Build
Joey Velez-Ginorio
Computer Engineering (BSCE)
MCU - Programing
MCU/CPU Integration

## Slide 37: Progress
Need finalized PCB to work
Need final drone to work
Have run multiple tests
Overall
50%
Did prototype testing - motors, FC, sensors
Test flight of final drone
Test tracking of final drone
Testing
40%
Built and ran test on prototype
On last phase of PCB
Need final drone working
Hardware Implementation
40%
Ordering through UCF
Remote Control is on it’s way
Need to order additional parts for backup
Parts Acquisition
90%
Requirements
Design
Part Selection
Research
90%
Establish MAVLink
Implement flight and tracking
Software Implementation
5%

## Slide 38: Budget Analysis
$2,000 Budget
60.31% Used $1,206.29 Spent
$1,500 Final Product Budget
64.24% Used
$963.65 Spent
$500 Testing Budget
48.52% Used
$242.64 Spent
MAE, CS
ECE
MAE, CS
ECE
36.41% Used
$546.20 Spent
27.83% Used
$417.45 Spent
37.53% Used
$187.66 Spent
10.99% Used
$54.98 Spent

## Slide 39: Challenges
MavLink Communication
Programming Pixhawk with Mission Planner Software
Camera Connection Issues
Budget Constraints

## Slide 40: ¿QUESTIONS?