## Slide 1
Group 32
Andrew Brahim, EE
Jourdain Francis, CpE
Reduced Gravity Flight: TEARDR0P

## Slide 2: Motivation
Low cost reduced gravity experimentation
  Other methods include the use of the the NASA Zero Gravity Flight (the “Vomit Comet”), Drop towers, the International Space Station
Time effective testing and availability
Further expansion of the use of drones in industry

## Slide 3: Goals and Objectives
A quadcopter capable of simulating a reduced gravity environment
A Terrestrial Experimentation and Research Drone Regulating 0-G Parabola [TEARDR0P]
Autonomous flight missions
Carry a small payload for experimentation
Datalog sensor readings and process them into an easily understandable format

## Slide 4: Specifications & Requirements
Parameter | Specification
Reduced Gravity Time | 2.5-7.5 secs
Reduced Gravity Environment | 10-5-10-1G
Maximum Drop Height | 400ft
Payload Weight | <10lbs
Payload Dimension | 7.5in x 5.125in x 14.375in

## Slide 5: Top Level Diagram

## Slide 6: Interdisciplinary Implementation

## Slide 7: Flight Systems

## Slide 8: Flight Controller
SP Racing F4 EVO vs 3DR Pixhawk Mini
Parameter | SP Racing F4 Evo | 3DR Pixhawk
GPS | Not included (Hardware can be added) | Yes
Autopilot | Available through external means | Yes
Onboard IMU | ICM 20602 IMU | ICM 2060
Barometer | BMP280 | MS5611
Processor | STM32405, ARM | STM32F427, ARM
Compatible Software | Cleanflight/Betaflight BLHeli32 | Arducopter
Bidirectional Support | Yes | No
SD Storage | Yes | No
Cost | $37 | $250

## Slide 9: Receiver & Transmitter
FlySky FS-i6
6 Channel 2.4Ghz with telemetry
Bandwidth: 500KHz
Uses UART2/PPM
IBUS Telemetry
Receiver: 4.0-6.5V
Price: $36.99

## Slide 10: GPS
Ublox M8N
Accurate up to 2.5m
Heading accuracy of 0.5°
Velocity accuracy of 0.1 m/s
Maximum altitude ceiling of 50,000 meters.
GPS accuracy may vary based on location of the test flight
GNSS (Global navigation satellite system) support

## Slide 11: Power Distribution & ESCs

## Slide 12: Battery
Lumenier 16000mAh LiPo Battery
Parameter | Specification
Voltage / Cell Count | 22.2V (6 Cell)
Capacity | 16000mAh
C-Rating | 20c – Burst 40c
Discharge Plug | EC5
Weight | 2010g
Price | $269.99

## Slide 13: Power Distribution
Lantian 7oz 200A
Price: $5.55
Supplies battery voltage to ESC’s and UBEC
V
Hobbywing 5V/3A Switching Regulator (UBEC)
DC-DC regulator supplied with a 2-6 cells lithium battery pack
Supplies safe and consistent voltage for flight controller and receiver
Input: 5.5V-26V
Price: $2.99

## Slide 14: Speed Controllers
Lumenier BLHeli_32 51A
Input: 2-6s LiPoly
Constant: 51 A
Burst: 80 A
BEC: No BEC
DSHOT 1200 protocol
Bidirectional mode
Latest Bl Heli 32 firmware
GD32 ARM Cortex-M MCU, 72mhz clock speed, PWM freq 48khz

## Slide 15: Power Distribution Board Wiring

## Slide 16: Black Box Sensor

## Slide 17: Black Box Sensor/ PCB
Arduino based
Added redundancy to the sensor capabilities
MPU 9250 9-axis (Gyro + Accelerometer + Compass)
Raw data stored into an SD Reader
Makes up for lack of redundancy when choosing SP Racing F4 EVO over the 3DR Pixhawk Mini
Has DC power jack for 9-volt battery box power source
Can also be powered from main PDB (contingency: to save all-up weight)

## Slide 18: Black Box Sensor/ PCB Schematic
Notes: We can highlight different parts to explain and expand this to multiple slides

## Slide 19: Black Box Sensor/ PCB Schematic
Notes: We can highlight different parts to explain and expand this to multiple slides

## Slide 20: Black Box Sensor/ PCB Layout
Notes: We can highlight different parts to explain and expand this to multiple slides

## Slide 21: Black Box Sensor/ PCB Final Board
Notes: We can highlight different parts to explain and expand this to multiple slides

## Slide 22: Software
Flight Controller Configuration - Betaflight
DSHOT Commands
BLHeli_32 Passthrough and Telemetry Support
SP Racing F4 EVO compatible
Automatic Notch Filtering
Blackbox Logging
Failsafe configuration

## Slide 23: Software
ESC Controller Configuration – BLHeli_32
Configure the onboard speed controller using a Betaflight passthrough
Direct configuration of ESC from flight controller with DSHOT commands
Motor calibration

## Slide 24: Software
Drone Autopilot Software– iNAV & MWP
Waypoint missions
Physically map and trace out the course of action for the quadcopter drone
Needed for GPS modes: external GPS, magnetometer, barometer
MWP allows for uploading XML Mission Scripts

## Slide 25: Software
Drone Autopilot Software– iNAV3D
Custom firmware developed by KenImhof, branched from iNAV
Incorporates features to enhance 3D navigation beyond base iNAV, i.e. reverse thrust control
Modification to the iNAV3D navigation code was needed to achieve desired microgravity results

## Slide 26: Software
Drone Autopilot Software– iNAV & MWP

## Slide 27: Testing & Simulation
Blackbox Protoyping

## Slide 28: Testing & Simulation
Notes: We can highlight different parts to explain and expand this to multiple slides

## Slide 29: Testing & Simulation
Notes: We can highlight different parts to explain and expand this to multiple slides

## Slide 30: Testing & Simulation
Thrust and Torque Testing – Integration with MAE
Thrust Rig
Measures weight from thrust on analog scale
Comparator circuit with phototransistor to measure RPM
Arduino used to run motors

## Slide 31: Testing & Simulation
Thrust and Torque Testing – Integration with MAE

## Slide 32: Testing & Simulation
MATLAB Simulink & FlightGear
Motivation: Ability to test various control system approaches to best obtain clean reduced gravity, and iron out kinks in our flight dynamics
FlightGear enables a fully-fledged simulation of our craft in certain simulated scenarios
Flight dynamics uses our drone dimensions
Thrust and torque calculations fed into the data analyzer in the Quad Sim GUI MATLAB application
Quad Sim attitude simulation to test hovering with yaw, roll, and pitch responses
Create aerospace blocks in Simulink and then simulate in flight gear

## Slide 33: Testing & Simulation

## Slide 34: Testing & Simulation

## Slide 35: Interdisciplinary Implementation-MAE
Motor: P60 KV340
Propellers: P22x6.6 Prop
Arms: Carbon Fiber Tubing

## Slide 36: Interdisciplinary Implementation-CS
WebApp implements:
Connecting PC to drone via USB
User sign-in
Mission Selection
Remote launch using FlySky FS-i6
Auto Abort Sequences in case something goes wrong
Collect, store, and display flight information

## Slide 37: Test Flights

## Slide 38: Administrative Content

## Slide 39: Work Distribution
Name | Power Distribution | PCB | Simulation | Prototyping/Data Collection | Firmware Integration/Configuration
Andrew | X | X | X |  | 
Jourdain |  |  | X | X | X

## Slide 40: Overall Budget

## Slide 41: ECE Budget
Item | Cost | Quantity
SP Racing F4 EVO | $37 | 1
FlySky FS-i6 (tx & rx) | $37 | 1
Ublox M8N GPS | $26 | 1
Lumenier 16000mAh LiPo Battery | $270 | 1
Lumenier BLHeli_32 51A | $25 | 6
Lantian 7oz 200A | $5.55 | 1
UBEC Regulator | $2.99 | 1
PCB | $54.32 | 3
Total | $691.51 | 

## Slide 42: Financing
Sponsored by Northrup Grumman
Total Budget: $2000 ($1500 for Build/ $500 for Testing)
Donation of wire and sample chips reduce cost

## Slide 43: Issues
Delay in progress due to hardware issues (PDB short, blowing ESCs, PCB errors)
Bidirectional speed control support came at a cost of having to research and learn additional software/firmware suites to build an autonomous platform (piecemeal hardware, e.g. gps)
Custom firmware builds leads to instability, causes errors in typically straightforward procedures
Pilot availability limits testing days, flight location and constraints limits full scale testing of more advanced mechanisms

## Slide 44: Questions?