## Slide 1: Solar powered Water Filtration System
Group 24

## Slide 2: Project Motivation
-Help underdeveloped countries
-Make a difference in someone’s life
-Decrease the number of deaths
https://www.thenational.ae/world/rains-or-not-india-faces-drinking-water-crisis-1.194811
https://www.livemint.com/Politics/WoHowGWquof0lr7KPDV7GO/India-has-worlds-highest-inhabitants-without-safe-water-re.html
https://www.prweb.com/releases/the_point_of_grace_academy_children_in_kenya_africa_do_not_have_access_to_clean_safe_drinking_water_cannedwater4kids_cw4k_is_trying_to_change_that/prweb15813295.htm
https://news.un.org/en/story/2019/08/1045051

## Slide 3: Goals and Objectives
Create a simple, efficient water filtration system with low power consumption
    -Solar panels
Make it portable
  -Small in size and lightweight
Build an Android app
  -Shows sensors data (pH, turbidity, and
  temperature)

## Slide 4: Quality Standards from EPA (Environmental Protection Agency)
Make it portable
  -Small in size and lightweight
Factors | Acceptable Level
pH of Water | 6.5-8.5
Turbidity | For systems that use conventional or direct filtration, at no time can turbidity (cloudiness of water) go higher than 1 nephelometric turbidity unit (NTU), and samples for turbidity must be less than or equal to 0.3 NTU in at least 95 percent of the samples in any month. Systems that use filtration other than the conventional or direct filtration must follow state limits, which must include turbidity at no time exceeding 5 NTU.
Dust Lead Hazard | 40 micrograms of lead per square foot (µg/ft2) to 10 µg/ft2 on floors and from 250 µg/ft2 to 100 µg/ft2 on window sills.
https://www.epa.gov/sites/production/files/2016-06/documents/npwdr_complete_table.pdf

## Slide 5: Quality Standards of the Air Quality Index (AQI) from EPA (Environmental Protection Agency) Cont’d.
Make it portable
  -Small in size and lightweight
Air Quality Index (AQI) Values | Level of Health Concern
When the AQI is in this range: | … air quality conditions are:
0-50 | Good
51-100 | Moderate
101-150 | Unhealthy for Sensitive Groups
151-200 | Unhealthy
201-300 | Very Unhealthy
301-500 | Hazardous
https://www3.epa.gov/airnow/aqi_brochure_02_14.pdf

## Slide 6: Quality Standards of H2O from EPA (Environmental Protection Agency) Cont’d.
Make it portable
  -Small in size and lightweight
Chemicals | SDWR (Secondary Drinking Water Regulations)
Aluminum | 0.05 to 0.2 mg/L
Chloride | 250 mg/L
Color | 15 color units
Copper | 1.0 mg/L
Corrosivity | non-corrosive
Fluoride | 2.0 mg/L
Foaming agents | 0.5 mg/L
Iron | 0.3 mg/L
Manganese | 0.05 mg/L
Odor | 3 threshold odor numbers
Silver | 0.1 mg/L
Sulfate | 250 mg/L
Total dissolved solids (TDS) | 500 mg/L
Zinc | 5 mg/L
https://www.epa.gov/sites/production/files/2018-03/documents/dwtable2018.pdf

## Slide 7
Specifications
Component | Design Specification
Case | < 5 lbs
Solar Panels (4) | Open: 34.4 x 9.6 x 0.1 in Folded: 7.6 x 9.6 x 0.8 in Weight: 1.7 lbs
Solar Panels Output | 19.8 W
Microcontroller | 2.7 in X 2.1 in
Water precision | ± 5 degrees Fahrenheit
Water tank | At least ½ a gallon of H20
Water pump | 4 L/min
Water pump | < 12V to power save on battery power
UV lamp | < 12 W
Bluetooth | < 6V

## Slide 8
Block Diagram
Solar Panels
Battery
Water Pump
Water Flow Sensor
Sediment Filter
Pre-Carbon Filter
UF Filtration Membrane
UV - Chamber
Water Flow Sensor
Purified Water Outlet
MCU
pH Sensor
Turbidity Sensor
LCD Display
Bluetooth Transmitter
MCU
Power
Filtration System
Peripherals

## Slide 9
Filtration System
Solar Panels
Battery
Water Pump
Water Flow Sensor
Sediment Filter
Pre-Carbon Filter
UF Filtration Membrane
UV - Chamber
Water Flow Sensor
Purified Water Outlet
MCU
pH Sensor
Turbidity Sensor
LCD Display
Bluetooth Transmitter
MCU
Power
Filtration System
Peripherals

## Slide 10: Water Filtration System
Consist in four different types of filters:
  Sediment filter
  Pre-carbon filter
  Ultrafiltration membrane
  Ultraviolet water purifier
Combination of these filters ensures purified water meets all required standards
For convenience of the user the filters selected have minimum lifetime of 12 months

## Slide 11: Ultraviolet filter
Selection criteria:
Large lifetime
Low power consumption
Cheap to reduce overall cost
Overall effectiveness
Ultraviolet water purifier | Size | Cost | Lifetime | Power consumption
Express Water – Ultraviolet Water Filter | 16 x 4.5 x 3.6 inches | $69.99 | 6 months | 12 W
Boeray Ultraviolet Light Water Purifier | 17.8 x 4.9 x 3.9 inches | $53.99 | 12 months | 6W

## Slide 12: Water Pump
Comparison of 2 types of water Pump:
Transfer water pump easy to maintain, more efficient, large use of energy
Submersible water pump not portable, less efficient, conserve energy
Specifications:
Voltage: 6-12 volts
Current Drawn: 1.7 Amp
Liters per minute: 4.3 L/min
Cost: $16.48
17cm x 10cm x 67cm

## Slide 13
MCU
Solar Panels
Battery
Water Pump
Water Flow Sensor
Sediment Filter
Pre-Carbon Filter
UF Filtration Membrane
UV - Chamber
Water Flow Sensor
Purified Water Outlet
MCU
pH/Temperature Sensor
Turbidity Sensor
LCD Display
Bluetooth Transmitter
MCU
Power
Filtration System
Peripherals

## Slide 14: Microcontroller
Selection Criteria:
Cheap to reduce overall cost
Enough number of pins for multiple peripherals
Low power consumption to optimize battery lifetime
Easy to mount on PCB
Compatibility with different types of sensors
 | ATSAMG51 | MSP430FR6989 | Atmega328P
Memory | 256 KB | 128 KB | 32 KB
RAM | 64 KB | 2 KB | 2 KB
Pin Size | 38 | 83 | 23
Communication Protocols | UART, I2C, SPI | UART, I2C, SPI | UART, I2C, SPI
Low-Power Mode | 103 uA/MHz | 101.25 uA/MHz | 0.75 uA/MHz

## Slide 15: ATmega328p
• Arduino bootloader
• Compatible with multiple types of sensors
• Programmable in C
•Extensive list of hardware libraries
• Simple layout and easy to use
• Large support community
• Open source

## Slide 16
Peripherals
Solar Panels
Battery
Water Pump
Water Flow Sensor
Sediment Filter
Pre-Carbon Filter
UF Filtration Membrane
UV - Chamber
Water Flow Sensor
Purified Water Outlet
MCU
pH Sensor
Turbidity Sensor
LCD Display
Bluetooth Transmitter
MCU
Power
Filtration System
Peripherals

## Slide 17: Wireless Technology Selection
Connection | Power Consumption | Range | Interference | Bandwidth
Bluetooth | 100 mW | 10 meters | Minimum of 2.4 GHz | 1 Mb/s
Wi-Fi | 750 mW | 100 meters | 2.4 GHz -5 GHz | 54 Mb/s
In order for the microcontroller to send the information received from the sensors to a mobile device a wireless communication is needed
Selection criteria:
Easy to connect to devices
Low power consumption
No need of internet connection
Easier to implement in microcontroller environment

## Slide 18: Bluetooth module comparison
 | HC-05 | HC-06
Dimension | 26.9mm x 13mm x 2.2 mm | 26.9mm x 13mm x 2.2 mm
Operating Voltage | +3.3V to +6V | +3.3V to +6V
Security | Authentication and encryption | Authentication and encryption
Operating temperature range | -20 ~ +75Centigrade | -20ºC to +55ºC
Bluetooth protocol | Bluetooth Specification v2.0 | Bluetooth V2.0 protocol standard
Pins | 6 | 4
Modes | Master or slave | Slave

## Slide 19
Turbidity Sensor
Turbidity Sensor Model | DFRobot Gravity SEN0189 | Thermometrics TSD - 10 | Thermometrics TSW – 10
Operating Voltage | 5V | 5V | 5V
Operating Current | 40mA (max) | 30mA (max) | 30mA (max)
Insulation Resistance | 100MΩ (min) | 100MΩ (min) | 100MΩ (min)
Operating Temperature | 5°C – 90°C | -10°C – 90°C | -30°C – 80°C
Storage Temperature | -10°C – 90°C | -20°C – 90°C | -10°C – 80°C
Selection Criteria:
Low power consumption
Low price
https://www.dfrobot.com/product-1394.html
DFRobot Gravity SEN0189: Available from DFRobot.com

## Slide 20
pH Sensor
Selection Criteria:
Low power consumption
Low price
Waterproof
pH sensor model | pH Measuring Range | Response Time | Waterproof | Operating Voltage
DFRobot Gravity SEN0161 | 0 – 14 pH | < 1 min | Only the tip | 5 V
DFRobot Gravity SEN0169 | 0 – 14 pH | < 1 min | Yes | 5 V
GAOHOU Probe BNC | 0 – 14 pH | < 6 sec | Yes | 5 V
https://www.amazon.com/GAOHOU-PH0-14-Detect-Electrode-Arduino/dp/B0799BXMVJ
GAOHOU Probe BNC: Available from Amazon.com

## Slide 21
Water Flow Sensor
Selection Criteria:
Low power consumption
Low price
Durability
Water flow rate measuring capacity
Water flow sensor model | Water Flow Rate Measuring Range | Material | Working Temperature | Operating Voltage
Seeed Flow Sensor YF-B3 | 1 – 25 L/min | Cooper | < 120 ◦ C | 5 V
Seed M11 water flow sensor | 0.3 – 6 L/min | Plastic | < 80 ◦ C | 5 V
Seed G3/4 water flow sensor | 1 – 60 L/min | Plastic | < 80 ◦ C | 5 V
https://www.seeedstudio.com/Water-Flow-Sensor-YF-B3-p-2880.html
Water Flow Sensor YF-B3: Available from Seeedstudio.com

## Slide 22
LCD Screen
LCD 16x02 screen module
System is designed so it can be operated without the application.
The LCD screen will display the readings from the sensors and alert the user in case there is a problem with the system.
https://www.digikey.com/product-detail/en/mikroelektronika/MIKROE-55/1471-1236-ND/4495600?utm_adgroup=Accessories&gclid=CjwKCAjwvtX0BRAFEiwAGWJyZOwM39n_hSP3fWXW6l0F4G0A0QhQG5_s9Y7RydgSesNh8aurzWGtcRoCvqsQAvD_BwE

## Slide 23
Power
Solar Panels
Battery
Water Pump
Water Flow Sensor
Sediment Filter
Pre-Carbon Filter
UF Filtration Membrane
UV - Chamber
Water Flow Sensor
Purified Water Outlet
MCU
pH Sensor
Turbidity Sensor
LCD Display
Bluetooth Transmitter
MCU
Power
Filtration System
Peripherals

## Slide 24: Solar Panels
Comparison of 3 types of solar panels:
Monocrystalline Cells- Small, highest efficiency, very portable
Polycrystalline Cells-Large in size (heavy), less efficient, not portable
Thin Film Cells-Large in size, less efficient, not portable
Specifications:
19 % efficiency rates, 16V output, peak current of 1.1 A, and peak power of 19.8 W
Has a built-in USB port

## Slide 25: Battery
Battery Features | Lead-acid | Li-ion | Li - polymer
Weight | heavy (13 Lb.) | 1.6Lb | Light (1.5Lb.)
Energy capacity | 26,000 mAh | 24,000mAh | 24,000 mAh
Discharge stability | Less stable | stable | Very stable
Efficiency % | Less (50-70) | medium | High(>90)
safety | Less safe | Medium more volatile | More safe
Charging duration | longer | medium | Short
Cost ($) | 70 | 90 | 110

## Slide 26: Battery Omars 2400 mAH 80W Portable power bank
Specification
Capacity : 24,000 mAh / 80 Watt Hours
Output: 2-A USB 5V 2.1A
AC output
Battery Type: Li-Polymer
DC Input:16.8V/2.0A
Dimensions
Size : 4.91*7.4*1.73 inches (124.8x188x44mm)
Weight : 2 pounds (907g)
https://www.omars.com/

## Slide 27: Advantages
Protection: Short Circuit, Over Charge, Over Discharge, Over Current, Over Temperature
Very light weight 2 pounds
2.5-3 hours from included additional AC charger
Safe for air travel
No need for charge controller (MPPT).
Battery features always ON mode
https://www.omars.com/

## Slide 28: PCB schematic

## Slide 29: PCB Layout

## Slide 30
Sensor Testing
Measured Substance | pH Reading | Expected pH
Vinegar | 2.98 | 2.4-3.4
Distilled Water | 7.13 | 7
Salted Water | 8.53 | ~8
The pH sensor is tested by measuring the pH in liquids with know pH concentrations.
We used vinegar, distilled water and salted water for our tests.

## Slide 31
Sensor Testing
Subtance | Turbidity (NTU) Reading
Liquid #1 | 0.79
Liquid #2 | 40.39
Liquid #3 | 1057.19
The turbidity sensor measures the amount of particles suspended in the water.
The unit for turbidity measurement is called NTU.
The higher amount of particles in the water, the higher the NTU value.

## Slide 32
Software Testing

## Slide 33
Software Testing

## Slide 34: Work Distribution
Task | Alejandro | Cecile | Henok | Gabriel
Wireless Communication |  |  |  | 
Mobile Application |  |  |  | 
Microcontroller |  |  |  | 
Power Supply |  |  |  | 
Rechargeable Battery |  |  |  | 
Sensor Integration |  |  |  | 
Water filtration Module |  |  |  | 
User Interface |  |  |  | 
PCB Design |  |  |  | 
Solar Panel Integration |  |  |  | 
Primary task 
Secondary task 

## Slide 35: Project constraints
Access to laboratory due to covid-19 pandemic
Shipment delays
Water leaks
UV- Filter
Powers from Ac – 120V
Need for additional circuitry

## Slide 36: Project Expenses
Number | Component name and | Vendor’s Name | Cost/unit
1 | Arc 20W Solar charger kit | Voltaic Systems | 97.10
2 | Waterproof Case | GSI outdoors | 24.22
3 | Miscellaneous (magnets, components, pin headers) | Home Depot / Sparkfun and Mouser | 75.02
4 | Omars 2400mAH Battery | Well-made brands | 65.0
5 | Housing (case) | Fright harbor | 42.0
6 | Microcontroller (X2) | ELEGOO | 14
7 | PCB | Mouser | 35
8 | Water pump | Amazon | 15.48
9 | Sediment filter | DFRBOT | 7.99
10 | Turbidity sensor | DFRBOT | 15
11 | Ph/temperature sensor | GAOHOU | 38
12 | Water flow sensor (X2) | Amazon | 22
13 | Ultrafiltration membrane | Amazon | 19.0
14 | Pre-carbon filter | Amazon | 15
15 | Bluetooth module | Mouser | 8
16 | LCD | ELEGOO | 8
17 | Document printing | Office depot | 17
 | Grand Total |  | 517.81

## Slide 37: Progress …
Chart: 
| Overall | Code | HW-Testing | Design | Research
Column2
Column3
Series 3 | 100 | 100 | 100 | 100 | 100

## Slide 38
Any Questions… ?