## Slide 1: BikeSystem Final Presentation
Group 21 Keegan Van Wyk – EE Daniel Birath – EE Benjamin Tamayo – EE Sandhya Singh – CpE

## Slide 2: Motivation
Alternative to expensive bikes
Make locking a bike more convenient
Provide useful metrics to the user
Appeal to a niche in the market
Notes: Keegan

## Slide 3: Goals & Objectives
Basic Goals | Advanced Goals | Stretch Goals
RFID module as the main locking/unlocking method | Fingerprint locking/unlocking methods as failsafe | Generate power/charge from the bicycle itself instead of replaceable batteries
Lights added to frame as safety measure | Temperature Sensor added to measure ambient temperature | Creating of the mobile to connect via Bluetooth
Mounted LCD on handlebars | - | GPS tracking module for location purposes
Sensors attached to wheels to measure distance and speed | - | -
- | - | -
Notes: Ben

## Slide 4: Specifications
Inclusive bike locking system that can be attached to a pre-existing bike frame
Main marketed method of locking/unlocking via RFID module
Alternate unlocking mechanism in the case of low power
Measure revolutions of wheel and tire assembly
Notes: Danny

## Slide 5: Specifications Cont’d
Additional lights mounted on bicycle frame as a safety measure
A DC power generator with drive pulley will be fixed to the frame of the bike to charge the battery
Creation of a mobile app to save the metrics (health data, ambient temperature, distance, and average speed) from each trip
Notes: Danny

## Slide 6: 3 Demonstratable Specifications
Specification #1:
  LED Brightness greater than 50 lux
Specification #2:
  Measured distance is accurate within +/- one foot
Specification #3:
  RFID unlocks within less than 5 seconds
Notes: Danny

## Slide 7: Block Diagram
Notes: Keegan

## Slide 8: Bike System
Notes: Keegan

## Slide 9: Related Standards
JESB8C.01 3.3V Standard
ISO/IEC/IEEE 29119 – Life Cycle of Software Development
ISO/IEC standard 18000-3:2008
OSHA standard 1915.82 General Requirements for Lighting
Notes: Keegan/Sandy/Ben/Danny

## Slide 10: Constraints
Economic
  Lack of funding – the BikeSystem is entirely self-funded
Microcontroller and relating sensors were confined to the power design (3.3V)
Time
  Shipping and manufacturing delays due to the pandemic
Notes: Danny

## Slide 11: Power Subsystem
Power provided by battery and dynamo
Rectifies and regulates power generated by dynamo
Switches between sourcing power from dynamo and battery
Automatic switching between power sources
Indicates when battery is in use
Charges the battery when the battery is not in use
Regulates selected source to 3.3V output
Notes: Keegan

## Slide 12: Power Subsystem Block Diagram
Notes: Keegan

## Slide 13: Input Rectification and Regulation
Rectification and Filtering
Dynamo Input
Voltage Regulation IC
Notes: Keegan

## Slide 14: Battery and Charging Circuit
For External Charging
Charging IC
Battery Connection
Notes: Keegan

## Slide 15: Power Circuit Switch
Voltage Reference
Comparator
Power Switching IC
Notes: Keegan

## Slide 16: Output Regulation
Voltage Regulation IC
Notes: Keegan

## Slide 17: Methods for Unlocking the Bicycle
Potential Components
Fingerprint Scanner
Cell Phone Application (App)
RFID System
Reasons for Selected Component
Due to limited coding experience among the three EE’s in the group, the cell phone application was ruled out.
The fingerprint scanner proved more difficult to implement, and more expensive, during the research phase of the project when compared to the RFID System.
The RFID System had relevant libraries to rely upon when debugging code and was the cheapest of three options in terms of time and effort.
Notes: Ben

## Slide 18: RFID Module
Only complete RFID modules were considered.
RC522 was chosen because of stark difference in price and freedom of communication protocol.
Notes: Ben

## Slide 19: RFID Module
Benefits to using the RC522 RFID module include:
  Proof of concept and code with an existing embedded antenna and impedance matching network.
  Proof of schematic for specific communication standard (SPI).
Notes: Ben

## Slide 20: Integrating RFID Module
The IC that drives the RC522 RFID module is called the MFRC522 IC. This IC is responsible for communicating with the chosen microcontroller and RFID card.
The two primary steps to integrate the RFID module into the final PCB is to design an antenna with a known inductance and then design an impedance matching network that connects the antenna to the MFRC522.
Notes: Ben

## Slide 21: RFID Subcircuits

## Slide 22: RFID Matching Network
Notes: Ben

## Slide 23: RFID Circuit Simulation Schematic

## Slide 24: RFID Smith Chart Simulation

## Slide 25: Locking Mechanism
Provide user with a better alternative to traditional bike locks
Convenience
Efficiency
Notes: Danny

## Slide 26: Locking Mechanism
Key Features:
Automatic locking/unlocking of the bike system
Lock assembly mechanics
Rotating arm driven by a servo motor
Set Backs:
Redesign of device used for locking
Comparison of Electromagnet and servo motor
Notes: Danny

## Slide 27: Speed and Distance Calculation
Potential Components
Accelerometer
Hall Sensor
Reed Switch
Reason for Selected Component
The Reed Switch offers the relevant information, for example the revolutions of the bicycle tire per unit time, while the other two options offer information that will not be used for the purpose of speed and distance calculation.
Reed Switch requires the least pins of all the options aforementioned.
Reed Switch is the less expensive option when compared to the accelerometer.
Notes: Ben

## Slide 28: Reed Sensor
The Littelfuse 59145 Reed Sensor was chosen because of its mounting style and sensitivity.
Normally-open configuration will be used.
Notes: Ben

## Slide 29: Reed Sensor
Reed Sensor is basically a switch that is actuated by an electromagnetic field.
Output of reed sensor will be used to calculate speed and distance traveled by the system.
Notes: Ben

## Slide 30: Magnet for Reed Sensor Actuation
Magnet needs to be able to actuate the Reed Sensor from at least 0.5 inches away.
D81AD-P magnet was chosen, although it was the most expensive per part of all magnets considered, because it has the highest magnetic field strength when considered from 0.5 inches away.
D81AP-P also comes with adhesive pad, which will be needed to secure magnets to the rim of the bicycle tire.
Notes: Ben

## Slide 31: Microcontroller
MSP430G2553
3.3 v
Low power consumption
Notes: Sandy

## Slide 32: Microcontroller Comparison

## Slide 33: Use Case Diagram
Notes: Sandy

## Slide 34: Software Functionality
Input from:
    Reed Sensor
    TMP 235 Temperature Sensor
    RFID Module
    Lights
Code written in the C language
Developed and tested within Code Composter Studio (CCS) environment
Notes: Sandy

## Slide 35: User Interface
Simple design to avoid user/rider distraction
Metrics such as the temperature, current trip distance and current trip average speed are constantly updated and displayed on the LCD
Notes: Sandy

## Slide 36: LCD Comparison

## Slide 37: LCD
HiLetGo IL19341
3.3 V operating voltage
Resolution: 240 x 320
Dimensions: 43.2 mm x 57.6 mm
Notes: Sandy

## Slide 38: Temperature Sensor Comparison

## Slide 39: LED Lights
Provide a deterrent from motor vehicles
Provide light for the rider
Efficiently use power resources
Notes: Danny

## Slide 40: LED Lights Features
Auto dimming
Driver for LED’s
Manual On/Off switch
Notes: Danny

## Slide 41: Light Comparison
Incandescent VS LED Lighting
Power
Lifespan
Image provided from Wiki.com

## Slide 42: System Integration
Each subsystem was integrated together to form the Bike System
Split up amongst three interconnected PCBs
System Testing
Notes: Keegan

## Slide 43: Layout
Notes: Keegan

## Slide 44: Layout
Notes: Keegan

## Slide 45: Administrative Content

## Slide 46: Work Distribution
Group Member | Power Circuitry | Locking Mechanism | Temperature Sensor | Code | UI Design | RFID | Reed Sensor | Lighting | PCB Schematics
Keegan | Primary |  |  |  |  |  | Secondary | Secondary | Primary
Daniel | Secondary | Primary | Secondary | Primary |  | Secondary |  | Primary | Secondary
Benjamin |  | Secondary |  | Secondary |  | Primary | Primary |  | Secondary
Sandhya |  |  | Primary | Primary | Primary | Secondary |  |  | 
Notes: Sandy

## Slide 47: Budget
Self-funded
Initial budget of $ 600
Notes: Sandy

## Slide 48: Thank you