## Slide 1: Group 27: Chromesthesia Simulation Device
Angel Garcia – CpE
Wesley Ellery – CpE
Nicholas Alban – EE
Brooke Roeder- EE
Notes: Angel Hello everyone, we are group 27, my name is Angel Garcia,
For our project we have designed and created our chromesthesia simulation device.

## Slide 2: Project Overview
We strived to design a device that would take audio and visual inputs and produce a visual output to simulate the visual experiences a person with chromesthesia would experience.
The way it will work is by combining audio input devices and an optical capture device on a single platform that can be oriented and pointed in any direction.
Notes: Angel Essentially we wanted to design a device that would take audio and visual inputs and produce an output to simulate similar experience a person with chromesthesia would experience. The way it works is by combining audio input devices, like microphones, along with an optical capture device such as a camera, on a single platform which can be oriented and pointed in any direction.

## Slide 3
Simply a compelling technological device to create
  Augmented reality is an up and coming field
Create a device which can have educational applications from a consumer point of view
Create awareness of Chromesthesia, and Synesthetes overall (about 1 in 3000 individuals)
Motivation
Notes: Angel Our motivation for this project was for one, to challenge ourselves and create a unique technological device. We feel like this is close to augmented reality which is something currently being developed and improved on as the days go by. Our other reason for our motivation was to create awareness of chromesthesia and synesthetes overall.

## Slide 4: What is Chromesthesia?
Chromesthesia is an audio-visual variant of the phenomenon called "synesthesia", which is when the stimulation of one sensory or cognitive pathway leads to involuntary experiences in a second sensory or cognitive pathway.
Chromesthesia is the involuntary association of sounds to visual effects such as shapes and colors.
It is well known with related research that lower frequencies are associated with dark colors and high frequencies are paired with bright colors.
Notes: Brooke

## Slide 5: 2017 Study in Japan
15 subjects with moderate to high levels of absolute pitch(the ability to identify without effort the pitch of a note)
Administered twice a day on two different days half a year apart, order was randomized, and the results pertaining to the RGB values of the colors chosen were recorded and averaged
Notes: Brooke

## Slide 6: Goals and Objectives
Design an efficient and user-friendly consumer device that can simulate the chromesthesia phenomenon
Low-cost design and good product longevity
Energy efficiency in processing audio and visual data
Notes: Wes – READ AS IS

## Slide 7: Similar Past Projects
Sound Color Project
  Web app created by Kevin Groat(University of Mary Washington) and Derek Torsani (Musician/Designer)
E-MOCOMU(E-MOtion, COlour, and Music)
  Based on Kinect, which is a technology that allows players to operate and interact with the console without maintaining physical touch with a videogame joystick
We referenced both these projects to get a start for our project and avoid any similar constraints.
Notes: Angel We ended up finding two projects that were related to chromesthesia. The first one was named the sound color project, which was a Javascript web app that would analyze frequency and volume. It would use an audio input source such as a device’s microphone and these two variables would then be transformed into light, color, and textures using a predetermined color pattern and mapping audible into visual quantities. The second one was a prototype called EMOCOMU, which was developed by a PhD student in Spain where by moving around in space freely with no physical touch with the console through a joystick, her device would let users change sounds, pictures and colors by moving and interacting with the console through the Kinect technology. We referenced both of these projects to get a start on our projects and avoid any similar constraints.

## Slide 8: Project Constraints
Economical and Environmental
  Chip and Electrical components shortage
  Pandemic
  low budget, self-funded project
Time and Educational
  Managing project design time with other classes and work schedules
  Education constraints, using many new hardware and design ideas
Safety constraints
  Working with electricity and soldering iron
Notes: Wes- As for our project constraints, we wanted our device to be economical and environmental, due to supply chain issues and our budget that we set. We also had to manage the scope of our project, as we had other commitments, as well as limited industry knowledge.

## Slide 9: Engineering Specifications
Component(s)​ | Parameter​ | Specification​
Microphones​ and PCB | Audio Input​ | Amplify signal in the Frequency Range of 20Hz-20KHz​
Microphones and PCB | Audio Input and Processing​ | 70% accuracy up to 5 meter range​
Microprocessor​ | Processing Speed​ | Associate color with designated frequency under 2 seconds (i.e Red is associated with the key of A, frequency 440Hz)​
Microprocessor and Screen Display | Refresh rate | Able to update a new overlay every 1 second
Camera | Power Consumption | 6.7 to 10 watts power consumption
Battery​ | Discharge Time​ | 2 hours​
Notes: Wes – Here are our Engineering Specifications. Our testable specifications that we demonstrated are the first 4, showing that we can amplify a signal in the range between 20Hz to 20KHz, have a 70% accurate detection range up to 5 meters away, associate a color with a designated frequency we have defined in under 2 seconds, with an example being that the color red associates with the key of A, which is a 440Hz frequency. Finally, our device is expected to update a new overly every 1 second with a new color should we change the frequency.

## Slide 10: Electrical Components & Hardware Design
Notes: Wes – Next, here is our Components and Hardware Design.

## Slide 11: Device Block Diagram Overview
Notes: Wes – Our Device Block Diagram is shown here. Our device will take directional audio inputs from a source, along with a visual input, which is our optical capture device. The devices to capture these inputs are placed on our build. We will process this data with algorithms we have written. We will get into the issues we had with our 3D sound localization later in the presentation. Finally, our software will also take the frequencies and render an image, which is then output to a screen.

## Slide 12: Microprocessor
A microprocessor is needed to receive data from the camera and microphones
Will read and store all the data as a dataset
Process visual data smoothly
Necessary for datasheets to be available
Notes: Wes – As for our microprocessor, this is needed to process data from the camera and microphones. This data will be read, and stored as a dataset. With the amount of information we will be processing, it is important we have a high quality, fast microprocessor for the job to process our data as smooth as possible.

## Slide 13: MCU Comparisons
Notes: Wes – Here is our MCU comparison table. Note, while we have pictures of the entire board, we are evaluating based on the Chip, not the board itself. We were very interested in the Processor Speed for the graphics we need to render.

## Slide 14: Raspberry Pi 4 Model B 2GB
Datasheets also readily available
Device needed a video engine, so instead of a single microcontroller, we went with a system on a chip (SoC) for video processing.
In order to encode and decode the video effectively, we needed something faster with a data bus bandwidth of at least 32bit with an integrated GPU
RPi 4 had enough RAM and processing power for the task we needed it to do
Notes: Wes – In order to properly render graphics, we need a strong board with a proper video engine to do this. We will only be using the Raspberry Pi Graphics processing, and we will mount our PCB on top of it.

## Slide 15: MSP430FR6989
Datasheets also readily available
All group members familiar with this MCU due to classes in Embedded Systems
Each member owned one so was easy to start working with it
No video engine or GPU, could not process higher resolution RGB images
Perfect for the audio data processing
Notes: Wes – The MSP430 is a board we have plenty of experiencing using in classes at UCF, so we decided to use the chip from this board to handle audio data processing. Unfortunately, it was not powerful enough to handle the video processing we needed. Since we all owned the board, it made initial design work a lot more simple, since we did not have to spend additional money.

## Slide 16: Microphones
Device needs microphones that can detect audio signals with a narrow cone
  We want it to work in a unidirectional manner
  Larger cones would result in detecting signals beyond the scope of the camera's aperture.
Design requires 3 small microphones
When all frequencies are acquired, the average will be taken and sorted through our algorithm
dB Unlimited MU06442:
Electret microphone
Unidirectional
40~20k Hz
Notes: Brooke

## Slide 17: Display Panel
GeekPi 7 inch 1024 x 600 HDMI Screen LCD Display with Driver Board Monitor for Raspberry Pi
Extremely user friendly
Full Color
$49.98
7” wide display
Comes ready for use
Notes: Angel – the display we ended up choosing was the greekpi 7 inch LCD display. We chose this because it is very user friendly, it displays full color, and we believe it was a pretty reasonable price along with being on amazon so the shipping was extremely quick.

## Slide 18: Camera Comparison
Arducam Mini Module Camera Shield with OV2640
Notes: Wes – Our camera we selected is the Arducam Mini Module OV2640, which provides us enough resolution to handle 1600 x 1200 video. We spent a lot of time reviewing different cameras, and this one met all of our requirements for resolution, power and frames per second.

## Slide 19: Power Supply Table
Notes: Angel – this is our power supply comparison table. During our initial round of researching we ended up looking into Nickel cadmium, nickel metal hydrides, 9V batteriers and Lithium ion batteries. We ended up deciding on using a lithium ion battery for our project.

## Slide 20: Power Supply
Video processing is power hungry, so we decided on a lithium ion battery, since they are safe and have high energy density
Ideal battery would hold a charge for at least two hours in order to be useful for educational and practical setting
Ideal battery would be able charge in a short period of time and not lose too much charge when not in use
Notes: Angel – Due to our power hungry video processing, We picked the lithium ion battery because we needed to make sure we use a battery that is safe and had high energy density. These batteries are capable of holding a charge for at least 2 hours in a practical setting and they are also able to charge in a short amount of time.

## Slide 21
PCB, Project Schematic (KiCad)
Notes: Angel - This is the first part of our schematics where it is the overall picture, with all of our components.

## Slide 22: Battery and Charging, Project Schematic (KiCad)
Notes: Angel - So it starts with the usb input here on the top left, which connects to the battery charger, which has a battery discharge protection which makes sure that the battery doesn’t discharge when its not plugged in or in use. The discharge protection is then connected to a step up converter which would step up the voltage if it is low to 5v which is then connected to a drop down regulator which will take the 5v and drop it down to 3.3 as needed. The 3.3v will power up the components we have connected to the MCU which are our microphones.

## Slide 23: MSP430, Project Schematic (KiCad)
Notes: Angel -
Our microphones are connected to the MCU via ports 52 to 54. We have the two LEDs that will tell us if the MCU is powered on or not. We have the reset button to reset the microcontroller whenever it is needed. We also have some test points(TP) that the microphones are connected to on the left hand side in ports 25 through 28. The TEST/RESEt, TXD,RXD ports are all connected to our ezfet pin header, which allows for serial communication between the mcu and the components that are connected and then Our I2c header allows us to have communication between our raspberry pi and MCU

## Slide 24: Microphones, Project Schematic (KiCad)
Notes: Angel -
These are our schematics for our microphones that will be connected to the Microcontroller.

## Slide 25
Printed Circuit Board Layout
Notes: Angel -
On the left, here we have our PCB design that we did through Kicad, and on the right is a render that we were able to do.

## Slide 26
Notes: Angel -
This is a render of that we did on how it would look like overall. We made the pcb compact and sort of like a hat for the raspberry pi to save space.

## Slide 27: Assembled Board
Notes: Angel-
Here is a picture of the final board.

## Slide 28: Software Design
Notes: Nick

## Slide 29: Software Block Diagram
Flowchart highlighting Datapath from input to output
Highlights where certain processes are handled
Within each of these microcontrollers (MSP430 & Raspberry PI), the software will be written to receive and deliver the specified data in the flowchart
Notes: Nick

## Slide 30: Audio Processing Software Flowchart
Click to add text
Flowchart detailing the functions and data from start to end of the Software handing the audio inputs
All functions will be performed on the MSP430
Notes: Nick

## Slide 31: Audio Processing Functions
Fourier Transform
  Mathematically decompose a signal into its constituent frequencies
  Will determine frequencies of audio input signals from microphones
  Fast Fourier Transform (FFT) - a common method
Notes: Nick

## Slide 32: Audio Processing Functions
Noise Filtering
  Reducing the excess noise in the frequency data from the Fourier Transform
  Will improve accuracy of desired frequencies
    Possibly Bandpass filtering
Notes: Nick

## Slide 33: Audio Processing Functions
Obtaining Frequency of Audio
  Convert the input signal from Analog input to a numerical value of the frequency that can be sent to the Raspberry PI
3D Sound Localization
  Determines the direction of the audio frequency source using the known physical orientation of the microphones and the received audio input signals from each microphone
  Used to send polar coordinates to Raspberry PI for audio source localization
  We were unable to implement this feature due to hardware limitations. ADC and the FFT algorithm were already taxing one the MSP430, and the calculations required to do 3D sound localization would be too intense.
Notes: Nick

## Slide 34: Visual Software Flowchart
Flowchart detailing the functions and data from start to end of the Software handing the audio inputs
All functions will be performed on the Raspberry PI
Notes: Brooke

## Slide 35: Frequency-to-Color Algorithm
The pitch class and pitch height (octave) are calculated from the frequency detected
The pitch class determines the hue, and the octave determines the lightness of the color
Key number:
Pitch class:
Octave:
Notes: Brooke

## Slide 36: Frequency-to-Color Algorithm
Pitch class to hue:
Octave to lightness:
Notes: Brooke

## Slide 37: Visual Processing Functions
Frequency-To-Color Algorithm
  Function to determine the color corresponding to a given frequency
  RGB value output
Image Generation/Acquisition
  Acquiring and displaying the image using the camera module
Image Overlay Generation
  Creating an RGBA overlay using RGB value output and an alpha value matrix to display a circle
Notes: Nick

## Slide 38: Programming Languages
Programming languages will include the C and Python.
  C will be used for the MSP430
  Python will be used for image processing on the Raspberry PI
Notes: Nick

## Slide 39: Functional Prototype
Notes: nick

## Slide 40: View of Camera and Microphones
Notes: nick

## Slide 41: Development Issues
Flashing code on PCB was complicated.
Software Development was more complicated that initially expected due to limitations of the MSP430.
Change from I2C protocol to UART mid-development.
3D sound localization was not possible with hardware speed limitations. Need stronger hardware, but this requires an increase in budget that we could not afford.
3D printing of our housing. Several issues came up including warping of the material.
Notes: Wes- Read as is.

## Slide 42: Future Considerations
Virtual Reality Component
Reprint the PCB and design it to include more microphone inputs
Different processing to enable more consistent results
More efficient algorithms
Notes: Wes- Read as is.

## Slide 43: Motivation and Lessons Learned
We chose this project because it was an idea that felt different than a lot of previous projects we researched. We wanted to bring awareness to this phenomenon and building a device that simulates this behavior was a great way to achieve that.
Biggest takeaway from working on this project is that things do not always go as intended. We had several rewrites and design changes that became overwhelming at times, but having clear communication resolved a lot of the issues we had.
Defining clearer requirements in the early stages of planning is an important lessons that will help us in the industry, as this sets up for development success.
Notes: Wes- Read as is.

## Slide 44: Administrative Details
Notes: Finally, we will go into administrative details pertaining to budgeting, division of labor, and project progress.

## Slide 45: Project Budget (Update for grand total cost)
Component | Part | Vendor | Quantity | Price/Unit | Total Cost
Camera | Arducam Mini Module Camera Shield with OV2640 2 Megapixels Lens | Amazon.com | 1 | $25.99 | $25.99
PCB | Custom Design | PCBway.com | 3 | $200 | $600
Microcontroller | Raspberry Pi 4 Model B 2GB | Amazon.com | 1 | $106.49 | $106.49
Display | GeekPi 7 inch 1024 x 600 HDMI Screen LCD Display with Driver Board Monitor for Raspberry Pi | Amazon.com | 1 | $53.23 | $53.23
Housing | 3D Printer Spool | Amazon.com | 1/8th of a spool | $20 | $2.50
Microphone | DB Unlimited Unidirectional Electret Microphones | Mouser.com | 6 | $1.84 | $11.04
Li-Ion Batteries | EVE 25P 18650 2500mAh 20A Battery | 18650batterystore.com | 4 | $3.99 | $17.78
 |  |  |  |  | Total - $817.03
Notes: Here is our budget sheet, where we tracked all the components we purchased, their price, and the quantity. The PCB costs include the expedited shipping, along with all of the components needed to build it, and the design costs.

## Slide 46: Division of Labor
Angel | Wesley | Brooke | Nicholas
PCB Design and Schematics | PCB design and Schematics | Pitch to color Algorithm Development | Software Design for Audio
Chromesthesia Research | Product Hunting | Microphone and Amplifier Design | Prototype Development
Product Hunting | Documentation | Software Design for Image Processing | Software Integration
Notes: This is our division of labor, essentially highlighting the higher-level responsibilities of each group member. Our top row depicts our primary roles, while the row under is for our secondary roles, as is the same for the third row. Nick was primarily in charge of software development for both the
MSP430 and raspberry pi. Wes and I were in charge primarily for the PCB design and product hunting in addition to researching chromesthesia.
Last but not least, Brooke was in charge of developing the pitch-to-color algorithm microphone and amplifier design, and testing.

## Slide 47: Project Progress
Notes: For our project, we managed to be 100% complete pretty efficiently towards the end of the semester. We were able to get most of our hardware before our midterm presentation with the exception of the PCB. Fortunately, it arrived shortly after and we began properly assembling our device. We managed to finish the hardware construction within second to last week, since it was a category that involved several aspects such as 3D printing our chassis. The software was the most difficult aspect of the device, but we managed to make it work with some minor changes. Notably switching from I2C to UART. Once all of the main categories were finished, we were able to quickly develop a web page for our project and group.

## Slide 48: Thank you for taking the time to listen to our presentation.
Notes: Overall, our project is 100% complete. Thank you for taking the time to listen to our presentation.