## Slide 1: Pick pocket tuner
Critical Design Review Group 42
Lucas Grayford - Electrical Engineering (Comprehensive Track)
Paul Grayford - Electrical Engineering (POWER TRACK)
Luis Vargas – Computer Engineering (Comprehensive Track)
Jamie Henry – Computer Engineering (Comprehensive Track)

## Slide 2: Presentation overview
Project Description / Motivation / Goals
Specifications
Hardware and Software Block Diagrams
Design / integration / Testing
Administrative Content

## Slide 3: Project Description
Guitar / stringed instrument automatic tuner
Handheld device
One string at a time
LCD display with a user interface
USB-C Chargeable

## Slide 4: Project motivation
Aid musicians in tuning their instruments quickly in any environment
More specific for guitar players
Make it easy for beginner guitar players to tune their guitar
Get rid of tedious tuning, with a smart simple all-in-one system

## Slide 5: Features and options
Comfortable, ergonomic, and able to fit in one hand
Ability to tune a guitar to alternative strings (Drop-D, Drop-C, DADGAD, and more)
Tune new strings from start to finish
Added ¼” jack input for increased accurate tuning of electric guitars

## Slide 6: Stretch Goals and objectives
Ability to tune multiple types of stringed instruments
Tune instrument faster and more accurately than competitors

## Slide 7: Restrictions and constraints
Budget of the project
Allotting enough time for the project
Potential learning curves
Supply chain issues (difficulty in part acquisition)

## Slide 8: Supply Chain issues
Trouble with general part acquisition
Required looking into other options due to availability
Main supply troubles
  Regulators
  Charging circuit parts

## Slide 9: specifications
Requirement Specifications | Measurement | Units | Interval
Tune a guitar in a maximum time | 3 | minutes | ±1
String a new guitar in a maximum time | 5 | minutes | ±1
Tune strings to the correct frequency | 4 |  | ±5
Battery life with respect to strings tuned | 100 | strings | ±15
Max weight | 2 | pounds | ±0.5
Ease-of-use interface with respect to time to select and tune a string | 45 | seconds | ±10
Requirement Specifications | Measurement | Units | Interval
Tune a guitar in a maximum time | 3 | minutes | ±1
String a new guitar in a maximum time | 5 | minutes | ±1
Tune strings to the correct frequency | 4 |  | ±5
Battery life with respect to strings tuned | 100 | strings | ±15
Max weight | 2 | pounds | ±0.5
Ease-of-use interface with respect to time to select and tune a string | 45 | seconds | ±10
1. Unit of measurement for the ratio between two frequencies

## Slide 10: House of Quality
Notes: This is our house of quality diagram which shows consumer requirements related to our technical requirements. This diagram also shows many positive correlations between our technical requirements which will aid in creating a well received product.

## Slide 11: competition
Device | Battery | Motor | Display
Roadie3 | 3.7V Rechargeable LiPo 500 mAh, USB type-C | 110 RPM DC motor | Full color LCD display
Jowoom | 3.7V 2,600mAh micro microUSB-Rechargeable Lithium Battery | 180 RPM DC motor with built in encoder | LCD display
Pick Pocket Tuner | 3.7V 1,200 mAh LiPo USB type C rechargable | 160 RPM DC motor with built in encoder | TFT LCD 3.3V 240x240 display

## Slide 12: Design Strategy

## Slide 13: Components: needed/used
LiPo Battery 3.7 V
ESP8266 (ESP-12F)
2 Regulators (3.7V to 12V) and (3.7V to 3.3V)
12V DC Brushless Motor
TFT Display
Piezoelectric sensor
¼” Audio jack
On/off switch, buttons/inputs, peg winder head, housing
USB-C Chargeable Circuit (500mA rate)
Semiconductor Devices (Transistors, resistors, Capacitors

## Slide 14: Hardware block Diagram

## Slide 15: Software Block Diagram
Notes: The software flow for our project is fairly simple as our tuner will give the user a choice between four modes that mostly share the common algorithm of the Fast Fourier Transform coupled with the peg winding.

## Slide 16: Work Distribution
Role | Software Design | Hardware Design | Testing and Integration | Prototyping and Design Validation
Primary | Luis Vargas and Jamie Henry | Paul Grayford and Lucas Grayford | Luis Vargas and Paul Grayford | Lucas Grayford and Paul Grayford
Secondary | Paul Grayford and Lucas Grayford | Jamie Henry and Luis Vargas | Lucas Grayford and Jamie Henry | Jamie Henry and Luis Vargas

## Slide 17: Components: Battery 3.7 V and Usb type C charger
Original ideas were between NiMH and LiPo batteries
Chose a 3.7V LiPo battery mainly due to
  Friendly size and shape
  Lightweight
  Good at holding a long charge
Using 1200 mAh, allows longer life than Roadie3
USB-C charger (500mA charging rate)

## Slide 18: ESP8266 (ESP-12E)
Specifications | Values
GPIO Pins | 17
Operating Voltage | 3.3V
Memory | 4Mb cache
Size | 2.5cm X 1.5cm
Analog Inputs | 1
Clock Frequency | 80MHz
Notes: For our processing unit, our group chose the ESP8266 chip. This chip features 17 GPIO pins which allows for our PWM connections to the DC motor, the SPI connection to our display, and an analog input to connect to our quarter inch jack and our vibration sensor.

## Slide 19: 3.3V Regulator MCP1700T – 33002E/TT
LDO Regulator to regulate from 3.7-3.3V
SOT-23 Package
350mV max Dropout Voltage
Input Voltage: 2.3-6.0V
Output Voltage: 3.3V
Output Current: 250mA
73-91% efficient

## Slide 20: 12V Regulator
LM25118MH/NOPB Controller
Buck/Boost Design
I/P Voltage 4.2V-3.0V - O/P 12V
84.5% efficiency

## Slide 21: DC Brushless motor: fit0441
12V DC
.7A stall current
159 RPM
.235 Nm of torque (2.4 kg*cm)
Encoder, Arduino friendly

## Slide 22: MakerFocus ST7789 TFT LCD Screen Display
Full color TFT LCD 1.3"
240x240 pixels
SPI connection
Notes: For our display, we chose the ST7789 TFT Liquid Crystal Display. The display is full color and is 240 by 240 pixels and features a clock and data pin to set up an SPI connection with our ESP8266. It also comes equipped with an Arduino integrated circuit driver which has a well documented library for implementing graphics in the Arduino ide to help create our graphical user interface.

## Slide 23: Components: Vibration sensor
2 contact points
Located in housing to read string's vibration
Accurate withing 4 cents (Tuning standard)
Mounted inside housing
Notes: For our vibration sensor, we chose a Buzzer Piezo. This sensor has two contact points that will pick up the string’s vibration when tuning the guitar. The sensor will be located within the housing since the housing will be in contact with the vibrating string via the peg winder. The sensor will then send its frequency reading as an analog voltage to be stored in the software and used during the Fast Fourier Transform.

## Slide 24: Components: ¼” audio jack
4 contact points for better connection
Longer life span
More accurate readings (within 4 Cents)
Used for acoustic electric or standard electric guitars
Notes: For our quarter inch audio jack, we chose the Pure Tone Mono Multi Contact Output Jack. This jack has four contact points which entail two positive tips and two tension grounds for extremely low noise. These multiple connections as opposed to a regular one contact quarter inch jack will result in a greater signal reading. The output for the jack is identical to the vibration sensor as it will send its frequency reading as an analog voltage to be transformed via the Fast Fourier Transform.

## Slide 25: Housing / Peg Winder
Designed with Fusion 360
Fits all components
Includes mounting holes for the PCBs, motor mount, and pick holder slot
3D Printed

## Slide 26: 3D printing for components
Printer used is an SainSmart Ender 3 pro owned by Lucas Grayford
Slicer used is cura
Filament used 1kg, 1.75mm pla+
Layer height used will be .2 mm for better layer adhesion
Pegwinder will use 50% infill
Housing will use 100% varying on the wall thickness

## Slide 27: PCB with Controller
Integrated board with ESP-12E module
Compact design
Includes 3.3V regulator on the board
Created using Fusion 360

## Slide 28: Components: Miscellaneous
On/off switch to cut off power to unit
3 push buttons for interacting with the display and interface
  Left/select/right
Semiconductor Devices
Guitar pick holding slot

## Slide 29: Software development
GitHub used for version control/task designation
VSCode IDE used for code development – C/C++
  LiveShare extension used for real-time collaboration
Arduino IDE for used for code deployment
  Necessary board/graphics libraries available for components
Notes: To develop our software, GitHub was used for version control and task designation. For the environment, both VSCode and the Arduino IDE were used. VSCode was mainly used for development as it has key extensions for ease of programming. The extensions we used were Git source control manager, which helped connect the IDE to the project’s repository, and LiveShare, which allowed real-time shared code editing. Meanwhile the Arduino IDE was used for code deployment as it had the available libraries and board managers for our ESP8266 and ST7789 display.

## Slide 30: Software libraries
Adafruit_GFX/Adafruit_ST7789
  Graphics driver for communicating with the LCD display
arduinoFFT
  Used to compute data intensive calculations through fast Fourier transform
Libraries found on Arduino IDE
Notes: The libraries used for this project so far include the Adafruit Graphics library coupled with the ST7789 driver library. These libraries are for interfacing and creating our graphical user interface onto the display. ArduinoFFT was also chosen to be the Fast Fourier Transform library used to transform our analog voltage readings into its frequency in Hz.

## Slide 31: Fast Fourier transform
Transforms raw analog input data into its frequency value
O complexity vs. DFT’s O complexity
Notes: The Fast Fourier Transform, as mentioned previously, is used to translate the raw analog voltage input over time into its frequency reading in Hz. This transform is similar to the Discrete Fourier Transform and is used in programming due to its faster runtime and decreased complexity. The Fast Fourier Transform algorithms cuts the data recursively in half to create a drastically faster runtime. For our implementation of the Fast Fourier Transform, we tested and concluded that 512 data samples from the analog input would give the most accurate reading for its computation time. From our testing, the transform takes approximately half of a second and reads the frequency with less than one percent of error.

## Slide 32: Graphical User Interface
Simple directional menu hierarchy to be compatible 3 buttons
  Left and right directions for traversing the menus
String tuning interface will consist of target frequency, current frequency and string name
Range of color-coded boxes at bottom of screen will indicate flat/sharp/in-tune frequencies
Notes: For the graphical user interface, since we are using three total buttons (left, right and select) we decided to have the menus flow in the same directional pattern. Pictured is an early sketch of the string tuning interface. The screen will show the current string name, target frequency and current frequency that the sensor has read from the string. At the bottom, a colorful array of rectangles will appear as the string is being winded and tuned to its desired frequency. Both the sharp and flat frequencies will be shown on the screen as shown with their respective symbols for optional tuning if the user desires.

## Slide 33: Troubleshooting
Motor selection
Screen selection
Fast Fourier Transform library selection
Using LDO for 3.7V - 3.3V
Using ESP12E instead of integrating ESP8266 chip alone

## Slide 34: Component Design Change
Old Display (left) New Display (right)
Old Motor (left) New Motor (right)
Notes: Our first display choice was a 280 by 240-pixel ST7789 that unfortunately arrived broken. The old display also had problems communicating with the graphics library as its size was different than the new display we acquired. Another component that was changed was the motor for winding the pegs. We replaced the old stepper motor we got with a brushless DC motor due to the old motor not having the right amount of torque and power to wind the pegs efficiently.

## Slide 35: Component Design Change
Cost effective
Design efficiency and reliability
Able to access all GPIO Pins
Simpler to implement

## Slide 36: Component Design Change
Smaller Footprint
More Efficient (93%)
Variable to perfect accuracy
Could not get designed regulator to function properly

## Slide 37: Hardware integration
Compact hand-held design
Housing fits all required components
Regulator saved room with buck boost
(Not visible 2x 10mm piezo sensors epoxied to housing under PCB)

## Slide 38: Testing results
Requirement Specifications | Expected | Actual | Pass/Fail
Accuracy of sensor readings | Within ±4 cents | Within ±1.75 cents | Pass
Motor Torque | Turn Guitar Peg | Turned Guitar Peg | Pass
Battery Life | Tune 100 Strings | Tuned 100+ Strings | Pass
Time To Tune Guitar | < 3 minutes | < 1.5 minutes | Pass
Device Weight | < 2 lbs. | ~ 0.5 lbs. | Pass

## Slide 39: Data
Base String-Note | Min (Hz) | Max (Hz) | Max. Cent (~+3¢) | Min. Cent(~-3¢) | Average | Cent Range
6-E – 82.41Hz | 82.42 | 82.62 | 82.56 | 82.25 | 82.51 | 2.1
5-A – 110.00 Hz | 109.97 | 110.28 | 110.20 | 109.81 | 110.13 | 2.04
4-D – 146.83 Hz | 146.49 | 146.83 | 147.09 | 146.57 | 146.69 | 1.65
3-G – 196.00 Hz | 196.00 | 196.66 | 196.35 | 195.65 | 169.27 | 2.38
2-B – 246.94 Hz | 246.69 | 247.40 | 247.37 | 246.51 | 247.08 | 0.84
1-E – 329.63 Hz | 329.08 | 330.07 | 330.21 | 329.05 | 329.71 | 0.42

## Slide 40: Administrative Content

## Slide 41
Click to add text

## Slide 42: Budget: development costs
Components | Quantity | Costs
Snark ST 8 Clip-on Super-Tight Chromatic Tuner | 1 | $14
ADXL345 Digital Accelerometer | 1 | $17.50
Nema 16 Stepper Motor | 1 | $12
Nema 17 Stepper Motor | 1 | $15
3D print material 1kg | 1 | $20
Node MCU ESP8266 | 1 (3 pack) | $15
SN754410NE | 5 | $3
L298N Motor Driver | 1 (4 pack) | $10
Piezo Vibration Sensor | 1 | $4.95
Piezo Element | 4 | $1.50
28byj 5V DC Stepper Motor with Dirvers | 1 (5 pack) | $12
12V DC Brushless Stepper Motor | 1 | $20
Stepper Driver | 1 | $35
Jowoom | 1 | $34
Guitar Strings | 1 (3 pack) | $17
Electric Guitar Strings | 1 (3 pack) | $15
Lithium-ion Polymer battery | 1 | $12
Boost up Converter 2V-24V | 1 (10 pack) | $11
Adafruit 4410 Micro Lipo charger usb type C | 1 | $9
Rocker on /off switch | 1 (8pack) | $9
Tactile Momentary Push Buttons | 1 (25 pack) | $8
¼ Inch Output Jack | 1 | $5
Total Estimated Development Cost Range: | 29 | $316.45

## Slide 43: Task Management
GitHub
ClickUp
Google Drive
Notes: For task management, GitHub, ClickUp and GoogleDrive were used. GitHub was used mainly for a code repository and for version control of the project when developing for the different components. ClickUp was mainly used for creating tasks with their desired completion date as well as designating those tasks to the members of the group for accountability. ClickUp was essential as tasks could be created with subtasks that helped divide the project up into its needed components. Google Drive was used for document sharing throughout both the first semester with the 120-page report and this semester with any needed documents.

## Slide 44: Methods of Communication
Discord
Email
Phone Communication
Consistent Weekly Meetings
Notes: Discord was mainly used for constant communication, updates on deadlines, as well as updates on meeting times and locations. Consistent weekly meetings were also used for weekly check ups on upcoming project deadlines and tasks needed to be completed during that week. This helped keep the group on the same page and well prepared to tackle the tasks that needed to be completed during that week. Email was also used for any necessary document sharing or communication with professors.

## Slide 45: Thank you