## Slide 1: ACDC A Helping hand Group a
Akash Jinandra - EE/CPE
Carlos Cuesta - EE/CPE
Devin Defond - EE
Chang Ching Wu - EE

## Slide 2: Motivation
Tele-Robotic Arm
  That is control by an Exo-skeleton
Robots can go into hazardous conditions that humans cannot.
  Fires, Water, Space, Minefield
Use of robots overtime allows for automation
  Through human control robots can learn to do the job better

## Slide 3: Goals and Objectives
Mission is to change Hewlett Packard Inc. LaserJet printer cartridge
To develop a new control system to control HP’s in house robotic arm wireless via an exoskeleton
To fit exoskeleton with sensors that can effectively, accurately, and efficiently map user’s movements onto robotic arm

## Slide 4: Arm
The arm has capability for 5 DOF (project focus only on 4 DOF)
  Shoulder (rotation on the y-axis in relation to stand)
  Elbow (rotation on the parallel axis to the Shoulder)
  Forearm (rotation on the perpendicular axis to the rotation plane of Elbow)
  Wrist (rotation on the perpendicular axis to the rotation plane of Forearm)
Each degree of freedom is achieved through usage of 24V DC motor with reduction gear
The position of each degree of freedom is tracked through usage of integrated rotary encoder mounted on the corresponding motor

## Slide 5: Hand
The manipulator of the arm is a 3D printed hand individual movement capability for the fingers and thumb
Each finger is manipulated with a micro metal gear servo and metal braided wire
The thumb is manipulated with a standard servo and metal braided wire

## Slide 6: Specifications
Communications
Shall have an operating range of 2.4 – 2.5 GHz.
Shall have an operating distance of at least 30 meters.
Shall transmit data at 2 megabits per second.
Power
The exoskeleton shall not consume more than 15 watts of power.
The arm control system shall not consume more than 100 watts of power.
Exoskeleton Sensors
Shall have 5 potentiometer sensors, 1 per finger.
Shall have 1 encoder for the elbow and 1 for the shoulder.
Each potentiometer will rotate up to an angle of 180 degrees based on the finger input.
Each encoder will track 4000 lines per revolution
The Shoulder joint shall capture 90 degrees of rotation
The Elbow joint shall capture 150 degrees of rotation

## Slide 7: Overall Block Diagram

## Slide 8: Sensors

## Slide 9: Sensors – Elbow, Shoulder
AMT102 Encoder
Manufacturer | CUI INC
Power Supply | 3.6 – 5.5 V
Operating Current | 6mA
Dimensions | 43.88 x 28.77 x 9mm
Count | 4000 lines/rev
Price | $0.55 per
Purpose:
The use of these encoders is to get the most accurate information possible from the elbow and the shoulder.

## Slide 10: Sensors – Forearm
Gyroscope: MPU6050 Module
Manufacturer | InvenSense Inc
Power Supply | 2.375 – 3.46V
Operating Current | 3.6mA
Serial Interface | I2C
Dimensions | 4.0 x 4.0 x 0.9mm
Price | $4.75
Purpose:
The need for the gyroscope is to be able to record all movement on the forearm accurately.

## Slide 11: Sensors – Fingers
Uxcell Rotary Linear Taper Potentiometer
Manufacturer | Uxcell
Power Supply | 3 – 5 V
Operating Current | 40µA
Shaft Dimensions | 16 x 7.3mm
Knob Dimensions | 14 x 17mm
Price | $0.55 per
Purpose:
To record all movement in the user’s fingers.

## Slide 12: Processing

## Slide 13: Atmel Atmega16U2
Manufacturer | Atmel
Operating Voltage | 2.37 – 5.5V
Package | TQFP32
Dimensions | 9 x 9 x 1.2mm
Price | $4.35
Purpose:
USB-to-Serial programming chip

## Slide 14: Atmel Atmega328P
Manufacturer | Atmel
Operating Voltage | 1.8 – 5.5V
Package | TQFP32
Dimensions | 9 x 9 x 1.2mm
Price | $3.81
Purpose:
Main MCU and processing MCU for Rotary Encoder

## Slide 15: PCA9685
Manufacturer | NXP Semiconductors
Operating Voltage | 2.3 – 5.5V
Package | 28-TSSOP
Dimensions | 9.8 x 6.6 x 1.1mm
Price | $2.43
Purpose:
Generating PWM to control Servos in the manipulator module

## Slide 16: Processing PCB Exo Schematic

## Slide 17: Processing PCB Exo Schematic

## Slide 18: Processing PCB Exo Schematic

## Slide 19: Processing PCB Exo Schematic

## Slide 20: Processing PCB Arm Schematic

## Slide 21: Processing PCB Arm Schematic

## Slide 22: Processing PCB Arm Schematic

## Slide 23: Processing PCB Arm Schematic

## Slide 24: Processing PCB Arm Schematic

## Slide 25: Processing PCB Arm Schematic

## Slide 26: Processing PCB Arm Schematic

## Slide 27: Communications

## Slide 28: Communication Module
Bluetooth HC-05
Categories | Items | Values
Wireless Parameters | Bluetooth Version | V2.0
 | Frequency Range | 2.4-2.5 GHz
Hardware Parameters | Operating Voltage | 1.8 - 3.6V
 | Average Current | 25 mA
 | Package Size | 28 x 15 x 2.35mm
Security | Encryption | 128 bit
Purpose:
The need for the Bluetooth module is to allow for that data gathered from the exoskeleton to be transmitted wirelessly to the mechanical arm.
Manufacturer | HC Electronics
Price | $4.98

## Slide 29: Power

## Slide 30: Power Supply
Manufacturer | Meanwell
Operating Voltage | 24V
Output Current | <63A
Dimensions | 278 x 127 x 83.5mm
Price | Provided by HP
Purpose:
Used to power both the exoskeleton and arm control systems.

## Slide 31: Voltage Regulator – 5V Output
TPS 54302 (will be using two of them)
  Step down DC-DC switching converter
Manufacturer | Texas Instruments
Operating Voltage | 4.5-28V (24V nominal)
Output Current | 1A
Package | SOT-23 (6)
Dimensions | 1.60 x 2.9mm
Operating Efficiency | 93%
Price | $0.60 each
Purpose:
Used to regulate power from the main power supply to the MCUs, some sensors, and feed into the 3.3V regulators.

## Slide 32: 5V Voltage Regulator Schematic

## Slide 33: Voltage Regulator – 6V Output
TPS 54560
  Step down DC-DC switching converter
Manufacturer | Texas Instruments
Operating Voltage | 4.5-60V (24V nominal)
Output Current | 5A
Package | HSOP (8)
Dimensions | 4.89 x 3.9mm
Operating Efficiency | 88%
Price | $2.30 each
Purpose:
Used to regulate power from the main power supply to the servo controller and each of the manipulator’s finger servos.

## Slide 34: 6V Voltage Regulator Schematic

## Slide 35: Voltage Regulator – 3.3V Output
TPS 562208
  Step down DC-DC switching converter
Manufacturer | Texas Instruments
Operating Voltage | 4.5-17V (5V nominal)
Output Current | <0.5A
Package | SOT (6)
Dimensions | 1.60 x 2.90mm
Operating Efficiency | 90%
Price | $0.30 each
Purpose:
Used to regulate power from the 5V regulator to the Bluetooth modules.

## Slide 36: 3.3V Voltage Regulator Schematic

## Slide 37: Exoskeleton Software

## Slide 38: Arm Software

## Slide 39: Administrative Content

## Slide 40: Work Distribution
Name | Power | Communications | Software | Processing | Sensors
Akash Jinandra | - | - | P | S | S
Carlos Cuesta | - | P | S | - | P
Devin Defond | P | - | - | S | S
Chang Ching Wu | - | - | S | P | -

## Slide 41: Budget
Item | # | Approximate Price | Overall Price
Exoskeleton | 1 | $0 | $0
Mechanical Arm | 1 | $20,000 | $20,000
Robotic Hand | 1 | $200 | $200
Meanwell RSP 1500-24 | 1 | $255.90 | $255.90
Exoskeleton PCB | 1 | $20 | $20
Arm Controller PCB | 1 | $20 | $20
Exoskeleton Power PCB | 1 | $20 | $20
Arm Power PCB | 1 | $20 | $20
Atmega 328P | 8 | $3 | $24
Atmega 16U2 | 2 | $5 | $10
Item | # | Approximate Price | Overall Price
TPS54302 | 2 | $0.60 | $1.20
TPS54560 | 1 | $2.30 | $2.30
PUT 3.3V Regulator | 2 | $0.3 | $0.60
Bluetooth HC-05 | 2 | $4.98 | $9.96
MPU6050 | 1 | $4.75 | $4.75
Potentiometers | 5 | $0.55 | $2.75
Encoders | 2 | $33 | $66
Resistor Pack | 1 | $5 | $5
Capacitor Pack | 1 | $10 | $10
LED Pack | 1 | $5 | $5
Zip ties | 1 | $12.50 | $12.50
Wires Pack | 1 | $10 | $10
Total |  | 178.06** | $20,700
** - actual spending price of project.

## Slide 42: Finance
Received sponsorship from Hewlett Packard Inc.
  Robotic Arm
  Robotic Hand
  3D printed parts
  Financial Reimbursement
  Engineering Mentorship

## Slide 43: Progress
Chart: Progress Percentage
| Research | Design | Prototyping | Testing | Total
 | 0.9 | 0.33 | 0.75 | 0.2 | 0.3

## Slide 44: Issues
Construction of Exoskeleton and robotic arm
Mounting potentiometers and encoders on exoskeleton
Porting code from Python to C

## Slide 45: Questions?