## Slide 1: SEMS (Smart EV Monitoring System)
By: Nathan Rodriguez
Edwin Lomans
Symone Adams

## Slide 2: Motivation and Purpose
Low cost smart electric vehicle charger
Secure access for UCF students/faculty only
Power monitoring capabilities
Flexibility for Level 1 and Level 2 Charging

## Slide 3: Solution
Low cost smart electric vehicle charger
  Multi-annual updates can cost companies up to $600 per charging station software update, anything to lower installation and software cost is a bonus.
Secure access for UCF students/faculty only
  Currently anyone from the public can use charging stations in Garage A as well as other locations.
Power monitoring capabilities
  Energy can be monitored and broadcasted to parking services where university monitors the use of the EV stations.

## Slide 4: Solution
Flexibility for Level 1 and Level 2 Charging
  Typical Work day 9-5.
  UCF Research work day 8 A.M – who knows….
Case Example:
  Volkswagan eGolf (24 kW battery)
Charging (from garage)
  Level 1: 120V x 10A = 1.2 kWh
  Level 2: 240V x 16A (limitation) = 3.8 kWh
Battery Completely Discharged
  Level 1 = 20 Hours
  Level 2 = 6.32 Hours
Charging 12 kW only
  Level 1 = 10 Hours
  Level 2 = 3.16 Hours
Cost Savings
  Michigan Public Service Commission
    11 A.M – 7 P.M: 13.39 cents per kWh
    Otherwise: 4.283 cents per kWh
Notes: But this allows for one to charge during a long if you arrive late at home, gives you schedule flexibility and less depleting over time

## Slide 5: System Requirements
Operating Voltage: 120-240V
Center Frequency: 50-60 Hz
Output Current: 6-32A
Output Power:
  Level 1: <2.4 kW
  Level 2: <9.6 kW
Weight: 1.5kg/3.3lbs
System Temperature <155°C
Garage A Charging Stations

## Slide 6: J-1772

## Slide 7: Hardware Design
PCB/Prototype functionalities
  Input Power
  System Power Distribution
  Pilot Signal Generation
  Ground Fault Protection
  Current Sensing
  Relay Check
  LED status
  Arduino Programming
Design Methodology
  Schematic Design
  Simulation
    Power Dissipation
  Part Selection
  PCB Routing Techniques
  Gerber File Generation

## Slide 8: Full PCB System level
Transformer
220V to 30V AC
Grid
Full wave bridge rectifier
Level 2
Or Level 1
Transformer
120V to 20V AC
15.5V min
LT3502A
LT3502A
LT3580
5V to 3V
LT3502A
12V to 5V
12V to -12V
20-30V to 12V
Ground Fault Protection Circuit
5V
Pilot Generation Circuit
12V
-12V
-12V
Arduino
16MHz Oscillator
5V

## Slide 9: Power Distribution
15.5-35V
Input to 12V
12V to 5.5V
5V to 3V
-12V
LT3502A
12V to -12V
USB 5V
3V
12V input option
LT3502A
LT3502A
LT3580

## Slide 10: Regulator Information
LT3502A
Short-circuit protection
Integrated Soft-Start function
Internally Compensated
Current Mode control
10-Lead MS10 Package
Linear Technology (now part of Analog Devices)
LT3580
8-Lead MSOP Package
Adjustable switching frequency, Single feedback resistor, inverting converter
Integrated Soft-Start function
Wide-input voltage range (2.5-32)
Linear Technology (now part of Analog Devices)

## Slide 11: Regulator part selection
Inductors
  Inductance
    Higher values for lower frequency, lower values for high frequency
  DC current Rating
    Main spec related to heating due to resistance in coils
  Saturation Current Rating
    If this is exceeding the inductance value can drop to 0 and it behaves like a wire
  DCR
    Indicator of power loss
  Core Loss
    Loss due to magnetic switching
  Saturation Profile
    Core dependent
Capacitors
  Value
    Controls output ripple
    Load supporter
  DC Voltage Rating
    Not choosing aluminum or electrolytic
  DC Bias
    Consideration in ceramics, determines how much “effective capacitance” will drop.
  ESR
    Limits voltage in transitions
    Limits RMS current
  ESL
    Limiting factor in transient response
  RMS Current Rating
  Dielectric Material
  Lifetime
Notes: Switch mode power supplies rely on “Steady-State” Inductor principle. DC current rating is how much current can inductor handle at steady-state? The saturation current is the amount of current when the inductance value drops 30% of its value. Core loss is energy lost due to changing magnetic energy in the core during switching cycle and eddy currents, which are induced in the core material by a time varying flux…During off time the control switch, the capacitor holds up the output voltage as the energy of the inductor decreases, thefore the amount of power supply ripple is directly related to the amount of output capacitace, when the load current or power supply suddenly changes from light load to heavy load, the capacitor must support the extra current while the current ramps up in the inductor. Like when your lights dim briefly when you turn on washer or dryer., ESL tells you how fast current can change in the capacitor, limiting in transient response, ESR determines voltage dip during transition

## Slide 12: LT SPICE simulation

## Slide 13: LT SPICE simulation Results

## Slide 14: Power Distribution Schematic

## Slide 15: 24V to 12V

## Slide 16: 12V to 5V

## Slide 17: 5V to 3V

## Slide 18: 12V to -12V

## Slide 19: Pilot Signal Generation
Notes: Make sure to mention that Arduino cannot read negative voltages so that a 5V pull up is necessary so that way at -12V one would read 4.5V

## Slide 20: Ground Fault Protection
Notes: Mention the feedback path

## Slide 21: Current Sensing
CR8450-1k-T7QC
From CR Magnetics
Level 1: 10A goes to 312mV
Level 2: 16A goes to 500mV

## Slide 22: Relay check
Explanation and picture
Explain that one time
  Diode shorted out, plans to
  Isolated this circuit with
  Electrical tape
Other components are
  Not drawing current when
  Isolated.
  This concept is important in system integration
Creating Unstable Ground in prototype when enabled and disabled.
Notes: Show a picture of it pulling current and mentioned how you eliminated the diode and still a short was detected. ESD sensitive objects

## Slide 23: LED Status
Notifies of Arduino is being programmed.
Gives off different colors for different modes of operation
Standard RGB LED from sparkfun

## Slide 24: Arduino Programming
Jumpers
Limits to 1 oscillator
Arduino off-programmer jumpers (USB to SPI)
Notes: Make notes about how Arduino has one oscillator as opposed to two like most normal programming systems such as the CC3100, CC3200 or MSP430

## Slide 25: Routing
Separate power and digital areas
For data signals keep traces orthogonal.
Support max current rating to determine trace width
  For 1A 10 mils is sufficient

## Slide 26: Design Costs
Fast PCB ordering
  $729.05
PCB and prototype part acquisition
  $250.67
J1772 Cable
  $149
Total: $1,128.72

## Slide 27: System Diagram
Power Supply
220V AC at 60 Hz
Wi-Fi Board (WFB)
Electric Vehicle
Inlet + Charger + Battery
Charging Station
Power Processing Board (PPB)
System Power Generation Board (SPGB)
Keypad
Android Phone Application
Magnetic Card Reader
Online Database

## Slide 28: Previous Design Summary
Excessive Coding requirements
    2 MSP430F5529’s
    CC3100 Wi-Fi MCU
    Application Software
    Data base
Hardware requirements
  4 PCB Designs layouts
  1 RF 4-layer board to support Wi-Fi capabilities

## Slide 29: New Design
Configure for single MCU implementation
  Eases coding
  Saves Space
Hardware reductions
  2 prototype boards
  1 PCB
Adjusts to late customer change
  October 11

## Slide 30: Bluetooth Module

## Slide 31
A popular IDE for developing applications on Android devices.
Features include:
  Debugging
  Android Phone Emulator
  Connectivity with real devices through USB
  XML files for layout design
  Useful APIs (Application Programming Interfaces)
Programming language is Java.
Because of its wide use, there are many resources available.

## Slide 32
Main Features of Application
Sign page that is accessible for only UCF students/faculty.
Database to store NID and password information.
Second screen that displays the state of charge.
Connection using Bluetooth to Wireless Module.

## Slide 33
Sign-in Page
Simple NID and password sign in familiar to all UCF students/faculty.
On button click, code will compare input to database and respond according to that input.

## Slide 34
Database
For prototyping purposes, a database was created in Android Studio.
NID is set as a unique constraint; new entries are entered based on this. No one with the same NID can be in place.
SQLite Open Helper: A helper class that connects to the Firefox plugin, SQLite Manager.

## Slide 35
Second Screen
When NID and password are correct
On the connect button click, phone will connect to wireless MCU server to receive information.
Information is displayed as percentage on progress bar.

## Slide 36: Bluetooth Set-up
Verification of Bluetooth
Search for Devices
Connection as Client
Broadcast Receiver

## Slide 37: Verification Code
The API Bluetooth_Adapter is called to ensure the device can support Bluetooth.
If Bluetooth is supported but not enabled, an intent is called to switch it on.
If already enabled and supported code will continue.

## Slide 38: Searching for Devices
Device will connect to Bluetooth module first as a paired device.
The code list the module’s name and address. This verifies that the discovery of new devices is working.

## Slide 39: Connections
The APIs BluetoothDevice and BluetoothSocket are used to first make connections with the module. The device creates a socket and connects to the device through the UUID (Universally unique identifier).
The call connect() is called to connect through the socket.
The initial connection happens in a separate thread from the main class.

## Slide 40: Connections Code

## Slide 41: Connections
The next step in connection is receive data from the HC-05 module.
Once a connection is established, the socket passes information to the InputStream where it’s read an transmitted to the User Interface of the application.

## Slide 42: Broadcast Receiver
Broadcast Receiver are used for any wireless connectivity.
Intents or operations to be performed are called in the Broadcast Receiver once certain functions in the code are implemented.
For this code, once connection has been established with the device, an intent is called to send a message that Bluetooth is connected.

## Slide 43: Broadcast Receiver Code

## Slide 44: Obstacles
Displaying data
Connection works with Arduino sending serial data.
Code sets up a Handler to deal with user interface activities. Data not displaying.
Narrowed down to: Incorrect Handler code or error in InputStream.