## Slide 1: FAUX FIND ALL USERS ‘X’
GROUP 2: AMISH KANJI (CPE)
JOEL GARDYASZ (CPE)
JOSH RADICCHI (EE)

## Slide 2: PROJECT PROBLEM AND MOTIVATION
People misplace items of value all the time
They also leave behind their laptops on their way to work
We want to create a product that prevents these things from happening as well as a means to locate the lost item
There are other similar products on the market right now
  We want to learn from these implementations and make ours better

## Slide 3: GOALS AND OBJECTIVES
To make it so that people don’t “freak out” when they misplace or leave something behind
  They will know that they can track it using FAUX
To create a device that is easy to use
To create a mobile application that enables the user to locate their device and the belonging that it was attached to

## Slide 4: REQUIREMENTS AND SPECIFICATIONS
The location of the object shall be found by using a smartphone or tablet.
The tracking device shall be of portable size and weight.
The tracker shall be water resilient, and be able to withstand fall damage.
Your smartphone shall respond to the tracker if need be.
The tracker shall produce sounds and light up when prompted.
The tracker shall work well up to 40 feet.
The tracker shall notify the user if the item being tracked gets too far away from the user.
The tracker shall be able to survive for 6 months without a battery change.

## Slide 5: PROJECT SUMMARY
Wireless tracking device
Paired with mobile application
Project will have multiple features
  Takes into account all possible human senses
Will help users retrieve lost/stolen items
Will also help reduce the chance an item is lost in the first place

## Slide 6: WORK DISTRIBUTION
Amish – Red
Josh – Green
Joel – Blue

## Slide 7: WIRELESS COMMUNICATION
Bluetooth (BLE & iBeacon)
  Advantages: Low Battery Consumption, cheap, low latency, integration, range
  Disadvantages: Data Rate, strength of signal, receiver battery life, receiver
Wi-Fi
  Advantages: Cheap, high data rate, integration, range
  Disadvantages: Security, battery consumption, strength of signal
GPS
  Advantages: Cheap, integration, range
  Disadvantages: Battery consumption, indoor capability, inaccuracy

## Slide 8: IBEACON
What is iBeacon?
  Protocol developed by Apple, referred to as beacons
  Broadcast identifier to nearby devices which causes some action
  Uses Bluetooth Low Energy
Why iBeacon?
  Most other product don’t uses this technology
  Always broadcasting
  No syncing requirement

## Slide 9: ESTIMOTE
Top companies for beacons
  Other companies considered: BlueSense, BlueCats, Kontakt
What are Estimote Beacons?
  Small wireless sensors
  Broadcast radio signals
  Devices interpret unlocking micro-location and contextual awareness
Why Estimote?
  Estimote SDK
  Requirements
  Tutorials/community

## Slide 10: ESTIMOTE BEACONS VS ESTIMOTE STICKERS

## Slide 11: ESTIMOTE STICKER
Why Estimote Sticker Beacons?
  Size (3 mm thin)
  Easier to stick to everyday objects
How are Stickers different?
  Packets
  More information
    iBeacon/Nearables
  Examples: ID, motion, power, voltage, temperature
Manufacturer | Estimote
Product | Sticker Beacons
Price | $99
Quantity | 10

## Slide 12: Estimote SDK
Instructions
  Access information
Integratable
  Multiple environments
Communicated with cloud
  Identifier

## Slide 13: BLUETOOTH LOW ENERGY (BLE)
Advantages
Has a range of up to 50 feet away.
Has reduced energy consumption.
Very cost effective.
Stays on in the background.
Disadvantages
The signal strength is not always the strongest.
Does not have a high bandwidth.

## Slide 14: PUNCH THROUGH
Small hardware company
Creator of the Light Blue Bean
Uses Arduino to program the Bean wirelessly
Uses BLE to wirelessly communicate
Why Punch Through?
Has a Bluetooth module that you
can program wirelessly.
They sell some of the parts that we
need to create the PCB.

## Slide 15: CHOSEN BLE MODULE
LBM313
Key Features:
2.4Ghz Bluetooth low energy
Data rates from 250kbps to 1Mbps
Operating voltage of 2.0V - 3.6V
8051 microcontroller with 256kB of in
system programmable flash and 8kB of
RAM
Manufacturer | Punch Through
Product | LBM313
Price | $10
Quantity | 1

## Slide 16: PCB LAYOUT OF BLE MODEL

## Slide 17: CHOSEN MICROCONTROLLER
ATMEGA328
Low-power CMOS 8-bit
microcontroller.
Based on the AVR enhanced RISC
architecture.
Allows the system designer to
optimize power consumption
Manufacturer | Atmel
Product | ATMEGA 328
Price | $4.95
Quantity | 1

## Slide 18: PCB LAYOUT OF MICROCONTROLLER

## Slide 19: WIRING OF OUR PCB

## Slide 20: OUR PCB
Our PCB is made up of:
  A Bluetooth module
  A microcontroller
  A LED
  A buzzer
  Resistors
  Capacitors
  N-MOS
  Other smaller components
Manufacturer | OSH Park
Product | Printed circuit boards
Price | $7.75
Quantity | 3

## Slide 21: LED
We will be using a RGB LED
Used to find item in the dark
You can choose different colors
Each color has a different
operating voltage.

## Slide 22: CHOSEN SPEAKER
The speaker’s purpose is to aid the user in locating the device if they are nearby
  It adds an auditory component for tracking
We could not use a standard magnetic driven speaker
  This would require the addition of an amp which is too big for our design
Manufacturer | Multicomp
Product | Piezo buzzer
Price | $3
Quantity | 1

## Slide 23: CHOSEN SPEAKER
Therefore we decided to go with a piezoelectric speaker
The piezo does not need a magnet to produce sound
  Creates sound by passing electric charge through a crystal
  Uses a lot less energy
  More resistant to breaking
Manufacturer | Multicomp
Product | Piezo buzzer
Price | $3
Quantity | 1

## Slide 24: CHOSEN BATTERY
CR2032 (coin cell battery)
Lithium battery
3V
Commonly used in electric devices
Reasoning
  Meets voltage requirements of our project
  Size
Manufacturer | Energizer
Product | CR2032
Price | $3.49
Quantity | 1

## Slide 25: PCB SCHEMATIC

## Slide 26: PCB SOFTWARE
Arduino IDE
  Used to upload sketches MCU
  Microcontroller will then use the sketch to communicate with the other components
Had to be able to communicate with the application as well
  Application sends instructions to the BLE module
    BLE module sends instructions to the MCU
      MCU uses the sketch uploaded via Arduino to fulfill the instructions

## Slide 27: PUT IT TOGETHER

## Slide 28: HIGH LEVEL ARCHITECTURE DESIGN

## Slide 29: MOBILE APPLICATION – ANDROID VS IOS
Practicality
  Testing/Debugging
Compatibility
  Estimote
Written in Swift or objective-C, less code than Java
Online guide and API reference
>

## Slide 30: MOBILE APPLICATION – DEVELOPMENT ENVIRONMENT
Xcode
  IDE dedicated for application design
  Programmed using Swift
  Software Integration
  Included multiple software tools for creation of UI
    Creation from scratch
CocoaPods
  Dependency manager
  Allows for third party libraries to be kept up to date
  Integration simplicity

## Slide 31: MOBILE APPLICATION - USER INTERFACE
Labels
  Zone
Legend
  Description/Instructions
Buttons
  Reconnect
  Components

## Slide 32: MOBILE APPLICATION - NOTIFICATIONS
Reminders
Alerts

## Slide 33: MOBILE APPLICATION - NOTIFICATIONS

## Slide 34: MOBILE APPLICATION – PRIMARY FUNCTION
Tracking
Ranging/Monitoring
Hotter/Colder
User friendly messages/guidance added

## Slide 35: MOBILE APPLICATION – PRIMARY FUNCTION

## Slide 36: MOBILE APPLICATION – SECONDARY FUNCTIONS

## Slide 37: SOFTWARE – SUCCESS AND DIFFICULTIES
Difficulties
Testing
  Obstacles
    Environment
    Distance
Ranging/Monitoring
Signal dependent
Success
Acceptance testing
User friendly mobile application
  Negligible learning curve
Features can be successfully completed
No issues occur when in correct range
End goal is achieved without any errors

## Slide 38: HARDWARE – SUCCESS AND DIFFICULTIES
Difficulties
Making the PCB as small as it possibly could be
Printing and populating the board
  OSH Park
  QMS
Success
Being able to make a backup
Testing
  Light up
  Make sound

## Slide 39: PROTECTIVE CASE
3D printed using ABS plastic
Water resistant
Durable
Customizable

## Slide 40: BUDGET AND FINANCING
Part | Cost Per Unit | Quantity | Total Cost
iOS Device | Already Owned | 1 | $0.00
LightBlue Bean | $30.00 | 1 | $30.00
Casing (3D printed) | $0.00 | 1 | $0.00
Speaker | $3.00 | 1 | $3.00
Estimote Sticker Beacons | $100.00 | 10 | $100.00
LBM 313 | $10.00 | 1 | $10.00
ATMEGA328 | $5.00 | 1 | $5.00
Misc. Parts | $50.00 | NA | $50.00
PCB | $2.58 | 33 | $7.75
Total Cost |  |  | $205.75
Most of the materials for the project were either already owned by someone in the group or were relatively inexpensive
Therefore, the entire project was funded by the members of the group

## Slide 41: QUESTIONS?