## Slide 1: Auto-Logger Sponsored by Florida Solar Energy Center
Group #13
Hassan Siddiqui (EE)
Zachary Ross (EE)
Justin Wright (EE)

## Slide 2: Real Time Clock DS1307
DS1307 was chosen as the RTC because of compatibility with ATmega2560
DS1307 runs in LPM while the car is off
Helps keep track of time parked and time stamps data logs

## Slide 3: SparkFun Serial Enabled 16x2 LCD
Runs on 3.3V compatible with ATmega2560
Can use 9600 baud rate
Uses 3 wires serial to connect to ATmega2560
Used to show data collected from OBD-II and successful data transfer
Only used for Senior Design because FSEC does not want interaction between the device and user.

## Slide 4: Project Overview
Vehicle interface for characteristics transportation data capture
  Engine load and fuel combustion rates
  Time spent and location on campus
  Battery health and charge capacity
Compatible with both Internal Combustion Engine and Electric Vehicles
Wireless Communication with database
Minimal User Interface required
  Autonomous functionality

## Slide 5: Project Goals
Low Power design
Minimal/Non-invasive package
Robust vehicle compatibility
High reliability
Resistant to temperature fluctuations
Autonomous data logging and transmission

## Slide 6: Project Specifications
Powered by 12V Lead-Acid car battery
Compatible with various vehicle makes and models
  Internal Combustion Engines (ICEs) produced after 1996
  Electric Nissan LEAF provided by FSEC
10cm x 10cm x 20cm Package Dimensions
Resistant to 50°C/hr temperature fluctuations
Per-Second data point resolution

## Slide 7: Block Diagram of System

## Slide 8: MCU Comparison
ATmega2560
Digital I/O Ports: 54
Clock Speed: 16MHz
Analog Ports: 16
Operating Current: 50mA
Flash Memory: 248KB
ATmega328P
Digital I/O Ports: 14
Clock Speed: 16MHz
Analog Ports: 6
Operating Current: 50mA
Flash Memory: 31.5KB

## Slide 9: Wi-Fi Comparison
CC3100 MOD
RX Sensitivity: -94dBm
Rx Operating Current: 53mA
UART Transmission Limit: 3 Mbps
Package Size: 20.5mm x 17.5mm
ESP-12E
RX Sensitivity: -98dBm
Rx Operating Current: 50mA
UART Transmission Limit: 4.5 Mbps
Package Size: 24mm x 16mm

## Slide 10: ESP-12E Additional Functionality
Provides various Low Power operating modes
Additional GPIO pins for custom firmware applications
Fast sleep/wake context switching
Light-Sleep Mode:
  Less than 1mA operating current
  300mS wake time

## Slide 11: GPS Comparison
Copernicus II
Tracking Sensitivity: -160dBm
Location Accuracy: ±7.6m
Power Consumption: 132mW
Update Rate: 1Hz
  Operating Temperature: -40 °C to 85 °C
Dimensions: 19mm x 19mm
FGPMMOPA6B
Tracking Sensitivity: -165dBm
Location Accuracy: ±3m
Power Consumption: 138.6mW
Update Rate: 10Hz
  Operating Temperature: -40 °C to 85 °C
Dimensions: 16mm x 16mm

## Slide 12: Device Schematic

## Slide 13: PCB Design

## Slide 14: OBD-II Interface Capabilities
Internal Combustion Engine
Electric Engine

## Slide 15: OBD-II to UART Conversion Overview
Our device is compatible with most OBD-II protocols
  CAN, KWP2000, ISO 9141-2, VPW, PWM, and raw CAN
Two ICs were needed to communicate

## Slide 16: OBD-II to UART Conversion Overview
Two chips were utilized to communicate with different

## Slide 17: Operating Modes
Standby – Vehicle Parked
  Entire device in Low Power
  MCU awakens periodically to check vehicle engine status
Wake Up – Engine Started
  Vehicle localization
  Location dependent startup log
    Logs parking duration, date, time and location if identified as on campus

## Slide 18: Operating Modes
Localization/Acquisition – Vehicle Operational
  MCU identifies vehicle location
  Collects or ignores data depending on current location
    For privacy reasons, the Auto Logger will not continuously log transportation data
Transmission – Vehicle Parked on UCF Campus
  GPS module in Low Power
  Attempt to establish reliable Wi-Fi connection with database
  If successful, transmit newly collected data

## Slide 19: Data Storage and Reliability
Data logs will be stored on the micro SD card in a cyclical manner
  For reliability reasons, the entire volume of the memory will be utilized before any logs are over-written or deleted
Logs will be populated with pertinent data gathered by the device
Logs will be formatted using the following nomenclature
  “YYMMDD.hhmmss” denoting Year, Month and Day followed by the hour, minute and second the log was captured
  Military time will be used to prevent confusion between AM and PM readings
Logs are stored as text files for simplicity

## Slide 20: Example Mobile Data Log File name: 160607.093016.txt
Internal Combustion Engine
Vehicle Make/Model
Engine Load
Vehicle Speed
Vehicle Location
Fuel Level
Fuel Economy/Consumption
Electric
Vehicle Make/Model
Battery Health
Battery State of Charge
Vehicle cabin temperature
Atmospheric temperature
“Fuel” economy

## Slide 21: Example Static Data Log File Name:
Date
Time
Location
Parking Duration

## Slide 22: Power Evaluation
Lead-Acid batteries not designed to support charge depletion
  Charge capacity cannot drop below 80% otherwise the battery would be irreversibly damaged
  Utilize Peukert's Formula for Battery Discharge Time to estimate battery life using the worst case value of Peukert’s number (n=1.3)
Component | Peak Current Draw(mA) | Low Power Current Draw (mA)
MCU | 200 | .015
Wi-Fi Module | 170 | .05
GPS Module | 75 | .015
MicroSD | 80 | .015
LCD | 50 | .015
Total | 575 | .56
Equation 1 - Lead Acid Battery Discharge Time with Peak Load
Equation 2 - Lead Acid Battery Discharge Time with LPM Load

## Slide 23: Interpreting NMEA Sentences
Ex: $GPRMC,064951.000,A,2307.1256,N,12016.4438,E,0.03,165.48,260406,3.05,W,A*55
  Desired values are Latitude and Longitude (DDmm.ssss) and Current Speed (knots)
  Standard NMEA output sentences provide significantly more information than needed
Open Source libraries available for parsing of information for easy accessibility

## Slide 24: GPS Module Configuration
GPS's are very sensitive to noise, so LDO regulators have been implemented to reduce noise
Module will maintain a minimum refresh rate of 1Hz so that most accurate data is available upon request by the MCU
MCU will determine if the vehicle is within the footprint of the UCF main campus. Footprint defined as:
  28°36'41.3”N, 81°12'24.8''W to 28°35'33.8''N, 81°11'17.4''W
NMEA supplies current speed in knots
  1 Knot = 1.15078 MPH

## Slide 25: GPS Module Initiation and Boundary Region

## Slide 26: Communications Overview

## Slide 27: Signal Acquisition
Once the MCU identifies the vehicle as parked on campus, Wi-Fi signal acquisition will be initiated
  Timeouts will be implemented to terminate the process if a connection cannot be established
Network stability will be determined through the evaluation of the received signal strength indicator (RSSI)
  A signal stronger than -80dBm is sufficient for reliable file transfer

## Slide 28: Serial AT Commands
The MCU will communicate with the ESP-12E via AT commands sent through a serial UART interface
  Set power mode
  Establish connection
  Manage file transfer
  Configure network characteristics

## Slide 29: Useful Commands
AT+CWJAP=ssid, pwd Establish Connection
AT+CWLAP=ssid, mac, ch Returns RSSI of Network
  Return string: +CWLAP:(3,"UCF_WPA2",-53,"20:cf:30:ce:60:fe",11)
AT+CIPSTART=type, addr, port Start TCP connection as client
AT+CIPSEND Send data
  Successful transmission reciprocated w/ confirmation packet containing “+++”
AT+CIPSTO=time Set server timeout

## Slide 30: Work Distribution
Member | Wireless Communications | Vehicle Interface | Data Management | Software | PCB Design
Hassan Siddiqui |  | Main |  |  | Secondary
Justin Wright |  |  | Main | Secondary | 
Zachary Ross | Main |  |  | Secondary | Secondary

## Slide 31: Issues and Concerns
Wi-Fi propagation range
Efficiency of Patch on Top GPS antenna
Proprietary Vehicle Interfacing

## Slide 32: Current Progress
Chart: 
| Total | Testing | Software Development | Hardware Development | Research
Progress Made | 56 | 45 | 55 | 40 | 90

## Slide 33: Budget

## Slide 34: Questions?