## Slide 1: Smart Crib
GROUP 7
ELECTRICAL ENGINEERING
David Brunat
Thinh Nguyen
COMPUTER ENGINEERING
Phuoc Nguyen
COMPUTER SCIENCE
Brian Nguyen

## Slide 2: Motivations
Sadie Kay was Born December 26, 2017
Alleviate the stresses of raising young children.
  Is the child breathing? Are they gaining weight? Is the child awake?
  Postpartum depression.
SIDS prevention.
The Smart Crib system will replace baby monitors, nanny cams, weight scales, and pulse monitoring devices.
AP9101CK6-CQTRG1 | 0ZCJ0035AF2E

## Slide 3: Goals
Monitor the temperature of the environment the child is in.
Notify parents when child is crying or in distress.
Transmit data wirelessly to a mobile application.
Measure Biometrics of a child.
  Weight tracking
  Pulse
Display biometric data on a mobile application.

## Slide 4: Specifications
Component | Specification | Design
Sound Sensor | Accuracy and speed | Detects the baby crying within 5 seconds and alert the MCU
Weight Sensor | Accuracy | Average the weight of the baby over 4 weight sensors within +/- 1% accuracy
Temperature Sensor | Accuracy | Reads the ambient temperature of the crib within 0.8 C degrees accuracy
Motion Sensor | Accuracy and Speed | Detects the constant movement of the baby within 2 seconds
Pulse Sensor | Accuracy | Takes pulse readings every 5 seconds
Battery | Battery life | 6 hour lifespan
WiFi Module | Range | 20 meters

## Slide 5: Overview

## Slide 6: Block Diagram
12V AC TO DC
-12V
Regulator
Main MCU
5V Regulator
3.3V
Regulator
Wearable
MCU
Weight Sensor
Sound
Sensor
Temp
Sensor
Motion Sensor
Pulse Sensor
WiFi
Module
Battery Charger
Battery
Battery
Regulator
Cloud Storage
Mobile Application
Camera

## Slide 7: Microcontroller Unit
 | EK-TM4C123GXL | MSP430G2553
Flash(KB) | 256 | 16
RAM (KB) | 32 | 0.5
ADC Channels | 2 | 2
ADC Resolution(Bits) | 12 | 10
GPIO | 40 | 24
I2C | 4 | 1
SPI | 6 | 2
UART | 8 | 1
Speed(Mhz) | 80 | 16
Hibernation module | Yes | yes
Cost | $10.64 | $2.43
TM4C123GH6PM (32-bit ARM® Cortex®-M4F)
Accelerometer

## Slide 8: Motion sensor
PIR
Accelerometer

## Slide 9: Motion sensor: PIR
Detect the amount of IR

## Slide 10: Motion sensor: Accelerometer
When an acceleration is detected in either axis
Specification | MPU6050
Cost | $6.99
Power Consumption | 1.4mA
Angle Sensor | 180 degrees
Operating voltage range | 2.375V-3.46V

## Slide 11: Temperature sensor
Measure ambient temperature
Features | MS5611_01BA03
Cost | $12.48
ADC | 24-bit
Power consumption | 1.0uA
Interface | I2C & SPI
Accuracy | ±0.8C
Supply voltage | 1.8V to 3.6V
Operating Temperature | -40c to +85c

## Slide 12: Weight sensor
Keep track of the baby weight over the 2st year of age.
4 x Load Cell

## Slide 13: Instrumentation Amplifier
INA125 SPECIFICATION | 
FEATURES | 
LOW QUIESCENT CURRENT | 460mA
PRECISION VOLTAGE REFERENCE | 1.24V, 2.5V, 5V or 10V
SLEEP MODE | Yes
LOW OFFSET VOLTAGE | 250mV max
LOW OFFSET DRIFT: | 2mV/°C max
LOW INPUT BIAS CURRENT: | 20nA max
HIGH CMR: | 100dB min
LOW NOISE | 38nV/ÖHz at f = 1kHz
INPUT PROTECTION | ±40V
WIDE SUPPLY RANGE | Single Supply: 2.7V to 36V Dual Supply: ±1.35V to ±18V
Gain | 4 to 10000 (v/v)
1x Instrumentation Amplifier

## Slide 14: Pulse sensor
Measure Baby Heart-rate
  PulseSensor(NOT From PulseSensor.com)
Features | PulseSensor
Cost | $2.04
PCB’s size | small
Accuracy | 12-bit
Data Communication | ADC
Operation Temp | -40C to +85C
Operation Voltage | 3.3V to 5.0V
User Friendly | Yes

## Slide 15: Pulsesensor Flow Diagram

## Slide 16: Wifi Module
Transfer sensor’s data to the Database
  ESP8266 Wifi Module
Specifications | ESP8266
SPI/I2C/I2S/UART | 2/1/2/2
Working Temperature | -40C ~ 125C
Operating Current | 80mA

## Slide 17: ESP8266 Data Flow Diagram

## Slide 18: Sound SENSOR
 | High Sensitivity Microphone Sensor | PZM11 LL WR
Input Voltage | 5 V | 12V to 24V
Output Voltage | 0.6 V | 1.25 V
Price | $0.57 | $179
Two different sound sensors were tested for performance.
The High Sensitivity Microphones low level output made amplifying the signal difficult.
The PZM11 LL WR had much higher output signal, which made amplifying and filtering better.
The PZM11 LL WR was also donated.

## Slide 19: Cry Detection system
MCU
Sound Sensor
Mobile Application
Motion Sensor
Notification to User
Live Camera
Feed

## Slide 20: Cry Detection hARDWARE

## Slide 21: Cry Detection hARDWARE
555 timer in Monostable mode

## Slide 22: Cry Detection hARDWARE
Sound Sensor Input and Amplification of signal by Gain of 8

## Slide 23: Cry Detection hARDWARE
3rd Order Bandpass Filter, set to the cry frequency range of a child

## Slide 24: Cry Detection hARDWARE
AC signal that passes through the filter turns on the switch, allowing the trigger to discharge.
Switch
Trigger

## Slide 25: Mobile Application
Live look-up
Data logging
Intuitive ( in computer terms easy to use and understand)

## Slide 26: Live Look-up

## Slide 27: Database
 | Relational Database (SQL) | Non-Relational Database (NoSQL)
Data Format | Highly Structured | Highly Unstructured
Data Volatility | Rigid | Versatile
Data Size | Costly | Cheap
For this project we have chosen NoSQL database.
Interval of 5 seconds is 6 million entries per sensor.
{
TableName: “Temperature”
Item: {
“id”: “100”,
“value”: “72”,
“timestamp” : “6/8/2018”,
“flag” : “1”,
}
}

## Slide 28: User Interface
Tap – live look-up.
Hold to view more detailed page.
Tap to view baby.

## Slide 29: Main Schematic
Power
Headers
Peripherals
MCU

## Slide 30: MAIN PCB LAYOUT

## Slide 31: Wearable Pcb overview
USB B
Battery
Charger
Battery
Fuse
PMIC
Voltage
Regulator
MCU
JTAG
MCU
Header
JTAG
WiFi
Header
UART
Debug
Header
Pulse Sensor
Header
Motion
Sensor
WiFi
Module
Power
Headers
Peripherals
MCU

## Slide 32: Wearable pcb Schematic
Power
Headers
Peripherals
MCU

## Slide 33: Wearable PCB LAYOUT

## Slide 34: Rechargeable BATTERY System
 | Battery | Battery Charger | Power Management IC | Fuse
Part Number | RJD3555HPPV30M | STBC08PMR | AP9101CK6-CQTRG1 | 0ZCJ0035AF2E
High Voltage | 4.28 V | 4.2 V | 4.2 V | 
Low Voltage | 2.35V |  | 2.8V | 
Current Capacity | 500 mAh |  |  | 
Charge Current | 250 mA | Programmable By Resistor |  | 
Maximum Current | 1 A |  |  | 750 mA
Li-Ion Coin Size Battery was selected
Battery Charger uses Constant Voltage and Constant Current.
Power Management IC has Overvoltage and Undervoltage Protection.
Fuse has implemented for discharge and short circuit protection.

## Slide 35: Wearable power distribution
Made to work with Li-ion batteries whose input voltages will fluctuate.
Provides an output voltage of 3.3V regardless of voltage from the battery.
Configured to operate as both a step up and step down DC converter.
MAX1701EE+ | 
Input Voltage | 2.7V to 5.5V
Output Voltage | 3.3 V
Output Current | 800 mA
Efficiency | Varies as Input Voltage changes
Price | $7.80

## Slide 36: Work Distribution
 | Wearable PCB | Main PCB | Firmware | Software
David | Primary | Secondary |  | 
Thinh | Secondary | Primary |  | 
Brian |  |  | Secondary | Primary
Phuoc |  |  | Primary | Secondary

## Slide 37: Budget and Financing
Self-funded project. Our group has decided to contribute $100 each for a total of $400 for this Senior Design Project.

## Slide 38: Smart crib progress

## Slide 39: Issues
Redesign of the battery charging system to work with one battery instead of two.
Have not solidified the process to implement the camera.
WiFi IC, we had initially designed the traces and spent a lot of time trying to match the impedance and are now using a module instead.
Designing a waterproof housing for the wearable PCB.

## Slide 40: Disclaimer
*Currently, no babies were harmed in the testing of this project.

## Slide 41: Questions