## Slide 1: Ion Interactive Robot Assistant
Group 11
Dennis Gebken, CpE
David Jaffie, CpE
Mohammad Rizeq, EE

## Slide 2: Motivation
Combat boredom at the desk
Helping to counter this can boost productivity
  Can help toddlers learn
  Grade-school students study
  Business professionals in the workplace
Source: Management Education Group
Objective
Produce an all-in-one robotic assistant
  Natural movement and conversation
  Small, lightweight for portability
  Wirelessly utilize the internet to carry out tasks
Meet Peeqo! Made by Abhishek Singh

## Slide 3: Requirements & Specifications
Property | Design Specification
Weight | < 5lb
Size | < 7”x7”x15”
Voice Command Response Time | < 2 seconds
Voice Recognition | 80% of what is spoken
Supported Language | English
Face Recognition | 80% of faces recognized under normal lighting
Power Consumption | < 50W
Cost | < $500

## Slide 4: Overall Block Diagram & Tasking
Task | Primary | Secondary
Controller | Dennis | David
Camera & CV | Dennis | David
GUI | David | Dennis
Voice Recognition | David | Dennis
Body Design | David | Dennis
MCU & Servos | Dennis | Mohammad
Power Module & Battery | Mohammad | Dennis
Soundcard, Speakers, & Microphone | Mohammad | Dennis
PCB | Mohammad | Dennis

## Slide 5: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 6: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 7: Body Design
3D-printed skeleton to house components
  Designed using Autodesk Fusion 360, a 3D CAD program
  ABS filament
    Strong, heat-tolerant
    Commonly-used for prototyping
Flexible cloth or spandex body to allow for easy, fluid movement

## Slide 8: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 9: Display
Important factors:
  Cost
  Touch capability - GUI
  Size & Resolution – GUI & multimedia
  Built-in adaptor board
Source: Adafruit

## Slide 10: Pi Foundation Display
Size: 7”
Resolution: 800x480
Liquid Crystal Display (LCD)
  Cheaper, more energy-efficient compared to TFT
Capacitive touchscreen allowing for multi-touch
Attached driver board that handles power and signal processing
Easily integrates with Raspberry Pi
Cost: $80

## Slide 11: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 12: GUI
Secondary means of interaction with the device
Allows the user to login, change settings, and link accounts
Using Python
  Included with Raspbian
  Event-driven language
  Using Kivy
    Open-source
    Easily integrates with the Raspberry Pi
    Great for multi-touch user interfaces and apps

## Slide 13: GUI User Flowchart

## Slide 14: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 15: Voice Recognition
Primary means of interaction with the device
Works the same as Amazon Echo, Siri, etc.
Senses when a command is being given by looking for a ‘wake up’ keyword
Records the command that follows and utilizes Google Speech API to translate it into a command that Ion can recognize

## Slide 16: Voice Recognition State Diagram & Flowchart

## Slide 17: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 18: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 19: Face Detection
Purpose:
  Detect faces
  Return position of face closest to center (x,y)
  Feedback for Face-the-User (name TBD) system
Language: Python
Library: OpenCV

## Slide 20: Face Detection Algorithm
Reduces capture size
Transforms to grayscale
Blurs
Detects faces
Returns coordinates

## Slide 21: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 22: Face-the-User System
Purpose
  Turn Ion so the screen faces the user
Camera
Raspberry Pi
MCU
Capture image
Image is sent to Raspberry Pi
Detects face
Calculates distance vector to center
Instructs MCU to update position
Changes servo position

## Slide 23: Face-the-User System Challenges
Position vector’s magnitude could be off
  Too large
    Overshoot
    Oscillation
  Too small
    Many minor adjustments
  Both are a waste of power and resources
User may move while position is updated

## Slide 24: Face-the-User System Solutions
Dynamic feedback
  Position change in increments
Variable buffer rectangle
Target rectangle while adjusting position.
Buffer rectangle. The center of the face needs to cross one of its borders to initiate movement.
Position updated until face is centered

## Slide 25: Face-the-User Algorithm
Get position of face from face detection
Determine face distance to center
Turn Ion to center on face
  Turn fast if face is far from center
  Turn slowly if face is close to center
Once face is in center, only adjust position once face is
outside a certain threshold

## Slide 26: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 27: Facial Recognition
Purpose:
  To identify saved users and load their settings
Not a safety feature
  Not accurate enough because of 2D picture
Accuracy vs. Speed
  Eigenfaces – fast but unreliable
  Fisherfaces – More reliable but slow
Will only run when a face has not been detected for a while

## Slide 28: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 29: Processor Load
Facial Recognition
Face Detection
GUI & Multimedia
Voice Recognition
OS (Linux)

## Slide 30: Single Board Computer (SBC) Choices
Asus Tinkerboard
Beagleboard
Raspberry Pi
Sopine A64

## Slide 31: SBC Comparison
 | Raspberry Pi | BeagleBoard | Asus TinkerBoard | Sopine A64
CPU/SOC | 4-core 1.2 GHz | 1-core 1.0 GHz | 4-core 1.8 GHz | 4-core 1.152 Ghz
Memory (RAM) | 1 GB | 512 MB | 2 GB | 2 GB
Price | $35.00 | $49.00 | $55.44 | $35.00
Component Availability | Readily available | Readily available. CPU can be bought directly for $20 | Prototype board available on Amazon. Components for final design not yet found | Readily available
Interfaces | Everything necessary, except 2nd PWM output | All necessary interfaces available | All necessary interfaces available | Everything necessary, except 2nd PWM output
Final Implementation | Connect Raspberry Computer Module 3 via fixed SODIMM connector to PCB | SBC design to be used as reference to add CPU directly to final PCB | Currently not possible because components have not been found | Connect Sopine A64 via fixed SODIMM connector to PCB

## Slide 32: SBC Choice: Raspberry Pi 3 Compute Module Lite
Performance deemed sufficient
Smaller when added to PCB
Lowest cost
Already own development board and SBC (version 3 B)
Abundant information and tutorials online
Most future-proof
Raspberry Pi Compute Module 3 Lite
WaveShare Compute Module IO Board Plus

## Slide 33: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 34: Motor Control Unit (MCU) Tasks
Rotate servos
Analog to digital conversion (Audio in)
LED control

## Slide 35: MCU Main Choices and Comparison
 | Atmel Mega328 | Ti M430
Prototyping Board | Arduino Uno | LaunchPad
Operating Voltage | 1.8-5.5V | 2.0-3.6V
Clock Speed | 20 MHZ @ 4.4+ V | 16 MHz
I/O | 23 GPIO 8 10-bit ADC channels | 15 GPIO 8 10-bit ADC channels
Price | $1.30 | $2.48

## Slide 36: MCU Choice: Atmel mega328
Faster
Cheaper
Can be prototyped on breadboard (see picture)
Already own Arduino Uno and Bootloader

## Slide 37: Mohammad’s Responsibilities
Audio Processing
WiFi System
Misc.
Power Management
PCB

## Slide 38: Mohammad’s Responsibilities
Audio Processing
WiFi System
Misc.
Power Management
PCB

## Slide 39: General User-Device Voice Interaction
User issues the device a command; the device responds.
Example:
User: What is the time right now?
Device: It is 12:30 P.M.
Audio
Signal
Digital Signal
Analog
Signal
Audio
Signal
Digital Signal
Analog
Signal

## Slide 40: Electret Microphone
Very common in audio projects.
Specs:
  -44dB sensitivity
  20Hz-20kHz frequency response
  Operating voltage range of 1VDC-10VDC
  Breadboard-friendly
  Downside: Requires filtering and amplifying

## Slide 41: Speakers
Parameter | Regular Speaker | Thin Speaker
Diameter | 50mm | 40mm
Power Rating | 0.5W | 0.25W
Impedance | 8Ω | 8Ω
Price | $1.95 | $0.95
Quality | Much clearer sound | Needs filtering and amplifying
Thin Speaker
Source: SparkFun
Regular Speaker

## Slide 42: Analog-To-Digital Converter (ADC)
The ATMEGA328-20P chip (MCU) analog input will be used.
Backup component:
ADC081S021CIMF/NOPB
Specs:
8-bit resolution
1 channel
SPI, Serial, 3-Wire interface
Operating voltage of 3.3V-5V
1.3mW power consumption
2.92mm x 1.6mm x 1.02mm
Source: Texas Instruments

## Slide 43: Digital-To-Analog Converter (DAC)
Parameter | MCP4725A3T-E/CH | DAC081S101CIMK/NOPB
Resolution | 12 bit | 8 bit
# of Channels | 1 | 1
Interface | 2-Wire/Serial/I2C | Serial/SPI
Operating Voltage | 3.3V-5V | 2.7V-5.5V
Operating Current | 210µA | 256µA
Price | $1.16 | $1.44
Component Familiarity | More familiar | Never used before
MCP4275
3.1mm x 3.2mm x 1.3mm
Source: Microchip Technology
DAC081
Size dimensions unknown
Source: Microchip Technology

## Slide 44: Mohammad’s Responsibilities
Audio Processing
WiFi System
Misc.
Power Management
PCB

## Slide 45: WiFi Chip
Parameter | Xbee S6B | ESP-12S
Standard | 802.11 b/g/n | 802.11 b/g/n
Frequency Band | 2.4GHz | 2.4GHz
Security | WPA/WPA2/WEP | WPA/WPA2/WEP
Interface | SPI/UART | SPI/I2C/UART
Operating Voltage | 3.12V-3.46V | 3.0V-3.6V
Transmit Power | +/- 16 dBm | +/- 20 dBm
Price | $29.00 | $6.95
ESP-12S WiFi Chip

## Slide 46: Mohammad’s Responsibilities
Audio Processing
WiFi System
Misc.
Power Management
PCB

## Slide 47: Storage
MicroSD card breakout board+
Source: Adafruit
MicroSD Card Socket

## Slide 48: Light Emitting Diodes (LEDs)
 | Single-Color LEDs | RGB Programmable LEDs
Advantages | Desired colors are already programmed Simpler to use Least expensive | Less LEDs are required Many different colors can be used per LED Not too expensive
Disadvantages | A bunch of LEDs will be needed for each color for the project; takes more space | Color programming required
Chosen by the group | No | Yes

## Slide 49: LED Specifications & Functions
Specs:
Single Wire Single Transmission
800kHz internal frequency
Operating voltage range of 4.5VDC-6VDC
Color | Meaning
Blue | Device is ON
Yellow | Device is currently listening to user commands (processing)
Green | Device understood the command
Red | Device did not understand the command
5mm Clear Head RGB LED

## Slide 50: Mohammad’s Responsibilities
Audio Processing
WiFi System
Misc.
Power Management
PCB

## Slide 51: Power Consumption
Component | Nominal Input Voltage (V) | Nominal Current Draw (mA) | Power Consumed (mW)
Processor | 5 | 16 | 80
LCD | 5 | 2,400 | 12,000
Servo Motors | 5 | 500 | 2,500
Motor Control Unit | 5 | 0.5 | 2.5
WiFi Chip | 3.3 | 80 | 264
Camera | 5 | 250 | 1,250
LEDs | 5 | ~20 | ~100
microSD Card | 3.3 | 100 | 330
DAC | 5 | 0.21 | 1.05
Total: |  | ~3.36A | ~16.5W

## Slide 52: Battery
Parameter | Tenergy Li-Ion 18650 #1 | Tenergy Li-Ion 18650 #2
Nominal Voltage | 7.4V | 3.7V
Nominal Capacity | 4400mAh | 5200mAh
Dimensions | 37mm x 37mm x 70mm | 133mm x 19mm
Weight | 7oz | 3.3oz
Cycle Life | >300 cycles | >300 cycles
Tenergy 18650 #1
Source: Tenergy
Tenergy 18650 #2
Source: Tenergy

## Slide 53: Power Connections
7.4V-5V Step Down Regulator
5V-3.3V Step Down Regulator
3.3V-2.5V Step Down Regulator
2.5V-1.8V Step Down Regulator
DC-DC Voltage Regulators

## Slide 54: Mohammad’s Responsibilities
Audio Processing
WiFi System
Misc.
Power Management
PCB

## Slide 55: PCB Schematic Overview

## Slide 56: Budget
Component | Projected Cost ($) | Actual Cost ($)
Microphones | 3.00 | 1.90
Speakers | 6.00 | 3.90
Display | 60.00 | 80.00
Controller | 35.00 | 26.00
Camera | 15.00 | 10.00
PCB(s) | 50.00 | -
Body | 50.00 | -
Buttons, switches | 10.00 | 1.50
Resistors, capacitors, etc | 10.00 | -
LEDs | 10.00 | 5.90
MCU | 20.00 | 1.30
Servo(s) | 30.00 | -
WiFi Modules | 32.00 | 6.95
Mono Audio Amplifier | 8.00 | 7.95
DAC Breakout Board | 5.00 | 4.95
Battery | 20.00 | -
Voltage Regulators | 15.00 | 10.00
Total | 494.00 | -
Updated Projection: $320.35

## Slide 57: Current Progress
Chart: 
| Total | Testing | Parts Acquisition | Software Development | Prototyping | Design | Research
Series 1 | 50 | 25 | 75 | 40 | 40 | 75 | 85
To-do:
Get working PCB
Finish up software
Integrate all components together
Test PCB

## Slide 58: Issues
Creating a PCB voltage bus and a jack.
Integrating hardware and software together.

## Slide 59: Questions?