## Slide 1: ANGULAR POSITION
Group 14
Amber Haley
Jenna Soto
Benjamin Williamson

## Slide 2: Motivation
Ride Control
Programmable Logic Controller
Explore different wireless possibilities
Exposure to a real world project design

## Slide 3: Goals
Transmit angular position wirelessly from the ride vehicle
Receive angular position track side for interpretation
Functioning prototype that proves technology
Possibly incorporated into a ride control system.
No Limits 2 [Suspended Coaster] - Jungle Swinger by JozParks

## Slide 4: Sponsor requirements
Withstand Florida weather conditions
Reliably and accurately transmit/receive data wirelessly
Supported for PLC I/O
Standardized not customized components (COTS)
Use PCB in testing capacity
Light weight and relatively small
Vibration Tolerant
180º range
Fail Safe

## Slide 5: Specifications
Component | Parameter | Design Specification
Battery | Charge Time | <5 Hours
Battery | Time Before Recharge | >24 Hours
Encoder | Accuracy | +/- 2 degrees
Z-wave Module | Min Range | > 50 feet
Raspberry Pi | Data Rate | < 1 millisecond
Battery Monitor | Accuracy | +/- 5 %

## Slide 6: System Overview
WIRELESS DATA
ON-BOARD
WAY SIDE

## Slide 7: Work Distribution
 | On Board |  | Wayside |  | Testbench
 | Power | Components/ Programming | Power | Components/ Programming | Components/ Programming
Amber Haley |  | S | P | P | 
Jenna Soto | P |  | S |  | S
Ben Williamson | S | P |  | S | P
P = Primary
S = Secondary

## Slide 8
Battery
Battery Monitor
Voltage
Regulator
Circuit Breaker
Raspberry Pi
11.1 V
11.1 V
5 V
5 V
Z-Wave
Module
5 V
Raspberry Pi
Z-Wave
Module
Encoder
Wireless Data
Wall outlet
120 V
PLC
Indicator Lights
Sola Power Supply
On Board
Way Side
Polling
Overall Block Diagram
Power
MCU
PLC
Sensor
Power Line
Data Line
Legend
Test Object
Stuck
Key
5 V
24 V
5 V
5 V

## Slide 9
Battery
Battery Monitor
Voltage
Regulator
Circuit Breaker
Raspberry Pi
11.1 V
11.1 V
5 V
5 V
Z-Wave
Module
5 V
Raspberry Pi
Z-Wave
Module
Encoder
Wireless Data
Wall outlet
120 V
PLC
Indicator Lights
Sola Power Supply
On Board
Way Side
Polling
On-Board Power
Power
MCU
PLC
Sensor
Power Line
Data Line
Legend
Test Object
Stuck
Key
5 V
24 V
5 V
5 V

## Slide 10: Battery
 | Lead Acid | NiCd | NiMH | Li-Ion | Li-Poly
Nominal Voltage | 2V | 1.2V | 1.2V | 3.6V | 3.7V
Energy Density (Wh/kg) | 40 | 45 | 90 | 160 | 130-200
Life(Years) | 3 | 2 | 3 | 6 | 3
Charge Time (hrs) | 8 | 1.5 | 4 | 2.5 | 1
Self-Discharge Rate (%/mo) | 2-5% | 10% | 30-50% | 2-8% | 2-8%
Average Capacities (mAh) | 4000-7000 | 600 | 2000 | 2000-6000 | 6000-12000
Average Cycle life | 500-800 | 800-1500 | 500-1000 | 400-1200 | >1000
Specification | Rating
Type | Lithium Polymer (LiPo)
Cell(s) | 3S – 3 cells in series
Capacity | 22,000mah
Volts | 11.1 V
Charge Capability | 5C
Rating | 40C
Warranty | Lifetime
Wire | 12awg
Charging Connector | JST-XH
Plug | XT60
Cost | $399
MAXAMPS

## Slide 11: BATTERY CHARGER
SKYRC iMAX B6AC V2
AC Input Voltage 100-240V
Li-Po/Li-Ion/NiMH/Ni-Cd/PB
5.3inches x 5.7inches x 1.5inches
2-6S HX Plug in Balance Sockets
Check each battery cell voltage
Temperature threshold
PC connect to upgrade
$54.55

## Slide 12: Battery Monitor
Powerwerx Watt meter, DC Inline Power Analyzer
Monitors four values of the battery for safety purposes
Easy to read backlit LCD for visibility in all light conditions
Main use is to monitor battery capacity
High resolution for battery values (.01 for A/V, .001 for A-h)
Source power is fed through the device to load
Specification | Rating
Amps | 100 A, 0.01 resolution
Voltage | 5-60 V, 0.01 V resolution
Wire Gauge | 12 AWG
Watts | 0 – 7800 W, 0.1 W resolution
Amp-hours | 0-65 Ah, 0.001 Ah resolution
Display | High-Contrast blue backlit LCD
Weight | 0.18 lbs (82 g)
Size | 3.3” x 1.7” x 1.0”
Cost | $48.99

## Slide 13: Voltage Regulator
DROK LM256
5V Voltage Regulator
Amazon – 2 day shipping
Red LED Display
Adjustable output voltage
Reversed polarity protection
 | Vetco Electronics | Co_electronics | Getfpv | DROK
Input | 4.5 – 40 VDC | 0 - 30 VDC | 4.5 to 38 VDC | 4 to 32 VDC
Output | 1.5 – 35 VDC | 1.25 – 28 VDC | 3 to 32 VDC | 1.25 to 30 VDC
Output Current | 2A | 2A | 2.5A | 3A
Efficiency | 92% | 91% | 85% | 92%
Operating Temp | -40 to +85 C | -40 to + 85 C | -40 to +80 C | -45 to +85
Cost | $14 | $7.16 | $8.99 | $8.99

## Slide 14
Battery
Battery Monitor
Voltage
Regulator
Circuit Breaker
Raspberry Pi
11.1 V
11.1 V
5 V
5 V
Z-Wave
Module
5 V
Raspberry Pi
Z-Wave
Module
Encoder
Wireless Data
Wall outlet
120 V
PLC
Indicator Lights
Sola Power Supply
On Board
Way Side
Polling
Overall Block Diagram
Power
MCU
PLC
Sensor
Power Line
Data Line
Legend
Test Object
Stuck
Key
5 V
24 V
5 V
5 V

## Slide 15: Encoder Sensor
Miniature absolute magnetic regular shaft encoder
Miniature – encoder is .48” in diameter and about 1” in length
Absolute – unique postions,10-bit resolution = 0.351°
Magnetic - series of magnetic poles, manufactured for dirty, industrial environments.
Regular Shaft – see picture
Analog output

## Slide 16
Battery
Battery Monitor
Voltage
Regulator
Circuit Breaker
Raspberry Pi
11.1 V
11.1 V
5 V
5 V
Z-Wave
Module
5 V
Raspberry Pi
Z-Wave
Module
Encoder
Wireless Data
Wall outlet
120 V
PLC
Indicator Lights
Sola Power Supply
On Board
Way Side
Polling
Overall Block Diagram
Power
MCU
PLC
Sensor
Power Line
Data Line
Legend
Test Object
Stuck
Key
5 V
24 V
5 V
5 V

## Slide 17: On-board Raspberry pi/Z-wave module
Raspberry Pi
  On-board power management system to a micro USB connection
  The “Brains” of the On-Board system
  Initialized using a button to zero all of the data.
  Takes Encoder data in and converts it for the PLC before transmitting
  Algorithm it uses has a fail-safe to insure accurate data transmission
Z-Wave Module
  Powered by the Raspberry Pi
  Plug – and - play
  Sub-GHz bandwidth
  Secure wireless specification
Encoder data | Algorithm 1 | Algorithm 2 | Comparison
In-range | TRUE | TRUE | TRUE
In-range | TRUE | FALSE | FALSE
Out of range | FALSE | TRUE | FALSE
Out of range | FALSE | FALSE | TRUE

## Slide 18: Way-side raspberry pi/z-wave module
Way-Side
  Powered with a standard Micro USB Power Supply
  Receives data from attached Z-Wave module and transfers it to an output pin
  Secondary pin used to tell the PLC if the signal is being received by the Z-Wave module
Signal | Received Data | Signal Output Pin | Range Output Pin
Received | TRUE | HIGH | HIGH
Received | FALSE | HIGH | LOW
Not received | TRUE | LOW | X
Not received | FALSE | LOW | X

## Slide 19: Weatherproof enclosure
Main purpose is for mitigating Florida weather conditions
The On-Board system will be in a NEMA Type 4X/IP66
Way-side MCU and Module will be a smaller dust tight enclosure
Dehumidifying silica packets inside with indicator cards

## Slide 20
Battery
Battery Monitor
Voltage
Regulator
Circuit Breaker
Raspberry Pi
11.1 V
11.1 V
5 V
5 V
Z-Wave
Module
5 V
Raspberry Pi
Z-Wave
Module
Encoder
Wireless Data
Wall outlet
120 V
PLC
Indicator Lights
Sola Power Supply
On Board
Way Side
Polling
Overall Block Diagram
Power
MCU
PLC
Sensor
Power Line
Data Line
Legend
Test Object
Stuck
Key
5 V
24 V
5 V
5 V

## Slide 21: PLC
Industrial computer, robust, widely used in control industries
Power supply – powers the modules
CPU is its own module
Input module – takes in the information
Output module – turns on or signals external components

## Slide 22: PLC Inputs & outputs
Inputs
  Signal
  Range
  Polling
  Stuck
  Maint. Key
Outputs
  Stuck / Not stuck
  Signal received
  In Range / Out of Range
  Stop Request

## Slide 23: Prototyping
PCB Test Board
  ATMega328 takes an analog input from a potentiometer to set a servos angle from 0 – 180
  The servo will have a shaft that has the encoder coupled to it.
  ATMega328 will also take digital data in from on-board MCU
  PCB LCD will show the current input angle and current encoder angle
  All of this will be powered by a 5V micro USB power supply

## Slide 24: PCB Schematic

## Slide 25: PCB Schematic
LCD
Displays input Servo Angle
Displays output Encoder angle
Potentiometer to adjust contrast
Resistor to not blow up backlight

## Slide 26: PCB Schematic
ATMega328P-PU
Conversion of analog pot data to send to servo
Sends digital data to display on LCD
16 MHz Crystal Oscillator
Controls clock on ATMega

## Slide 27: PCB Schematic
Encoder input pin
Sends digital data to ATMega
Servo Control/Power
3 pins to power and control servo
Servo Potentiometer
Controls servo angle

## Slide 28: PCB Schematic
MicroUSB Connector
Powers ATMega, LCD, and Servo
Only using 5V and GND

## Slide 29: PCB Layout

## Slide 30: PCB Layout
LCD
LCD Contrast Control

## Slide 31: PCB Layout
ATMega328P-PU &
16 MHz oscillator

## Slide 32: PCB Layout
Servo Power/Input
Servo Angle Control
Input pin for
Encoder data
Output pin for
Encoder data

## Slide 33: PCB Layout
MicroUSB
Power Supply

## Slide 34: Administrative content

## Slide 35: Budget
Item | QTY | Cost
Battery | 1 | $399.99
Microcontroller | 2 | $69.89
Battery Monitor | 1 | $48.99
Encoder | 1 | $55.50
Battery Charger | 1 | $54.55
Z-Wave Module | 2 | $99.98
5V Voltage Regulator | 1 | $8.99
Step up Regulator | 2 | 
Battery Connectors | 1 | $9.56
Encoder Connector | 1 | $8.30
Encoder coupling | 1 | $50.00
Zero Push button | 1 | $1.95
Microcontroller Power | 1 | $9.00
PLC | 1 | Sponsor
Indicators | 1 | Sponsor
Wiring/ Clips | A/R | Sponsor
Total | $725.71 | 

## Slide 36: Financing
  Out-of-Pocket
    PCB
  Sponsor
    Components

## Slide 37: Issues
PCB
  Soldering
  Power
  ATMega328p vs ATMega328
Ordering Parts – Approval

## Slide 38: Questions?