## Slide 1: FINAL PRESENTATION
Presented By:
Annette Barboza
Ayanna Ivey
Brandon Kessler
Group 13
July 29th 2019
Sponsored By:
Sound Enhancing Autonomous Network
Notes: brandon

## Slide 2: Special Thanks
Applied Research – Sensor Systems and Technology
Director: Scott Nelson
Mentor: Jonathan Tucker
Notes: brandon

## Slide 3: Project Idea
Sound Enhancing Autonomous Network (Sean): Portable device designed to be an improved hearing aid alternative focused on human-to-human conversation.
Enhance the sound of another human’s voice
Utilize multiple microphones to identify the location of signals
Employ camera to determine if and where humans are in the scene
User interacts with system though a phone app
Notes: annette

## Slide 4: Motivation & objectives
Main Motivation:
Current hearing aides do not effectively amplify desired signals and attenuate unwanted noise
Objectives:
Provide a directed sound experience that allows the user to have a seamless conversation with another person and control the level of background noise
Prove that there is value in integrating a visual aspect to a hearing aid
Create a comfortable wearable platform that highlights the utility of a portable system
Be a user-friendly and intuitive product
Stay under budget of $2000
Notes: annette

## Slide 5: System design
Notes: Brandon

## Slide 6
Notes: Brandon

## Slide 7: Processors
Processor | GPU | CPU | Wireless Compatibility | Price | Power
Jetson TX2 Developer Kit | 256-core Pascal GPU | 2 Denver 64-bit CPUs + Quad-Core A57 | Bluetooth® 4.1 and WiFi enabled | $600 | 7.5W / 15W
Raspberry Pi 3 | Broadcom VideoCore IV | Quad-Core ARM Cortex-A53 | Bluetooth® 4.2 and WiFi enabled | $35 | 1.2 W
TX2 Functions:
Run deep learning face detection algorithm
Host for Raspberry pi 3
Run algorithm to merge audio and visual outputs
Display face detection live feed
Capture raw audio and outputting processed audio
Raspberry Pi 3 Functions:
Collect information from microphone array
Run Direction of Arrival (DOA) algorithm
Save DOA outputs
Notes: Brandon

## Slide 8: Camera
Camera Module | Resolution | FOV
e-CAM132_TX2 | 13MP (4192 x 3120) | 74.4°(D) 60.2°(H) 46.4°(V)
Logitech C920s Pro | 1920 x 1080 | 78.0°(D) 72.4°(H) 44.7°(V)
Original Camera: e-CAM132_TX2
  Optimized for TX2
  Achieved 20 – 25 FPS during face detection
  Broke during testing; likely due to Electrostatic Discharge
New Camera: Logitech C920s Pro
  USB camera with similar FOV
  Easy to integrate with existing code
  Achieves 15 – 20 FPS during face detection when resizing the image to 640 x 480
Notes: Brandon

## Slide 9: Microphones
Matrix Voice
  8 microphones
  SNR=62.5 dB
  THD
    <1% @ 100dBSPL
    <5% @ 115dBSPL
Samson Go Microphone
  1 microphone
  Directionality patterns:
    Cardioid
    Omnidirectional
  16-bit, 44.1kHz resolution
Notes: Annette

## Slide 10: Power Supply
4 x Double A Batteries (6V)
  PCB
Pilot Pro
  TX2
  USB Cooling Fans
  Raspberry Pi
Notes: Ayanna

## Slide 11: Wireless communication
Bluetooth
  Used to connect to headphones or a speaker within Mobile App
Gstreamer
  A pipeline-based framework used for streaming media applications
  Compatible with iOS and TX2
  Streams over Wi-Fi
  Con: Degrades audio quality
Notes: Ayanna

## Slide 12: Final Packaging
Laser printing
  More sensible for a simple design
  Takes less time than 3D printing
  Better for larger projects
Acrylic
  Durable
  Impact Resistant
Notes: Ayanna

## Slide 13: final Packaging design
Table 18 -- Dimensions of Sean Packaging |  |  |  |  | 
Component | Part Name | Length (mm) | Width (mm) | Height (mm) | Thickness (mm)
Rectangular casing | Housing for processor, PCB, and battery | 394.46 | 240 | 76.20 | 5
Notes: Ayanna – annette pit picv

## Slide 14: Safety
Notes: ayanna

## Slide 15: Packaging
Cooling
  TX2 built in cooling
  Vents in packaging
  USB Fans
TX2 Thermal Cooling Plate
TX2 built in fan
USB Cooling Fan
Sean Vents
Packaging
Notes: Ayanna – put pic pf venting

## Slide 16: Printed circuit board
Beeps continuously when the temperature in the packaging reaches 43 C and does not cease until temperatures drop below again.
  LM358P is used as a comparator to trigger 5V to be supplied to piezoresistive buzzer once the output of the LM35DZ passes reference voltage from the voltage divider circuit
Notes: Annette - schematic

## Slide 17: Software Design Overview
Notes: aNNETTE

## Slide 18: Audio Processing Algorithm
Direction of Arrival (DOA)
    Energy is determined by the amplitude and duration of the signal
    ( Longer and Louder signals = Higher Energy) Lights up LEDs blue or green in the direction of a signal with a high enough "energy level"
    Blue: source with high enough energy detected
    Green: source that has built up enough energy to be classified as a potential person the user cares about listening to
  Angle of direction of the source is measured and sent to cross-reference with the location of any human face detections in the visual algorithm
Notes: Annette

## Slide 19: Visual Processing Algorithm
Human Face Detection
  Goal: Identify Humans in FOV as likely candidates to be talking to the user
  Deep-learning based approach: FaceNet
      Convolutional Neural Network using InceptionNet
      as base network fine tuned on faces.
      Trains on sets of 3 images that are different in size, lighting, and pose
      Open source network built with caffe framework
  Codebase set up to use any compatible camera
  Smooths detection over time
    Only considers detections that have been collected 10 frames in a row
    Allows detections to persist until there are 10 missed detections in a row
InceptionNet Module
Notes: Brandon v
Variant of yolo
Video

## Slide 20: Merging Audio and Visual SPaces
44.7°
0°
72.4°
Camera and microphone array are center aligned
Spaces are divided up into 4 vertical slices
Audio and visual detections correspond to one of the 4 slices
A detection in the audio space occurs when energy from that slice reaches the threshold (light turns green)
Detection in visual space occurs when a human face is detected. (Confidence value > 0.5)
Audio is amplified when detections are found in the same slice in both domains
Microphone Angle Space
Camera Angle Space
0
1
2
3
Notes: Brandon
Make ocmments about resolution

## Slide 21: Audio Mixing
 | Tier 1 Amplification | Tier 2 Amplification
State | No confirmed human face detection mapped to a voice | Confirmed human face detection mapped to a voice
Gain | 1 | *1.9
Environment Based
High Noise
  Ex: Restaurant, lobby
  Gain*Y
Medium Noise
  Ex: Classroom,
  Gain*X
Low Noise (Default)
  Ex: Quiet room
  Gain*1
NOTE: X>1, Y>X
*1.9 was tested with a participant and was found to be a good level of amplification.
Notes: Annette

## Slide 22: Sean mobile app symbology example
Final Audio Output
Audio is amplified by default 1.9 through Gstreamer. This amplification does result in some distortion.
Final Visual Output
Combining Visual and Audio Detections to Produce Visual Display with Symbology Overlayed
Notes: Annette (how to remerge) and brandon

## Slide 23: Mobile application - user interface
Notes: Ayanna

## Slide 24: Mobile application - DESIRED FEATURES
User Select
Environment Select
Settings
Video Mode
Notes: Ayanna

## Slide 25: Materials & Budget
Item | Price
Microphone array | $61.05
Double A Batteries and battery holder | $11.72
Camera | $284.00
1st PCB | $27.00
2nd PCB | $26.10
Power Source | $80.00
USB Cooling Fans | $13.95
Processors | $0.00
Microphone array processor | $37.27
RPi Memory | $10.54
Thermal Sensor Circuit | $30.00
Thermal Sensor | $6.35
Op Amp | $9.49
Item | Price
LEDs | $4.99
Wifi Adapter | $8.99
Acrylic (2 sheets) | $80.84
Monitor + Keyboard + Mouse | $141.61
Mounting adhesive stickers | $7.99
1ft ethernet cables | $6.99
Harness | $16.85
Beeper | $8.99
Lowes Screws | $1.37
Home depot screws (1) | $6.98
Michael's mounting supplies | $15.58
Velcro | $19.57
Item | Price
GOMIC USB MICROPHONE | $42.59
LOGITECH C920S PRO HD WEBCAM | $74.54
Screws and Spacers | $11.73
VCE HDMI Male to VGA Female Converter Adapter | $8.99
2nd TX2 | $607.04
Total: | $1647.77
Remaining: | $352.23
Notes: Ayanna
What to do with extra money

## Slide 26: Demo

## Slide 27: SEAn mobile app
https://youtu.be/Tukr-ofB_SU

## Slide 28: PCB Video
https://youtu.be/zx9sFiW92N0

## Slide 29: Demo Test case 1
CASE dESCRIPTION:
User is alone, no other people, no unexpected noise.
Desired result:
“Natural” and clear environment noise.
Notes: Annette

## Slide 30: Demo Test case 2
CASE dESCRIPTION:
User is with one other person (not talking) and noise in the background.
Desired result:
“Natural” and clear environment noise.
Notes: Annette

## Slide 31: Demo Test case 3
CASE dESCRIPTION:
User is with one other person who is in front of the camera talking.
Desired result:
Signal is amplified with Target’s voice.
Notes: Annette

## Slide 32: Demo Test case 4
CASE dESCRIPTION:
Case 3 with another person in the background not talking.
Desired result:
Signal is amplified with Target’s voice.
Notes: Annette

## Slide 33: Demo Test case 5
CASE dESCRIPTION:
User is with two people having their own conversation in the background.
Desired result:
Nothing is amplified. “NATURAL” AND CLEAR ENVIRONMENT NOISE.
Notes: Annette

## Slide 34: Results
Proved the value of adding a visual aspect to a hearing aid in order to focus more on human to human interaction
Needs more testing in nonideal environments
Limitations:
  User only wants to talk to one person at one time.
  User cannot speak.
Test Results | 
Case | Results and Feedback
1 | 3, Sound is the same as hearing aid in ideal environment.
2 | 3, Sound is the same as hearing aid in ideal environment.
3 | 4, Voice comes through clear and accurate timing of amplification. Again, consider ideal environment.
4 | 4, Voice comes through clear and accurate timing of amplification. Inconsistent recognition and amplification.
5 | 4, Nothing was amplified as we did not care about that separate conversation.
"On a scale of 1 to 5, please rate how Sean operates in the given situation in reference to the hearing aids you use daily."
1=Totally worse than my current hearing aids
2= Slightly worse than my current hearing aids
3=About the same as my current hearing aids
4=Slightly better than my current hearing aids
5=Totally better than my current hearing aids
Notes: Annette

## Slide 35: Future work and Considerations
Time was the most valuable and limited resource
More testing with hearing impaired persons
Focus on developing audio algorithms further
  Complete what was initially planned
    User voice filter
    Separation of signals
    Confidence based Audio Mixing
Full implementation of Gstreamer within Sean Mobile App
  Complete what was initially planned
Path to miniaturization
  Reduce weight and size
Aligned Audio Space Output
Human Face Detection Output
- High-Confident Voice Detection
- Mid-Confident Voice Detection
- Face Detected
- Face Detected but No Voice Signal
- Face Detected and Voice Signal Amplified
- No Face Detected and Voice Signal Attenuated
Final Output
Notes: Everyone