## Slide 1: Multi-sensor Passive ranger (MSPR)
Pedro A. Alvarez Fernandez Photonic Science and Engineering
John Haynes Electrical Engineering
Ilina Sunkara Photonic Science and Engineering
Taylor Whitton Computer Engineering
Group 3:

## Slide 2
• overall project block diagram, or system design diagram
• discuss the project design approach and proposed implementation
• discuss and support significant design decisions and significant component decisions
• discuss the impact of realistic design constraints including economic, environmental,
social, political, ethical, health and safety, manufacturability, and sustainability
• Identification and review of related standards
• discuss project successes and difficulties for each project subsystem
• show the project budget and financing to date, and to the end of the project
• clear statement of current progress made by the group (% done by category)
• discuss the group's immediate plans for the successful completion of the project

## Slide 3: Motivation
In military applications, the element of surprise is of vital importance:
  Many range-finding systems utilize detectable means of obtaining the range of a given object.
  These systems rely on “active” methods that require the system to send out some form of signal to detect the distance of the object
    Radar and laser-based range-finding systems
  Ideally, a military adversary should not be aware that they are being tracked, to keep the element of surprise.
General Surveillance purposes (mobile, non-mobile)
  For surveillance we want to receive as much information as possible (range, speed, identification)

## Slide 4: Solution
We present the Multi-Sensor Passive Ranger (MSPR) as our solution to the problem with “active” range finding systems.
  Make use of both stereo and infrared cameras to accurately range the distance of an object.
  No risk of detection since these cameras only absorb input from the environment, rather than producing some form of output.
  The IR band can track in no visible light scenarios and low visibility
  Each system can feed information to each other for accuracy

## Slide 5: Goals and objectives
Produce a system that can accurately find the range of an object in a passive, undetectable manner.
  Other systems, such as radar, transmit radio waves.
    Systems can detect these radio waves, leading them to be detectable.
    This is suboptimal for military applications where one wants to restrict the enemy’s knowledge as much as possible.
A real-time stream of range data that can be used to continuously monitor an object’s position relative to the device.
Cross reference the range data from the IR camera and the stereo system to detect inconsistencies.
Implement a software algorithm that can extract range from IR camera images

## Slide 6: Specifications and requirements
Category | Specification
Range estimation accuracy | ±5% of true value
Range estimation speed | 10 times/sec
Background/Target differentiation | 2 s
Time of arrival estimation (velocity) | ±5% of true value
Disparity image | 15 FPS (480p<)
Object motion tracking | 2 s
Temperature sensitivity | ±5°C or ±5% of reading
IR Field of View | 90°(H) × 69°(V) <- might be less
IR Resolution | 2.267 mrad

## Slide 7: Layout Design: overall
USB Interface

## Slide 8: Block Diagram: overall

## Slide 9: Block Diagram: Electrical

## Slide 10: Block Diagram: Software

## Slide 11: Software Design
The basic flow of the software system is simple:
  Initialize a connection to each camera
  Iteratively retrieve a frame from each camera
  Apply preprocessing steps to reduce the complexity of each algorithm (convert to greyscale)
  Run each image through each system’s respective distance calculating algorithm to extract the range of the object
  Output result to GUI, await next frame

## Slide 12: Layout Design: Visual Cameras
Planes pleft and pright
  Represent intersections between the image plane and lines from the camera centers to the object
Since the two triangles shown in the diagram are similar, the ratios of base to height in both should be equivalent.
By taking the center from the distance between the cameras as the origin, the can be represented as positive and as negative
Depth and disparity have an inverse relationship, where the distance Z increases as the disparity decreases

## Slide 13: Ir Ranging Theory (Point source)
To be considered a point source, R needs to be larger than 5X the source diameter, or (1).
A point source is subject the inverse square law which says that irradiance (H) decreases as (1/R), with R being the distance away from the point source
The point source radiant intensity is given by (2) and the detected irradiance at the detector is (3)
From this equation we also arrive at the equation for detected power

## Slide 14: Ir Ranging Theory (Extended source)

## Slide 15: Closing object simulation and alignment

## Slide 16: Camera alignment and spatial calibration
Scotch™ Brand 88 black vinyl electrical tape
  Emissivity of 0.96 ( for 3-5 um and 8-12 um wavelengths)
Aluminum sheet metal
  Emissivity close to 0

## Slide 17: Sample Calibration pictures taken
Tau 640 with 7.5mm Lens for 4ft high x 5ft wide panel at 200 meters.

## Slide 18: Part Selection: computer System
 | Nvidia Jetson Nano | Raspberry Pi 8GB | Google Coral Dev Board 1GB
CPU | ARM A57 | Cortex-A72 | Cortex-A53, Cortex M4F
CPU clock rate | 1.43 GHz | 1.5 GHz | 1.3 GHz
CPU cores | 4 | 4 | 4
Coprocessor | - | - | Google Edge TPU
GPU | 128-core Nvidia Maxwell |  | Integrated GC7000 Lite
Network Connectivity | Gigabit Ethernet | Gigabit Ethernet, 802.11ac wireless, Bluetooth | Wi-Fi, Gigabit Ethernet
Storage | MicroSD | MicroSD | MicroSD, 8GB eMMC
RAM | 4 GB 64-bit LPDDR4 | 8 GB 64-bit LPDDR4-3200 SDRAM | 1 GB 64-bit LPDDR4
MIPI Lanes | 1x MIPI CSI-2 DPHY | 1x MIPI CSI, 1x MIPI DSI | 1x MIPI-DSI, 1x MPIP-CSI2
USB Ports | USB 3.0, USB 2.0, Micro-B | 2x USB 3.0, 2x USB 2.0 | Type-C, Type-A 3.0, Micro-B
Display Ports | HDMI, DP | 2x micro-HDMI | HDMI 2.0a
 | C | C++ | Python | Rust
Paradigms | Imperative | Imperative, Object Oriented | Imperative, Object Oriented | Imperative, Object Oriented
Compilation | Compiled | Compiled | Interpreted | Compiled
Language Level | Medium | Medium | High | Medium
Libraries | Libccv, TensorFlow, OpenCV | OpenCV, TensorFlow, Pytorch | OpenCV, TensorFlow, PyTorch, SimpleCV, Matplotlib, Keras | OpenCV, TensorFlow, PyTorch
Type System | Strong Statically | Strong Statically | Weak Dynamically | Strong Statically
Safety Design | Unsafe | Unsafe | Safe | Safe
Portability | Highly Portable | Highly Portable | Highly Portable | Highly Portable
Standard Library | Large, Extensive | Large, Extensive | Large, Extensive | Large, Extensive
Microprocessor Selection
Programming Language Selection

## Slide 19: Jetson nano
The Jetson Nano was suitable for this project for several reasons:
  Onboard GPU
  Runs on Nvidia’s custom Ubuntu distribution
  2x MIPI ports for stereo vision
  High-performance quad-core processor
  Enough RAM for our use-case
  Cost of $119.99

## Slide 20: Python
Python was chosen as the language of choice for most of the code base for several reasons:
  Large selection of libraries relating to computer vision.
  Rapid development and prototyping.
  Seamless integration with MATLAB and C++ where necessary.
  A memory safe language.
  Supports parallelism to take advantage of the quad-core microprocessor.

## Slide 21: IR camera
Parameter | FLIR A65 25 mm | Tau 2 7.5 mm
FOV | 25° × 20° | 90° x 69°
iFOV | 0.68 mrad | 2.267 mrad
Pixel pitch | 17 μm | 17 µm
Frequency/framerate | 30 Hz | 30/60 Hz (NTSC)
Temp. range | -25°C to +135°C | -25°C to +135°C
Sensitivity | ±5°C (±9°F) | < 30 mK (NETD)
Shock rating | 25 g (IEC 60068-2-27) | 200g shock pulse w/ 11 msec sawtooth
Size | 4.2" × 1.6" × 1.7" | 1.75" x 1.75" x 1.18"
Thermal imager | Focal Plane Array (FPA), Uncooled VOX microbolometer | Uncooled VOX Microbolometer
Connection | Ethernet | 50-pin Hirose / BNC with VPC
Input voltage | 10–30 VDC | 4.0 - 6.0 VDC

## Slide 22: IR Lens selection

## Slide 23: A65 radiometric Calibrations
Chart: Counts vs Radiance
| 42.190730517422303 | 45.9688473464022 | 54.1429123992352 | 63.155779351240497 | 73.021608213580905
Mean Count | 86.512 | 88.178 | 95.638 | 100.812 | 98.115
 | 86.512 | 88.178 | 95.638 | 100.812

## Slide 24: Part Selection: Visible Cameras
 | Arducam MINI High-Quality Camera IMX477 HQ Camera Module | Arducam 12MP IMX477 Motorized Focus High Quality Camera | Arducam IMX219 Wide Angle Camera Module
Sensor | IMX477 | IMX477 | Sony IMX219
Optical Format | 1/2.3″ (diagonal 7.857mm) | 1/2.3” | 1/4 inch
Resolution | 4056(H) x 3040(V) 12.3MP | 4056 x 3040 pixels, 12.3MP | 8MP
Pixel Size | 1.55um x 1.55um | 1.55 µm x 1.55 µm | 
Interface | 2-lane MIPI CSI-2 | 2-lane MIPI | MIPI CSI-2 2-lane/4-lane
Frame Rate | 1920×1080 @ 60fps 4032×3040 @ 30fps | 1920×1080 @ 60fps 4032×3040 @ 30fps | 30fps@8MP, 60fps@1080p, 180fps@720p
Format | 1/2.3 inch | 1/2.3” | -
Focal Length | 3.9mm | 3.9mm | 2.5mm
Aperture | F2.8 | F2.8 | 2.8
Field of View | 75° (H) | 75° (H) | 175(D) x 155(H) x 115(V)
MOD | 0.1m | 0.3m | -

## Slide 25: Part Selection: Power
 | TPS56623x | TPSM84624 | TPS543620
Efficiency of Circuit at maximum power (5 amps) | 95.6% | 94.4% | 94.5%
Efficiency of Circuit at half power (2.5 amps) | 96.3% | 94.3% | 95.4%
Efficiency of Circuit at .5 amps | 94.8% | 83.3% | 89.3%
Current Range (at 5 Volts) | Up to 6 amps | Up to 6 amps | Up to 6 amps
BOM count | 15 | 8 | 17
Recommended Maximum Power at 5 volts | 30W | 30W | 30W
Vout peak to peak at 5 volts and 5 amps output | 8.71 mV | 11.9 mV | 8.32 mV
Circuit Footprint | 130 mm2 | 145 mm2 | 237 mm2
12V to 5V DC-DC Regulator Comparison
 | UCC28730-Q1 | UCC28631 | LM5023
Efficiency of Circuit at maximum power (3 amps) | 83.4% | 87.2% | 86%
Efficiency of Circuit at half power (1.5 amps) | 84.5% | 87.8% | 85%
Efficiency of Circuit at .5 amps | 84.2% | 84.5% | 78%
Current Range (at 12 Volts) | Up to 8.33 amps | Up to 5 amps | Up to 3.43 amps
BOM count | 26 | 23 | 37
Recommended Maximum Power | 100W | 60W | 41W
Vout peak to peak at 12 volts and 3 amps output | 75.47 mV | 62.27 mV | 92.04 mV
120V to 12V AC-DC Flyback Controller Comparison

## Slide 26: Constraints
Economic
  IR camera was donated by Air Force Research Base
  All other costs come from out of pocket
Environmental
  Power usage of board
Ethical / Political / Social
  Could be used by military to aid in ending lives
  Our system is only being built to range objects
  Specific applications are entirely up to user
COVID19
  Precautions and limitations to what can be done as group
  Must maintain 6 ft distance between group members when working in person
Time

## Slide 27: standards
IPC-2220 (IPC-2221)
  Follows the IPC-2220 Generic Standards on Printed Board Design
UL 1642
  Follows the UL 1642 Standard for Safety of Lithium Batteries
FLIR Tau 640
  Has use restrictions defined by Sony Semiconductor Solutions Tau2
  Compliant with the following directives and regulations:
    Directive 2002/95/EC, “Restriction of the use of certain Hazardous Substances in electrical and electronic equipment (RoHS)”.
    Directive 2002/96/ EC, “Waste Electrical and Electronic Equipment (WEEE)”.
    Regulation (EC) 1907/2006, “Registration, Evaluation, Authorization and Restriction of Chemicals (REACH)”.
Arducam MINI 12.3MP IMX477 Camera
  Has use restrictions defined by Sony Semiconductor Solutions Corporation (SSS)
Nvidia Jetson Nano
  Compliant with the Federal Communications Commission (FCC)

## Slide 28: Financing
Item Number | Item Type | Model | Price
1 | IR Camera | FLIR Tau w/ 7.5 mm lens | $6000
2 | Variable pinhole | Thorlabs Pinhole Wheel (PHW16) | $496.70
3 | Off-Axis Parabola | Thorlabs Ø2" 90° OAP (MPD239-P01). | $375.50
4 | Stereo Camera Set | 2X | $128.98
5 | Microprocessor | Nvidia Jetson Nano Microprocessor B01 Model | $119.99
6 | Touch Display | Elecom 7” Display | $73.00
7 | Jumper cables and breadboard | - | $20.00
8 | 120V to 12V AC-DC converter circuit |  | $10.00
9 | 12V to 5V DC-DC converter circuit |  | $5.00
10 | 12V battery | - | $10.00
11 | Misc Electrical Components (resistors, capacitors, etc.) | - | $20.00
12 | Checkerboard Material | Aluminum Metal | $0.00
13 | Checkerboard coating | Scotch™ Brand 88 black vinyl electrical tape | $5.00
14 | Blackbody Source | TC-720 thermoelectric temperature controller | $1000.00
15 | Mechanical-Optical components | - | -
Total | - | - | $8264.17

## Slide 29: Current progress
Project part | Progress
Housing | 90%
IR and Visible calibration and alignment | 80%
IR range code | 25%
Visible Camera ranging code | 25%
GUI and Streaming | 0%
Electrical interface and implementation | 60%

## Slide 30: Successes and Difficulties - Computer
Successes
Screen works and takes touch input.
Difficulties
COVID-19 restrictions limiting the team’s ability to work together as a group on the project.
Financial difficulties in acquiring all the required parts.
Short summer semester.
Design and implementation of IR ranging algorithm.
Can access all camera systems and receive input streams.
Successful manipulation of received input through OpenCV.
SSH support allows for programming on the Jetson Nano remotely.
Hard to begin work until the camera systems are in place and calibrated.

## Slide 31: Successes and Difficulties - Power
Successes
Difficulties
Successfully designed a power system to work with the MSPR
Hard to begin work on implementing power system until the rest of the system is finalized
Need to acquire a PCB to begin testing with the system
Selection of components for the power system complete

## Slide 32: Successes and Difficulties – Visible Cameras
Successes
Able to connect to the Jetson Nano and LCD Display to show a visual stream and take images
Difficulties
Must write python scripts to manipulate cameras in any way
Could not guarantee alignment until housing was built and cameras were secured in place

## Slide 33: Successes and Difficulties – IR Camera
Successes
IR stream is being detected by Jetson and can obtain images
Difficulties
Interfacing was an initial issue
Radiometric calibration done
Spatial calibration works with in house checkerboard
Ranging code complexity
Determining object to demonstrate

## Slide 34: Plans for completion
Complete adjustments on housing
  Ensure the cameras can be secured and aligned correctly
  Set up incoming and outgoing wired connections to go through sides of housing
Develop complete software for visual cameras
  Calibrate and create disparity map
  Obtain ranging information
Develop complete software for IR camera
  Calibrate along visual cameras to establish common grid
  Obtain ranging information based on visual camera calculations
Interface display with camera and microprocessor system
Integrate power system

## Slide 35
Hot object: cube/sphere/flat surface/car. Perhaps coat it with common application paint.
How will it move to camera?
RC car, drone, string pulled trolley,
Where?
Inside (long hallway)
Outside (open field)
Or Parking garage