## Slide 1: Multi-sensor Passive ranger (MSPR)
Pedro A. Alvarez Fernandez Photonic Science and Engineering
John Haynes Electrical Engineering
Ilina Sunkara Photonic Science and Engineering
Taylor Whitton Computer Engineering
Group 3:

## Slide 2: Overview/Skip
• overall project block diagram, or system design diagram
• discuss the project design approach and proposed implementation
• discuss and support significant design decisions and significant component decisions
• discuss the impact of realistic design constraints including economic, environmental,
social, political, ethical, health and safety, manufacturability, and sustainability
• Identification and review of related standards
• discuss project successes and difficulties for each project subsystem
• show the project budget and financing to date, and to the end of the project
• clear statement of current progress made by the group (% done by category)
• discuss the group's immediate plans for the successful completion of the project

## Slide 3: Motivation
In military applications, the element of surprise is of vital importance:
  Many range-finding systems utilize detectable means of obtaining the range of a given object.
  These systems rely on “active” methods that require the system to send out some form of signal to detect the distance of the object
    Radar and laser-based range-finding systems
  Ideally, a military adversary should not be aware that they are being tracked, to keep the element of surprise.
General Surveillance purposes (mobile, non-mobile)
  For surveillance we want to receive as much information as possible (range, speed, identification)

## Slide 4: Solution
We present the Multi-Sensor Passive Ranger (MSPR) as our solution to the problem with “active” range finding systems.
  Make use of both stereo and infrared cameras to accurately range the distance of an object.
  No risk of detection since these cameras only absorb input from the environment, rather than producing some form of output.
  The IR band can track in no visible light scenarios and low visibility
  Each system can feed information to each other for accuracy

## Slide 5: Goals and objectives
Produce a system that can accurately find the range of an object in a passive, undetectable manner.
  Other systems, such as radar, transmit radio waves.
    Systems can detect these radio waves, leading them to be detectable.
    This is suboptimal for military applications where one wants to restrict the enemy’s knowledge as much as possible.
A real-time stream of range data that can be used to continuously monitor an object’s position relative to the device.
Cross reference the range data from the IR camera and the stereo system to detect inconsistencies.
Implement a software algorithm that can extract range from IR camera images

## Slide 6: Specifications and requirements
Category | Specification
Range estimation accuracy | ±10% of true value
Range estimation speed | 1 times/sec
Background/Target differentiation | 1 s
Time of arrival estimation (velocity) | ±5% of true value
Disparity image | 15 FPS (480p<)
Object motion tracking | 1 s
Temperature sensitivity | ±5°C or ±5% of reading

## Slide 7: Layout Design: overall
USB Interface

## Slide 8: Block Diagram: overall

## Slide 9: Block Diagram: Electrical

## Slide 10: Software Flowchart

## Slide 11: Software Design
The basic flow of the software system is simple:
  Initialize a connection to each camera
  Iteratively retrieve a frame from each camera
  Run each image through each system’s respective distance calculating algorithm to extract the range of the object
    Nvidia TensorRT with the MobileNet Single Shot Detector v1 to detect object
    Trained on the COCO dataset (common objects in context)
  Output result to GUI, await next frame

## Slide 12: Layout Design: Visual Cameras
Planes pleft and pright
  Represent intersections between the image plane and lines from the camera centers to the object
Since the two triangles shown in the diagram are similar, the ratios of base to height in both should be equivalent.
By taking the center from the distance between the cameras as the origin, the can be represented as positive and as negative
Depth and disparity have an inverse relationship, where the distance Z increases as the disparity decreases

## Slide 13: Ir Ranging Theory (Point source)
To be considered a point source, R needs to be larger than 5X the source diameter, or (1).
A point source is subject the inverse square law which says that irradiance (H) decreases as (1/R^2), with R being the distance away from the point source
The point source radiant intensity is given by (2) and the detected irradiance at the detector is (3)
From this equation we also arrive at the equation for detected power
Diagram inspired from Steve Marlow (AFRL)
Notes: In terms of IR detection, we need to understand that IR imaging is thermal imaging. Every object off a certain amount of radiation depending on how hot it is. So the hotter the object the more thermal radiation and more the IR sensor detects. In this case we take into account a point source where

## Slide 14: Ir Ranging Theory (Extended source)
Apparent surface algorithm:
Good method for moving objects
Initial information required:
  Reference distance needed
  Changes in distance needed
  Useful for Extended Targets
Ranging equation:
Apparent surface algorithm (modified):
Created a model for objects of known size and movement
  Car moving straight towards the camera
  Recorded area above threshold for the car at every slab distance
Car at far and close positions

## Slide 15: Camera alignment and spatial calibration
Scotch™ Brand 88 black vinyl electrical tape
  Emissivity of 0.96 ( for 3-5 um and 8-12 um wavelengths)
Aluminum sheet metal
  Emissivity close to 0

## Slide 16: Sample Calibration pictures taken
Tau 640 with 7.5mm Lens for 4ft high x 5ft wide panel at 200 meters ( taken AFRL).
Scotch™ Brand 88 black vinyl electrical tape
  Emissivity of 0.96 ( for 3-5 um and 8-12 um wavelengths)
Aluminum sheet metal
  Emissivity close to 0

## Slide 17: Part Selection: computer System
 | Nvidia Jetson Nano | Raspberry Pi 8GB | Google Coral Dev Board 1GB
CPU | ARM A57 | Cortex-A72 | Cortex-A53, Cortex M4F
CPU clock rate | 1.43 GHz | 1.5 GHz | 1.3 GHz
CPU cores | 4 | 4 | 4
Coprocessor | - | - | Google Edge TPU
GPU | 128-core Nvidia Maxwell |  | Integrated GC7000 Lite
Network Connectivity | Gigabit Ethernet | Gigabit Ethernet, 802.11ac wireless, Bluetooth | Wi-Fi, Gigabit Ethernet
Storage | MicroSD | MicroSD | MicroSD, 8GB eMMC
RAM | 4 GB 64-bit LPDDR4 | 8 GB 64-bit LPDDR4-3200 SDRAM | 1 GB 64-bit LPDDR4
MIPI Lanes | 1x MIPI CSI-2 DPHY | 1x MIPI CSI, 1x MIPI DSI | 1x MIPI-DSI, 1x MPIP-CSI2
USB Ports | USB 3.0, USB 2.0, Micro-B | 2x USB 3.0, 2x USB 2.0 | Type-C, Type-A 3.0, Micro-B
Display Ports | HDMI, DP | 2x micro-HDMI | HDMI 2.0a
Microprocessor Selection

## Slide 18: Part Selection: Programming Language
 | C | C++ | Python | Rust
Paradigms | Imperative | Imperative, Object Oriented | Imperative, Object Oriented | Imperative, Object Oriented
Compilation | Compiled | Compiled | Interpreted | Compiled
Language Level | Medium | Medium | High | Medium
Libraries | Libccv, TensorFlow, OpenCV | OpenCV, TensorFlow, Pytorch | OpenCV, TensorFlow, PyTorch, SimpleCV, Matplotlib, Keras | OpenCV, TensorFlow, PyTorch
Type System | Strong Statically | Strong Statically | Weak Dynamically | Strong Statically
Safety Design | Unsafe | Unsafe | Safe | Safe
Portability | Highly Portable | Highly Portable | Highly Portable | Highly Portable
Standard Library | Large, Extensive | Large, Extensive | Large, Extensive | Large, Extensive
Programming Language Selection

## Slide 19: Jetson nano
The Jetson Nano was suitable for this project for several reasons:
  Onboard GPU
  Runs on Nvidia’s custom Ubuntu distribution
  2x MIPI ports for stereo vision
  High-performance quad-core processor
  Enough RAM for our use-case
  Cost of $119.99

## Slide 20: Python
Python was chosen as the language of choice for most of the code base for several reasons:
  Large selection of libraries relating to computer vision.
  Rapid development and prototyping.
  Seamless integration with MATLAB and C++ where necessary.
  A memory safe language.
  Supports parallelism to take advantage of the quad-core microprocessor.

## Slide 21: IR camera
Parameter | FLIR A65 25 mm | Tau 2 7.5 mm
FOV | 25° × 20° | 90° x 69°
iFOV | 0.68 mrad | 2.267 mrad
Pixel pitch | 17 μm | 17 µm
Frequency/framerate | 30 Hz | 30/60 Hz (NTSC)
Temp. range | -25°C to +135°C | -25°C to +135°C
Sensitivity | ±5°C (±9°F) | < 30 mK (NETD)
Shock rating | 25 g (IEC 60068-2-27) | 200g shock pulse w/ 11 msec sawtooth
Size | 4.2" × 1.6" × 1.7" | 1.75" x 1.75" x 1.18"
Thermal imager | Focal Plane Array (FPA), Uncooled VOX microbolometer | Uncooled VOX Microbolometer
Connection | Ethernet | 50-pin Hirose / BNC with VPC
Input voltage | 10–30 VDC | 4.0 - 6.0 VDC
Price | $8000 | $6000

## Slide 22: IR Lens selection

## Slide 23: Part Selection: Visible Cameras
 | SainSmart IMX219 Camera Module ¦ 8MP Sensor ¦ 160 Degree FoV | Arducam MINI High-Quality Camera IMX477 HQ Camera Module | Arducam IMX219 Wide Angle Camera Module
Sensor | Sony IMX219 | Sony IMX477 | Sony IMX219
Optical Format | 1/4 inch | 1/2.3” | 1/4 inch
Resolution | 8MP | 12.3MP | 8MP
Interface | 2-lane MIPI | 2-lane MIPI | 2-lane/4-lane MIPI
Frame Rate | 1080p @ 30fps, 720p @ 60 fps and 640 x 480 | 1920×1080 @ 60fps 4032×3040 @ 30fps | 30fps@8MP, 60fps@1080p, 180fps@720p
Focal Length | 3.15mm | 3.9mm | 2.5mm
Aperture | F2.35 | F2.8 | F2.8
Field of View | 160° | 75° (H) | 175(D) x 155(H) x 115(V)
Board Size | 24mm × 25mm | 24mm × 25mm | 36mm x 36 mm
Price (Per Camera) | $29.99 | $64.99 | $54.99

## Slide 24: Part Selection: Power 1
 | TPS56623x | TPSM84624 | TPS543620
Efficiency of Circuit at maximum power (5 amps) | 95.6% | 94.4% | 94.5%
Efficiency of Circuit at half power (2.5 amps) | 96.3% | 94.3% | 95.4%
Efficiency of Circuit at .5 amps | 94.8% | 83.3% | 89.3%
Current Range (at 5 Volts) | Up to 6 amps | Up to 6 amps | Up to 6 amps
BOM count | 15 | 8 | 17
Recommended Maximum Power at 5 volts | 30W | 30W | 30W
Vout peak to peak at 5 volts and 5 amps output | 8.71 mV | 11.9 mV | 8.32 mV
Circuit Footprint | 130 mm2 | 145 mm2 | 237 mm2
12V to 5V DC-DC Regulator Comparison
 | UCC28730-Q1 | UCC28631 | LM5023
Efficiency of Circuit at maximum power (3 amps) | 83.4% | 87.2% | 86%
Efficiency of Circuit at half power (1.5 amps) | 84.5% | 87.8% | 85%
Efficiency of Circuit at .5 amps | 84.2% | 84.5% | 78%
Current Range (at 12 Volts) | Up to 8.33 amps | Up to 5 amps | Up to 3.43 amps
BOM count | 26 | 23 | 37
Recommended Maximum Power | 100W | 60W | 41W
Vout peak to peak at 12 volts and 3 amps output | 75.47 mV | 62.27 mV | 92.04 mV
120V to 12V AC-DC Flyback Controller Comparison

## Slide 25: Power design 1 schematic

## Slide 26: Power design 2

## Slide 27: Constraints
Economic
  IR camera was donated by Air Force Research Labs
  Some optical components given by CREOL
  All other costs come from out of pocket
Environmental
  Power usage of board
Ethical / Political / Social
  Could be used by military purposes
  Our system is only being built to range objects
  Specific applications are entirely up to user
COVID19
  Precautions and limitations to what can be done as group
  Must maintain 6 ft distance between group members when working in person
Time

## Slide 28: standards
IPC-2220 (IPC-2221)
  Follows the IPC-2220 Generic Standards on Printed Board Design
UL 1642
  Follows the UL 1642 Standard for Safety of Lithium Batteries
FLIR Tau 640
  Has use restrictions defined by Sony Semiconductor Solutions Tau2
  Compliant with the following directives and regulations:
    Directive 2002/95/EC, “Restriction of the use of certain Hazardous Substances in electrical and electronic equipment (RoHS)”.
    Directive 2002/96/ EC, “Waste Electrical and Electronic Equipment (WEEE)”.
    Regulation (EC) 1907/2006, “Registration, Evaluation, Authorization and Restriction of Chemicals (REACH)”.
Arducam MINI 12.3MP IMX477 Camera
  Has use restrictions defined by Sony Semiconductor Solutions Corporation (SSS)
Nvidia Jetson Nano
  Compliant with the Federal Communications Commission (FCC)

## Slide 29: Financing
Item Number | Item Type | Model | Price
1 | IR Camera | FLIR Tau w/ 7.5 mm lens | $6000
2 | Variable pinhole | Thorlabs Pinhole Wheel (PHW16) | $496.70
3 | Off-Axis Parabola | Thorlabs Ø2" 90° OAP (MPD239-P01). | $375.50
4 | Stereo Camera Set | 2X | $128.98
5 | Microprocessor | Nvidia Jetson Nano Microprocessor B01 Model | $119.99
6 | Touch Display | Elecom 7” Display | $73.00
7 | Jumper cables and breadboard | - | $20.00
8 | 120V to 12V AC-DC converter circuit |  | $10.00
9 | 12V to 5V DC-DC converter circuit |  | $5.00
10 | 12V battery | - | $10.00
11 | Misc Electrical Components (resistors, capacitors, etc.) | - | $200.00
12 | Checkerboard Material | Aluminum Metal | $0.00
13 | Checkerboard coating | Scotch™ Brand 88 black vinyl electrical tape | $5.00
14 | Blackbody Source | TC-720 thermoelectric temperature controller | $1000.00
15 | Mechanical-Optical components | - | -
Total | - | - | $8264.17
*donated

## Slide 30: Work Distribution
Chart: 
| Stereo Range Finding | IR Range Finding | General Program Control Flow and Object Tracking | Electrical System
Work By Team Member | 25 | 25 | 25 | 25
Team Leadership:
Primary Team Lead: Pedro Alvarez
  IR theory
  Extraction of IR range function
  Project planning
Secondary Team Lead: Taylor Whitton
  Handled source control
  Software architecture

## Slide 31: Results
Stereo system
Able to calculate range given the right object coordinates
Process expensive and slow but requires no object training
Better for closer range
IR system
Can range object up to 100 m as long as object can be detected with specific requirements and some information is known
Harder to detect object through single shot algorithm but good with motion tracking algorithm
Requires extensive radiometric calibrations for best results
Power House
Can output desired voltages although not under load
Unable to integrate onto overall system
Object Tracking
Contour motion detection approach
  Slower but versatile (CPU)
  Prone to errors
Single shot Nvidia TensorRT object detection
  Fastest (Graphics card)
  Precise and extensive

## Slide 32: Successes and Difficulties - Computer
Successes
Project structure allowed quick updates
Difficulties
Libraries were time consuming to configure
Git for version control
Optimized code to use the GPU
Difficulties with object tracking
Optimizing for performance

## Slide 33: Successes and Difficulties - Power
Successes
Difficulties
Power system outputs the required voltages
Drawing too much current from the wall caused by rush in without transformer in front under load
2 different power solutions
Capacitance not high enough for voltage to stay high enough for Jetson Nano under load
Integration into final system.

## Slide 34: Successes and Difficulties – Visible Cameras
Successes
Difficulties
Able to calibrate and rectify images to create disparity map​
Could not guarantee the alignment of the cameras until housing was built and cameras were secured in place
Able to detect objects
Able to determine distance of objects within certain range
Difficult to test with certain objects and in certain lighting conditions

## Slide 35: Successes and Difficulties – IR Camera
Successes
IR image undistortion
Difficulties
Contrast issues (radiometric calibration)
IR object detection and tracking
IR range extraction
Needs ideal conditions to function properly

## Slide 36: Future work and expansion possibilities
How do we improve?
Stronger processing power
  Can achieve better detection due to more detail and speed
  More ranging algorithms able to run simultaneously for more accuracy and consistency
  Extensive object training and software optimization
Is there a future for this technology?
Passive ranging is of great interest
  Vital for surveillance sensor hubs
  Race for autonomous technology (such as cars)
  Quantum computing opens new doors