## Slide 1: Electric Blind
Group 13
Adedoyin Adepegba – Computer and Electrical Engineering
Joshua Forrest – Electrical Engineering
Ryan Meinke – Computer Engineering
Tien Tran – Electrical Engineering

## Slide 2: Project Idea
Simple Idea of automating the process of interacting with window blinds
Smart blind:
  to replace conventional blinds
  To provide energy saving benefits in addition to environmental advantages

## Slide 3: Project Description
Motivation
  Cost-efficient and energy saving product due to team member’s interests
  Get teamwork experience before proceeding into workplace
Goals and Objectives
  Remove conventional blinds and replace with smart ones
  Meet the requirement specifications (engineering and marketing specifications)
  Develop great teamwork
  Produce a successful project

## Slide 4: Requirement Specifications
Engineering Specifications
  Power Consumption < 20 Watts
  Accuracy <= 150cm
  Time of Response <= 10 seconds
  Idle Time <= 5 minutes
  PCB Board Dimension <= 4’’ x 4’’
  Activation methods
    Switch
    Different sensors like PIR sensor
    Digital application interface

## Slide 5: Requirement Specifications
Marketing Specifications
  High Safety
  Low Cost
  High Reliability
  Ease of Use
  High and efficient performance
  Low Power Consumption

## Slide 6: Research – Existing Projects and Products
Dream Glass (Smart Blinds)
Sunshade (SD Project 2019)

## Slide 7: Overall Project Design

## Slide 8: Microcontroller Unit Comparison Table
MICROCONTROLLER UNIT | ESP32-WROOM32 | PIC16f877A-I/P 1243J SA | MSP430G2452
Processor | Dual-core processor | 1-core processor | 1-core processor
Architecture | 32-bit RISC | 8-bit RISC | 8-bit RISC
Clock Frequency | 240MHz | 20MHz | 12kHz
Flash Memory | 4K | 8K | 8K
Operating Voltage/Power Supply | 3.0V – 3.6V | 2.0V – 5.5V | 1.8V – 3.6V
Operating Current | 80mA | 250mA – 300mA | 220uA at 1MHz
I/O Pins | 32 General Purpose I/O Pins | 5 I/O Ports | 16 capacitive-touch enabled I/O Ports
Built-in Modules/Peripherals | 2.4GHz Wi-Fi, Bluetooth BLE, SPI, DAC, I2C, Temperature Sensor, ADC, UART, USB | PWM, ADC, USART, I2C | ADC, Serial Onboarding Programming, USI supporting SPI and I2C
Integrated Development Environment | Arduino | Circuit Wizard Software | Energia

## Slide 9: ESP32-WROOM
ESP32-WROOM Chip
TTGO-Koala with ESP32-WROOM and 4K Flash memory

## Slide 10: Hardware

## Slide 11: Proximity Sensing Technologies

## Slide 12
 | Inductive | Capacitive | Magnetic | Ultrasonic | Photoelectric
Effective Range | 5-10 mm | 25 mm | 70 mm | 4m | 12m
Detectable | Metallic object | Metallic and non-metallic object, fluid | Metallic object | Object with simple surface | Metallic and non-metallic, object radiates wavelength
Application | Industrial | Industrial | Industrial | Industrial/Residential | Industrial/Residential

## Slide 13: Different Modes for Photoelectric Proximity Sensing Technology

## Slide 14: PIR Sensor Selections
 | Dimension (mm) | Range (m) | Input Voltage (V) | Output Voltage (V) | Price (US Dollars) | Repeatable Trigger Mode | Range and Sensitivity Adjustable
MCM 287-18001 | 24.03 x 32.34 x 24.66 | 7 | 5 - 20 | 3.3 V | 2.99 | Y | Y
HC-SR505 | 40x 10 x 13 | 3 | 4.5 - 20 | 0 - 3 | 3.23 | Y | N
Onyehn PIR | Unknown | 5 | 2.7 – 3.3 | Unknown | 4 | N | N

## Slide 15: Voltage Regulator

## Slide 16
 | Linear Regulator | Switching Regulator
Efficiency | Low (around 30-40%) | High (can be up to 90%)
Complexity | Low | High
Ripple/Noise | Low | High (Due to switching sequence)
Cost | Low | High
Vin Range | Narrow | Wide
Vout | Not adjustable | Wide adjustable range

## Slide 17: Voltage Regulator Selections
 | XRP7659 | LM2575-ADJ
Input Range | 4.5 V – 18 V | 1.2 V – 37 V
Output Voltage | 3.3, 5, 12 V | 3.3, 5, 12 V
Output Current | 1.5 A | 1 A
Efficiency | Up to 92 % | 87.5 %
Operating Switching Frequency | 1.4 MHz | 52 kHz
Dimension | 2.82 x 2.65 x 1.45 mm (with distance between 2 pins is 0.95 mm) | 10.67 x 4.83 x 30.84 mm (with distance between 2 pins is 1.7 mm)

## Slide 18: Transformer Selection

## Slide 19: Tamura 3FD-424

## Slide 20: Power Delivery

## Slide 21: Schematic
Xformer
5V Regulator
3.3V Regulator
SSR
Rectifier

## Slide 22: Power Delivery
Components | Operating Voltage (V) | Operating Current (mA) | Power Consumption (W)
PIR Sensor | 5.3 | 39.1 | 0.207
MCU | 3.3 | 250 | 0.825
Relay | 1.25 | 1.5 | 0.0019
Light Sensor | 5.3 | 34.8 | 0.184
Temperature Sensor | 5.3 | 20 | 0.106
PDLC Film | 65.6 | 0.069 | 4.5
Total Power Consumption |  |  | 5.8239

## Slide 23: PCB Design & Testing

## Slide 24: PCB Progression

## Slide 25
Xformer
5V Regulator
ESP32 WROOM
3.3V Regulator
5V pins
3.3V pins
SSD

## Slide 26: Testing
PDLC
PDLC
65.6 V AC
6.8 mA AC
Light Sensor
34.8 mA DC

## Slide 27: Energy Savings

## Slide 28: Department of energy recommendations
Our system has a SHGC of 0.1!

## Slide 29: Potential Uses

## Slide 30: Implementation in Residential/Corporate Spaces

## Slide 31: Software
By Ryan Meinke

## Slide 32: Arduino
Open Source Platform
Large Community Support
Abstraction

## Slide 33: Software Jobs
Control Window State
Interpret Inputs
Provide Interfaces

## Slide 34: Software Job : Control Window State
Simple
  on/off

## Slide 35: Software Job : Interpret Inputs
Continually Check for Inputs
Two classes of Inputs
Sensors
  Proximity
  Light
  Temperature
Network Communication
  UDP on IPv4
  Bluetooth
  Uses Custom protocol for both

## Slide 36: Sensors
Continually get value
Operates off a threshold

## Slide 37: Sensor Threshold
Input occurs when value passes input
Two types of inputs
  Value goes above threshold
  Value goes below threshold
Each input has a specific action
  Turn Window On
  Turn Window Off
  Do nothing
Threshold, actions, and enabled status configurable

## Slide 38: Custom protocol Advantages
Standardized IO
Streamline Adding Functionality
Keep things clean
UDP
  Multicast functionality

## Slide 39: Custom protocol

## Slide 40: Software Jobs : Provide Interfaces
3 Different Interfaces
  Website
  Computer Desktop App
  Phone App

## Slide 41: Website
Apache with PHP Backend
Benefits
  Available to many devices
  Available to many users
Drawbacks
  Requires Web Server
  Requires Window to be on computer network

## Slide 42: Computer App
Python3
Benefits
  Ease of use with computer
Drawbacks
  Has to use a desktop computer
  Requires Window to be on computer network
Admin Console

## Slide 43: Phone App
Android app using Kotlin
Benefits
  Widespread use of Android Phones
  Configure Network Credentials
  No Configuration needed to connect
Downsides
  Physical Proximity
  Must have Android Phone (can be remediated)

## Slide 44: Administrative Content

## Slide 45: Budget
Components | Part | Initial Budget | Quantity Used | Final Cost
MCU | ESP32-WROOM32 | 50 | 1 | 3.80
Components (Resistors, Capacitors, Schottky diode, inductors. Male pin header, jumpers etc.) |  | 70 | Multiple | 15.76
Relays | AQZ205 | 15 | 5 | 57.10
Light Sensor |  | 1.50 | 1 | 1.50
Temperature Sensor | DS18B20 | 150 | 1 | 5.99
Blind | PDLC Film | 150 | 1 | 129.67
Transformer | Tamura 3FD-424 | 10.00 | 1 | 10.00
Full Bridge Rectifier | MB8S-G | 0.325 | 2 | 0.65
Printed Circuit Board |  | 150 | 1 | 2.70
Voltage Regulator | LM2575 |  | 2 | 7.76
PIR Sensor | MCM287 | 15 | 1 | 2.99
Window Frame |  |  | 1 | 20
Total Cost |  | <$600 |  | $257.92

## Slide 46: Work Distribution
Project Aspect | Power Delivery and Circuit Assembly | PCB Design and Testing | Software | Microcontroller Unit and Administrative Content
Adedoyin Adepegba |  |  |  | Primary
Joshua Forrest |  | Primary |  | 
Ryan Meinke |  |  | Primary | 
Tien Tran | Primary |  |  | 

## Slide 47: Challenges
Time Constraints
Student-funded

## Slide 48: Conclusion