## Slide 1: Group Members: Amidtzalee Laguna Mundo Electrical Engineering Jean Seda Computer Engineering Majed Halawa Electrical Engineering Jordan Sole Computer Engineering
Hydroponic System
Senior Design Summer 2021
Group 23
Notes: Amidtzalee Laguna Mundo

## Slide 2: Project Motivation
There are many issues with conventional farming
- The need of large land spaces
- Climate can damage
- Rodent and bug infestation
- Waste a lot of water
- Help lower the amount of waste that current conventional farming creates
Notes: Amidtzalee Laguna Mundo

## Slide 3: Solution
Hydroponic systems can solve the issues with conventional farming:
- They require less space
- They use less water
- They can be set up indoors or outdoors
- User friendly
Notes: Amidtzalee Laguna Mundo

## Slide 4: Project Goals & Objectives
We wanted to make our system low cost
Transferrable
Low power consumption
Small in size
Simple to use
Notes: Amidtzalee Laguna Mundo

## Slide 5: Hydroponic Systems out in the Market
Wick System
Dynamic Roots Floating Technique
Ebb and Flow
Drip System
Nutrient Film Technology
Aeroponics System
Vertical Systems
Notes: Amidtzalee Laguna Mundo

## Slide 6: Requirements and Specs of Hydroponic System:
Requirement Specification | 
1. ½ gallon per minute | 
2. 12 inches of water level measure. | 
3. Range from 5.0 and 7.0 | 
4. Data transfer rate of every 1 minute | 
5. Led array is able to turn on and off after every 14 hours. | 
6. The lights need to provide up to 80,000 Lux | 
7. Power Input voltage ranges from 3.3 to 5 | 
8. Range of 50ft of wireless connection | 
Notes: This is done so there is appropriate water flow, and the nutrients can properly reach the plants. We measured this by calculating how long it takes to fill a container.
The tank should be filled with water at 12 inches at all times. It is done to ensure the plants are getting the correct amount of water. This is calculated by measuring the water, and monitoring it with our water level sensor.
The water needs to stay on this pH level for the plants to grow healthy and can better absorb the nutrients. The pH level was measured by using our Ph level sensor.
To keep the hydroponics monitored the updates will be send every 800 milliseconds to ensure that the data is always updated.
The lights should be on for 14 hours out of the day, and they should be turned off automatically
Exceeding the Lux of 80,000 can damage the plants, so we don’t want to exceed it.
The microcontroller requirements and sensors require 3.3 and 5 voltage to function properly. The voltage was measure using a voltmeter.
The communication module should have a reasonable range to access wireless internet connection. This requirement was tested by moving away from the router since the webserver functions by connecting to the router.

## Slide 7: ESP32-DEV-Kit
The microcontroller was chosen based on Three characteristics:
Compatibility | Capability | Reliability
32 I/O pins | Memory Size | IEEE 802.11 Standard
IDE | Data Rate | Flash Encryption
Libraries | Wireless, Web Server | WPA/WPA2
Notes: ESP8266, the predecessor of produced by Espressif Systems in Shanghai, China, attracted many professionals because of the low cost. Later, Westerners translated the documentation into English. The integrated WIFI module drew the group to this microcontroller. This WIFI module would cut time and add simplicity to the project. The downside of this microcontroller is that it contains only one analog input. It is possible to increase the number of analog inputs by using an analog multiplexer.
Compatibility
It is essential to consider the microcontroller aspects that will make our workflow more manageable. That is compatibility between the device's hardware and software, including sensors, communication categories, programming platforms, and programming languages.
the interface category is crucial to consider; it includes direct digital, direct analog, and protocol-based communications.
ESP32
3.0V - 3.6V
WIFI, UART, SPI, I2C
In 2020, Espressif introduced a new chip, ESP32, and it is pin-compatible with ESP8622. The ESP32 also includes the WIFI MODULE, and it has much better capabilities than its predecessor. However, we had second thoughts about choosing this microcontroller since it is not as widely used as ESP8266 due to being relatively new. The scarcity of information could limit the research or tutorials public on the internet, imposing a more significant learning curve on the group. This microcontroller made it to the list due to its increasing popularity.
Capability
The flash memory that the ESP32 includes ranges from 2Mib to 4Mib, and some do not have any in the chip. However, if the board has the memory mounted, then it comes from 2Mib to 8Mib. It is more than enough for our purposes. The RAM of ESP32 is 520 KiB SRAM. The SRAM memory consumes less power, and it is much faster than dynamic memory. The microcontroller is either single-core or dual-core. It can operate from 160 or 240MHz, and It includes an ultra-low-power (ULP) co-processor.
Reliability
The ESP32 can be a power-hungry device if it's not set on a low power mode. There are five configurable power modes. They are active, modem sleep, light sleep, deep sleep, and hibernation modes.

## Slide 8: Microcontroller: ESP32-DEV
Manufacturer | Espressif Systems
Part Number | ESP32­-WROOM­-32D
Memory Size | 420kB ROM, 536 kB SRAM
Data Rate | 150Mbps
Voltage Supply | 2.7V ~ 3.6V
Number I/O Pins | 38
Cost | 4.08

## Slide 9: Component’s Code
TDS Sensor | Ph Sensor | Water Level sensor
Collects the measurements from the probe into an array | The pH sensor works by collecting the readings into an array similar as the tds sensor. | The water level sensor collects values from 0 to 2000 depending on the water level.
It samples every 40 milliseconds, and it prints the value every 800 milliseconds. | The readings are sampled every 20 milliseconds and it prints every 800 milliseconds. The average of the array is used for increase precision. | These values were used as a guideline to predict the water level of the water. The levels are high, medium, or low.
The average voltage, compensation coefficient and compensation voltage are calculated. Finally these values are used to convert voltage value to tds value. | The voltage value is then converted to pHValue. Then that information is converted to pH value by using the formula pHValue = 3.5*voltage+Offset; | 
Notes: TDS sensor
to calculate the median of the calculation for increase precision.
Very easy to the user's eyes so that there is no confusion, and we get straight to the point with the sensor data.
When it comes to software, we had to choose what kind of language we would use. Since we have two computer engineers in our group, it came down to what we thought was fitter and more comfortable. Java is a preferred language amongst the group. Still, since we were going to be dealing with an Arduino, we thought it would be easiest to program in C. Also, this would be the better language since the coding environment is best for these types of embedded systems.
When it comes to our software design, it will revolve around writing code to interpret the different types of data being retrieved by the various sensors. The data being retrieved will then be saved and sent out via Wi-Fi to an online server that will then display vital information about the plant's health.
The code will be approximately 1,000 lines code.
We chose C language because it is still very relevant today, and especially in the embedded coding space, and one of the oldest. The low-level aspect of C makes it very desirable for coding embedded systems. It has low-level access to memory, a loose data typing policy, and smooth porting of embedded programs, in addition to being very fast when we compare it to other programming languages. A big community of coders backing this language provides excellent support for embedded systems programming. Also, the familiarity the team has with this language makes it perfect for this project. We all have worked with C before.

## Slide 10: ESP32 Webserver
One of the cool features of ESP32 is the integrated web server. Me and our team has been using this to display the information obtained using HTML code.
Communicates through a protocol HTTP.
Requests are sent to the server and responses are received.
The ESP32 is connected to the Wi-Fi router as a client and can access the internet through the router.
An IP address is created to show the website created.
Notes: My teammate decided to go another approach to the webserver. However I feel like the webserver of the ESP32 is such a great feature that it should still be highlighted, so I decided to create the webserver and make it display the value reading from the sensors. It is a very simple html design nothing fancy due to the time constraints and other responsibilities, and the only intention was to showcase this great feature of esp32.

## Slide 11: PCB Design
Notes: Amidtzalee Laguna Mundo

## Slide 12: Alternative PCB designs
Notes: The design on the left it has a voltage level converter from 5V to 3.3V to provide to the microcontroller. The components all use 5V so a connection is left to power the components as well. It does not include a USB port because it is meant to be program through a USB to UART programmer.
The design on the right is very similar to the one on the left but the board is powered through an USB. It has a CP2102 USB to UART bridge that provides a complete plug and play interface solution, and it is USB 2.0 compliant.
It didnt make it to production due to the high cost spent in the other PCB’s. We wanted to keep the cost of the project as lowest as posible. However one of this board is on it’s way here that I will be working on my free time for fun.

## Slide 13: PCB Design: Board Specks
The PCB Board Contains the Following Connections:
- Microcontroller Chip: ESP32-DEV-Kit
- Power Supply Circuit
- TDS Water Quality Sensor
- Liquid Level Sensor
- pH Sensor
- LED Strip
Notes: Majed Halawa

## Slide 14: PBC Design: ESP32-DEV
Microcontroller schematic
On the right side:
- Water Level Sensor Output
- pH Sensor Output
- Temp output from Pin 1 for the pH Sensor
- ON/OFF LED connection
- Ground connections
- TDS Output
On the left side:
- Programming Port
Notes: Jordan Sole

## Slide 15: PCB Design: Power Supply Circuit
Power Supply Module for Arduino Board Solderless Breadboard
Input Voltage : DC 6.5-12V;Output Voltage : DC 3.3V 5V
Needed to power up several of the components such as the lights
Notes: Majed Halawa

## Slide 16: PCB Design: Power Circuit
The ESP32 chip is connected to the 3.3V power source on the power circuit.
The power circuit has two types of different input voltage connection. One is 12V and the other (micro USB) is 5V.
The lights will be connected to 5V and the rest of the sensors will be connected to 3.3V.
Notes: Majed Halawa

## Slide 17: Compatible ISE Sensors
ISE stands for Ion-Selective Electrode
It converts the activity of a specific Ion dissolved in a solution into electrical potential

## Slide 18: PCB Design: TDS Water Quality Sensor
TDS Indicates how many milligrams of dissolved solids are dissolved in 1 liter of water.
Wide supply voltage of 3.3~5.5V
Transfer data to a control system
It can be used for water quality testing in the field of domestic water and hydroponics.
Notes: Majed Halawa

## Slide 19: PCB Design: TDS Water Quality Sensor
TDS has 3 pins
Pin 1 connects to the microcontroller as the output
Pin 2 connects to the 3.3V source
Pin 3 connects to the ground
Notes: Majed Halawa

## Slide 20: Possible Choices for Water Level Sensors
The red option gives us specific levels of water (High, Medium, Low)
The red option is cheaper

## Slide 21: Water Level Sensor
Operating Voltage: DC 3-5V
Operating Current: 20 mA
Operating Temperature: 10° - 30°
Sensor Type: Analog
Notes: Majed Halawa

## Slide 22: PCB Design: Liquid Level Sensor
Pins 2 & 3 are the most important.
The second Pin is connected to ground .
The third Pin is connected to a 560Ω Resistor and then to a 3.3V power source.
The first and fourth Pins are for temperature control which will not be used in our project.
Notes: Majed Halawa

## Slide 23: Possible Choices for pH Sensors
Three Types of pH sensors
Cheapest option is the Laboratory Analog pH Sensor

## Slide 24: pH Sensor
Liquid PH0-14 Value Detect Sensor Module + PH Electrode Probe BNC for Arduino
Heating voltage: 5 ± 0.2V (AC · DC)
Working current: 5-10mA
Detectable concentration range: PH0-14
Detection Temperature range: 0-80 ℃
Humidity: 95% RH (nominal humidity 65% RH)
Output: analog voltage signal output
Notes: Majed Halawa

## Slide 25: PCB Design: pH Sensor
This module comes with 6 pins
Pin 1 & Pin 3 are both connected to the ESP32 Chip
Pin 4 & Pin 5 are connected to the ground
Pin 6 is connected to the 5V power source circuit, this sensor needs a 5V power source.
Notes: Majed Halawa

## Slide 26: Possible Choices for LED’s
◤

## Slide 27: LED Ring
WS2812B 5050 RGB LED Ring Lamp Light
Power Source: DC 5V
Working environment: -20℃to +50℃
Color: 24-bit full color
Easy to install on the structure
Notes: Amidtzalee Laguna Mundo

## Slide 28: PCB Design: LED Ring
The lights have 3 pins which are connected to the microcontroller
Pin 1 is connected to the 5V power source
Pin 2 is connected a Logic Level Converter Circuit
Pin 3 is connected to a transistor then it connects to the microcontroller through a 1K resistor, and then to ground
Notes: Amidtzalee Laguna Mundo

## Slide 29: Programming Port

## Slide 30: PCB Design
Notes: Majed Halawa

## Slide 31: Wireless Communication
WIFI 802.11 b/g/n integrated on the chip (802.11n @ 2.4 GHz up to 150 Mbit/s), and Bluetooth v4.2 BR/EDR and BLE
In the project we will only use the WIFI capabilities like
  over the air updates
  easy server setup

## Slide 32: Why we want website application?
When creating the smart hydroponic system we wanted to create a system where the vital information can be displayed remotely, information such as
  pH sensor data readings
  Temperature of the system
  Water level readings
  Whether the lights are on or off
We are also interested in the user being able to control certain components remotely as well, such as switching of the lights etc.

## Slide 33: Hosting Services
A specification of our system is allowing the user to monitor their hydroponic system from anywhere in the world.
To do so we had to purchase a online server so we would have an IP address that we can connect to a domain name so it can be accessed remotely
To do this we went with BlueHost since it was one of the more affordable options and included WordPress.

## Slide 34: Website Application
Will use WordPress since it is highly recommended for website design and functionality.
Website will display the different sensor readings and can send feedback back to the controller in order to adjust components.
Will be using the elementor extension to wordpress

## Slide 35: WordPress Elementor
Wordpress elementor is top leading in building websites
Elementor is very easy to use and uses a drag and drop method to build the site
Elementor has included themes that will make the website look sleek and clean

## Slide 36: Data Storage
When using the hydroponic garden we needed somewhere to store the data being received by the sensors.
We would need some sort of database to store all the information and we choose MySQL database.

## Slide 37: MySQL Database
We choose MySQL as our database for its ease of functionality and popularity.
Have seen it being used in other classes
Easy direct access with PHP code in order to display it to a website via HTML.

## Slide 38: MySQL Database Obstacles
Main obstacles of using the MySQL database was sending information from the microcontroller to the database.
  Due to Covid this was a major issue since in person meeting were very limited
Testing to ensure the correct sensor data was properly being transferred was difficult to debug.

## Slide 39: Website Flowchart

## Slide 40: Block Diagram
Notes: This is the way the project was divided. We needed to organize responsibilities quick and efficiently. The assigned blocks were decided based on the students strong backgrounds for example the computer engineers took the software part of the project, and electrical engineers took the hardware. However we all have worked in a little bit of everything when troubleshooting. We also assigned a secondary task.

## Slide 41: Work Distribution
Primary Tasks | Individual
PCB Design | Majed Halawa / Jean Seda
Components Code | Jean Seda
Prototype Breadboard Connections | Amidtzalee Laguna Mundo / Jean Seda
Building Structure | Amidtzalee Laguna Mundo
ESP32 Server - Website & Data Analysis | Jordan Sole / Jean Seda

## Slide 42: Budget
Equipment | Price
Hydroponic Body | 80
PCB | 15.3
Modules for PCB | 38
LED Strip | 16.99
Microcontroller | 10.39
pH Sensor | 13.53
TDS Sensor | 20.56
Water Level Sensor | 39.95
Seedlings | 59.96
Water Pump | 15.99
Power Supply | 6.99
Total | 317.66

## Slide 43: QUESTIONS???
◤
Notes: This concludes our CDR presentation if there are any questions we welcome them in class.