## Slide 1: GROUP 13 OSCAR CEDENO CESAR ROMERO CAMILO ROMERO
E-SKATE

## Slide 2: Goals and Objectives
Create a skateboard with simple user feedback
Create a fast transportation method inside a college campus
User will control the E-Skate by a wireless controller
Portable and easy to charge
Low cost

## Slide 4: E-SKATE OVERVIEW
BATTERY + ELECTRONICS
DC MOTOR
LCD
WIRELESS
REMOTE CONTROL
(Used while
E-Skating)

## Slide 5: Specifications
$500 Budget for Project
Under 15 Pounds
3 Hours Battery Life
10 Feet Range for Wireless Communication
Cruising in Clear Weather Conditions
12 V Battery System
5A per Battery
100 Watts DC Motor

## Slide 6: Design
TRANSMITTER
ATmega 328P
RECEIVER
ATmega 328P
DC Motor
BATTERY
ACCELEROMETER
ATmega 328P
MOTOR ENCODER
GPS
LCD
BATTERY SENSOR
POTENTIOMETER
WIRELESS CONTROL
MOTOR CONTROL
DATA CONTROL

## Slide 7: ATMEGA 328P
Max operating frequency of 20 MHz
Serial Communications SPI, RS232, I2C
Operating Voltage: 1.8 to 5.5 V
Internal Temperature Sensor
32 Kbytes Flash Memory
23 I/O Pins
6 Channel 10 bit ADC
6 PMW Channels
Price: $4.87 / Free

## Slide 8: ARDUINO DEVELOPMENT BOARD
16 MHZ Clock Speed
5V Operating Voltage
7-12V Input Voltage
14 Digital I/O Pins
6 Channel 10 bit ADC
6 Pins provide PWM output
40 mA DC Current per I/O Pin
Programmed with Arduino Software
Price: ~$30.00

## Slide 9: WIRELESS CONTROL
ATmega 328P
RECEIVER
TRANSMITTER
POTENTIOMETER

## Slide 10: RF LINK TRANSMITTER WRL-08945
315 MHz Transmitter Frequency
500 Feet Range
2400 or 4800bps Transfer Rate
Operational voltage 1.5-12 V
Operational Temperature of -20 to 85 C
Price: $ 1.95

## Slide 11: RF LINK RECEIVER WRL-10533
Frequency Range: 315MHz
Modulate Mode: ASK (Amplitude Shift Keying)
Date Rate: 4800 bps
Supply Voltage: 5V
Price: $ 4.95

## Slide 12: HANDS ON REMOTE CONTROL
9V BATTERY
ON/OFF SWITCH
SIGNAL SWITCH
ATMEGA 328 + TRANSMITTER + POTENTIOMETER

## Slide 13: CONNECTING TRANSMITTER TO ATMEGA 328P

## Slide 14: CONNECTING RECEIVER TO ATMEGA 328P

## Slide 15: DATA CONTROL
ACCELEROMETER
ATmega 328P
MOTOR ENCODER
GPS
LCD
BATTERY SENSOR

## Slide 16: GPS Module

## Slide 17: EM-406a Module
Pin Layout
20-Channel Receiver
10m Positional Accuracy / 5m with WAAS
Hot Start : 1s
Warm Start : 38s
Cold Start : 42s
70mA at 4.5-6.5V
Outputs NMEA 0183 and SiRF binary protocol
Small foot print : 30mm x 30mm x 10.5mm
Built-in LED status indicator
6-pin interface cable included
Price : $40.00

## Slide 18: NMEA 0183 Protocol
Some Protocol Descriptions:
Message | Description
GGA | Time, Position, Fix Type
GSA | GPS receiver operating mode, Satellite used in position solution. DOP values
GSV | The number of GPS satellites in view, satellite ID number, Elevation Azimuth, SNR values.
RMC | Time, Date, Position, Course, Speed
$GPGSV,3,1,12,20,00,000,,10,00,000,,25,00,000,,27,00,000,*79
$GP which start the message all the time
Next would be the message which in this case is the GSV, which is described in Table
Each data element is separated by a comma, and the data elements are terminated by the * character
There is a 8-bit XOR of each character between $ and * to form the checksum
Finally the last two characters are hexadecimal representation of the calculated checksum.

## Slide 19: GPS Schematic for the Arduino

## Slide 20: Serial Monitor of the Arduino
EM-406a is sending data to the arduino development board and it is displayed on the computer screen.

## Slide 21
GPS is connected hardware to the arduino board and it send data to the computer.
GPS And Arduino And LCD

## Slide 22: Data Display Microcontroller
Microcontroller will display data to LCD
Will take input from sensors and GPS
  Sensors include Accelerometer, Motor Encoder and a Battery Sensor
Separate unit from microcontroller which controls motor

## Slide 23
Data Microcontroller
GPS
LCD
Accelerometer
Battery Sensor
Motor Encoder

## Slide 24: Programming
Programming through Arduino which is similar C++
Use libraries Wire.h, inttypes.h, LCDi2cNHD.h, TinyGPS.h, NewSoftSerial.h
With these create a new LCD instance, GPS instance, and a Serial Connection Instance
Able to call functions to get data from GPS and to print to LCD

## Slide 25: Data Microcontroller Flowchart
Setup Variables
Check GPS, Sensors
Start Devices
Read from Sensors and GPS
Send Welcome
to LCD
Make Calculation
Output data to LCD
Go back to read Sensor and GPS

## Slide 26: Software UML for Data Microcontroller

## Slide 27: LCD
 | Lumex LCM-S01604DSF | Newhaven 0420D3ZFLGBW | Matrix Orbital LK204-25
Display Format | 16 x 4 | 20 x 4 | 20 x 4
Connection Type | Parallel | I2C, RS232, and SPI | I2C, RS232, and TTL
LCD Type | Transflective | Transflective | Transmissive
Voltage | 5 V | 5 V | 5 V
Outline Area | 8.7 cm x 6 cm x 1.27 cm | 9.8 cm x 6 cm x 1.35 cm | 9.8 cm x 6 cm x 2.75 cm
Price | $29.73 | $24.90 | $69.75

## Slide 28: Newhaven LCD
Display data related to E-Skate state
Distance Traveled
GPS Location
Velocity
Time Used
Battery Left
Motor RPM
Acceleration

## Slide 29: Newhaven LCD

## Slide 30
LCD Built In Character Table
Has to be programmed into microcontroller

## Slide 31: LCD Programming
Arduino playground LCDi2cNHD library
Implements Arduino Wire Library
Connects to microcontroller through the I2C protocol
  Only needs 2 wires to connect to the microcontroller
Allows for easier control of LCD

## Slide 32: Accelerometer
Records acceleration data
Can provide data on how hard E-Skate hits a rock or a crack
Easily implemented into the Arduino Environment

## Slide 33: Accelerometer
 | Dimension Engineering DE-ACCM2G2 | Freescale MMA7361L Accelerometer
Axis | 2 | 3
Operation Voltage | 3.5V-15V | 2.2V-3.6V
Selectable g Sensitivity | No | Yes
Output Buffers | Yes | No
Size | 1cm x 1.8 cm x .8cm | 1 cm X 1.27 cm
Price | $23.00 | $12.00

## Slide 34: DE-ACCM2G2 Accelerometer
Dual axis ±2g sense range
660mV/g sensitivity
500Hz bandwidth
Operating voltage 3.5V to 15V
Standard DIP-14 form factor
Draws under 2mA
<4% typical 0g bias deviation
from 1.65V which is Vcc/2

## Slide 35: DE-ACCM2G2 Accelerometer

## Slide 36: Battery Sensor
Allows for knowledge of how much battery is left based on how much voltage is provided by battery
Range of 10.5 - 13V
Voltage divider lowers battery voltage to a readable voltage by the microcontroller
Unity Gain Buffer used for controlling current, has low current going into the microcontroller

## Slide 37: Battery Sensor
=

## Slide 38: MOTOR CONTROL
RECEIVER
ATmega 328P
DC Motor
BATTERY

## Slide 39: POWER SYSTEM

## Slide 40: Battery RT 1250
Cells Per unit : 6
Voltages Per Unit : 12 V
Capacity: 5.0Ah at 20hr-rate to 1.75 V
Weight : Approx. 1.60 Kg
Maximum Discharge Current: 50 A (5 sec)
Internal Resistance: Approx. 35 mΩ Operating Temperature Range:
  Discharge: -20 - 60C
  Charge: 0 -50C
  Storage: -20 - 60C
Recommended Maximum Charging: 1.5A
Price: $17.99

## Slide 41: Motor MY6812A
12Volts DC 100W Drive Motor
3400 RPM
It is heavy duty and used by companies for electric scooters
Price: $19.50

## Slide 42: KY-05036S AC Charger
Leadman KY-05036S-12 AC power Adapter 5V-12V
Input 100Volt~240 Volts / 1A
The Dimensions are 125x48x31mm
Output 12 Volt / 1.5A
Price: $25

## Slide 43: JTN1S-TMP-F-DC12V Relay
Relay Type: General Purpose Contact Rating (Current): 20A
Coil Current: 66.7mA
Coil Voltage: 12VDC
Turn On Voltage (Max): 9 VDC
Turn Off Voltage (Min): 1.2 VDC
Quick Connect
  Coil Power: 800 mW
  Coil Resistance: 180 Ohms
Price: $4.00

## Slide 44: Design

## Slide 45: COMPLETED SO FAR
Chart: Completed
| Research | Parts Acq. | Prototype | Parts-Test | Software | Design
Completed | 0.9 | 0.7 | 0.35 | 0.5 | 0.2 | 0.32

## Slide 46: BUDGET SPENT
CURRENT SPENDING | 
ITEM | AMOUNT
Battery/ Charger | $65
GPS | $40
RC Unit | $7
Skateboard | Donated
Motor | $20
Electronics | $20
PCB | 
LCD Display | $25
TOTAL | $ 177
REMAINING BUDGET | $ 323

## Slide 47: WORK DISTRIBUTION
Chart: 
| RC | MicroController | GPS | Motor | LCD | Software
Cesar | 0.5 | 0.3 | 0.2 | 0.4 | 0.3 | 0.25
Oscar | 0.35 | 0.2 | 0.55 | 0.4 | 0.25 | 0.3
Camilo | 0.15 | 0.5 | 0.25 | 0.2 | 0.45 | 0.45

## Slide 48: Remaining Tasks And Problems
PCB Design in Eagle CAD
Testing Motor
GPS Velocity is off
Testing Receiver and Transmitter
Finish Programming
Power Regulator and Potentiometer to be Designed

## Slide 49: Lets Start E-Skating!
Questions?