## Slide 1: Smart Umbrella
Group 9
Derek Workman EE
Eugene Mcdonald EE
Nicholas Van Nice CpE

## Slide 2: Motivation
Work with photovoltaics
Design a unique solar panel tracking application
Implementation of multiple controlled systems into a single design
- Lighting control
- Motor control
- Sensor control

## Slide 3: Goals and Objectives
Light weight means of collecting solar energy using solar panels.
Maximize efficiency from the solar panels by designing, building, and coding a Maximum Power Point Tracking synchronous switching regulator with a greater than 90% efficiency.
Design a solar panel tracking system
Learn how to design and create a PCB

## Slide 4: Project Specifications
Specification | Explanation
Lightweight Design | Less than 12 pounds total weight
Increased Shading | Motorized sun tracking umbrella top provides no user interaction to maintain shading
Self Sustained Power Supply | Solar panel battery charging
Long Battery Life | 4 hours of battery life in low sunlight under normal operating conditions
Transportable | Needs to be easily foldable for transporting or storing
Weather Resistant | Able to withstand high heat and high humidity conditions
3 Mode Lighting System | Constant lighting, lighting pattern, and entertainment modes
USB Phone Charger | 2.0 USB phone charging port able to maintain trickle charge of 0.5 amps.
Solar Panel Status Screen | Back lit LCD screen shows Solar Panel status
Battery Charging Status Indicators | Shows status of battery including battery present, charging and fully charged.

## Slide 5: Umbrella
Height: 7.0’
Width: 7’ 6”
Reason:
1 ¼” hollow steel pole Price: $26.00
6 steel straight splines wind flap decreases affects of added torque
7 lbs. total weight easy setup

## Slide 6
Solar Panel
Project Block Diagram
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control

## Slide 7
Solar Panels
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control
Solar Panel
Power Generation
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control

## Slide 8: Solar Panel
Issues:
Finding a lightweight solar panel
Size of solar panel
Mounting that required no heavy bracket
Durability of solar panel
Cost of solar panels
Solution?
Build our own panel using individual solar cells

## Slide 9: Solar Panel
Solopower’s CIGS thin film technology
Highest efficiency in thin film technology
28 individual 1.25 watt solar cells connected in series
Produces 35 watts
14 volts at 2.5 amps
Lightweight and flexible
Raw solar cell needs weatherproof encapsulation
item | value
Manufacturer | Solopower
Total weight | 1lb
Price | $130.60
Courtesy of Solopower

## Slide 10: Solar Panel Build
Copper tape tabbing
Benefits:
Electrically conductive glue
Low resistivity
Solderable
Gorilla shipping tape encapsulation
Benefits:
Durable non stretching
Non yellowing
High heat rating
positive
negative
14 inch
1.75
inch

## Slide 11
Solar Panels
Maximum Power Point Tracking (MPPT)
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control
3 analog inputs
to MCU
2 outputs from MCU
PWM control
10mA
130mA

## Slide 12: Current and Voltage Sensors
Solar panel and battery voltage sensors are simple voltage divider circuits
Allegro’s hall effect-based ACS712 linear current sensor IC
Allows MCU to calculate maximum power from solar panel and regulate output voltage to battery
Item | Value
Manufacturer | Allegro
Model Number | ACS712ELCTR-05B-T
Packaging | SOIC 8
Price | $1.58
Courtesy of Allegro

## Slide 13: Power MOSFETS
Testing 2 different power MOSFETS in Prototype board
Texas Instruments CDS18503KCS Power MOSFET much more efficient
 | CDS18503KCS | IRFZ44N
Manufacturer | Texas Instruments | International Rectifier
Max voltage | 40V | 55V
Max current | 100A | 49A
Threshold voltage | 1.9V | 2-4V
Drain-to-Source On-Resistance | 3.6mohm | 17.5mohm

## Slide 14: MOSFET Driver
 | LM27222 | IR2104
Manufacturer | Texas Instrument | International Rectifier
Input voltage | 4V to 6.85V | 10 V– 20V
Operating current | 0.65mA | 130mA
Packaging | SOIC 8 | DIP 8
Chose the LM27222 to begin testing mainly because of input voltage and lower operating current
Had issues with LM27222 not switching MOSFETS
Decided to switch to IR2104 with great success

## Slide 15: Initial Testing of Switching Regulator
Light blue: Output after Inductor
Issue:
Having trouble getting consistent output
MOSFET output before filtering
12 volt input
62.75kHZ switching frequency
50% duty cycle
Yellow: Output from microcontroller
Light Blue: Output from MOSFET's

## Slide 16
Solar Panels
Battery Charging
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control
2A
0.5 A

## Slide 17: Battery
Tenergy’s 7.4V 5200mAh Li-ion battery pack
Lightweight
Small size
No battery memory effects
Low self discharge rate
Built in over charge and over
discharging IC prolongs battery
life
Courtesy of Battery Junction
item | value
Manufacturer | Tenergy
Weight | 0.42 lbs (6.7 oz)
Dimensions(lxwxh) | 2.83”x2.76”x0.79”
Fully charged voltage | 8.4V
Cut-off voltage | 6V

## Slide 18: Battery Charging
BQ24123 charge management IC
Charges 2 cell Li-ion battery packs
3 stage charging: conditioning,
constant current, and constant
voltage
Added safety features include
charging timer, thermal protection
Charging indicator LED’s
Courtesy of Texas Instruments
item | value
Input voltage | 8.4V
Max charge rate | 2A
price | Free

## Slide 19: USB charger
USB 2.0 female dedicated charging port
Type A Female breakout board
for easy enclosure mounting
Restricted to a 0.5A trickle charge
Future upgrade possible:
USB charging chip to charge
Apple devices
item | value
Output voltage | 5V
Max output current | 0.5A
Price | $1.50
Courtesy of ebay

## Slide 20: Eagle Schematic: MPPT and Charger

## Slide 21: Eagle Schematic: MPPT and Charger
Solar panel
voltage sensor
Battery
Voltage
Sensor
5 volt
voltage
regulator
Battery
Charging IC

## Slide 22: Eagle Schematic: MPPT and Charger
MPPT Switching regulator
Battery feedback
MOSFET

## Slide 23: Eagle Board Layout: MPPT and Charger

## Slide 24
Solar Panels
Motors and Motor Control
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control
580 mA
580 mA
14 output pins
7 per motor driver

## Slide 25: Motors
Bipolar stepper motor
Open loop feedback design with position control
2 motors control rotation and tilt of umbrella
Issues:
  Motors may not deliver enough torque for the tilt portion of umbrella
  Complex control scheme
Item | Value
Manufacturer | SOYO
Model Number | SY35ST26-0284A
Current | 280 mA/phase
Voltage | 7.4 V

## Slide 26: Motor Control
Simplify motor control
Step on rising edge of signal
Adjustable current output range
Sleep mode
Item | Value
Manufacturer | SparkFun
Model Number | ROB-12779
Current Output | 150-750 mA
Motor Voltage | 6-30 V
Courtesy of Brian Schmalz
 | MS1 | MS2 | RST | ENABLE
Digital | 0 | 0 | 1 | 0

## Slide 27
Solar Panels
Peripherals
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control
20mA per LED
2 output pins
12 output pins

## Slide 28: LCD and Charging LED Indicators
LCD screen:
Simple 20 x 4 char LCD display
Backlit lighting will be on push button
to increase efficiency
Displays:
Solar panel voltage, current, power
Battery voltage
Charging Status LED’s:
3 LED’s show battery charging status
Courtesy of ebay
Battery Battery Battery
present charging full

## Slide 29: Lighting System
Light weight with high efficiency
24 individual LED’s connected in pairs (4 per umbrella spline)
Display different blinking patterns for entertainment mode
Issues:
  12 IO pins from MCU
Item | Value
Manufacturer | China Young Sun LED Technology Co.
Model Number | YSL-R547W2C-A13
Max Current | 20 mA
Forward Voltage | 3.4 V
Luminous intensity | 8000-10,000 mcd

## Slide 30
Solar Panels
Control Block Diagram
Solar Panel Current Sensor
Battery Charger IC
LI-ION
Battery
Top Motor Controller
Bottom Motor
Controller
5 Volt Regulator
MCU
Top Motor
Bottom Motor
Motor
Control Sensors
LED’s
Solar Panel
Voltage Sensor
MPPT Synchronous Switching Regulator
Battery Voltage Sensor
MOSFET Driver
Battery charging indicator LED’s
LCD Screen
USB Charger
10-13 variable voltage
8.4 volt
7.4 volt
5 volt
3.3 volt
Power
Control

## Slide 31: MPPT Algorithms
Two types of algorithms under consideration
Perturb and Observe
Incremental Conductance

## Slide 32: Perturb and Observe
Most common
Adjusts PWM
Less computations
Computes power, compares power to previous, compares voltage
Oscillates around Maximum Power Point

## Slide 33: Incremental Conductance
Measures incremental Changes in current and voltage
Predicts the change in voltage change
Requires More Computations
Tracks changing conditions more rapidly
This method computes the maximum power point by comparing the incremental conductance IΔ/ VΔ to the array conductance (I/V).

## Slide 34: Solar Tracking Sensor Design
Controller needs inputs from sensor to efficiently track the sun
Two prototypes under consideration
1- Sensor Using LDRs
2- Sensor using Photovoltaic Cells

## Slide 35: Sensor Using LDRs
3 Light Dependent Resistors
Measure voltage across 10k resistor
Controller pins A0-A5 can measure voltage
Light Shading mechanism to receive better readings
Photoresistor or Light Dependent Resistor

## Slide 36: Sensor using Photovoltaic Cells
Keeping it Solar
2 Photovoltaic Cells
1 Wooden Block
2 Current Sensors

## Slide 37: Prototyping with ATmega 2560
Item | Value
Operating Voltage | 5V
Input Voltage | 6-20V
Digital I/O Pins | 54 (15 provide PWM output)
Analog Input Pins | 16
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 256 KB
Clock Speed | 16 MHz

## Slide 38: Eagle Schematic: Microcontroller

## Slide 39: Eagle Board layout: Microcontroller

## Slide 40: Entertainment Mode
Night Time Use
Rotate umbrella 360 degrees
4 Lighting Modes

## Slide 41: Pole Design
Wire welding instead of bolts to reduce weight
Mounting bracket for top motor
Mounting bracket for bottom motor
Mounting bracket for enclosure

## Slide 42: Top Motor Mounting
Motor placement 36 inches from top of umbrella to allow folding for storage or transporting
Welded hinge to decrease pole displacement
Stepper motor will be used as an actuator to control tilt of umbrella
- increases motor torque capabilities
- allows for sleep mode increasing system efficiency
5mm diameter motor shaft extended with 10-24 all thread rod
Rotatable smooth pin and all thread connector inside pole allows motor shaft to remain straight
3 stages at 10, 20, and 30 degrees tilt

## Slide 43: Bottom Motor Mounting
Bottom motor mounted inside pole at 51 inches from top of pole
Top part of pole sleeves into bottom part of pole
Pole will rest on ball thrust bearing to take weight off motor shaft
Shaft extended to be able to pin to bottom part of pole with removable pin allowing pole separation for storing and transporting
Allows 360 degree rotation

## Slide 44: Enclosure
Houses:
Battery
MPPT
Microcontroller
LCD screen
Battery status lights
USB charging port
Motor drivers

## Slide 45: Work Distribution
 | Derek | Eugene | Nicholas
Lighting System | Primary |  | 
MPPT design |  | Primary | 
Pole design | Primary | Primary | Primary
Coding |  |  | Primary
Motor system | Primary |  | 
USB Charger |  | Primary | 
Solar Panels |  | Primary | 
Solar tracking |  |  | Primary
MCU design |  |  | Primary
Battery |  | Primary | 

## Slide 46: Budget
item | supplier | number | Total cost | item | supplier | number | Total cost
7’6” patio umbrella | Target | 2 | $52.00 | LCD screen | ebay | 1 | $7.24
Solopower solar cells | Solopower | 30 | $81.00 | Push button switches | ebay | 10 | $1.60
Battery pack | Battery Junction | 1 | $47.04 | USB type A | ebay | 2 | $3.18
Stepper Motor | Robotshop | 2 | $31.42 | Weatherproof on/off switch | ebay | 1 | $4.99
Motor controller | Amazon | 2 | $16.00 | Gorilla Packaging tape | Lowe’s | 1 | $10.00
LED’s | SparkFun | 24 | $21.60 | Copper tabbing tape | amazon | 1 | $22.95
microcontroller | ebay | 1 | $35.00 | wire | ebay | 200ft | $30.00
BQ24123RHLT charging IC | Texas Instrument | 5 | Free | Thrust bearing | Grainger | 1 | $8.84
PCB boards | PCB’s4u | 2 | $135.00 | Various resistors and capacitors | Mouser | N/A | $50.00
CDS18503KCS MOSFET | Texas Instrument | 5 | Free | Metal for mounting | Lowe’s | N/A | $30.00
IR2104 MOSFET driver | Mouser | 2 | $3.50 | enclosure | Lowe’s | 1 | $10.00
TPS63060DSCR 5 volt regulator | Texas Instrument | 5 | Free | connectors | N/A | N/A | $20.00
ACS712 current sensor | ebay | 5 | $8.50 | miscellaneous | N/A | N/A | $20.00
Light dependent resistors | ebqy | 6 | $19.50 | Shipping and Handling | N/A | N/A | $75.00
UF4003 fast switching diode | Mouser | 2 | $1.72 |  |  |  | 
IN4148 diode | Lab | 2 | Free |  |  |  | 
P6KE10A TVS diode | Mouser | 2 | $0.88 | TOTAL |  |  | $752.03
P6KE15A TVS diode | Mouser | 2 | $1.12 |  |  |  | 
5505-RC 100uH inductor | Mouser | 2 | $2.85 |  |  |  | 
EEU-FC1A561 560uF capacitor | Mouser | 2 | $1.08 |  |  |  | 

## Slide 47: Progress
Chart: 
| Total | Testing | Prototyping | Design | Research
Series 1 | 0.55 | 0.2 | 0.3 | 0.5 | 0.9

## Slide 48: Projected Schedule
milestone | Oct 2 – Oct 9 | Oct 10 – Oct 16 | Oct 17 – Oct 23 | Oct 24 – Oct 30 | Oct 31 – Nov 6 | Nov 7 – Nov 13 | Nov 14 – Nov 20 | Nov 21 – Nov 27 | Nov 28 – Dec 1
prototyping |  |  |  |  |  |  |  |  | 
PCB ordering |  |  |  |  |  |  |  |  | 
Pole build |  |  |  |  |  |  |  |  | 
Solar panel mounting |  |  |  |  |  |  |  |  | 
Motor mounting and testing |  |  |  |  |  |  |  |  | 
LED mounting and testing |  |  |  |  |  |  |  |  | 
PCB build and testing |  |  |  |  |  |  |  |  | 
Enclosure build |  |  |  |  |  |  |  |  | 
Sun tracking sensor build and testing |  |  |  |  |  |  |  |  | 
Final testing |  |  |  |  |  |  |  |  | 

## Slide 49: Questions?
“The important thing is to not stop questioning. Curiosity has its own reason for existing.”
- Albert Einstein – Life Magazine, May 2, 1955