## Slide 1: Solar Blinds

## Slide 2: Group 11
Artis Coleman - Computer Engineer
Sean Diamond - Optical Engineer
Dakota Jordan - Computer Engineer
Stephen Walsh - Electrical Engineer

## Slide 3: Motivation
Renewable energy source
Complement an energy-efficient home
Easily added to any residential home

## Slide 4: Goals
High Energy Efficiency
Easy installation
Remote controllable
Self-sustaining operation
Relatively low-cost
Lightweight

## Slide 5: Concept
Front View Back View

## Slide 6: Block Diagram

## Slide 7: MCU

## Slide 8: MCU
Wifi vs. Bluetooth vs. Zigbee

## Slide 9: MCU
Needed an ARM processor
We first considered the Atmel SAM3N00A & TI CC3200
CC3200 had more features than we needed & used WiFi, so we looked into the CC2640 instead
 | Atmel SAM3N00A | TI CC2640
Sleep Current @48MHz | 8.4mA | 0.550 mA
Active Current @48MHz | 18 mA | 2.938 mA
Bluetooth | Requires additional module | On-board, requires additional antenna

## Slide 10: MCU
Texas Instruments CC2640
Part | Vendor | Cost | Shipping/Tax | Total
CC2640 | Mouser Electronics | $6.25 | $7.99 | $14.24
SmartRF06 | Mouser Electronics | $149.00 | $7.99 | $156.99
SaBLE-x Evaluation Kit | Digi-Key | $69.99 | $5.99 | $75.98
$247.21
Dev Board SmartRF06
SaBLE-x Evaluation Kit

## Slide 11: Motor

## Slide 12: Motor
Horizontal Slats Vertical Slats
Source: Blinds Parts
Motor selection depends on blind type
Horizontal and vertical blinds originally considered, both required two motors

## Slide 13: Motor
Original design required two motors and complex wiring for photovoltaics

## Slide 14: Motor
Benefits of rolling blinds:
One motor
Easier to design for different windows
Easier to mount solar panels
Less complex wiring
Saves power
Simpler manual button controls
Source: Innovative Openings

## Slide 15: Motor
Attributes | Value
Manufacturer | RollerTrol Automation Systems
Lift Capacity | 12 lbs
Torque | 1.5 Nm
Speed | 28 rpm
Nominal Voltage | 12 V DC
Minimum Voltage | 9.5 V DC
Current Consumption | 1.5 A
Stall Current | 3 A
Lifetime | 30,000+ cycles
Total Cost | $118.00
Source: RollerTrol

## Slide 16: Motor

## Slide 17: Solar Cells

## Slide 18: Solar Cells: Thin Film Module
Built in blocking diode
Attribute | Value
Manufacturer | PowerFilm
Model | R-14
Size | 14.5" x 42"
Power | 14 W
Max Voltage | 15.4 V
Max Current | 0.9 A
Total Cost | $185.99

## Slide 19: Solar Cells: Monocrystalline Module
Attribute | Value
Manufacturer | Sunpower
Module Size (7 Cells) | 35" x 5"
Module Power | 23.1 W
Max Voltage (after boost) | 15.4 V
Max Current (after boost) | 1.5 A
Total Cost (10 Cells) | $46.99

## Slide 20: Solar Cells: Monocrystalline Module
Source: Sunpower

## Slide 21: Solar Cells: Combined Module
Attribute | Value
Connection | Parallel
Total Power | 36.96 W
Max Voltage | 15.4 V
Max Current | 2.4 A
Charge Controller | Genasun Gv-5 MPPT
Charge Controller Refresh Rate | 15 Hz
Charge Controller Cost | $75.00

## Slide 22: Battery
Attribute | Value
Manufacturer | Universal Power Group
Model | UB1250 (SLA AGM)
Capacity | 60 Wh (12V, 5Ah)
Dimensions | 3.54" x 2.76" x 3.98"
Maximum Charge Current | 2.4 A
Lifetime (50%-30% discharge) | 500-1200 cycles
Total Cost | $14.93

## Slide 23: Power Generation
Light Condition | Solar Power | Time to Charge 60 Wh Battery
100% Max Power | 36.96 W | 1.62 Hr
75% Max Power | 27.72 W | 2.16 Hr
50% Max Power | 18.48 W | 3.25 Hr
25% Max Power | 9.24 W | 6.49 Hr

## Slide 24: RFID
NFC = Near Field Communication, subset of the RFID band
Requires tag & reader
Recent Android phones have NFC reader built-in
Part | Vendor | Cost | Shipping/Tax | Total
NFC Tag | TagStand | $1.00 | $2.99 | $3.99
Source: TagStand

## Slide 25: USB Charger
Mainly for phone charging
Will not be using the data lines
Mounted directly on PCB with extender port mounted on the housing
Source: Global Sources
Source: USB Gear

## Slide 26: Other Features
Manual motor control buttons
Phone Holder (for use while charging)

## Slide 27: Power Consumption
Component | Voltage | Current | Power
Motor | 12V | 1500mA | 18W
USB | 5V | 500mA | 2.5W
MCU | 3.8V max | 2.94mA | 11.17mW
Bluetooth RX | 3.8V max | 5.9mA | 22.42mW
Bluetooth TX | 3.8V max | 9.1mA | 34.58mW

## Slide 28: PCB

## Slide 29: PCB
CC 2640 Bluetooth Chip
USB Charger
Motor Controls
LCD
Switching Regulators
Temperature Sensor

## Slide 30: PCB
MCU

## Slide 31: PCB
Switching
Regulators

## Slide 32: PCB
USB Charging

## Slide 33: PCB
Motor
Controls

## Slide 34: PCB
Part | Vendor | Cost | Shipping/Tax | Total
PCB | APC Circuits | $60.00 | $30.00 | $90.00
Components | Digi-Key | $66.59 | $11.32 | $77.91

## Slide 35: PCB

## Slide 36: Mobile Application

## Slide 37: Mobile Application
Want to target many users without developing for multiple OS
By popularity: Android > iPhone > Windows

## Slide 38: Mobile Application
Desired Functionality:
Control blinds securely
Display info about usage
Report info on battery life
Display any other relevant info

## Slide 39: Main Menu
Controls blinds up/down
Shows local weather info with embedded API
Controls sync between phone & RFID tag
Shows battery info & statistics

## Slide 40: Motor
Toggle blinds to roll up
Toggle blinds to roll down
Stop motor

## Slide 41: Sync
Begin Sync
List of Registered Devices
Device #1
Additional Synced Devices Here

## Slide 42: Weather
Room Temperature
Forecast Display Toggle
Forecast Chart
Forecast Effect on Battery
Go to Battery screen

## Slide 43: Battery
Battery in blinds
Time to recharge from solar
Based on info from weather screen
Display graph based on history since device sync
Displays another graph based on selected $ rates

## Slide 44: Housing
Bottom ->
Room side ->
Top ->
Window Side ->

## Slide 45: Testing
Test reflectance/ transmittance for energy efficient glass
Test voltages and currents for individual and combined solar modules and compare to expected values
Test PCB points to ensure power is being delivered correctly

## Slide 46: Glass Testing
Equipment used:
Newport Power Meter Model 1918-R
Dolan-Jenrier Industries Fiber-Lite High Intensity Illuminator
StellarNet Inc Spectrometer
Glass Tested:
AGC Tinted Single & Double Pane
Solarban 60 Low-E Single & Double Pane

## Slide 47: Glass Testing
Glass Type | Transmittance
AGC (Tinted, Single-Pane) | 61.87%
AGC (Tinted, Double-Pane) | 41.25%
Solarban 60 Low-E (Single-Pane) | 74.52%
Solarban 60 Low-E (Double-Pane) | 49.67%

## Slide 48: Glass Testing
Source: Panasonic

## Slide 49: Glass Testing
Incident light spectrum

## Slide 50: Glass Testing
AGC (Tinted, Double-Pane) Transmission Spectrum

## Slide 51: Glass Testing
Solarban 60 Low-E (Double-Pane) Transmission Spectrum

## Slide 52: Solar Test Data
 | Monocrystalline Module (before boost) | Monocrystalline Module (after boost) | Thin Film Module | Combined Module
Expected Vmax (V) | 4.06 | 15.40 | 15.40 | 15.40
Tested Vmax (V) | 3.86 | 15.40 | 15.32 | 15.32
Expected Imax (A) | 5.93 | 1.50 | 0.90 | 2.40
Tested Imax (A) | 5.33 | 1.21 | 0.88 | 2.16
Expected Pmax (W) | 24.08 | 23.10 | 13.86 | 36.96
Tested Pmax (W) | 20.57 | 18.63 | 13.48 | 33.09

## Slide 53: PCB Testing
 | Expected V (V) | Tested V (V) | Expected I (A) | Tested I (A)
12 V Plane | 12 | 11.98 | x | x
5 V Plane | 5 | 5.05 | x | x
3 V Plane | 3 | 3.01 | x | x
Up Motor Button | 1 | 1 | 1.5 | 0.85
Down Motor Button | 2 | 2 | 1.5 | 0.85
USB Charger | 5 | 5 | 0.5 | 0.09-0.5

## Slide 54: Work Distribution
 | Artis | Dakota | Sean | Stephen
Power |  |  | Primary | Secondary
PCB |  |  |  | Primary
Mobile App | Primary | Secondary |  | 
Embedded | Secondary | Primary |  | 
Housing |  | Primary | Secondary | 

## Slide 55: Budget
Component | Vendor | Budget | Actual
Hard solar cells | Genasun | 46.99 | 46.99
Flex solar cells | PowerFilm Solar | 185.99 | 185.99
Boost converter | RioRand | 10.04 | 15.99
Battery | 1000Bulbs | 9.93 | 14.93
Battery Monitor | Avnet | 0.00 | 5.44
GV-5 Charge Controller | Genasun | 75.00 | 75.00
Microcontroller CC2640 | Mouser Electronics | 13.08 | 14.24
Development Boards | Mouser Electronics | 37.17 | 232.97
USB Charger | Donated by member | 19.50 | 0.00
PCB Assembly | APC Circuits | 30.00 | 90.00
PCB Components | Digi-Key | 0.00 | 77.91
Temperature Sensor | Maxim | 0.00 | 4.89
RFID Chip | TagStand | 0.00 | 3.99
Housing | Donated by member | 0.00 | 0.00
Display | Digikey | 21.72 | 12.85
Motor | Rollertrol | 100.00 | 118.00
Canvas | Lowe's | 0.00 | 7.00
Wooden Test Frame | Lowe's | 0.00 | 4.00
 | TOTAL | $549.42 | $919.19

## Slide 56: Issues
Energy transfer from thin film solar module to the battery
Space issues in the enclosure for electronics
Programming MCU on PCB
Data exchange over Bluetooth

## Slide 58: Questions