## Slide 1: Harris Heatsink Test Rig
Patrick Armengol – CpE
Adam Blair – EE
Eric Guest – CpE
JinJin Lin - EE

## Slide 2: Goals and Objectives
Testing Platform
  Sensor measurements for data collection
  Observe friction and temperature phenomena in steady state and pulsating airflow conditions
  Analog feedback control
  Data acquisition

## Slide 3: Approach
Problem: Collect data from various sensors and precisely control fan speed
Solution:
Install pressure and temperature sensors in test unit
Collect data from sensors with custom-built DAQ
Pass data to computer as well as fan control system
Adjust fan speed and cycle rate given “desired” output and “actual” output from sensors

## Slide 4: System Diagram
Endplate
AC Power /
VARIAC
T/C
P/S
Endplate
Heater
Heater
FAN
DAQ
P/S
PC
P/S = Pressure Sensor
T/C = Thermocouple
DAQ = Data Acquisition
CONTROL SYSTEM
T/C
T/C
T/C
Thermocouples (~20/Plate)
ORIFICE Plate
Discharge Area
Housing
DC Power Supply
Inlet Area

## Slide 5: Interface Matrix

## Slide 6: Requirements
Create a steady state pulsating air flow
Measure the temperature change
Measure the mass flow
Measure the differential pressure between two ends
Control the heaters and fans
Power various components
Collect temperature, mass flow, pressure data

## Slide 7: Specifications
Input air flow is sinusoidal velocity
Pulsation frequency from 0.1 Hz to 10 Hz
Pulsation amplitude from 0.3 to 0.8
Constant heat flux boundary on both side of plate
The test rig shall be capable of easily replacing the test article
Data Output in transient and time domain
Response time shall be higher than 10Hz
All Dimension shall be form of inch

## Slide 8: Design Constraints
Some of the following constraints have been taken in to account in our design:
Economic – although we have a large budget, we must be mindful of spending
Safety – we are dealing with considerable amount of power, heat, and weight. Our design must keep safety of the operator and surroundings in the forefront
Modularity – the heatsink plates must be removable and must be able to be disassembled
Longevity – the test bed needs to last a reasonable amount of time without service

## Slide 9: Standards
Universal Serial Bus Standard
  Guarantees fast transfer rates (480 Mb/s), high polling rate, standard connectors, and stable power source (4.45-5.25 VDC)
Power Supply Standards
  DoE efficiency standards for PSUs – 10 CFR Part 430
Output Power | Min Average Efficiency | Max Power Under No Load
Pout < 1 W | > 0.497 × Pout + 0.067 | < 0.300
1 W < Pout < 49 W | > 0.075 × ln(Pout) + 0.561 | < 0.300
Pout > 49 W | > 0.860 | < 0.300

## Slide 10: Fan
Capable of achieving relatively high cycle rates (~2-3 Hz in testing)
Easily meets max airflow requirement of 20 CFM
Simple to control by manipulating voltage
Potential problem: cycle rates lower than expected
  Solution: change size of fan, increase peak voltage

## Slide 11: Orifice Plate
Measures flow rate by restricting airflow and measuring the pressure drop
Differential manometer can be used to measure the pressure drop

## Slide 12: Fan Controller (Feedback Controller)
The exact type of controller is TBD awaiting data from tests
By testing the response of the fan-duct system we can determine the location of the fan-duct system's transfer function poles
Based on the location of the transfer function poles we will decide on a type of controller

## Slide 13: Oscillator
R2 Controls oscillation amplitude
R1,R9 Controls oscillation frequency
R5 Controls DC value

## Slide 14: Thermocouple
Type T Thermocouple
Operating range from 0 to 149 °C
0.08 seconds response time, higher than 10 Hz
Excellent accuracy
Good linearity
0.001" diameter thermocouple
Small output voltage( mV) must be amplified

## Slide 15: Thermocouple Placement
The exact number of thermocouples is 40. They will be placed at various lengths from the inlet at the centerline of each plate.
The thermocouples near the inlet will be more closely spaced together than the thermocouples near the end of the plate.
Length: 60” Width: 8”
Inlet

## Slide 16: DAQ
FPGA
USB Controller
PC
Sensors
ADC
Signal Cond.
PCB
Dev Board

## Slide 17: Thermocouple Connectors
Allows connection of thermocouple alloy to copper for PCB
Omega PCC-SMP-V-T-50-ROHS
  Miniature
  Vertical mount
  T thermocouple calibrated
  50 count
  ROHS compliant
  $126.00

## Slide 18: Analog-to-Digital Converters
AD7794
  24-bit
  6-channel
  480 Sps
  Low noise
  Low power
  Internal amplifier
  Internal temp sensor for cold junction compensation
  SPI
  $6.90 * 7 = $48.30
6 channels * 7 ADCs = 42 inputs
7 ADCs * 24 bits * 480 samples/s = 80640 bits/s
480 samples/s / 6 channels = 80 samples/s for each input
AD7680
  16-bit
  1-channel
  100 kSps
  T/H
  SPI
  $6.97

## Slide 19: Cold Junction Compensation
Thermocouples are differential not absolute.
Voltage produced at reference junction (connector) depends on temperatures at both the measurement junction and the reference junction.
We must utilize equations provided by the National Institute of Standards and Technology (NIST) to determine the actual (absolute) temperature at the measurement point.

## Slide 20: Why an FPGA?
Microcontrollers
  Easy to use
  Low cost
  Built in functionality
FPGA
  Custom interfaces
  High speed parallel processing
  Flexible timing
  Large configurable I/O
  Complex design

## Slide 21: FPGA Board
ZTEX USB-FPGA Module 2.01
  Open Source
  Custom firmware
  SDK and examples; ISE compatible
  Configurable Flash memory
  480 Mbit/s uplink rate
  $108.90

## Slide 22: Embedded Software
Written in Verilog
Utilization of open source code
  opencores – SPI module
  FPGAlink – Comm module
Customization for parallelization
SPI Master Module
Clock Divider
FIFO Buffer
Comm FPGA
USB Interface
Control
Configuring the FPGA

## Slide 23: PC Software
Collection of USB data – FPGAlink
Cold junction compensation calculations
Translation to real measurement values (°C, psi)
Storage of data to file
Display of data on customizable graphs/tables
Control of SPI sampling rates
Written in Java
Compatibility with MatLab

## Slide 24: DAQ Flowchart and Schematic
Sensor Sampling
Signal Conditioning
Analog to Digital Conversion
Data collection and ordering
Data Transmission
Data Conversion and Display

## Slide 25: DC Power Supply
Input: 110V AC
Output: +12V@3A, -12V@0.5A,
and 3.3V@0.5A

## Slide 26: AC Power Supply (Variac)
The variac will be used to power the heaters
0-1500W power output required
Will feature printed label on dial indicating power output

## Slide 27: PCB
Advanced Circuits - 4pcb.com
2-layer
60 sq. in
$33
Schematic and PCB design developed in KiCAD

## Slide 28: Platform
Testing rig designed and manufactured by ME team
Initial testing platform for electrical components will be accomplished with breadboards, prototype boards, and lab equipment
PCB will house final design

## Slide 29: Power Requirements
Component | Voltage Requirement | Current Requirement | Amount in System
Fan | 12V | 2 A | 1
Thermocouple ADC | 3.3V | 400 uA | 7
Pressure ADC | 3.3V | 4.8 mA | 1
Fan Controller | 12V and -12V | 20 mA | 1
Pressure Sensor | 3.3V | 2 mA | 2

## Slide 30: Testing
A small heated box will be created first to test the general concept
Values will be verified using a small pre-made DAQ
Steady-state cases will be verified first
Fan controller will be created based on data collected in testing

## Slide 31: Fan Controller Preliminary Testing
Purpose is to determine the response of the fans
Pitot tubes were used to obtain velocity data
Data for the transient response was insufficient for a usable model. Sensor with improved transient response needed.

## Slide 32: Fan Controller Preliminary Testing
Assuming a first order response:

## Slide 33: Schedule / Milestones
Chart: 
| Housing Design | Equipment Selection and Ordering | Thermocouple/Heater/Fan Initial Testing | DAQ Assembly and Initial Testing | Fan Controller Assembly and Initial Testing | Oriface Plate Initial Testing | Subsystem Integration | Testing and Data Analysis | Completely finished product
Start | 42249 | 42249 | 42255 | 42263 | 42263 | 42270 | 42270 | 42293 | 42337
# Days | 8 | 7 | 8 | 7 | 7 | 7 | 22 | 44 | 1

## Slide 34: Work Breakdown
Task | Patrick | Adam | Eric | Jinjin
DAQ | X |  | x | 
Software | X | x |  | 
Fan Control |  | X |  | x
Power |  |  | X | x
PCB | x | x | x | x
Sensor Interfacing | x | x |  | X

## Slide 35: Progress
Chart: 
| Heating | Airflow Control | Data Acquisition | Data Processing
Design | 40 | 35 | 40 | 40
Part Acquisition | 10 | 5 | 0 | 0
Prototyping | 10 | 5 | 10 | 2.8
Testing | 0 | 20 | 3 | 0

## Slide 36: Budget
Part | Prototyping/Testing | Final
Fan | 2 x $13 = $26 | $15
Fan Control | - | $10
Heaters | $47 | 2 x $84 = $168
Thermocouples | - | $42
Thermocouple Adhesive | - | $21
Variac | - | $200
DC Power Supply | - | $50
Wiring | - | $15
DAQ | $400 | $282
Orifice Plate | - | $250
Pressure Transducer | - | 2x $100 = $200
PCB | $19 | $33
Total | $492 | $1286

## Slide 37: Questions?