## Slide 1: Heart Racer Go-Kart EEL 4915 Group E Department of EECS University of Central Florida
Daniel Franco, EE
Steve Monroy, EE
Andre Barrett, EE
Fall 2015

## Slide 2: Project Motivation
The concept of a Go-Kart, and the experience that comes with driving one, has remained unchanged since 1956 when Art Ingels invented the first one out of scrap metal and a lawn mower engine.
The purpose of this project is to present a revolutionary idea of what a Go-Kart should look like and the options it should have.
The main goal of the Heart Racer Go-Kart is to enhance the driving experience of the customer riding it by stimulating their senses and encouraging their nervous system to release more adrenaline than it regularly would with another, non-modified, Go-Kart.

## Slide 3
LEDs and set of speakers attached to cage.
Pulse sensor and display mounted on steering wheel
Microcontroller attached to the back of the display.
The whole system will be powered by a 12V/7Ah battery.
Objectives
Speakers
Display
Pulse Sensor
LED Lights
Cage

## Slide 4
Objectives
LED LIGHTS
DISPLAY
PULSE SENSOR
CAGE
SPEAKERS
SPEED SENSOR

## Slide 5: Challenges so far
Reduction of our group from four members to three.
Finding a proper location to store Go-Kart.
Speedometer we ordered did not fit.
Finding electronic parts that are compatible with each other.
Codes that blocked each other in one processor.
Testing of the PCB.
Deciding whether to implement speakers with display or not.

## Slide 6
Specifications
Component | Parameter | Design Specification
Go-Kart | Power | 40+ mph
LED Lights | Pattern Variation | Responds to Pulse Sensor
Pulse Sensor | Accuracy of reading | Reads driver’s bpm every 5s
Speakers | Output level | 90dB– 110dB
Display | Accuracy to display info | Displays updated stats
Speedometer | Speed Test | Provides accurate readings
Battery | Power Electronics | 12V

## Slide 7: Block Diagrams

## Slide 8
Block Diagrams

## Slide 9: Components – Go-Kart
We decided to choose a racing Go-Kart to be able to reach high speeds.
The Go-Kart holds a Yamaha KT100 engine on it.
Large enough area to have all electrical equipment installed on the Go-Kart itself.
55” x 71”
Cost = $300
Purchased from Craigslist

## Slide 10: Components – Microcontroller
Printed Circuit Board containing Processors
For initial testing purposes, all of the coding and testing was be done on Arduino UNO boards.
We transferred the ATmega328 processors to our designed PCB once design of code was complete.
More testing ensued upon transfer of processors.
Cost = $150
Designed on EagleCad
Purchased from AshPark

## Slide 11: Components – Microcontroller
Power Supply #1 – Output 5V

## Slide 12: Components – Microcontroller
Power Supply #2 – Output 3.3V (Later Updated to output 5V)

## Slide 13: Components – Microcontroller
I2C Communication between Processors – Third processor not shown, but Daisy Chained in the same manner to the two

## Slide 14: Components – Display
Reprinted with permission of Adafruit
3.5” TFT 320x480 + Touchscreen Breakout Board w/MicroSD Socket – HXD8357D
Can be used in either of two modes: 8-bit or SPI.
Display is backlit by six white LEDs
Operates at a voltage rating between 3.3V and 5V
Cost = $39.95
Purchased from Adafruit

## Slide 15: Display
Pin assignments on display controller
Pin | Name | Function
1 | Y- | Y-/GPIO-7
2 | INT | Interrupt output (VCC domain, open drain)
3 | A0/Data Out | I2C address in Reset, Data out in SPI mode (VCC domain)
4 | SCLK | I2C/SPI clock (VCC domain)
5 | SDAT | I2C data/SPI CS (VCC domain)
6 | VCC | 3.3 −5V supply voltage
7 | Data in | SPI Data In (VCC domain)
8 | NC | -
9 | Mode | MODE In RESET state, MODE selects the type of serial interface "0" - I2C "1" - SPI
10 | GND | Ground
11 | IN2 | IN2/GPIO-2
12 | IN3 | IN3/GPIO-3
13 | X+ | X+/GPIO-4
14 | Vio | Supply for touchscreen driver and GPIO
15 | Y+ | Y+/GPIO-5
16 | X- | X-/GPIO-6

## Slide 16: Display
Himax HX8357 PIN location and function

## Slide 17: Components – LED Lights
Neopixels WS2812B
Had to decide between Neopixels or Digital RGB LED Weatherproof.
Each pixel can be addressed independently since they each have their own microcontroller.
Can be cut at any point of the strip.
Consume less power (9.5W/m)
5V – 2A Power supply.
Reprinted with permission of Adafruit
Cost = $16.95/m
Purchased two meters
Purchased from Adafruit

## Slide 18: NeoPixel WS2812B
Pin | Name | Function
1 | VDD | Power Supply LED
2 | DOUT | Control Data Signal Output
3 | VSS | Ground
4 | DIN | Control Data Signal Input
Pin Distribution on NeoPixel WS2812B
Physical Distribution of single Pixel in NeoPixel

## Slide 19: NeoPixel WS2812B
Application of the circuit

## Slide 20: NeoPixel WS2812B
Circuit Schematic for LED lights

## Slide 21: Components – Pulse Senor
Pulse Sensor Kit
Pulse Sensor SEN-11574
We decided to use this sensor because it was the most cost effective option and space efficient.
It will be mounted directly on to the drivers finger and will be connected to the PCB.
Signals gathered from the Sensor will ultimately control the LED Strip.
It will be programmed to gather data every 5 Seconds.
Cost = $24.95
Purchased 1 unit
Purchased from Sparkfun

## Slide 22: Pulse Senor
Reprinted with permission from Avago Tech
PIN | Name | Description
1 | VCC | VCC
2 | NC | No Connect
3 | NC | No Connect
4 | GND | Ground
5 | NC | No Connect
6 | A0 | Communication

## Slide 23: Pulse Senor
Reprinted with Permission of Joel Murphy
Overall Pulse Sensor Circuit Schematic

## Slide 24: Pulse Sensor
Circuit Schematic for Pulse Sensor

## Slide 25: Components-Speakers
Reprinted with permission from Pyle
Pyle PLMRKT2A 2-Channel Waterproof Amplified 6.5-Inch Marine Speaker System
This product was chosen due to its pricing, specifications and its design.
100 Watts RMS / 200 Watts Peak, the frequency response ranges from 80-20k Hz, contains an impedance of 40Ω, at 4Ω 2 x 100 Watts RMS, at 4Ω 2x200 Watts Max, at 2Ω 2 x 300 Watts RMS.
Light weight – only 6.97lbs.
Sound Output = >95dB
Cost = $65.29
Purchased from Amazon
Purchased 1 unit

## Slide 26: Components-Speakers
Speakers Bridge Amplifier Schematic

## Slide 27: Pyle Hydra Speaker System
Pin Number | Pin Name
1 | Input Level
2 | Polarity
3 | Gain
4 | Volume Control
5 | Stereo RCA input
Permission to Reprint Requested from Pyle

## Slide 28: Components-Speedometer
Sunlite Speedometer, initially.
Reed Switch later.
Easy Installation
Cost effective
Reprinted with Permission from Sunlite
Cost = $5.55
Purchased from Amazon
Purchased 1 unit
Reed Switch Sensor

## Slide 29: Components-Speedometer
Reed Switch Schematic

## Slide 30: Components - Battery
Expert Power EXP1270 Black 12V 7 Amp Rechargeable Lead Acid Battery
BATTERY TYPE - 12 Volt 7 Amp 20 Hour Sealed Lead Acid Battery With F1 Style Terminals
Light weight and compact – only 3.2 pounds with the dimensions of 5.9 x 2.5 x 3.7 inches.
Easy to install
Cost effective
Cost = $16.03.
Purchased from Amazon
Purchased 1 Units
Reprinted with permission from Expert Power

## Slide 31: Components-Software
User Interface of the TFT Display

## Slide 32: Components-Software
Software Development Cycle

## Slide 33: Software – I2C Communication
Master Processor
Slave Processors

## Slide 34: Design Constraints
Time
  Progress Monitoring - Dropbox
  Inaccurate Predictions – Will attempt to finish early to be able to correct errors
  Motivation – Group meetings (2-3 times a week)
  Locating Parts – Ordered primary parts first

## Slide 35: Design Constraints
Power Consumption
  Powering all electronics using only one battery
  Recharging the battery under continuous load conditions
  Accurate power distribution to each electronic component
  Maximize operating time.

## Slide 36: Design Constraints
Knowledge
  As a group we need to understand elements in Electrical, Computer and Mechanical Engineering.
  As a group we lack knowledge in Computer and Mechanical Engineering so we must accommodate.
  Must learn how to implement multiple elements into a single microcontroller

## Slide 37: Design Constraints
Safety
  Driver is required to wear a helmet.
  Caution when entering and exiting the Go-Kart due to the engine placement.
  Cage must be properly built to prevent injury to the driver if involved in an accident.
  Lighting that is too distracting to the driver.
  Speakers being too loud could damage the drivers hearing.

## Slide 38: Design Constraints
Size
  The Go-Kart is a big piece with dimensions: 71”L X 55”W.
  Storage: Member’s house
  Transportation: 3 times max (to storage, to UCF for show, back to storage)
  How to fit all components: Used parts that we knew would fit
    Display
    LEDs
    Speakers
    PCB

## Slide 39: Standards
EPA phase III emission standards
IEEE standards
LED Lighting Standards (OSRAM)
IEC Standard, Publication 268-14 (1980)

## Slide 40
Work Distribution
Name | Go-Kart | LED Lights | Pulse Sensor | Speakers | Display | Speedometer | Battery | Micro- Controller
Daniel Franco |  | ✓ |  |  | ✓ |  |  | ✓
Steve Monroy | ✓ |  | ✓ |  |  |  |  | ✓
Andre Barrett |  |  |  | ✓ |  | ✓ | ✓ | ✓

## Slide 41
Budget
Item | Supplier | # Units | Price
Go-Kart | Craigslist | 1 | $400
Motor | Harbor Freights | 1 | $170
LED Lights | Adafruit | 2 | $30
Display | Adafruit | 1 | $70
Pulse Sensor | Sparkfun | 1 | $50
Speakers | Pyle | 1 | $50
Cage | Group E | 1 | $60
Speedometer | Sunlite | 1 | $60
12V Battery | Expert Power | 1 | $10
Micro-Controller | Arduino | 1 | $60
Wires | UCF | 5 (m) | $40
 |  | Total | $1000
Item | Supplier | # Units | Price
Go-Kart | Craigslist | 1 | $450
PCB | AshPark | 1 | $150
LED Lights | Adafruit | 2 | $33.90
Display | Adafruit | 1 | $39.95
Pulse Sensor | Sparkfun | 1 | $24.95
Speakers | Pyle | 1 | $65.29
Cage | Group E | 1 | $30
Speedometer | Sunlite | 1 | $20.45
12V Battery | Expert Power | 1 | $16.00
Micro-Controller | Arduino | 1 | $15
Wires | UCF | 5 (m) | $0
 |  | Total | $815.54

## Slide 42
Financing
Initially we planned for the worst case scenario of not receiving a sponsor.
  In this case each member would contribute $250.
We were able to receive a sponsorship from Boeing for the amount of $643.00.
  Now each member will contribute a max of $119.

## Slide 43
Progress
Chart: Percentage
| Total | Testing | Prototyping | Design | Research
Series 1 | 0.9875 | 1 | 0.95 | 1 | 1

## Slide 44
Immediate Plans
Present project to other students and faculty during Senior Design day
Update and submit project documentation
Create website

## Slide 45
Questions?