## Slide 1: The RF ChatterBox A Low-Cost Frequency Analyzer
Lance O’Sullivan | EE
Alexander Long | EE
Jakub Nishioka | EE
Julian Duque | CpE
GROUP 6

## Slide 2: Overview
Design, test, and construct an automated system which allows for the collection and visualization of frequency strength data.
Motivations
  Current equipment is very expensive​
  Researchers will be able to view and estimate signal strengths across broad areas
  Ability to work with hardware integration, communications, power, and server development

## Slide 3: Specifications
Targeted Frequencies | 240 MHz – 960 MHz: ISM Bands Television 2.4 GHz: Wi-Fi Bluetooth
Battery Life | Minimum 12 hours
Small Footprint | Maximum of 10"x6"x6"
Operate in outdoor environment | Up to 140 °F

## Slide 4: Project Top-Level View

## Slide 5: Microcontroller Comparison (32-bit)
TI MSP432P4011 | MICROCHIP ATSAM4LC4B
ARM Cortex M4F w/ Frequency 48MHz | ARM Cortex M4F w/ Frequency 48MHz
256 kB RAM | 64 kB RAM
2 MB Flash | 512 kB Flash
6 Serial I/O Ports | 1 Serial I/O Port
Operating Voltage: 1.7V - 3.3V | Operating Voltage: 1.7V - 3.3V
5 Different Low Power Modes | picoPower for ultra-low power consumption
Previous experience from School | Embedded voltage regulator

## Slide 6: Microcontroller Comparison (32-bit)
TI MSP432P4011 | MICROCHIP ATSAM4LC4B
ARM Cortex M4F w/ Frequency 48MHz | ARM Cortex M4F w/ Frequency 48MHz
256 kB RAM | 64 kB RAM
2 MB Flash | 512 kB Flash
6 Serial I/O Ports | 1 Serial I/O Port
Operating Voltage: 1.7V - 3.3V | Operating Voltage: 1.7V - 3.3V
5 Different Low Power Modes | picoPower for ultra-low power consumption
Previous experience from School | Embedded voltage regulator

## Slide 8: 2.4 GHz RSSI Sensor: TI CC2500
  High sensitivity (-104dB)
  Digital RSSI Output
  0.5 dB Resolution
  Uses SPI as communication protocol
  Existing libraries that work with MSP432
  3.3V Operating Voltage

## Slide 9: TI CC2500 Sensor Schematic

## Slide 10: 240 MHz – 960 MHz RSSI Sensor: RFM22B
  High sensitivity (-121 dBm)
  Frequency control registers allow operation from 240-960 MHz
  RSSI readout from 8-bit register
  Uses SPI as communication protocol

## Slide 11: RFM22B Sensor Schematic

## Slide 12: Network Processor: TI CC3100MOD
  802.11 b/g/n
    Uses the HTTP Protocol to connect with server
  Maximum 4000 Byte transmit buffer
  Integrated components:
    Power management subsystem
    Internal oscillator
  Low power modes
  Uses SPI as communication protocol

## Slide 13: TI CC3100MOD Processor Schematic

## Slide 14: Impedance Matching
Prevents reflection of signals when switching mediums
Improves efficiency between the antenna and the receiver and prevents damage of components
Typically simple LC circuits

## Slide 15: Battery: INR-18650
  Lithium Ion Technology
  3000mAh capacity
  3.6 cell voltage
  Size of an AA battery
  600mA Discharge Current

## Slide 16: Charge Control: TP4056A Module
  Combination of:
    TP4056 - Charges battery using Constant Current, Constant voltage method
    DW01A - Monitors discharge current
    FS8205A – Dual Channel MOSFET used for switching circuit state
  Overcharge and Discharge Protection
  Optimal 1A Discharge Current

## Slide 17: Voltage Regulation: TPS63000 Module
  Input Range of 1.2V to 5V
  Can act as a Buck or Boost regulator
  Constant output voltage of 3.3V
  Max Current of 1.2A
  Peak 96% efficiency

## Slide 18
POWER SCHEMATIC

## Slide 20: Antenna
Half wavelength
RFM – 6.6 inches
Vertically polarized
Omni-directional
Wire Antenna
- Copper:
  Low cost
  High conductivity
  Easy to solder
  Resistant to stretching, damage, being moved out of place
20 dBm = 0.1 Watt
Metal | Conductivity (1/Ωcm)
Silver | 106
Copper (pure) | 100
Copper (hard Drawn) | 89.5
Aluminum | 45
Steel | 3-15

## Slide 21: Rainsun Microwave Tech AN2051-245
  For CC3100 and CC2500
Item | Specification
Center Frequency | 2.45 GHz
Bandwidth (typ.) | 110 MHz
Peak Gain (typ.) | 0.5 dBi
Voltage Standing Wave Ratio (VSWR) | 2.0 (max)
Pattern | Omni-directional
Impedance | 50 Ω
Dimensions | 5.1mm(L)×2.0mm(W)×1.2mm(H)

## Slide 22: Enclosure Design
Prototype design provides protection for the PCB and Battery
Slots were added to allow access to the switch and USB Port
3D printed with ABS Plastic - makes it lightweight, durable for outdoor use
Size: 6.5"(L) x 4"(W) x 1.5"(H)

## Slide 23: Software User Case
Improvements to be made:
  Ability to retrieve data in datasheet format (csv)
  Include ability to read status messages from each individual board

## Slide 24: LAMP Stack
Advantages
  Free for development purposes
  Fast setup time
  Experience from previous projects
Disadvantages
  Not learning something new
  Not free if storing large amounts of data
Stack​ | Free​ | Previous Experience​ | Configuration Time​ | Technologies
LAMP​ | X​ | X​ | Low​ | Linux, Apache, MySQL, PHP
MEAN​ | X​ |  | High​ | MongoDB, Express.js, Angular JS, Node.js
WISA​ |  | X​ | High​ | Windows, IIS, SQL Server, ASP.NET

## Slide 25: Database
Database is stored in Amazon Web Services Relational Database Systems
Having a single table for devices allows us to store the location for each device
Using 6 devices we can store data continuously for a month without exceeding storage limits
  Limit for free tier is ~20 GB
Amazon RDS automatically creates a backup of data every 24 hours

## Slide 26: Webpage
Website holds a heatmap created using the Google Maps API
Updated with the latest data received by the server
Color Scale:
  Red indicates high, green is low
Decay ratio simulated by using FSPL average of 10 closest measured points
FSPL =(4π*D*F/c)²*
Radius calculated by solving for distance and solving at 80 dB
D*
FSPL = Free Space Path Loss Ratio Equation, D = Distance in meters, F = Frequency in KHz, c = speed of light in meters per second

## Slide 27: MCU Logic
Device holds log of all errors for further testing
If it is not able to connect to the Wi-Fi SSID it will simply turn off
Sends 15 measured records to server in one package to optimize Battery Life
  Buffer limit is 4000 Bytes
Measures 10 times and takes average for better data accuracy

## Slide 28: Technologies
Type | Name
IDEs | Visual Studio 2017 Code Composer Studio 2016
Server Hosting | Heroku
Database | Amazon Web Services RDS MySQL Workbench
Respository | Github
Device Flashing Software | Uniflash
UART terminal | Tera Term
Programming Languages | JavaScript, HTML, PHP, C

## Slide 29: Workload
Name | Responsibilities
LANCE O'SULLIVAN | Design and implement power system Design and test PCB
JAKUB NISHIOKA | Integrate microcontroller and sensors Design and test PCB
ALEX LONG | Antenna design for transceivers Program microcontroller
JULIAN DUQUE | Create webpage and configure server Program microcontroller

## Slide 30: Cost Evaluation
Component | Price | Qty | Total
MSP432P401RIRGCR | $6.86 | 1 | $6.86
CC2500RGPR | $2.84 | 1 | $2.84
CC3100MODR11MAMOBR | $13.56 | 1 | $13.56
RFM22B | $4.76 | 1 | $4.76
TP4056 | $0.58 | 1 | $0.58
DW01A | $0.01 | 1 | $0.01
FS8205A | $0.24 | 1 | $0.24
TPS63000DRCR | $2.27 | 1 | $2.27
INR-18650 | $3.50 | 1 | $3.50
AN2051-245 | $0.25 | 2 | $0.50
Copper Wire | $0.10 | 1 | $0.10
26 MHz Oscillator | $0.50 | 1 | $0.50
Passive Components | $2.50 | 1 | $2.50
PCB Manufacturing | $3.00 | 1 | $3.00
Total |  |  | $41.22

## Slide 31: RF ChatterBox Progress
Chart: 
| Total | Optimization | Testing | Development | Design | Research
 | 0.89 | 0.8 | 0.95 | 0.9 | 0.85 | 0.95

## Slide 32: Major Obstacles and Solutions
Obstacle | Solution
CC3100 and CC3200 are both optimized to work with WPA and not WPA2_ENT | Developed method to use a certificate to obtain the WPA2_ENT settings
RFM22B has very limited documentation on working with TI Products. It was created to work with the ATMEGA (Arduino) MCU | Spent extra man hours to translate the libraries into the TI environment
The first revision of the PCB had signals shorted together, causing errors with the JTAG connection | Performed Design Rules Check according with MCU manufacturer to entire PCB design before being sent for manufacturing
CC3100 Host Control/Flash Program pins absent from PCB design. | Used CC3200 development board to replace capabilities of CC3100

## Slide 33: Questions?

## Slide 34: DEMO
http://chatt3rb0x.herokuapp.com/​

## Slide 35: Meeting Specifications
Targeted Frequencies | 240 MHz – 960 MHz: ISM Bands Television 2.4 GHz: Wi-Fi Bluetooth
Battery Life | Minimum 12 hours
Small Footprint | Maximum of 10"x6"x6"
Operate in outdoor environment | Up to 140 °F

## Slide 36
Battery Life​ | Minimum 12 hours​

## Slide 37
Battery Life​ | Minimum 12 hours​
Battery Capacity: 3000 mAh
Peak Measured Current: 100 mA
Battery Life = Battery Capacity / Measured ~ 30 hours

## Slide 38
Small Footprint​ | Maximum of 10"x6"x6"​

## Slide 39
Small Footprint​ | Maximum of 10"x6"x6"​
Actual Size: 6.5"(L) x 4"(W) x 1.5"(H)

## Slide 40
Targeted Frequencies​ | 240 MHz – 960 MHz:​ ISM Bands​ Television ​ ​ 2.4 GHz:​ Wi-Fi​ Bluetooth​