## Slide 1
Caroline Kamm EE/ME
Patrick McBryde CpE
Olesya Nakonechnaya CpE
William Zhang CpE
WIlliam Young CS Matthew Wadle CS Frank Trapasso ME Arturo Coronado ME Cong Chen ME Lanie Greer ME Erik Datadeen ME
Interdisciplinary Team Blue
Autonomous Solar
Powered Beach Buggy
Notes: PRESENTATION NEEDS TO LAST 20 MINUTES, EVERYONE'S PART NEEDS TO BE EQUAL IN TIME (AND ~maybe~ SLIDES)
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 2: Project Goals
To stimulate interest in both autonomous vehicle design
and solar-powered devices
To provide an advanced form of transportation to make
the beach more accessible to more people
To promote renewable energy and environmental awareness
To address the safety concerns associated with beach vehicles
Patrick
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 3: Project Objective
Design and build an autonomous beach buggy
that runs completely off solar energy
Transport one passenger
Actively prevent collisions
Navigate from one location to another without user input
Incorporate safety protocols that protect people and the environment
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 4: Project Specifications & Requirements
Travel 20 miles
Transport a 120 lb. passenger
Travel at no more than 3 mph
Run completely on solar energy
Complete the journey in 8 hours
Stop within 100 feet of intended destination autonomously
Final product costs less than $2,000
Given Specifications:
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 5: Project System Diagram
Olesya
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 6: Mechanical Design Approach
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 7: Mechanical Design Approach
Dynamic Concept Development
    Motorized Power Steering
    Wheels and Tires
    Drivetrain
Frame design and stress analysis
Controls integration
    Sensor/camera mounts
    Electric steering
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 8: Electrical Design Approach
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 9: Electrical Design Approach
Load and power calculations
    Motor size
    Battery size
    Required solar array output
Hourly solar generation calculations
    Solar array size for required output
    Orientation requirements → physical layout
    Estimate available power for electronics
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 10: Electrical Design - Component Selection Battery Selection
Decision Factors included:
Maximum discharge rate
Maximum charge rate
Cost
Expected capacity
Charging efficiency
Physical handling
Weight
 | NPD12-120Ah (AGM) | Trojan J150 12V 150Ah (Flooded) | Comparison
Capacity | 120 Ah @ 10 hour | 134 Ah @ 10 hour rate | Flooded has 12% more capacity but less efficient charging
Weight (x2) | 160 lbs | 170 lbs | AGM 6% lighter
Price (x2) | $445.00 | $520.00 | AGM 17% less
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 11: Electrical Design - Component Selection Solar Panel Array Decisions
Max Power at STC | 235 W | 250 W | 190 W | 220 W
Max Power at NOTC | 172 W | 183 W | NA / Bifacial | 150 W
Efficiency | 14.4 % | 15 % | 15.7 % | 18.5 %
Weight | 40 lbs | 50 lbs | 50 lbs | 15 lbs
Cost | Free | Free | Free | $250
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 12: Electrical Design Approach Solar Panel Array
180 cells x 4.74 W = 850 W STC
49V 18A System
Adjustable angles and heights for optimal UV absorption without cross-shading
Weight: ~75 lbs total
Gintech 3BB Douro Specifications:
Maximum Power | 4.74 W
Short Circuit Current | 9.31 A
Open Circuit Voltage | 641 mV
Current at 0.5V | 9.12 A
Maximum Power Current | 8.78 A
Maximum Power Voltage | 544 mV
Efficiency | 19.4 %
Fill Factor | 79.95 %
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 13: Electrical Design - Component Selection
BlueSolar MPPT Charge Controller 150/35 | MorningStar TriStar 45 Amp 12/24/48 V PWM Charge Controller | TIDA - 00120 Charge Controller TI Reference Design
MPPT algorithm: >95% efficient | PWM algorithm: 75-80% efficient | MPPT algorithm: >95% efficient
Commercial Product | Commercial Product | Reference Design Only
Real-time mobile display | No real-time user interface | No real-time user interface
$295 | $167 | $150
Expensive, no design experience | Too inefficient per calculations | Most cost-effective, most design experience

## Slide 14: Hourly Power Calculations Electrical Design Approach
= 24.88%
(end of competition)
= 110.22% = +300 W
(compared to stationary array)

## Slide 15: Full System Power Distribution Electrical Design Approach
Protection devices
Fuse block
DC/DC converter
Voltage regulator
Controllers
Charge controller
Motor controller

## Slide 16: Computer Science Design Approach
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 17: Computer Science Design Approach
Using Raspberry Pi
Navigation using Simultaneous Localization and Mapping (SLAM technique).
Measuring distances by creating a disparity image to detect obstacles.
Looking into creating a neural network to identify detected objects.
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 18: Computer Engineering Design Approach
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 19: CpE Design Approach
SPI Interface
PWM
ADC
22 Pins Minimum
3.3v I/O
5V I/O
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 20: Charge Controller Design
TIDA-00120 Reference Design
(Texas Instruments)
MPPT - Maximum Efficiency
Supports systems up to 48V & 40A
Designed system is 49V & 18A
  Highly reconfigurable
Efficiency = >97%
Battery Protection
Programmable Software

## Slide 21: Charge Controller Design

## Slide 22: Charge Controller Programming
System Indicators
  System Status
System settings
  System Voltage
  Battery Current Limit
  Maximum Load
Real Time Feedback
  Panel / Battery Voltage
  Panel / Battery Current

## Slide 23: Motor Feedback
Absolute Encoder - Steering Motor Speedometer - Drive Motor
Encoder cost: $26
Speedometer cost: $12

## Slide 24: MCU PCB Design
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 25: MCU PCB Design
 | Program Size | Test Board | Familiarity | Design Opportunity | Available Pins | SPI | PWM | ADC
MSP430 F5529 | ++ | + | ++ | ++ | 63 | 2 | 14 | 17
MSP430 FR4133 | - | - | ++ | ++ | 24 | 2 | 6 | 9
MSP430 G2 | -- | ++ | +++ | ++ | 16 | 2 | 6 | 5
UNO | + | + | -- | + | 24 | 2 | 6 | 12
RPI | +++++ | + | -- | -- | 36 | - | - | -
Processor
+2
- 2
-1
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 26: MCU PCB Design
Eagle Board Layout
Actual PCB Prototype
Cost of PCB: $35
Cost of Components:$90
TOTAL
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 27: PCB Design
UART
Async
Half-duplex
2 wires max
Easy to implement
I2C
Sync
Any # of slaves and masters
Half-duplex
2 wires max
SPI
Sync
Any # of slaves
But only 1 master
Full-duplex
1 additional wire per slave
 | Synchronization | Full-Duplex? | # of Slaves | # of Masters | # of Wires
SPI | ++ | Yes | Any | 1 | 3 + (1 per slave)
I2C | ++ | No | Any | Any | 2
UART | -- | No | 1 | 1 | 2
Communication Protocol
+2
- 2
-1
Notes: PRESENTATION NEED TO LAST 20 MINUTES, EVERYONE'S PART NEED TO BE EQUAL IN TIME AND SLIDES
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 28: Sensors
Primary Purpose: Emergency System Stop feature that will add another layer of safety by detecting objects outside the view of the camera.
Secondary Purpose:
Redundant System to the Navigation System to check distance calculations and to identify out of scope objects.
Degree Coverage of the Navigation System
Notes: One of the main requirements for the project is safety, so we wanted to add another layer of safety through an emergency

## Slide 29: Sensors
Detection range of 5 feet and stopping range of 1.5 feet based on the buggy’s 3 mph speed limit
Need to cover the front and sides of buggy, about 5+ sensors
Budget constraint of 30 dollars, | 5 - 7 dollars a sensor unit.
Ultrasonic Inexpensive, durable, meets range requirement, accurate for cost
Infrared Inexpensive, work well outdoors, meets range requirement, accurate for cost
Radio
Constraints
 | Cost | Range | Outdoor | Accuracy | Total
 | $4-7 | 30-300 cm | 75 -90 ° | per cost | 
Ultrasonic | ++ | ++ | - | + | 8
Infrared | ++ | + | - | + | 6
Radio | - | - | + | + | 0
Lidar | -- | + | + | - | -1
Research was based on the constraints
+2
- 2
-1

## Slide 30: Sensor Mounts
Coverage around the Buggy
Added servos to the design to rotate the sensors
Created mounts that will allow the sensors and servos to be mounted anywhere on the buggy

## Slide 31: Sensors

## Slide 32: GPS
-> Serial communication support -> Cost effective (< $20) -> Well documented -> Compatible with MSP430
Adafruit Ultimate GPS Breakout
NEO-6M GPS Receiver Module
Copernicus II GPS Module

## Slide 33: Project Implementation

## Slide 34: PCB Software
Olesya
Software on the Main Control Unit
-> Communicate with two other systems
->Interrupts for certain pins
->Data polling for certain pins
->Create PWM signals
->Support SPI Interfaces

## Slide 35: MCU State Machine
Olesya
High Level Overview
-> Initializing: Checks all systems, handshake with CS system.
->Nominal Running: Reads and process all inputs, send data to navigation system, decode and execute navigation system data .
->Stopping: Stops motors.
->Recovering_Stop: Waits for Navigation system flag to continue.
->Recovering_Emergency: Waits for user input to continue.
Notes: Most significant states to implement

## Slide 36: Software Tools
TI RTOS and Code Composer Studio v8
More Hardware Control
TI-RTOS has support for multitasking and memory management. TI- RTOS also manages power and timers/interrupts Resource Helper Texas Instruments has a RTOS module that is supported out of the box.

## Slide 37: Software Overview
TI RTOS Tasks
GPS - Receives gps NMEA strings from module and parses the information for long, lat, and velocity.
PWM - Vary to duty cycle and control the speed of each motor.
Encoder - Tracks the movement of the steering motor to give us feedback for PID.
SPI - Send communication packet to the Navigation system.
Olesya, Patrick

## Slide 38: Software Overview
Interrupts
Speedometer - Times tire rotation to be able to determine speed
Start/Stop Buttons - Emergency stop button that disables both motors and Start button to enable them again
Olesya, Patrick

## Slide 39: Project Difficulties

## Slide 40: SPI and PWM Difficulties
Patrick
Problem | Solution
Hard to implement RPi Slave | RPi Master and MSP Slave
PWM Synchronization | Implement TI-RTOS

## Slide 41: Software Limitations
Concerned with initial PCB design using the FR43133 instead of the current design, space was concern.
To fix this problem and to simplify PCB design and code, we decided to offload the sensors to another microprocessor.
After switching the design we had enough space, but we wanted to keep this to streamline the code on the processor.
Olesya

## Slide 42
FRONT
RIGHT
LEFT
REAR
GPIO
GPIO

## Slide 43: Project Budget
Caroline/Patrick
Total Budget: $2,244.10
Final Buggy Value: $2,072.75
Development Cost: $171.35

## Slide 44: Administrative Roles
 | Power System |  | PCB Design and Manufacturing |  |  | Sensors | 
 | Solar Power | Batteries, Protection, Distribution | Main Control Unit | Charge Controller | Software Design and Implementation | Mounts | Software
Caroline | P | P |  | P | S |  | 
Olesya |  | S | S |  | P | P | 
Partick | S |  | P | S | S |  | 
William |  | S |  |  |  |  | P
P = Primary Responsibility S = Secondary Responsibility

## Slide 45
Demo
Autonomous Solar
Powered Beach Buggy
Charge Controller
Printed Circuit Boards PWM/GPS Encoder/Speedometer/SPI
Sensor System MSP430F5529: HC-SR04s Arduino UNO: VL53L0X
Notes: PRESENTATION NEEDS TO LAST 20 MINUTES, EVERYONE'S PART NEEDS TO BE EQUAL IN TIME (AND ~maybe~ SLIDES)
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.

## Slide 46
Questions?
Autonomous Solar
Powered Beach Buggy
Notes: PRESENTATION NEEDS TO LAST 20 MINUTES, EVERYONE'S PART NEEDS TO BE EQUAL IN TIME (AND ~maybe~ SLIDES)
It is required that each member be a presenter of technical information and present at least their portion of the technical design of the project.