## Slide 1
MOIST
(Mesh-Operated Irrigation
Sensor Technology)
Ahmed Hamdy
Elange Pierre
Gabriel Santos

## Slide 2
Problem Statement
-Excessive watering
-Costs
-Damages Lawn

## Slide 3
Goals & Main Objectives
Monitoring moisture to reduce water waste
Solar-powered
Weather-resistant
Reliable network
User-friendly interface
Notes: GABE
The devs or salesforce admins in our team use sandboxes which our workspace environments in which they can test out their code and data. Typically their code goes through different stages which are all different sandboxes before they are put into production. These stages are User Acceptance Testing, Quality Assurance, Integration, and then Production
As you can see in this slide, the production sandbox is much larger than all the other sandboxes. This is because the smaller sandboxes are only allowed a small limited storage in order to keep the costs of maintaining various sandboxes down for THD down. This is brings us to the issues that our team currently faces when transferring data between these sandboxes.
NOTES
Add problem statement slide

## Slide 4
Specifications
Component | Parameter | Design Specification
Nodes | Power Consumption | 10 W
Wireless Range | Distance | 5 m
Test Area | Size | 30 x 20 sqft
Status Updates | Time | 1 update/hour
Moisture Readings | Accuracy | 5%
Child-to-Parent Network | Strength | 5:1

## Slide 5
Node Block Diagram
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 6
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 7
Soil Moisture Detector
VH400
Component | VH400 | SEN92355P
Accuracy | 2% | 0 - 950
Impedance | 10 kΩ | N/A
Power Consumption | 13 mA | 35 mA
Supply Voltage | 3.5 – 20 V | 3.3 - 5 V
SEN92355P
Notes: Inexpensive
Portable
Accurate
Corrosion-Free

## Slide 8
Temperature/Humidity Sensor
DHT22
Component | DHT22 | AD7314
Temperature Reading | 40 – 80 °C | -35 – 85 °C
Operating Voltage | 5 V | 2.65 – 5.5 V
Max Current | 2.5 mA | 1.2 mA
AD7314

## Slide 9
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 10
RF Module
nRF24L01
XBee
Component | XBee | nRF24L01
Frequency | 2.4 GHz | 2.4 GHz
Size | 28 mm x 24 mm | 15 mm x 29 mm
Download Speed | 250 kbps | 256 kbps – 2 Mbps
Voltage | 2.8 – 3.4 V | 1.9 – 3.6 V
Range | 90 m | 100 m
Commercial Usage | Proprietary | Free License

## Slide 11
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 12
Microcontroller
ATmega328P-AU
Component | ATmega328P-AU | PIC16F15354 | BASIC Stamp 2
Frequency | 20 MHz | 32 MHz | 20 MHz
Program Memory | 32 kB | 14 kB | 2 kB
Data RAM | 2 kB | 1 kB | 32 B
Operating Voltage Range | 1.8 – 5.5 V | 1.8 – 5.5 V | 5 – 15 V
PIC16F15354
BASIC Stamp 2

## Slide 13
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 14
Battery
18650 Li-Ion
LP-503759-IS-3
Component | 18650 Li-Ion | LP-503759-IS-3
Supply Voltage | 7.4 V | 3.7 V
Charge Capacity | 1800 mAH | 1350 mAH

## Slide 15
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 16
Charge Controller
LTC4079
Component | LTC4079 | bq2057
Input Voltage Max | 60 V | 18 V
Charge Current | 250 mA | 40 mA
bq2057
Notes: Why We Chose It:
-Powerful
-Strong

## Slide 17
Voltage Regulator
LM1117
7805 TO-220
Component | LM1117 | 7805 TO-220
Input Voltage Range | 7 – 20 V | 7 – 35 V
Output Voltage | 5 V/3.3V | 5 V
Max Current | 800 mA | 1.5 A

## Slide 18
RF Module
Solar
Panel
MCU
Power Control
Battery
Sensor
Power
Communication
MCU
Peripherals

## Slide 19
Solar Panel
ECOWORTHY
Component | ECOWORTHY | NUZAMAS
Power | 5 W | 2 W
Vop | 17.9 V | 12 V
Iop | 0.28 A | 0.160 A
Dimensions | 10 x 7.6 in | 5.35 x 4.33 in
NUZAMAS
Notes: Why We Chose It:
-Powerful
-Strong

## Slide 20
Node Circuit Schematic

## Slide 21
Power
Communication
MCU
Peripherals

## Slide 22
Node PCB Design

## Slide 23
GPS Block
Diagram
GPS Module
Node
GPS Module
Node

## Slide 24
GPS Module
GP-20U7
Copernicus II
Component | GP-20U7 | Trimble Copernicus II
Input Voltage | 3.3 V | 2.7-3.3 V
Interface | UART | UART
Current Draw | 40 mA | 44 mA
Start Time | 29 s | 38 s
Frequency | 1.575 GHz | 1.575 GHz
Notes: Why We Chose It:
-Powerful
-Strong

## Slide 25
GPS PCB Design

## Slide 26
Gateway Block Diagram
RF Module
Web-App
Server
API’s
Database
Software
Communication
Computer

## Slide 27
RF Module
Web-App
Server
API’s
Database
Software
Communication
Computer

## Slide 28
Embedded Server
Raspberry Pi 3 B
Component | Raspberry Pi 3 B | Banana Pi M3 | Pine 64
RAM | 1 GB | 2 GB | 512 MB
Extra Storage | microSD | 8 GB eMMC | microSD
CPU | 1.2 GHz | 1.8 GHz | 1.2 GHz
WLAN | 802.11 n | 802.11 n/g/b | 802.11 n/g/b
External Attachments | 40 GPIO pins 4 USB ports | 40 GPIO pins 2 USB ports | 40 GPIO pins 2 USB ports
Banana Pi M3
Pine64

## Slide 29
Gateway Shield Schematic

## Slide 30
Gateway PCB Design

## Slide 31
Network Topology
Star Network
Mesh Network

## Slide 32
RF Module
Web-App
Server
API’s
Database
Software
Communication
Gateway
Solenoid

## Slide 33
API Diagram
PHP,
HTML
Linux,
Apache
C++
Python
MySQL
Front-End
Back-End
Database
Notes: -UI
-Status
-Commands

## Slide 34
RF Module
Web-App
Server
API’s
Database
Software
Communication
Gateway

## Slide 35
Web Page

## Slide 36
MOIST Setup

## Slide 38
Work Distribution
 | Nodes | Communications/Control | Web-App/Database | Power
Ahmed | P | P | S | S
Elange | S | S | S | P
Gabe | S | S | P | S

## Slide 39
Future Plans
Enclosure
Improved UI
Improved Network

## Slide 40
Questions?