## Slide 1: Keur-keg Automatic Craft brewing system
Group 4
Jason Carlisle EE
Laura Hoshino EE
Kyle Rits CPE
Kevin Ruzich EE
Notes: -Kevin

## Slide 2
Brewing beer takes time and some people lose interest in the hobby
Allows user to complete other tasks while beer is brewing which saves time
Adds consistency to recipes due to lack of human error
Easy user preparation before the start of the brew cycle
Easy operation and maintenance on the system
Motivation
Notes: -Kevin

## Slide 3
The Brew Boss
  $1,600
  240 Volts
Pico Brew
  $600
  5 Liters
Keur-Keg
  120 Volts
  5 Gallons
Existing Home-Brewers
Notes: -Kevin

## Slide 4
Preparation of equipment and sanitize
Steeping and sparging (15 – 60 mins)
Boiling the mash, malt, and hops (60 – 90 mins constantly stirring)
Fermenting the wort (2 – 8+ weeks)
Bottling or kegging (3 days – 2 weeks)
* Each different recipe has different temperatures, times, and amount
Brewing Process
Notes: -Kevin

## Slide 5: Goals and Objectives
✔ Supports multiple different recipes which brews different types of beer
✔ Make easy to sanitize components and flush the system after use
X Attempt to keep the cost to a minimum to make easily affordable
✔ Use a Standard Wall Outlet which keeps power under 2400 watts
✔ Make system user friendly and easy to operate
✔ Have the final output product yield 5 gallons
Notes: -Kevin

## Slide 6: Design Standards
Easy to remove kettles for cleaning and bottling
Flush cycle and sanitation cycle
Microcontroller reads temperatures, fluid information, and sends signals to output components
Interface to enter times, temperatures, and quantities
Support storage of multiple recipes
Temperatures and current status are displayed for the user
Updates are sent to the user via email
Notes: -Kevin

## Slide 7
Requirements and Specifications
Component | Parameter | Specification
Pots | Material | Stainless Steel
System | Size | 5 Ft3 (max)
Heating Elements | Power | 1650 Watts (max)
Hops Dispenser | Quantity | 4 Dispensers (min)
MCU Battery Power | Time | 4 Hours (min)
Input Power | Voltage | 120 VAC
Power Consumption | Power | 2000 Watts (max)
Notes: -Kevin

## Slide 8: Block Diagram
Filling /Steeping
Pump
Heating Element
120V
Power Input
Power supply & relays
MCU
User Interface
Refrigeration
System
Jason
Laura
Kyle
Kevin
Steeping Pot
Fermenting Unit
Mixing Motor
Filling/Cooling Pump
Boil Pot
Cooling
System
Filling/Transfer
Pump
Flow Meter
Temp Sensor
Level Sensor
Dispenser
Temp Sensor
Level Sensor
Heating Element
Power
Controls & Feed back
Temp Sensor
Level Sensor
Notes: -Kevin

## Slide 9: Project Design Approach
One kettle design
Two kettle design
Separate individual systems
Different hops and malt dispensing designs
Heating elements
Fermenting refrigeration
Notes: -Kevin

## Slide 10: Proposed Implementation
Fresh water system
Fluid transfer system
Food quality components
Steeping system
Boiling system
Fermenting system
Electrical control cabinet
User interface
Frame for all components
Notes: -Kevin

## Slide 11: Actual Implementation
Fresh water system
Fluid transfer system
Food quality components
Steeping system
Boiling system
Fermenting system
Electrical control cabinet
User interface
Frame for all components
Notes: -Kevin

## Slide 12: Project Components
Notes: -Jason

## Slide 13: Water and Fluid Transfer System
5 gallon jugs on a mount
Water Reservoir
½” food quality hose throughout
½” connectors for the solenoids, kettles, and fermenting unit
Float switch
120 VAC pump for circulation, water input, and transfer
Notes: -Jason

## Slide 14: Steeping System
Steeping kettle
½” metal quick disconnects
120 VAC 1650 watt heating element
Temperature sensor
Shelf for grains
Notes: -Jason

## Slide 15: Boiling System
The boiling system consists of :
Boiling kettle
Mixing unit
Hops dispensing unit
Malt dispensing unit
Chilling unit
Notes: -Jason

## Slide 16: Mixing Unit
12 VDC mixing motor
50 rpm synchronous motor
Thoroughly mix and stop boil overs
Notes: -Jason

## Slide 17: Hops Dispensing Unit
4 12 VDC linear actuators 2” stroke
4 PVC gate valves
Mounts for actuators and gate valves
PVC pipe for holding the hops
Notes: -Jason

## Slide 18: Chiller Unit
120 VAC pump
Heat exchanger cooling coil
Reservoir for ice water
Notes: -Jason

## Slide 19: Fermenting Unit
Refrigerator
Fermenting pot
½” quick disconnects for pot
Temperature sensor
Stopper and airlock
Dispensing spigot
Tube for dispensing flavors and dry hops
Notes: -Jason

## Slide 20: Control Cabinet
The control cabinet contains:
Relays and wiring
Power supply
Battery backup
MCU
Notes: -Jason

## Slide 21: Relays
Two 16 channel relay boards
  Linear actuators-4 , Solenoids-6,pumps, mixing motor, refrigerator
2 channel relay board
  Two heating elements
Relay Specifications
Relay | Voltage input | Supply voltage max | Coil current | Current max | MCU input signal
16 CH | 5 VDC | 250 VAC, 30 VDC | 40 mA | 10 A | High
2 CH | 5VDC | 250 VAC, 30 VDC | 85 mA | 30 A | High
Notes: -Jason

## Slide 22
Notes: -Jason

## Slide 23: Wiring Diagram
Notes: -Jason

## Slide 24: MCU – Comparisons
 | 8051 | PIC | AVR | ARM
Bus width | 8-bit | 8/16/32-bit | 8/32-bit | 32/ 64-bit
Communication Protocols | UART, USART,SPI,I2C | PIC, UART, USART, LIN, CAN, Ethernet, SPI, I2S | UART, USART, SPI, I2C, (special purpose AVR support CAN, USB, Ethernet) | UART, USART, LIN, I2C, SPI, CAN, USB, Ethernet, I2S, DSP, SAI, IrDA
Speed | 12 Clock/instruction cycle | 4 Clock/instruction cycle | 1 clock/ instruction cycle | 1 clock/ instruction cycle
Power Consumption | Average | Low | Low | Low
Families | 8051 variants | PIC16,PIC17, PIC18, PIC24, PIC32 | Tiny, Atmega, Xmega, special purpose AVR | ARMv4,5,6,7 and series
Community | Vast | Very Good | Very Good | Vast
Cost | Very Low | Average | Average | Low
Popular Microcontrollers | AT89C51, P89v51, etc. | PIC18fXX8, PIC16f88X, PIC32MXX | Atmega8, 16, 32, Arduino Community | LPC2148, ARM Cortex-M0 to ARM Cortex-M7, etc.
Notes: -Kyle

## Slide 25: MCU – ATmega2560
54 digital IO pins
16 analog input pins
Simple power supply
Easy to use coding environment
Arduino Board for testing
Notes: -Kyle

## Slide 26: Main PCB Design
ATmega2560
3.3V Regulator
VCC and GND protection
Reset button
Power on LED
16 MHz crystal
Multiple pinouts
Notes: -Kevin

## Slide 27
Notes: -Kevin

## Slide 28: Sub PCB Design
Touch Screen Driver Board (RA8875)
WiFi Module (ESP8266 ESP-01)
Voltage Divider for temperature sensors
Notes: -Kevin

## Slide 29
Notes: -KEVIN!!!!

## Slide 30: User Interface – (Input) Comparisons
Keypad
  Simple
  Cheap
Keyboard
  Requires translator
  Easier for user
Touchscreen
  Expensive
  2 for 1
  Complex
Notes: -Kyle

## Slide 31: User Interface – (Output) Comparison
LCD Character Display
  Cheap
  Simple
LCD Screen
  Expensive
  Elaborate/potential
Touch screen
  LCD Screen + Input
Notes: -Kyle

## Slide 32: User Interface
7 Inch LCD Touch Screen
Designing through MCU is challenging
  RA8875 Driver Board solves this
  Extra cost
Touch screen is more aesthetically pleasing
  Provides endless possibilities for designs
Notes: -Kyle

## Slide 33: WiFi (ESP8266)
Communicate updates via email
  Design
    Permanent email address for brewer
    Code sends info to IFTTT.com
  User
    User must connect device to WiFi
    User must manage forwarding email address
Notes: -Kyle

## Slide 34: Software Engineering
Overview
Fermenting
Flow Charts:
Notes: -Gay

## Slide 35: Software Engineering
Data Structures
Recipe:
Info:
Button:
Notes: -Kyle

## Slide 36: Software Engineering
  void transformCoordinates(int *x, int *y)
  void sendEmailBrewFinished()
  void printKeyBoard(int layout)
  int keyBoardTouched(int x, int y, int layout)
  void screen_in_progress(int cycle, int temp, float flow, int timer_time)
Functions
Notes: -Kyle

## Slide 37: Power Consumption
Possible Concurrent Loads
Notes: -Laura

## Slide 38: Power Distribution
Wall Outlet
Terminal Block
5 Volt Regulator
5 Volt Regulator
Power Supply
3.3 Volt Regulator
5 Volt Regulator
9 Volt Battery Backup
120VAC
WiFi Module Spare
5VDC
5VDC
9 VDC
120VAC
5VDC
3.3VDC
12 VDC
Relay Board 1
Relay Board 2
MCU
Notes: -Laura

## Slide 39: Power Supply PCB Design
5V Regulator –TI’s TPS563231DRLR
  $0.82
  1.6mm X 1.6mm
3.3V Regulator – TI’s TPS564201DDCR
  $1.15
  1.6mm X 2.9mm
5VDC
5VDC
5VDC
3.3VDC
12VDC
Notes: -Laura

## Slide 40
Notes: -Laura

## Slide 41: Battery Backup System
Only for MCU in the case of temporary power losses
  9 Volt battery, 500mAh
  Meets the 4 hour specification
  Protection against power flickering
9VDC
12VDC
Notes: -Laura

## Slide 42: Administrative
Notes: -Laura

## Slide 43: Proposed Project Budget
Description | Quanity | Price
Heating element | 2 | 200.00
Power supply components | 1 | 100.00
PCB | 1 | 100.00
Motor | 1 | 50.00
Pumps | 3 | 200.00
Stainless steel containers | 2 | 200.00
Hoses and components | 1 | 50.00
Cooling unit | 1 | 50.00
Sanitation materials | 1 | 50.00
Brewing material (Hops, malt) | 2 | 100.00
Total | 1100.00 | 
Notes: -Laura

## Slide 44: Actual Project Budget
Description | Quanity | Price
Water system | 1 | 180.00
Fluid transfer system | 1 | 350.00
Steeping system | 1 | 250.00
Boiling system ( Including dispensing units ) | 1 | 500.00
Fermenting system | 1 | 200.00
Control cabinet | 1 | 100.00
Relays, amplifiers, and wires | 1 | 120.00
Power supplies | 1 | 100.00
PCB/MCU | 1 | 100.00
Frame and brewing material (Hops, malt) | 1 | 100.00
Miscellaneous | ? | 500.00
Total | 2500.00 | 
Notes: -Laura

## Slide 45: Roles and Responsibilities
Name | Fluid Systems | Steeping System | Boiling Systems | Fermenting System | PCB/MCU | Power Supplies | Comm. and Coding | Frame and Control
Jason | X | X | X |  |  |  |  | X
Kyle |  |  | X |  | X |  | X | 
Laura |  |  | X |  |  | X |  | X
Kevin | X |  | X | X | X |  | X | 
Notes: -Laura

## Slide 46: Testing
Notes: -Laura

## Slide 47: Testing
Test | Outcome
Max Current of System | 14 A
Memory Storage of Recipes | 25 Recipes
Email | Sent and Received
WiFi | Connects
User interface | Reads input and displays properly
Functions | Communicate and run properly
Temperature Control | ±5 F
Flow Control | ±2%
Power Supply | Tested to full load
PCB Test | All input and outputs full function
Pumps | Proper flow
Float Switch | Properly operate
Relay Boards | Proper switching
Notes: -Laura

## Slide 48: Issues and Lesson Learned
MCU kept resetting
Condensation on electronics
Reaching boiling temperature and temperature readings
SPI communication with RA8875 and MAX31865 board
Email protocol refused communication
Notes: -Everyone

## Slide 49
Questions?