## Slide 1: Smart Tabletop Gaming
By:
Richard Almario CpE
Hubert Barrantes CpE
Coraima Orochena EE
Jose Castano EE

## Slide 2: Motivation and Objectives
Motivation | Objectives
To make the game paperless | To move the game pieces with a magnetic XY plotter
To merge a physical session with a Virtual tabletop | Implementation of the LEDs to add effect on the game
Able to communicate online | Able to use an application to command the game pieces' movement using an Wifi module

## Slide 3: Features
Main | Secondary | Stretch goals
Move the pieces of the board by using the app | Pinpoint Ending and Starting points for game objects while the object is moving. | LED Spell effects
Track the pieces on the board | Web app: have a responsive gui | LED range of sight of game pieces
Pinpoint pos on the board by using the web app |  | Layered/Scalable maps
Have a working pathfinding with the plotter (don’t collide game objects) |  | 

## Slide 4: Block Diagram

## Slide 5: Project Concept

## Slide 6: Controller and Schematics

## Slide 7: MCU Dev Board Types
Arduino MEGA 2560 | Raspberry PI
Relatively Cheap | Relatively Expensive
Less computational power | Mainly used for computer's HDMI visual I/O
Used perfectly for hardware | Used perfectly for software

## Slide 8: Arduino MEGA 2560

## Slide 9: ATMEGA2560 MCU

## Slide 11: PCB Diagrams

## Slide 12: XY Plotter

## Slide 13: XY Plotters
Name | Working Area | Price
Laser Engraver Machine | 15.7 X 19.7 in | $198.00
GoooGi Geeklab | 8.3 X 11.7 in | $255.00
EleksDraw Pen Writing Machine | 11 X 7.9 in | $299.90
IDRAW Machine | 11.7 X 16.5 in | $350.00

## Slide 14: IDRAW Machine

## Slide 15: LEDS

## Slide 16: LEDS

## Slide 17: LED WS2182B Matrix Diagram

## Slide 18: FastLED Library
Used to program LED's
FastLED has a more robust feature set
Fast math and memory functions
color palettes
Newer than Adafruit Neopixel Library

## Slide 19: LED WS2182B Sequence Diagram
For the power supply

## Slide 20: Sensors

## Slide 21: Reed Switch Matrix

## Slide 22: Sensor Input
Will be used to reduce the sensors input in the Arduino
Coding Algorithm to reduce input pins.
27 8:1 Mux and 1 4:1 Mux to create up to 192 inputs.
11x 16 positions = 176 sensor positions
8-bit binary data

## Slide 23: Power

## Slide 24: Voltage Source
Voltage Source | Component
5V | PCB
5V | LED Drivers
12V | XY Plotter

## Slide 25: WiFi-Communication

## Slide 26: WiFi Module- ESP8266
Self-contained SOC with integrated TCP/IP protocol stack
Integrated cache to improve the performance of the system and minimize memory requirements
Abundant Learning Resources
Relatively inexpensive
Flexible designed and enhanced functions
Item | Specification
CPU | Tensilica L106 32-bit processor
Operating Voltage | 2.5V ~ 3.6V
Wi-Fi Mode | Station/SoftAP/SoftAp
Security | WPA/WPA2
User Configurations | AT instruction set Cloud server
Network Protocols | IPv4, TCP/UDP/HTTP

## Slide 27: Web Server and Database

## Slide 28: DATABASE SELECTION
Database selection is between MongoDB and MYSQL systems

## Slide 29: MONGO DB
Object-oriented, simple, dynamic, and scalable NoSQL database
Data objects stored as separate documents inside a collection, instead of storing the data into the columns and rows of a traditional relational database

## Slide 30: Selection criteria
-Good For:
Single language use
Real-time analytics and high-speed logging, caching, and high scalability.
Configuration management.
Mobile and social networking sites.
Evolving data requirements.

## Slide 31: WEB SERVER
-Node JS is the chosen webserver to utilize a single page web application
Benefits:
allow us to create high performance, highly scalable, “real-time” applications.
benefit from re-usability of code and the lack of context switching.
Only one programming language used(JavaScript) which allows user to write both front and back end in the same language.

## Slide 32: Hosting Platform – Nodechef vs Heroku
 | Nodechef | heroku
Benefits | Offers great mobile backend platom. High performance | Can be created almost instantenously. Scaling is straighforward
Pricing | Starts at $9 a month | Starts at $25 a month
Trade-offs | Cannot SSH into an appplication and databases instances. | Can have performance issues where there is serious traffic. For high volume apps, premium charge

## Slide 33: Web App Block Diagram
Landing page after login validation
Large Grid space
User interaction with the Grid table reflects these actions on the physical gameboard

## Slide 34: Tabletop Block Diagram
Landing page after login validation
Large Grid space
User interaction with the Grid table reflects these actions on the physical gameboard

## Slide 35: User Interface
The Game board matrix displays the current state of the board
Selected objects display basic information on the UI

## Slide 36: Software Design
Graphical UI Advantages vs Disadvantages | 
Advantages | Disadvantages
Relatively easy to use, ideal for a beginner. | GUIs take a large amount of hard disk space compared to other interfaces
Easy to explore and find way around system using the WIMP/GUI interface method | Need significantly more memory(RAM) to run compared to other type interfaces
No need to learn complicated commands | Use more processing power compared to other type of interfaces
Help system available within the WIMP interfaces | Slow for experienced programmers. If experienced, CLI interfaces are better
Allows you to exchange data between different software applications | 

## Slide 37: Administrative

## Slide 38: Financing
Budget Expectations |  | 
Unit | Quantity | Cost
XY Plotter | 1 | $350
Sensors | 176 | ~$150
LEDs | 176(11x16) | $45
Controller | 1 | $15-$30
Server | 1 | $100
Power Source | 3 | $80
Magnet | Variable | ~$2-$20
PCB Frame |  | ~$700
Project Enclosure |  | ~150

## Slide 39: Work distribution
 | X/Y plotter | Sensors/LED | PCB/ Schematic Desgin | WiFi Communication | Web Application/Server
Jose | X | X | X |  | 
Coraima | X | X | X |  | 
Hubert |  | X | X | X | X
Richard | X |  | X | X | X

## Slide 40: Progress

## Slide 41: Issues
Wifi connection
arduino plotter communication