## Slide 1: SmartLeaf Indoor Greenhouse System
Group 12
Alex Lam – CpE/EE
Dany Mazboudi – EE
Jonathan Gilbert – CpE
Megan Morris - EE

## Slide 2: Administrative Introduction
Alex
Dany
Jon
Megan
GUI
Software Control
Microcontroller Communication
PCB Design
Sensors
Schematics
Software
IoT communication
PCB Design
Power Supply
Control Circuits & Programming
Greenhouse Design

## Slide 3: Project Description
  Project Goals
    Unit will provide a nurturing & sustainable environment for plant growth
    Environmental controls will be triggered by sensor data
    Users can monitor greenhouse data remotely through web application and locally on GUI interface
  Project objective
    Provide a fool-proof & fun gardening experience that can produce fresh fruit and vegetables, regardless of environment

## Slide 4: Project Motivation
Address the rise of “food deserts” - defined by the USDA as regions of the country without ready access to healthy and affordable food
  23.5mil Americans live in food deserts
  2.1mil households do not own a vehicle and live more than 1 mile from the nearest grocery store
  Low-income zip codes have 30% more convenience stores with limited selection of produce, as compared to middle-class zip codes
  Residents of low-income zip codes pay up to 37% more at these small neighborhood stores for produce as compared to their middle-class peers
Direct access to healthy food can positively impact food deserts

## Slide 5: Project Specifications & Requirements
Parameter | Specification
Height | < 6ft
Weight | < 50lbs
Max. Power Consumption | 120W
Bluetooth Range | 10m
Hostable Fruit & Vegetables | Small to mid-size root systems (cherry tomatoes, strawberries, spinach, etc.)
Requirements
  System must be equipped to provide water, humidity, air circulation, and ample lighting for photosynthesis
  Set-up and maintenance is achievable in a home or office environment

## Slide 6: Environmental Requirements
Plant Need | Provision | Engineering System
Sunlight | Radiant energy light source with either a full spectrum of light or red and blue wavelengths | LED strip lights of blue and red wavelengths on a timed schedule, 6-8 hours per day
Water | A watering system that fully waters plants only when the soil is dry and has a means of collecting and removing excess water from the soil to prevent root rot | Pump and tubing that delivers water to plant beds when moisture sensor indicates dry soil; runoff system that collects water prior to drainage
Balanced pH | Monitoring of soil pH to indicate nutrient absorption | pH sensor that communicates levels to be displayed to the user
Humidity | Relative humidity monitoring and maintenance of at least 50% | Small diffuser that activates upon low hygrometer measurements
Airflow | A ventilation system for providing carbon dioxide and preventing disease | Fans that operate on a regular basis and upon high hygrometer measurements

## Slide 7: Project Block Diagram

## Slide 8: Child UML Diagrams

## Slide 9: Parent UML Diagrams

## Slide 10: Project Design
5V Humidifier Disk
12V Fan

## Slide 11: Project Design
5V Humidifier Disk
5V LEDs
Soil Moisture Sensor & child MCU
Soil Moisture Sensor, LCD, & child MCU
Drainage Collect
Water Level Sensor
Drainage Tank
Clean Water Tank
Water Level Sensor
Drainage Collect
Pump
pH Sensor
Water Barrier
PCB & Power Components
Power to LEDs & Humidifier
Pump
pH Sensor
Water Level Sensor
Drainage Line
Water Level Sensor

## Slide 12: Project Design - Build

## Slide 13: Power Supply
Power Supply | Voltage & Current Rating | Warranty | Dimensions | Cost | Connection Type
Idealy IP67 Waterproof Power Supply | 12V/10A | 2 year | 6.61”x 2.67”x 0.78” | $31.99 | NEMA-15P
Yaetek IP67 Waterproof Power Supply | 12V/10A | N/A | 1.6” x 2.8” x 7.5” | $16.99 | No plug
YGS-Tech IP67 Waterproof Power Supply | 12V/10A | 1 year | 6” x 2.71” x 0.6” | $39.99 | NEMA-15P

## Slide 14: Power Supply
Power Supply | Voltage & Current Rating | Warranty | Dimensions | Cost | Connection Type
Idealy IP67 Waterproof Power Supply | 12V/10A | 2 year | 6.61”x 2.67”x 0.78” | $31.99 | NEMA-15P
Yaetek IP67 Waterproof Power Supply | 12V/10A | N/A | 1.6” x 2.8” x 7.5” | $16.99 | No plug
YGS-Tech IP67 Waterproof Power Supply | 12V/10A | 1 year | 6” x 2.71” x 0.6” | $39.99 | NEMA-15P

## Slide 15
Load | Required Voltage | Demand Current | Regulator | Manufacturer | Description | Footprint | Efficiency | Total Price (Reg. + Components)
LEDs | 5V | 12A | TPS40305 | Texas Instruments | Switcher: Synchronous Buck Controller | 17mm2 | 91.7% | $2.99
Pumps | 12V | 2A | TPS55330 | Texas Instruments | Switcher: X version, 1.6MHz, 22V Internal FET | 17mm2 | 95.9% | $2.52
Fans | 12V | 0.44A | LMR62014X | Texas Instruments | Switcher: Wide Input Range Boost DC/DC Converter | 15mm2 | 95.6% | $0.82
Humidifier | 5V | 0.5A | TPS560430Y | Texas Instruments | Switcher: 4V to 36V 0.6A Synchronous Step-Down Converter | 15mm2 | 88.5% | $1.27
LCD | 5V | 0.15A | TPS62175 | Texas Instruments | Switcher: High Light-Load Efficiency Buck Converter | 12mm2 | 90.6% | $0.96
MSP432 | 3.3V | 0.1A | TPS62177 | Texas Instruments | Switcher: Fixed 3.3Vout, High Light-Load Efficiency Buck Converter | 12mm2 | 85% | $0.86
pH Sensor | 5V | 0.5A | TPS560430Y | Texas Instruments | Switcher 4V to 36V 0.6A Synchronous Step-Down Converter | 15mm2 | 88.5% | $1.27
Switching Regulators

## Slide 16: Switching Regulators
Chart: Total System Efficiency
| 1.2 | 2.4 | 3.5999999999999899 | 4.8 | 6 | 7.2 | 8.4 | 9.6 | 10.799999999999899 | 11.999999999999901
Efficiency@Vin=11.0V | 0.9203 | 0.94787 | 0.95196 | 0.95078 | 0.94708 | 0.94165 | 0.93441 | 0.9238 | 0.892 | 0.91879
Efficiency@Vin=11.5V | 0.91729 | 0.94672 | 0.95101 | 0.94994 | 0.94631 | 0.94092 | 0.93369 | 0.92306 | 0.89111 | 0.91813
Efficiency@Vin=12.0V | 0.91428 | 0.94559 | 0.95007 | 0.94911 | 0.94554 | 0.94018 | 0.93296 | 0.92231 | 0.89022 | 0.91741

## Slide 17: Control Circuits
Switch: N-Channel Enhancement Type Logic Level MOSFET
  MCU pulls gate high/low to switch device ON/OFF respectively
Basic ON/OFF Control & Motor speed with PWM

## Slide 18: Control Circuits
MOSFET | Manufacturer | Description | VGS(th) | VDS | ID | Footprint | Price
CSD18501Q5A | TI | 40 V N-Channel NexFET™ Power MOSFET | 1.4-2.3V | 40V | 20A | 5mm x 6mm | $1.50
BUK9M20-40H | Nexperia | N-Channel Logic Level Enhancement Mode FET | 1.8-2.2V | 50V | 25A | 6mm x 6mm | $1.67

## Slide 19
MOSFET | Manufacturer | Description | VGS(th) | VDS | ID | Footprint | Price
CSD18501Q5A | TI | 40 V N-Channel NexFET™ Power MOSFET | 1.4-2.3V | 40V | 20A | 5mm x 6mm | $1.50
BUK9M20-40H | Nexperia | N-Channel Logic Level Enhancement Mode FET | 1.8-2.2V | 50V | 25A | 6mm x 6mm | $1.67
Control Circuits

## Slide 20: Control Circuits
Fans & pumps are inductive loads that add a spike in voltage when switched (flyback)
Flyback diode added for protection

## Slide 21: Control Circuits
Motors & pumps are inductive loads that add a spike in voltage when switched (flyback)
Flyback diode added for protection

## Slide 22: Control Circuits

## Slide 23: Control Circuits

## Slide 24: Parent Microcontroller Prototype
Justification
  More powerful processor
  Easy to access libraries
  Complexity and comfortability
  Price
Microcontroller Options | Chip Name | Manufacturer | Speed | Core Processor | Core Size | Dev Board Price | Chip Price
Arduino Mega 2560 | ATmega2560 | Arduino | 16MHz | ARV | 8-bit | $38.50 | $12.35
MSP-EXP432P401R Launchpad | MSP432P401R | TI | 48MHz | ARM Cortex M4F | 32-bit | $39.95 | $7.46

## Slide 25: Child Microcontroller Prototype
Reasons for Choosing this Microcontroller
  Easy to access libraries
  Ease to communicate to parent controller
  Complexity and comfortability
Microcontroller Options | Chip Name | Manufacturer | Speed | Core Processor | Core Size | Dev Board Price | Chip Price
Arduino Uno Rev3 | ATmega238P | Arduino | 16MHz | ARV | 8-bit | 12.35 | $2.14
MSP-EXP430G2 Launchpad | MSP432P401R | TI | 16MHz | MSP430 | 16-bit | $13.45 | $2.69

## Slide 26: Sensor Comparisons
Soil Moisture Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
LM393 | Smart Prototyping | 3.3-5V | <20mA | 10-30°C | $2.99
TE215 | XCSource | 5V | <20mA | 10-30°C | $6.59
Water Level Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
High Sensitivity Water Sensor | Emartee | 3.3-5V | <20mA | 10-30°C | $4.99
Water Level Liquid Depth Sensor | WINGONEER | 3-5V | <20mA | 10-30°C | $6.99
pH Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
PH0-14 | GAOHOU | 5±0.2V | 5-10mA | 0-80°C | $37.99
Analog pH Meter | Lysee | 5V | 5-10mA | 0-80°C | $74.89
Temp & Humidity Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
DHT22 | Adafruit | 3-5V | 2.5mA | -40-125°C | $9.95
AM2302 | Adafruit | 3-5V | 2.5mA | -40-125°C | $15.00

## Slide 27: Selected Sensors
Sensor Type | Manufacturer | Sensor Selection | Voltage Inputs | Maximum Current | Operating Temperatures | Price
Soil Moisture Sensor | Smart Prototyping | LM393 Soil Moisture Sensor | 3.3-5V | <20mA | 10-30°C | $2.99
pH Sensor | GAOHOU | PH0-14 | 5±.2V | 5-10mA | 10-50°C | $37.99
Water Level Sensor | Emartee | High Sensitivity Water Sensor - RED | 3.3-5V | <20mA | 10-30°C | $4.99
Temperature and Humidity Sensor | Adafruit | DHT22 | 3-5V | 2.5mA | 0-50°C | $9.95

## Slide 28: LM393 Soil Moisture Sensor
Justification
  Accuracy
  Price
  Easy to use and test

## Slide 29: DHT22 Temperature and Humidity Sensor
Justification
  We need to make sure that our system is running at optimal temperature and humidity to support the growth of our plants.
  Full range of humidity readings (0-100%)
  Price

## Slide 30: High Sensitivity Water Sensor - RED
Justification
  To monitor the water level in our water tank in order to notify the user when the water level is starting to run low in our system.
  Accuracy
  Price

## Slide 31: Fan
Justification
  Gives us the best airflow for our system
  Reasonable Price
Fan Options | Manufacturer | Power Requirements | Noise | Airflow | Cost
RA04010HD1 | RDK | 12V, 90mA | 28 dBA | 6.08 CFM | $13.99
490-CFM-5010-03-22 | CUI | 5V, 280mA | 36 dBA | 16.07 CFM | $7.90
CFM-6015-13-22 | CUI | 12V, 220mA | 39 dBA | 27.50 CFM | $8.74

## Slide 32: Humidifier
Justification
  Small size and low power consumption
  Price
Humidifier Options | Manufacturer | Power Requirements | Price
B00PAK245E | AGPtek | 24V, 1A | $9.99
11434 | IC Station | 5V, 400mA | $5.99

## Slide 33: Water Pump
Justification
  Lowest demand for current
  Reasonable Price
Water Pump Options | Manufacturer | Power Requirements | Price
Submersible Mini Pump | Ledgle | 12V, 300mA | $8.99
Submersible Brushless Water Pump | Daniu | 12V, 400mA | $7.88
Peristaltic Liquid Pump | Adafruit | 5V, 500mA | $24.95

## Slide 34: LEDs
Justification
  Easy to control each individual LED
  Easily assessable examples
LED Options | Manufacturer | Power Requirements | Price
WS2811 | Alitove | 5V, 180mA max per LED set | $26.99
WS2812B | Chinly | 5V, 60mA max per LED | $31.85

## Slide 35: Bluetooth Modules
Justification
  Price
  BLE 4.0
  UART communication
Module Options | Manufacturer | Chip | Power Requirements | Price
HM-18 | DSD Tech | CC264R2F | 5V | $9.99
HM-10 | HiLetgo | CC2540 | 3.3V-5V | $4.50

## Slide 36: WiFi Modules
Reasons for Choosing this module
  Price
  Compatibility
  Support
Module Options | Manufacturer | Chip | Power Requirements | Price
CC3100BOOST | TI | CC3100 | 3.3V-5V | $19.99
CC3220SF-LAUNCHXL | TI | CC3220SF | 3.3V-5V | $49.99

## Slide 37: Parent and Child PCB
Parent PCB
Child PCB

## Slide 38: Power PCB
Designed in Eagle
  Design files available on TI
Ordered through PCBway
  Fast shipping and cheap
$5 PCB with 2 layer <100mm board
  Solder Power PCB and Main PCB together

## Slide 39: Communication
Sensor modules collect data from the plants and send the readings over Bluetooth to a parent edge device.
  Scalable
  Wireless
  Low power
MSP432 gathers sensor information and communicates through MQTT messages over WiFi
  JSON message packets
  PubNub
  Secure

## Slide 40: Sensor Module
Hardware
  MSP430G2553
  HM10 BLE
  Soil Moisture
  Temperature/Humidity
  Lithium Ion Battery
Software
  Timer operated
  Low power efficient
  Low memory footprint

## Slide 41: Parent Module
Hardware
  MSP432p401r
  CC3100BOOST WiFi
  HM10 BLE
  Humidifier
  Fans
  Water Pumps
  LEDs
Software
  TI RTOS
  PubNub API
  Star-Network
Controls
  Sensor activated
  Timer regulated
  User interaction

## Slide 42: PubNub
PubNub
Subscribes to web server control
Recieves published sensor data
Broadcasts published messages to subscribed devices using MQTT

## Slide 43: Web Application
Losant
  Quick prototype for visualizing data
  No control or storage
Amazon Web Services
  Host web app on the cloud
  Publish messages using PubNub javascript api
  Database

## Slide 44: Programming
Embedded Software - Energia
  Offers a wide selection of APIs
  Object-Oriented C++
  Built-in Multitasking
Web Application – HTML/Javascript
  React Native GUI API
  Compatible with AWS, REST APIs
Cloud communication – HTTP/MQTT
  Elastic Compute Cloud Server
  Relational Database Service

## Slide 45: Prototype Development

## Slide 46: Financing
Component | Price
Plexiglass panels | $40
Wood & miscellaneous hardware | $30
Water Tanks & Tubing | $15
Pumps | $16
LEDs | $14
Power Supply | $32
PCB | $60
ICs & on-board components | $34
Humidity & temperature sensor | $9
Soil moisture sensor | $26
Humidifier | $7
Fans | $8
Plants & soil | $30
Breakout boards & other test equipment | $90
Total | $471
Budget: $500

## Slide 47: Changed Implementations
pH sensor: wasn’t adding the functionality that we thought
Touch screen LCD GUI: troubles adding the correct timings needed for our Kentec QVGA Display BoosterPack/correcting libraries

## Slide 48: GAOHOU PH0-14 pH Sensor
Reasons for choosing this sensor
  To monitor the pH levels of the soil that our plants will be growing in to ensure that they’re growing in the best possible environment.
  Accuracy of pH readings

## Slide 49: LCD Touchscreens
Reasons for Choosing this Touchscreen
  Small size and low power consumption
  Library availabilities
  Price
LCD Options | Manufacturer | Display | Power Requirements | Price
Kentec QVGA Display BoosterPack | Kentec | 3.5 inch 320x240 | 5V | $24.99
HXD8357D | Adafruit | 3.5 inch 320x480 | 5V | $39.95

## Slide 50: Next Steps
Receive PCBs & continue with prototyping
Get all systems working together as a cohesive unit
Calibrate sensor data
Further develop GUI & web application

## Slide 51: Questions?