## Slide 1: SmartLeaf Indoor Greenhouse System
Group 12
Alex Lam – CpE/EE
Dany Mazboudi – EE
Jonathan Gilbert – CpE
Megan Morris - EE

## Slide 2: Administrative Introduction
Alex
Dany
Jon
Megan
GUI
Software Control
Microcontroller Communication
PCB Design
Sensors
Schematics
Software
IoT communication
PCB Design
Power Supply
Control Circuits & Programming
Greenhouse Design

## Slide 3: Project Description
  Project Goals
    Unit will provide a nurturing & sustainable environment for plant growth
    Environmental controls will be triggered by sensor data
    Users can monitor greenhouse data remotely through web application
  Project objective
    Provide a fool-proof & fun gardening experience that can produce fresh fruit and vegetables, regardless of environment

## Slide 4: Project Motivation
Address the rise of “food deserts” - defined by the USDA as regions of the country without ready access to healthy and affordable food
  23.5mil Americans live in food deserts
  2.1mil households do not own a vehicle and live more than 1 mile from the nearest grocery store
  Low-income zip codes have 30% more convenience stores with limited selection of produce, as compared to middle-class zip codes
  Residents of low-income zip codes pay up to 37% more at these small neighborhood stores for produce as compared to their middle-class peers
Direct access to healthy food can positively impact food deserts

## Slide 5: Project Specifications & Requirements
Requirements
  System must be equipped to provide water, humidity, air circulation, and ample lighting for photosynthesis
  Set-up and maintenance is achievable in a home or office environment
Parameter | Specification
Height | < 6ft
Weight | < 50lbs
Max. Power Consumption | 7.1W
Bluetooth Range | 10m
Humidity Range | 50-60%
LED Growlight Sequence Time | 6-8hrs
Hygrometer Polling Rate | 1 measurement per minute
Soil Moisture Sensor Polling Rate | 1 measurement every 6 hrs

## Slide 6: Environmental Requirements
Plant Need | Provision | Engineering System
Sunlight | Radiant energy light source with either a full spectrum of light or red and blue wavelengths | LED strip lights of blue and red wavelengths on a timed schedule, 6-8 hours per day
Water | A watering system that fully waters plants only when the soil is dry and has a means of collecting and removing excess water from the soil to prevent root rot | Pump and tubing that delivers water to plant beds when moisture sensor indicates dry soil; runoff system that collects water prior to drainage
Balanced pH | Monitoring of soil pH to indicate nutrient absorption | pH sensor that communicates levels to be displayed to the user
Humidity | Relative humidity monitoring and maintenance of at least 50% | Small diffuser that activates upon low hygrometer measurements
Airflow | A ventilation system for providing carbon dioxide and preventing disease | Fans that operate on a regular basis and upon high hygrometer measurements

## Slide 7: Project Block Diagram

## Slide 8: Child UML Diagrams

## Slide 9: Parent UML Diagrams

## Slide 10: Project Design
5V Humidifier Disk
12V Fan

## Slide 11: Project Design
5V Humidifier Disk
5V LEDs
Soil Moisture Sensor & child MCU
Soil Moisture Sensor, LCD, & child MCU
Drainage Collect
Water Level Sensor
Drainage Tank
Clean Water Tank
Water Level Sensor
Drainage Collect
Pump
pH Sensor
Water Barrier
PCB & Power Components
Power to LEDs & Humidifier
Pump
pH Sensor
Water Level Sensor
Drainage Line
Water Level Sensor

## Slide 12: Power Supply
Power Supply | Voltage & Current Rating | Warranty | Dimensions | Cost | Connection Type
Idealy IP67 Waterproof Power Supply | 12V/10A | 2 year | 6.61”x 2.67”x 0.78” | $31.99 | NEMA-15P
Yaetek IP67 Waterproof Power Supply | 12V/10A | N/A | 1.6” x 2.8” x 7.5” | $16.99 | No plug
YGS-Tech IP67 Waterproof Power Supply | 12V/10A | 1 year | 6” x 2.71” x 0.6” | $39.99 | NEMA-15P

## Slide 13: Power Supply
Power Supply | Voltage & Current Rating | Warranty | Dimensions | Cost | Connection Type
Idealy IP67 Waterproof Power Supply | 12V/10A | 2 year | 6.61”x 2.67”x 0.78” | $31.99 | NEMA-15P
Yaetek IP67 Waterproof Power Supply | 12V/10A | N/A | 1.6” x 2.8” x 7.5” | $16.99 | No plug
YGS-Tech IP67 Waterproof Power Supply | 12V/10A | 1 year | 6” x 2.71” x 0.6” | $39.99 | NEMA-15P

## Slide 14
Load | Required Voltage | Demand Current | Regulator | Manufacturer | Description | Footprint | Efficiency | Total Price (Reg. + Components)
LEDs | 5V | 12A | TPS40305 | Texas Instruments | Switcher: Synchronous Buck Controller | 17mm2 | 91.7% | $2.99
Pumps | 12V | 2A | TPS55330 | Texas Instruments | Switcher: X version, 1.6MHz, 22V Internal FET | 17mm2 | 95.9% | $2.52
Fans | 12V | 0.44A | LMR62014X | Texas Instruments | Switcher: Wide Input Range Boost DC/DC Converter | 15mm2 | 95.6% | $0.82
Humidifier | 5V | 0.5A | TPS560430Y | Texas Instruments | Switcher: 4V to 36V 0.6A Synchronous Step-Down Converter | 15mm2 | 88.5% | $1.27
LCD | 5V | 0.15A | TPS62175 | Texas Instruments | Switcher: High Light-Load Efficiency Buck Converter | 12mm2 | 90.6% | $0.96
MSP432 | 3.3V | 0.1A | TPS62177 | Texas Instruments | Switcher: Fixed 3.3Vout, High Light-Load Efficiency Buck Converter | 12mm2 | 85% | $0.86
pH Sensor | 5V | 0.5A | TPS560430Y | Texas Instruments | Switcher 4V to 36V 0.6A Synchronous Step-Down Converter | 15mm2 | 88.5% | $1.27
Switching Regulators

## Slide 15: Switching Regulators
Chart: Total System Efficiency
| 1.2 | 2.4 | 3.5999999999999899 | 4.8 | 6 | 7.2 | 8.4 | 9.6 | 10.799999999999899 | 11.999999999999901
Efficiency@Vin=11.0V | 0.9203 | 0.94787 | 0.95196 | 0.95078 | 0.94708 | 0.94165 | 0.93441 | 0.9238 | 0.892 | 0.91879
Efficiency@Vin=11.5V | 0.91729 | 0.94672 | 0.95101 | 0.94994 | 0.94631 | 0.94092 | 0.93369 | 0.92306 | 0.89111 | 0.91813
Efficiency@Vin=12.0V | 0.91428 | 0.94559 | 0.95007 | 0.94911 | 0.94554 | 0.94018 | 0.93296 | 0.92231 | 0.89022 | 0.91741

## Slide 16: Control Circuits
Switch: N-Channel Enhancement Type Logic Level MOSFET
  MCU pulls gate high/low to switch device ON/OFF respectively
Basic ON/OFF Control & Motor speed with PWM

## Slide 17: Control Circuits
MOSFET | Manufacturer | Description | VGS(th) | VDS | ID | Footprint | Price
CSD18501Q5A | TI | 40 V N-Channel NexFET™ Power MOSFET | 1.4-2.3V | 40V | 20A | 5mm x 6mm | $1.50
BUK9M20-40H | Nexperia | N-Channel Logic Level Enhancement Mode FET | 1.8-2.2V | 50V | 25A | 6mm x 6mm | $1.67

## Slide 18
MOSFET | Manufacturer | Description | VGS(th) | VDS | ID | Footprint | Price
CSD18501Q5A | TI | 40 V N-Channel NexFET™ Power MOSFET | 1.4-2.3V | 40V | 20A | 5mm x 6mm | $1.50
BUK9M20-40H | Nexperia | N-Channel Logic Level Enhancement Mode FET | 1.8-2.2V | 50V | 25A | 6mm x 6mm | $1.67
Control Circuits

## Slide 19: Control Circuits
Fans & pumps are inductive loads that add a spike in voltage when switched (flyback)
Flyback diode added for protection

## Slide 20: Control Circuits
Motors & pumps are inductive loads that add a spike in voltage when switched (flyback)
Flyback diode added for protection

## Slide 21: Control Circuits

## Slide 22: Control Circuits

## Slide 23: Parent Microcontroller Prototype
Justification
  More powerful processor
  Easy to access libraries
  Complexity and comfortability
  Price
Microcontroller Options | Chip Name | Manufacturer | Speed | Core Processor | Core Size | Dev Board Price | Chip Price
Arduino Mega 2560 | ATmega2560 | Arduino | 16MHz | ARV | 8-bit | $38.50 | $12.35
MSP-EXP432P401R Launchpad | MSP432P401R | TI | 48MHz | ARM Cortex M4F | 32-bit | $39.95 | $7.46

## Slide 24: Child Microcontroller Prototype
Reasons for Choosing this Microcontroller
  Easy to access libraries
  Ease to communicate to parent controller
  Complexity and comfortability
Microcontroller Options | Chip Name | Manufacturer | Speed | Core Processor | Core Size | Dev Board Price | Chip Price
Arduino Uno Rev3 | ATmega238P | Arduino | 16MHz | ARV | 8-bit | 12.35 | $2.14
MSP-EXP430G2 Launchpad | MSP432P401R | TI | 16MHz | MSP430 | 16-bit | $13.45 | $2.69

## Slide 25: LM393 Soil Moisture Sensor
Justification
  Accuracy
  Price
  Easy to use and test
Soil Moisture Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
LM393 | Smart Prototyping | 3.3-5V | <20mA | 10-30°C | $2.99
TE215 | XCSource | 5V | <20mA | 10-30°C | $6.59

## Slide 26: DHT22 Temperature and Humidity Sensor
Justification
  Accuracy
  Full range of humidity readings (0-100%)
  Price
Temp & Humidity Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
DHT22 | Adafruit | 3-5V | 2.5mA | -40-125°C | $9.95
AM2302 | Adafruit | 3-5V | 2.5mA | -40-125°C | $15.00

## Slide 27: High Sensitivity Water Sensor - RED
Justification
  Notify the user when the water level is low/high
  Accuracy
  Price
Water Level Sensor | Manufacturer | Voltage Inputs | Maximum Current | Operating Temperatures | Price
High Sensitivity Water Sensor | Emartee | 3.3-5V | <20mA | 10-30°C | $4.99
Water Level Liquid Depth Sensor | WINGONEER | 3-5V | <20mA | 10-30°C | $6.99

## Slide 28: Fan
Justification
  Gives us the best airflow for our system
  Reasonable Price
Fan Options | Manufacturer | Power Requirements | Noise | Airflow | Cost
RA04010HD1 | RDK | 12V, 90mA | 28 dBA | 6.08 CFM | $13.99
490-CFM-5010-03-22 | CUI | 5V, 280mA | 36 dBA | 16.07 CFM | $7.90
CFM-6015-13-22 | CUI | 12V, 220mA | 39 dBA | 27.50 CFM | $8.74

## Slide 29: Humidifier
Justification
  Small size and low power consumption
  Price
Humidifier Options | Manufacturer | Power Requirements | Price
B00PAK245E | AGPtek | 24V, 1A | $9.99
11434 | IC Station | 5V, 400mA | $5.99

## Slide 30: Water Pump
Justification
  Lowest demand for current
  Reasonable Price
Water Pump Options | Manufacturer | Power Requirements | Price
Submersible Mini Pump | Ledgle | 12V, 300mA | $8.99
Submersible Brushless Water Pump | Daniu | 12V, 400mA | $7.88
Peristaltic Liquid Pump | Adafruit | 5V, 500mA | $24.95

## Slide 31: LCD Touchscreens
Reasons for Choosing this Touchscreen
  Small size and low power consumption
  Library availabilities
  Price
LCD Options | Manufacturer | Display | Power Requirements | Price
Kentec QVGA Display BoosterPack | Kentec | 3.5 inch 320x240 | 5V | $24.99
HXD8357D | Adafruit | 3.5 inch 320x480 | 5V | $39.95

## Slide 32: LEDs
Justification
  Easy to control each individual LED
  Easily assessable examples
LED Options | Manufacturer | Power Requirements | Price
WS2811 | Alitove | 5V, 180mA max per LED set | $26.99
WS2812B | Chinly | 5V, 60mA max per LED | $31.85

## Slide 33: Bluetooth Modules
Justification
  Price
  BLE 4.0
  UART communication
Module Options | Manufacturer | Chip | Power Requirements | Price
HM-18 | DSD Tech | CC264R2F | 5V | $9.99
HM-10 | HiLetgo | CC2540 | 3.3V-5V | $4.50

## Slide 34: WiFi Modules
Reasons for Choosing this module
  Price
  Compatibility
  Support
Module Options | Manufacturer | Chip | Power Requirements | Price
CC3100BOOST | TI | CC3100 | 3.3V-5V | $19.99
CC3220SF-LAUNCHXL | TI | CC3220SF | 3.3V-5V | $49.99

## Slide 35: Parent and Child PCB
Parent PCB
Child PCB
Version 1
Version 2

## Slide 36: Power PCB
Designed in Eagle
  Design files available on TI
Ordered through PCBway
  Fast shipping and cheap
$5 PCB with 2 layer <100mm board
  Solder Power PCB and Main PCB together

## Slide 37: Communication
Sensor modules collect data from the plants and send the readings over Bluetooth to a parent edge device.
  Scalable
  Wireless
  Low power
MSP432 gathers sensor information and communicates through MQTT messages over WiFi
  JSON message packets
  PubNub
  Secure

## Slide 38: Sensor Module
Hardware
  MSP430G2553
  HM10 BLE
  Soil Moisture
  Temperature/Humidity
  Lithium Ion Battery
Software
  Timer operated
  Low power efficient
  Low memory footprint

## Slide 39: Parent Module
Hardware
  MSP432p401r
  CC3100BOOST WiFi
  HM10 BLE
  Humidifier
  Fans
  Water Pumps
  LEDs
Software
  TI RTOS
  PubNub API
  Star-Network
Controls
  Sensor activated
  Timer regulated
  User interaction

## Slide 40: PubNub
Subscribes to web server control
Recieves published sensor data
Broadcasts published messages to subscribed devices using MQTT

## Slide 41: Web Application
Losant
  IoT platform
  Buildable Dashboard
    Display sensor data about the plants
    Graphs that display changes in readings over time
    Database included
  Control panel
    Send commands to edge device
    View system state

## Slide 42: Programming
Embedded Software - Energia
  Offers a wide selection of APIs
  Object-Oriented C++
  Built-in Multitasking
Web Application – HTML/Javascript
  Losant Dashboards
  Experience Views
Cloud communication – HTTP/MQTT
  Losant workflows
  PubNub clients

## Slide 43: Prototype Development

## Slide 44: Financing
Component | Price
Plexiglass panels | $40
Wood & miscellaneous hardware | $30
Water Tanks & Tubing | $15
Pumps | $16
LEDs | $14
Power Supply | $32
PCB | $60
ICs & on-board components | $34
Humidity & temperature sensor | $9
Soil moisture sensor | $26
Humidifier | $7
Fans | $8
Plants & soil | $30
Breakout boards & other test equipment | $90
Total | $471
Budget: $500

## Slide 45: Changed Implementations
pH sensor: wasn’t adding the functionality that we thought
Touch screen LCD GUI: troubles adding the correct timings needed for our Kentec QVGA Display BoosterPack/correcting libraries
PCB difficulties
LED programming
Humidifier disk waterproofing

## Slide 46: Questions?