## Slide 1: Solar Powered UV Water Purifying and Monitoring System
Designed and Presented by:
Kendra Kordack
Bradley Blackburn
Lucas Heredia
Grant Cooper

## Slide 2: Sponsors:
Ocean Insight: Lending a Raman Spectrometer and laser module for the water quality monitoring.
MKS Newport: Providing optics needed to complete Raman spectroscopy system.
BCI Technologies: Supplying electrical equipment for implementation and testing.
Bradley Blackburn

## Slide 3: Motivation
Wide-spread viruses
Filtration Quality
Sponsorships
Bradley Blackburn
Notes: Most filtration systems only use one type of filter
Ocean Insight

## Slide 4: Similar Products
Brita Filter
One filter
No monitoring
No UV treatment
Crazy Cap
No filters
No monitoring
Bradley Blackburn
Notes: CHANGE AUDIO RECORDING

## Slide 5: System Overview
Bradley Blackburn

## Slide 6: System Block Diagram
Bradley Blackburn

## Slide 7: Workload Distribution
Solar Power System
Charge Controller
Control Relay System
PCB Power Supplies
Filtration System
Pump
Brad
Grant
RaspberryPi
Lucas
User Interface
UV Filtration
Kendra
IR Temp. Sensor
Spectroscopy
Bradley Blackburn

## Slide 8: Objectives and Demonstrable Goals
In-Line contaminant and temperature monitoring
Off-Grid Operation
Interactive User Interface
Bradley Blackburn
Notes: CHANGE AUDIO RECORDING

## Slide 9: Specifications
 | Subsystems | Specification
1 | Solar Power System | Full off grid operation, generating 12-24V, 12V battery
2 | Water Analysis | Raman Spectrometer @ 785nm, 24V 4-20mA IR temperature sensor
3 | User Interface | Control over system operation, display (via LCD) feedback/data from the system
4 | Charge Controller | 12V, maximum operating current 20A
5 | Filtration System | 2.9 gpm, class C UV lamp, (1) 5 micron sediment filter, (1) carbon filter
6 | RaspberryPi4B | 4GB memory, Quad core Cortex-A72 ARM 64-bit CPU, (2) USB 3.0 ports, (2) USB 2.0 ports
7 | Control Relay System | Opto22 I/O board, 60V/3A output modules, 12V AD relays
Bradley Blackburn
Notes: CHANGE AUDIO
Solar/Power Supply: Completely off-grid (solar charges battery, battery supplies power), 8 hours of autonomy minimum
Water Filtration: 5 micron and carbon filter, Class C UV lamp (originally 6.5 gpm) Around 3 gpm to meet filtration system requirement,
Water Analysis: Done through raman spectroscopy Temperature monitoring Snake Poison, Laundry Detergent, Chlorine
Water Quality: Water should be cleaned via the filtration system. Free of: Sediment, heavy metal, Benzene, Chlorine
Zinc Cyanide, Arsenic free, Water temp between 70 F and 50 F
Microcontroller: Must be able to interface the spectrometer being used, at least 2GB RAM, include USB2 or 3
UI: offer control over system, LCD touch screen, be able to connect/interface with microcontroller
https://pixabay.com/vectors/clipboard-student-writing-work-pen-2899586/

## Slide 10: Solar Power System
2 x 100 Watt Polycrystalline Solar Panels
1 x 12V/20A Charge Controller, Cirkits.com, Model:SCC3
1 x 12V 75 Ah Battery, UPG, UB12750
Bradley Blackburn
Notes: Polycrystalline: b/c cheaper option (mono twice the price), 36x26x1, 12 VDC ($239)
Charge controller: THE ORIGINAL came with panels, has 2 USB ports 5V/3A can power LCD/mcu, protection features (ovr curr, shrt circ, low/high bat V), has its own UI (traverse fns: charge type, bat type, display for V I and P)
Battery: 75 Ah at 12 V, sealed lead acid, Depth of discharge high for many cycles
https://www.amazon.com/gp/product/B07S6MHGS1/ref=ppx_yo_dt_b_asin_title_o01_s00?ie=UTF8&psc=1
UPG (Universal Power Group). (n.d.). Sealed Lead-Acid Battery. Http://Files.Upgi.Com:8086/UPGFileService.Svc/GetSpecSheet/46082 . Retrieved July 16, 2020

## Slide 11: Solar Alternative Components
Solar Cell Tech. | Differences | Price
Monocrystalline | Made of one type of silicon Higher efficiency | High
Thin Film | Flexible Space efficient | Medium
Charge Controllers |  | 
Shunt/Series | Short circuit and Current interruption implementation | Low
MPPT | High efficiency Mainly commercial application | High
Batteries |  | 
Lithium Ion | Large depth of discharge Substantial protection circuitry needed | High
AGM Lead Acid | Light weight Low internal resistance | High
Bradley Blackburn

## Slide 12: Control Relay System
Why?
  The RaspberryPi was not built to handle large external loads.
Bradley Blackburn

## Slide 13: Filtration Technologies Comparison
Filtration Technologies | Pros | Cons
Sediment | Removes rust, dust, heavy metals, and any particles equal or larger than the micron rating | Doesn't remove particles smaller than the micron rating and doesn’t remove pathogens
Activated Carbon | Removes particles sized .5 - 1 micron Positively charged activated carbon attracts all the negatively charged chemicals in the water like chlorine and sulfur Removes unwanted odors Can remove some strains of bacteria | Cannot remove small bacteria, viruses, or other small pathogens Can fill up fast if used independent of other filters
Reverse Osmosis | Removes bacteria and small particles from water | Expensive Filter can be eaten away by bacteria Wastes a lot of water
Distillation | Removes pathogen via boiling | Sediment is not removed Energy intensive method Slow output
Chemical Disinfectant | Eliminates bacteria and viruses | Unsuccessful in treating protozoan cyst and parasites Can be harmful if exposed to humans
UV Water Sanitation | Eliminates bacteria, viruses, protozoan cyst, and parasites | Requires prefiltering e.g. sediment and carbon filters
Grant Cooper

## Slide 14: Filtration System
  Viqua VT4-DWS/12 UV Filter 3.5GPM (Gallons per Minute)
  AWP110-2 5 Micron Sediment filter
  C-02PB Carbon Block Filter for taste and odour removal
Grant Cooper

## Slide 15: Pump Technologies Comparisons
Water Pumping Technology | Self-Priming | Output Volume | Debris Sensitivity | Current Draw
Impeller | No | Middle | Highest | Middle
Centrifugal | No | Highest | Lowest | Highest
Diaphragm | Yes | Lowest | Middle | Lowest
Grant Cooper

## Slide 16: Water System Pump
Flojet 03526-144A Triplex Diaphragm Automatic Water System Pump
Self-priming up to 10ft and can be run dry.
Automatic pumps feature a mechanism that will start the pump by the opening of a faucet.
Flow rate of 2.9 GPM (Gallons per Minute)
Operates on 12V DC
Grant Cooper

## Slide 17: PCB Block Diagram
12V 12A Voltage Regulator
24V .3A Voltage Regulator
PWM Charge Controller
Relay / MOSFET component control circuits
Raspberry Pi 4b GPIO Pins
Loads
5V 4.5A Voltage Regulator
Grant Cooper

## Slide 18: Voltage Regulators
Why separate PCBs?
0805 parts
If max current increases, complexity increases
Reality of Webench Power Supply Designer
Grant Cooper
Grant Cooper

## Slide 19: 5V 5A REGULATOR
Grant Cooper
LMZ22005 5-A SIMPLE SWITCHER Power Module With 20-V Maximum Input Voltage

## Slide 20: 24V .03A REGULATOR
Grant Cooper
TPS61170QDRVRQ1 Automotive 3V to 18V Wide Input Range, 1.2A Boost Converter

## Slide 21: 12V 12A REGULATOR
Grant Cooper
LM34936RHFR 30-V Wide VIN Synchronous 4-Switch Buck-Boost Controller

## Slide 22: UV Cleaning
The wavelength of light for UV sanitation is from about 100 nm to 260 nm, otherwise known as deep UV, or UVC
There are both lamps and LEDs that produce this wavelength of light can sanitize water.
12VMonster, 2020
Moore, Photonics Online (2015)
Servapure (2020)
Kendra Kordack

## Slide 23: UV Cleaning Requirements
100% lethal dosage is 16,000 μW-sec/cm2
Oram, Water Research Center 2020
Kendra Kordack

## Slide 24: IR Temperature Sensor
Contactless
Digital readout
Fast
2:1 ratio
Calex Electronics Limited
Calex Electronics Limited
Kendra Kordack

## Slide 25: Raman Spectroscopy
In-line monitoring
Water is a weak Raman Scatterer
NIR to avoid fluorescence
Stokes Raman scattering
Expensive
Li, Sensors (2014)
Wegner, Geo Chemistry Worldwide (2018)
Kendra Kordack

## Slide 26: Other Forms of Contaminant Evaluation
Chromatography
Inductively coupled plasma mass spectrometer
Buckner, Bio-Geochemical Methods (2020)
UC Berkeley (2020)
Kendra Kordack

## Slide 27: Raman Spectrometer
Specifications
785 nm
SMA Fiber connected
Oceanview Software
Powered through computer
  USB C
3.5x2x2 inch
Kendra Kordack

## Slide 28: Raman Spectrometer Laser Source
Specifications
785 nm
499 mW
FC Fiber Connector
5 volt intake

## Slide 29: Spectroscopy System
Kendra Kordack

## Slide 30: Contaminants
Contains 94.05% trichloro-s-triazinetrione and 5.95% other ingredients
Contains naphthalene (7%) and sulfur (28%) as its active ingredients. Snake-A-Way has greater than 91% repellency rate for rattlesnakes and garter snakes.
Contains multiple toxic chemicals including benzyl acetate, methylisothiazolinone, and calcium chloride.
Kendra Kordack

## Slide 31: Comparing Spectras
Three main Contaminant being observed:
Snake Poison
Laundry Detergent
Chlorine
Kendra Kordack

## Slide 32: Ocean View Raman Spectroscopy
Integration time: 40 ms
Boxcar width: 6
Shift range: 552.78-1084.42 cm^-1
Light and dark spectrum subtraction
Records Raman shift with graph and table
Kendra Kordack

## Slide 33: Clean Water Spectrum
Kendra Kordack

## Slide 34: Spectroscopy Constraints
Parts per billion
Exact contaminants
Over saturation
Consistent movement
Arsenic Raman Shift
Wiley & Sons, Spectrabase (2020)
Kendra Kordack

## Slide 35: Overall Connection
Spectrometer
Microcontroller
(RaspberryPi)
Display
USB connection
DSI Cable
Sensor
laser
Control
UV light
temperature
sensor
Laptop
PUMP
Lucas Heredia

## Slide 36: Microcontrollers
Initial idea failed
$ Cheaper $
Soldered directly on the PCB
Arduino library
Difficult to interface
5V/ 2.5-12V
SRAM 2kB
Flash 32kB
It was clear that a microcontroller be not able to have enough memory to process the data from the spectrometer.
Lucas Heredia

## Slide 37: Rock64 Alternative
The rocket64 was the first one our first
options for the microcomputer
$45
4GB Ram / variable
HDMI
USB
It didn’t work because it was not touchscreen friendly. Using raspberry the raspberry pi would be simpler to interface.
Lucas Heredia

## Slide 38: Raspberry pi 4b
So we needed to use microcomputer
that possess more memory and cpu.
1 MicroSD socket
4 USB ports
4 core Cortex-A72 (ARM v8) 64-bit
DSI
Having a standard DSI cable that can be easily connected to the standard was a big advantage of using the microcomputer
Can be powered by a 5V pin and GND
Lucas Heredia

## Slide 39: Display
We decided to use a touch screen because it would we wouldn’t need to connect it a pad to the computer by doing so it also make the device a fancier.
The display by choice connects using an DSI cable it is designed to be used in with raspberry pi the raspberry pi
The other microcomputers did not have a DSA cable making interfacing the components trickier
The display is easier to interface with the raspberry pi
Resolution: 800x600 pix
Lucas Heredia

## Slide 40: Operating systems
Windows
Linux
Mac
>
>
The microcomputer will run a Linux distro, Ubuntu specifically
Linux is free and has no patent
Windows requires a license to use and is patent
Mac requires license and it is locked by hardware
Windows would be good.
Lucas Heredia

## Slide 41: OmniDriver/ Spam
Libraries given by Ocean Insights to control the spectrometer
OmniDriver and spam are both java native
Since both libraries are native to java(yet compatible with other languages) we decided to program the application entirely natively
OmniDriver is higher level than Spam
We decide to not use Spam it requires us to develop the regression algorithms to finding peaks in the data, it would run the application more efficiently, but it is not worth the time.
Lucas Heredia

## Slide 42: Programming language
Omnidrive and scam were written in Java
Omnidrive is not compatible with Python
The Omnidriver is not compatible with python
Time to execute the application is negligible to the time required to filter the water
Application doesn’t require very high performance
Lucas Heredia

## Slide 43: UI frameworks
Java Swing vs JavaFX
JavaFX
Java Swing standard Library
Using JavaFX the design looks more modern
Java Fx frameworks can be easily designed using netbeans designer tool.
VS
Lucas Heredia

## Slide 44: Graphical User Interface Before After
Java fx UI
GUI zero
Lucas Heredia

## Slide 45
Every component is now being handled by python scripts since we gave up on interfacing omniDriver
We switched to using python Scripts to Handle the IO
GUIzero
adafruit_DHT
Rasperry GPIO
widgetlord.pi_spi
Lucas Heredia

## Slide 46: Overall Progress
Task | New Deadline | Status
Build Software and User Interface | 11/20/20 | Finished
Build Electrical Panel | 11/20/20 | Finished
Integration of whole system | 11/20/20 | Finished
Test | 11/22/20 | Finished
Implementation & Presentation | 11/28/20 | Finished

## Slide 47: Successes & Difficulties
Successes
  UV Filtration System
  Solar Power System
  User Interface
  Analyzing the water
Difficulties
  Temperature Sensor
  Displaying Spectrometer Data
Calex Electronics Limited
Spectrometer
RaspberryPi
Bradley Blackburn

## Slide 48: Final Budget
The original budget goal
  $1000
The actual amount spent
  $1848
Bradley Blackburn

## Slide 49: Thanks for watching!