## Slide 1: GREEN STEEL GARDEN
GROUP 11
RYAN AZORE CHRISTOPHER HODGE
JON POWELL JEHRON WILLIAMS
Senior Design II
University of Central Florida
Department of Electrical Engineering and Computer Science

## Slide 2: OBJECTIVES & GOALS
Automated Hydroponics System
  Capable of Growing 12 Plants
  Automatic Nutrient Dispersion & Balancing
  Automatic pH Balancing
  Mobile App
    Wi-Fi Connectivity
Increase Growing Efficiency
  Air Stone / Diffuser
  Humidity & Temperature detector
  Luminosity Detector
  Growing Light Cycles
  Enclosure Exhaust Fan

## Slide 3: SPECIFICATIONS & REQUIREMENTS
PCB with an integrated Wi-Fi and BT module
  Runs on 12 to 3.3 VDC.
  Microcontroller will operate at a frequency of no less than 16MHz
  Control relays to power on and off the lights and pump
  Communication of sensor data and pictures via Wi-Fi to data storage in cloud server
  Interfaces with a custom iOS app that will display pictures and sensor data
3 liquid storage containers
  pH Up
  pH Down
  Nutrient Solution
Auto-normalize elements in water back to specified levels in less than 1 hour
  pH Balance
  Nutrient Solution
Exhaust fan
  Restore temperature and humidity levels in less than 30 minutes.

## Slide 4: SPECIFICATIONS & REQUIREMENTS
The total cost of the build shall not exceed $1300
Power Supply will receive 120 V 60 Hz AC power and covert to 12 V DC
Growing System will be completely enclosed
The system will be able to grow 12 plants at one time
The system will have LED lighting
  Placed no less than 24” above plants
Feature | Desired Value
Dimensions | 24”x36”x72”
Number of Plants | 12
Water Capacity (Reservoir) | 5 Gallons
pH Balance adjust time | < 60 mins
EC Level adjust time | < 60 mins
PCB Operating Voltage | 12 Volts
Operating Environment | Indoors
Sensor Readout Time | < 60 seconds
Project Requirement Table

## Slide 5: SYSTEM DIAGRAM

## Slide 6: DESIGN DECISIONS – HYDROPONIC SYSTEM
Nutrient Film Technique
  Reservoir tank holding nutrient solution
    Aerator oxygenates tank water
  Sloped Grow Tray
    Water + Nutrient Solution is fed down through the slope, with excess liquid returning to the reservoir tank
  Compatible with automation features
    Constant Feedback system
  Cheap to construct
Nutrient Film Technique

## Slide 7: DESIGN DECISIONS – PLANT CHOSEN
Arugula
  Works with any Hydroponic Method
  pH Range
    6 – 7.5
  EC Range
    .8 – 1.2
  Necessary Hours of Light per Day
    12+
  Days for Germination
    7 - 10
Arugula Leaves

## Slide 8: DESIGN DECISIONS – GROWTH ENCLOSURE
Frame constructed of steel
  Provides better strength and durability compared to other competitors
  Offers fixed structure instead of a tent-like build
  Wheels are attached for easy indoor and outdoor mobility
Frame Construction

## Slide 9: COMPONENT DECISIONS – MICROPROCESSOR
Arduino Mega 2560
  Open source
    Makes PCB design easier
  54 digital I/O pins
    Standard Arduino
    Has enough connections for all the sensors used in the design
Arduino MEGA 2560

## Slide 10: COMPONENT DECISIONS – EC SENSOR
Atlas Scientific Conductivity Probe
Grove Electrical Conductivity Sensor

## Slide 11: COMPONENT DECISIONS – PH SENSOR
Atlas Scientific pH Probe
PH0-14 pH Sensor

## Slide 12: COMPONENT DECISIONS – MISCELLANEOUS
Air stone
  This is not a required component for the system to function, but it improves the efficiency of the growing process
Nutrients Solution
  Dry vs. Liquid
  Plant Determined
Growing Medium
  Rockwool
MaxiGro Dry Plant Food
Air Stone Demonstration
Rockwool Medium

## Slide 13: DESIGN CONSTRAINTS
Economic
  Many parts proved to be more expensive than initially overviewed
Environmental
  Temperature fluctuations are difficult to control outdoors, necessitating indoor use
Size
  The enclosure must be suitable for indoor use and must be adequately proportioned
Health & Safety
  pH buffers and nutrient solution can cause irritation due to potency
  Potential build up of foreign agents in system after regular use
Time
  Design must be functional and constructed by a certain deadline

## Slide 14: DESIGN STANDARDS
IEE 802.11 Standard
  Wi-Fi compatibility with modern networks
Serial Peripheral Interface (SPI)
  Interface supported by microcontroller
Inter-Integrated Circuit (I2C)
  Interface supported by microcontroller
Programming Language
  C Standard
ISO/IEC/IEEE 29119
  Standards for software testing

## Slide 15: BUDGET & FINANCE
Part | Quantity | Price
Peristaltic Pump | 3 | $9 .50
Silicone Tubing | 1 | $9.99
Wi-Fi Module (4) | 1 | $11.99
5” Caster Wheels | 1 | $29.99
Main Water Pump | 1 | $11.99
Main Water Reservoir | 1 | $16.47
Solutions Container (6) | 1 | $11.99
Arduino MEGA 2560 | 1 | $19.90
Wi-Fi Breadboard Adapters (5) | 1 | $9.99
Water Filter | 1 | $8.99
Water Level Gauge | 1 | $28.99
Steel Structure | 1 | $280.68
LED Lights | 1 | $39.99
Air Pump | 1 | $9.99
pH Solution | 1 | $20.05
Plant Nutrients | 1 | $15.99
EC Probe | 1 | $113.99
pH Probe | 1 | $55.99
Luminosity Sensor | 1 | $10.98
Power Supply | 1 | $12.77
Flow Meter | 1 | $9.49
Temperature & Humidity Sensor | 1 | $19.84
Grand Total | 24 Parts | $759.55

## Slide 16: NOTABLE SUCCESSES
Wi-Fi Connectivity
  Setting up Wi-Fi Module
  Defined protocol, address, and port
    AT + CIPSTART
    Thingspeak.com
ESP8266 Wi-Fi Breadboard Layout

## Slide 17: DIFFICULTIES ENCOUNTERED
Camera Compatibility
  Arduino’s do not possess enough storage and processing capabilities for high resolution camera capability
Arducam 8 (IMX219)
Despite the name being Arducam, the sensor equipped is only compatible with Raspberry Pi’s
Arducam Mini (OV2640)
This Camera module is 2 Megapixels only and does not offer the quality expected by early design requirements

## Slide 18: CURRENT PROGRESS
Chart: Progress by Category
| Enclosure | PCB | Testing | Software | Parts
Series 1 | 50 | 30 | 80 | 45 | 95
Column1
Column2

## Slide 19: FUTURE GOALS
Development Plans | 7-Oct | 15-Oct | 21-Oct | 30-Oct | 7-Nov | 14-Nov | 21-Nov | 30-Nov
PCB Development |  |  |  |  |  |  |  | 
Enclosure Construction |  |  |  |  |  |  |  | 
Mobile App Development |  |  |  |  |  |  |  | 
PCB Assembly & Testing |  |  |  |  |  |  |  | 
Sensor & PCB Integration |  |  |  |  |  |  |  | 
Final Assembly |  |  |  |  |  |  |  | 
Growing Tests |  |  |  |  |  |  |  | 
Table of Development Plans